## Slide 1: Investigating Differences in O3 Production from CB05 and CBMIV Versions of the NAQFC
Rick Saylor, Hsin-Mu Lin, Pius Lee, Binyu Wang, Tianfeng Chai,
Ariel Stein, Daniel Tong, Hyun-Cheol Kim, Yunsoo Choi,
Fantine Ngan, Daewon Byun
9th Annual CMAS Conference, Chapel Hill, NC, October 11-13, 2010

## Slide 2
Emissions:
EPA CEM anthropogenic inventories
2005 base year projected to current year w/ EGU
BEIS V3 Biogenic Emissions
Met Model:
North American Model (NAM)
Non-hydrostatic Multi-scale Model (NMM)
12 km x 60 Levels
AQ Model:
USEPA Community Multiscale Air Quality (CMAQ)
  CMAQ v4.6: 12 km/L22 CONUS Domain
  Operational: CBMIV gas-phase
  Experimental/Developmental: CB05/ AERO-4 PM
Output available on National Weather Service Air Quality Forecast Guidance website (http://www.weather.gov/aq)
  48 hour O3 forecasts from 06/12 UTC Cycles
  PM2.5 forecasts to be operational in FY2015
442 grid cells
268 grid cells
CONUS “5x” Domain
National Air Quality Forecast Capability

## Slide 3
CB05 Ozone > CBM4 Ozone
Mechanism differences
Reactions responsible for ozone production?
Differences in speciation?
Systemic differences
Precursor emissions?
Meteorological parameters?
Some process common to both CB05 and CBM4
CBM4
CB05
2009

## Slide 4
G. Yarwood, S. Rao, M. Yocke, and G. Whitten, Updates to the Carbon Bond Chemical Mechanism: CB05, Final Report to U.S. EPA, December 8, 2005.
Incorporates current (as of 2005) kinetic and photolysis data.
Extends the CB mechanism to better support PM modeling needs such as SOA formation.
Adds extra species and reactions to treat additional VOCs for air toxics study.
Includes effect of reactive chlorine emissions in VOC degradation and oxidant chemistry.
• Explicit methylperoxy radical, methyl hydroperoxide and formic acid.
• Lumped higher organic peroxides, organic acids and peracids.
• Higher aldehyde species ALDX making ALD2 explicitly acetaldehyde.
• Recycling of NOy from organic nitrates.
Additional NOx recycling from HNO3, N2O5 and HO2NO2.
• Higher peroxyacyl nitrate species from ALDX called PANX.
• Explicit terpene gas phase chemistry.
Updates to the Carbon Bond Mechanism: CB05 vs CBMIV

## Slide 5
= concentration of species i in the box (µg/m3)
= time dependent mixed layer height (m)
= emission of species i into the box (µg/m2-s)
= chemical production rate of species i within the box (µg/m3-s)
= dry deposition velocity of species i (m/s)
= background concentration of species i (µg/m3)
= concentration of species i above the mixed layer (µg/m3)
= mixing rate of background air (s-1)
Box Model Equations

## Slide 6
Simulation Conditions
Fixed mixing layer height = 1000 m,
No dry deposition,
No mixing with background air,
Fixed initial conditions: T = 298 K
p = 1 atm
RH = 50%
O3 = 10 ppbv
CO = 100 ppbv
CH4 = 1600 ppbv
NOx = all VOCs = 0
Zaveri and Peters (1999) JGR,
104, 30387-30415.

## Slide 7
Simulation Suite
Scenario | NOx (μmol m-2 h-1) | ISOP (μmol m-2 h-1) | RNMHC (mol NMHC/mol NOx) | CO (μmol m-2 h-1)
u001 | 5 | 0 | 10 | 800
u002 | 20 | 0 | 10 | 800
u003 | 40 | 0 | 10 | 800
u004 | 5 | 0 | 1 | 800
u005 | 20 | 0 | 1 | 800
u006 | 40 | 0 | 1 | 800
u007 | 5 | 0 | 100 | 800
u008 | 20 | 0 | 100 | 800
u009 | 40 | 0 | 100 | 800
r001 | 1 | 50 | 1 | 80
r002 | 5 | 50 | 1 | 80
r003 | 10 | 50 | 1 | 80
r004 | 1 | 50 | 0.1 | 80
r005 | 5 | 50 | 0.1 | 80
r006 | 10 | 50 | 0.1 | 80
r007 | 1 | 50 | 10 | 80
r008 | 5 | 50 | 10 | 80
r009 | 10 | 50 | 10 | 80
Hourly emission = E0 * cos(zenith angle)

## Slide 8
NMHC Species Apportionment
CBM4 | mol i/mol NMHC |  | CB05 | mol i/mol NMHC
PAR | 0.860 |  | PAR | 0.845
 |  |  | ETHA | 0.0075
ETH | 0.050 |  | ETH | 0.050
OLE | 0.010 |  | OLE | 0.005
 |  |  | IOLE | 0.005
TOL | 0.030 |  | TOL | 0.030
XYL | 0.020 |  | XYL | 0.020
HCHO | 0.010 |  | HCHO | 0.010
ALD2 | 0.020 |  | ALD2 | 0.015
 |  |  | ALDX | 0.005

## Slide 9
Sensitivity Tests
Name | Description (changes made to CB05 from base mechanism)
xNTRrecycle | NTR recycling reactions removed
xiNOxrecycle | inorganic NOx recycling reactions removed
xallNOxrecycle | both NTR and inorganic NOx recycling reactions
xPANX | all PANX reactions removed (no ALDX emissions)
xPANXrecycle | PANX recycling reactions removed
xPANrecycle | PAN recycling reactions removed
PANcbm4 | PAN chemistry as in CBM4 (xPANX + CBM4 PAN rate constants)
PANjpl06 | PAN and PANX rate constants from JPL 2006
xNTR-PANcbm4 | xNTRrecycle + PANcbm4 (no NTR recycle and CBM4 PAN chem.)
xNTR-PANcbm4-xPANX | xNTRrecycle + PANcbm4 + xPANX (no NTR recycle, CBM4 PAN chemistry, and no PANX chemistry)
xPANX-xNTR | xPANX + xNTRrecycle (no PANX chem. and no NTR recycle)
noALDXemis | no ALDX emissions and ALD2 emissions as in base CBM4

## Slide 10
Sensitivity Tests
Name | Description (changes made to CB05 from base mechanism)
xNTRrecycle | NTR recycling reactions removed
xiNOxrecycle | inorganic NOx recycling reactions removed
xallNOxrecycle | both NTR and inorganic NOx recycling reactions
xPANX | all PANX reactions removed (no ALDX emissions)
xPANXrecycle | PANX recycling reactions removed
xPANrecycle | PAN recycling reactions removed
PANcbm4 | PAN chemistry as in CBM4 (xPANX + CBM4 PAN rate constants)
PANjpl06 | PAN and PANX rate constants from JPL 2006
xNTR-PANcbm4 | xNTRrecycle + PANcbm4 (no NTR recycle and CBM4 PAN chem.)
xNTR-PANcbm4-xPANX | xNTRrecycle + PANcbm4 + xPANX (no NTR recycle, CBM4 PAN chemistry, and no PANX chemistry)
xPANX-xNTR | xPANX + xNTRrecycle (no PANX chem. and no NTR recycle)
noALDXemis | no ALDX emissions and ALD2 emissions as in base CBM4

## Slide 11
Production –
R55. ROR + NO2 → NTR
R64. TO2 + NO → NTR
R68. CRO + NO2 → NTR
R78. ISOP + NO3 → … + 0.8 NTR + …
R81. XO2N + NO → NTR
R92. ISPD + NO3 → … + 0.85 NTR + …
R94. ISOP + NO2 → … + 0.8 NTR + …
No chemical destruction of NTR in CBM4,
thus NTR is an irreversible sink for reactive nitrogen in CBM4.
Organic Nitrate (NTR) Chemistry in CBM4

## Slide 12
Production –
R115. ROR + NO2 → NTR
R129. TO2 + NO → … + 0.1 NTR + …
R133. CRO + NO2 → NTR
R144. ISOP + NO3 → … + 0.8 NTR + …
R55. XO2N + NO → NTR
R147. ISPD + NO3 → … + 0.85 NTR + …
R156. ISOP + NO2 → … + 0.8 NTR + …
R152. TERP + NO3 → … + 0.53 NTR + …
Destruction –
R61. NTR + OH → HNO3 + …
R62. NTR + hν → NO2 + HO2 + …
Reactive N is recycled back into the gas phase via R61 & R62. NTR is an irreversible N sink in CBM4, but is a reversible temporary reservoir of N in CB05.
Organic Nitrate (NTR) Chemistry in CB05
xNTRrecycle

## Slide 15
R51. HO2NO2 + hν → 0.61 HO2 + 0.61 NO2 + 0.39 OH + 0.39 NO3
R52. HNO3 + hν → OH + NO2
R53. N2O5 + hν → NO2 + NO3
CBM4 does not include these recycling pathways for NOx.
NOTE: Removing these in the box model sensitivity test will likely overestimate the effect it will have on ozone in the full 3-D model because some HO2NO2, HNO3 and N2O5 will be removed via other processes (e.g., deposition and heterogeneous reactions).
Inorganic NOx Recycling Reactions in CB05
xiNOxrecycle

## Slide 18
NTR and Inorganic NOx Recycling Reactions in CB05
R51. HO2NO2 + hν → 0.61 HO2 + 0.61 NO2 + 0.39 OH + 0.39 NO3
R52. HNO3 + hν → OH + NO2
R53. N2O5 + hν → NO2 + NO3
R61. NTR + OH → HNO3 + …
R62. NTR + hν → NO2 + HO2 + …
xallNOxrecycle

## Slide 21
With NTR recycling reactions removed from CB05, differences in O3 between CB05 and CBM4 are substantially reduced (accounting for 40-50% of ∆O3).
CB05 – CBM4 Ozone
CB05-xNTR – CBM4 Ozone

## Slide 22
Box model sensitivity tests indicate that the primary causes of higher ozone biases from CB05 simulations are the additional NOx recycling pathways that were added to better represent the fate of NOx over multi-day timescales. This has resulted in a larger “effective” NOx level in the model (even with the same NOx emissions), which results in more O3 production.
Next Steps
Full-model sensitivity tests are underway to confirm the results of the box model simulations (results so far do confirm).
Future work will investigate individual chemical formation pathways of organic nitrates, compare predicted organic nitrate concentrations with available measurements, review all reactive N deposition parameters, and systematically re-evaluate NOx emission sources.
Conclusion