## Slide 1: Ambient Air Monitoring Networks
2010 CMAS Conference
Chapel Hill, NC
October 13, 2010
Rich Scheffe, Sharon Phillips, Wyatt Appel, Lew Weinstock, Tim Hanley, Nealson Watkins, Mike Jones, Kevin Cavender, Karen Wesson, Kirk Baker
- networks - observations and models - unique challenges associate with fine scale, multiple pollutant applications

## Slide 2: The Basic Networks

## Slide 8
PM2.5 Chemical Speciation Network (CSN) and IMPROVE

## Slide 11: Current areas of focus
Implementing NCore
New NO2 , lead and ozone requirements
School air toxics

## Slide 12: National Core (NCore) Network
  urban (about 63 sites)
  rural (about 17 sites)
  May achieve additional rural coverage with National Parks and CASTNET
Pollutants Measured - NAAQS multi-pollutant
  Particles
    PM2.5 - continuous mass, filter mass, speciation
    PM10-2.5 - mass
  Gases – O3 and high sensitivity measurements of CO, SO2, NO and NOy.
  Meteorology - basic meteorological parameters
    Temperature, Wind Speed, Wind Direction, Relative Humidity

## Slide 13
Minimum Near-Road NO2 Monitoring Requirements
Near Road NO2 Monitors Are Required in 102 Urban Areas
78 areas would require 1 monitor (> 500,000 population)
24 areas would require 2 monitors (> 2.5 million population or road segments with annual average daily traffic counts > 250,000 vehicles)
126 total monitors
Not shown on map
Anchorage, Alaska
Honolulu, Hawaii
San Juan, Puerto Rico
Approximately 40 additional monitors will be placed in locations to help protect communities that are susceptible and vulnerable to NO2-related health effects
Monitors required no later then January 1, 2013

## Slide 14
Community-Wide NO2 Monitors Are Required in 53 Urban Areas
Minimum Community-wide NO2 Monitoring Requirements
53 areas would require 1 monitor (> 1 million population)
418 existing NO2 monitoring sites in 2008 Many of these sites would satisfy the proposed community-wide monitoring requirements.
Not shown on map
San Juan, Puerto Rico
Honolulu, Hawaii
Monitors required no later then January 1, 2013

## Slide 15
*
* Proposed requirement

## Slide 16
MSAs highlighted in magenta may need to add ozone monitors based on proposed requirements

## Slide 17
Revising the Ozone Monitoring Seasons

## Slide 18
Revising the Ozone Monitoring Seasons

## Slide 19
School Air Toxics (short term, in response to USA Today)

## Slide 20: Why do we measure the air? Role of Observations and Models
Remember, traditional regulatory use drives network design
Models have been an untapped (or at least underutilized) resource for exposure/health assessments
  Solid linkage from regional to global scale characterization partly due to similar disciplines across EPA, NASA, NOAA, NCAR, Academia
  The link to fine scales is in an exploratory mode
Characterization of air quality over time, ambient space and composition is inherently a responsibility of the atmospheric science/modeling community
  What happens when that community does not prioritize for support of health assessments

## Slide 21: Acknowledge
Basic incommensurabilities between measurements and modeled estimates
  Point vs volume representation
  Instrument artifacts
    Yield a method defined estimate
  Modeled constraints
    Emissions limits
    Chemical/physical formulations

## Slide 22: Multiple Pollutant Considerations
Additional Pollutant Groups, particularly HAPs place greater emphasis on fine scale exposures
Challenge in availability of data bases for fine scale model evaluations and ability of models to match observations in time, space

## Slide 23
.
Nexus of ozone, PM2.5 (2003-5) and air toxics (NATA 1999)
High Risk Counties often Coincide with Locations where
Criteria Pollutant Issues are Significant -
Draft

## Slide 24
Multiple space and time scales
when addressing MPs
Source, K. Demerjian

## Slide 26: Detroit PM: 1km STN sites

## Slide 27: Near field Process considerations

## Slide 28
Source, K. Demerjian
Local (near source) scale processes

## Slide 29: Roadway Pollution Gradients
Source: S. Cal PM Center, 2004

## Slide 30: Model evaluation and human exposure applications
Terminology
  Operational
    Focuses on the statistical and qualitative relationship between observations and terminal model species
  Diagnostic
    Do the model processes work as intended,
    are we getting the right answers for the right reasons?
  Dynamic
    Does the model response to perturbations in inputs (emission, meteorology) reflect observed response to same changes?
  Probabilistic
    Bound model estimates
Model evaluation of regulatory models has focused on urban/regional scale applications
  NOAA, NASA field programs
    Regional to hemispherical scale
  Relatively close alignment between process based field campaigns and model evaluation
Analog with observation design for human exposure studies may(or may not) be as closely aligned

## Slide 31: How do we develop fine scale model evaluation data bases?