## Slide 1: Understanding fine particle episodes in the Upper Midwest during the 2009 LADCO Winter Nitrate Study using CMAQ and CAMx: model performance, processes, and response to emissions controls
Charles Stanier – University of Iowa
charles-stanier@uiowa.edu
319-335-1399
CENTER FOR GLOBAL AND REGIONAL ENVIRONMENTAL RESEARCH

## Slide 2: Co-authors and Acknowledgements
University of Iowa
  Scott Spak
  Gregory Carmichael
  Charles Stanier
  Jaemeen Baek
  Sang Rin Lee
  Yoo Jung Kim
  Timothy Rohlf
  Sinan Sousan
  Ashish Singh
University of Illinois
  Nicole Riemer
EPRI
  Stephanie Shaw
  Naresh Kumar
Measurements
  Eric Edgerton (ARA Inc)
  Mike Caughey (ISWS)
  Wisconsin DNR staff
  Joe Leair, Jerry Medinger, Dan Nickolie, Mary Mertes, Bruce Rodger, and Bart Sponseller
  Site operators by John Hillery, Janel Hanrahan, Laura Carnahan
LADCO (Lake Michigan Air Directors Consortium)
  Michael Koerber
  Donna Kenski
  Mark Janssen
  Abigail Fontaine
Wisconsin DNR
  Michael Majewski
  Bill Adamski
Funding
  LADCO
  Electric Power Research Institute

## Slide 3: Motivation?
Recurrent cold weather PM2.5 episodes greatly influence air quality in this region.
Similarities to California’s Central Valley (Pun and Seigneur 1999; McMurry, Shepherd et al. 2004) and to Northwestern Europe and the Po Valley of Italy (Schaap, van Loon et al. 2004; Putaud, Van Dingenen et al. 2010).
What is known?
  Episodes are tightly coupled with meteorological conditions.
  Ammonium nitrate comprises a large fraction of the PM2.5 during episodes.
  Chu 2004; McMurry, Shepherd et al. 2004; Blanchard and Tanenbaum 2008; Klatzman, Rutter et al. 2009; LADCO 2009; Pitchford, Poirot et al. 2009.

## Slide 4
LADCO Winter Nitrate Study
(Jan 1 – Mar 31, 2009)

## Slide 5
Species | Averaging time (hr) | Species | Averaging time (hr)
PM2.5 | 1hr | PM2.5 | 24hr 1 in 3days
SO4 | 1hr | NH4 | 24hr 1 in 3days
NO3 | 1hr | NO3 | 24hr 1 in 3days
NH4 | 1hr | SO4 | 24hr 1 in 3days
HNO3 | 1hr | OC | 24hr 1 in 3days
NH3 | 1hr | EC | 24hr 1 in 3days
NOy | 1hr | O3 | 1hr
NOx (note 6) | 1hr | Relative Humidity | 1hr
SO2 (note 7) | 1hr | Surface pressure | 1hr
Temperature | 1hr | Visibility | 1hr
Wind Speed | 1hr | Precipitation | 1hr
Wind direction | 1hr | HNO3 | 24hr
NH3 | 24hr | H2SO3, H2SO4 | 24hr

## Slide 6
Science Questions for the Study
Composition: Typical chemical composition during episodes and non-episodes?
Urban-rural contrast: Differences in PM2.5 concentrations (frequency and severity), chemical composition, and source regions?
Meteorology: What meteorological conditions favor winter-time episodes? How can we best use this information to improve wintertime episode forecasting?
Nitrate formation chemistry: What do the data tell us the nitrate formation chemistry leading to events?
Sensitivity of episodes: How sensitive are concentrations to hypothetical changes in total nitrate, total ammonia, and total sulfate? What sources categories have leverage on episodes? Do local sources have influence?
3D Model skill: Can photochemical modeling accurately predict PM2.5 concentrations during the observed winter-time episodes?

## Slide 7
Parameter | Milwaukee (Urban) | Mayville (Rural)
PM2.5 (µg m-3) | 17.1 | 11.7
Total nitrate (µg m-3) | 5.6 | 4.8
Total ammonia (µg m-3) | 3.3 | 3.3
Gas ammonia (ppb) | 2.3 | 2.4
Nitrate aerosol / total nitrate | 78% | 69%
NOy (ppb) | 27 | 6.3
Temperature (°C) | -3 | -5
Ozone (ppb) | 22 | 31
OC (µg m-3) | 3.6 | 3.2
EC (µg m-3) | 0.5 | 0.3
Gas Ratio (d’less) | 1.5 | 1.7
60
40
20
0
PM2.5 (µg m-3)
Jan
Feb
Mar

## Slide 8
Detailed view of an episode
Agreement between multiple independent measurements

## Slide 9
Composition
Gas ratios (ammonia availability) ranges 1.0-1.7. Lowest at the rural site during episodes. Evidence of gas ratio ↓ during episodes at multiple sites in the region.
PM2.5 (µg m-3)
PM2.5 fraction

## Slide 10
Urban-Rural Contrast During Episodes
Some excess in total nitrate, but nitrate and ammonium appear predominantly regional.
For aerosol species, urban excess of OC during episodes is significant.

## Slide 11
Meteorology
Episodes began under similar synoptic conditions – arrival of a surface low pressure system.
Episodes were marked by inversions with warm, moist air and low wind speeds.
Snow cover and fog were both correlated with episode occurrence.
Regional snow cover was present over southeastern Wisconsin and northern Illinois at the onset of late winter episodes and usually melted by episode end.

## Slide 12: Model Configuration
Community Multiscale Air Quality Model (CMAQ) v4.7.1
  CB05 gas phase / AERO5 aerosol module
  ACM2 PBL closure
  Mass-conserving advection
  14 vertical layers
LADCO’s 12 km regional modeling grid
  Hourly boundary conditions from a 36 km simulation (with the same configuration) covering the continental United States.
Meteorology
  WRF 3.1.1 with the RPO configuration selected by Iowa DNR, SESARM, and LADCO
  ACM2 PBL closure
  Pleim-Xu land surface module
  RRTM radiation
  Morrison microphysics
  Kain-Fritsch cumulus
  Boundary meteorology from the North American Regional Reanalysis 3-hourly
  Analysis nudging on NARR above the PBL (no direct observational nudging)
Emissions
  LADCO’s 2008 emissions inventory used for 12km domain.
  Day-specific biomass burning emissions from MODIS fire detection products.
  NEI with day- specific biomass burning will be used for 36 km continental simulations.
Process Analysis
  Chemical and process rates stored for all layers up to 550 m, with focus on NOy processing and N2O5 heterogeneous chemistry

## Slide 13: Model Skill
Chart: PM2.5 (µg m-3)
Network | Species | Observed | Model
AQS | Ozone | 29.8 | 35.0
Improve | PM2.5 | 7.0 | 8.6
 | SO4 | 1.8 | 2.6
STN | PM2.5 | 12.1 | 15.4
 | NO3 | 3.0 | 3.0
 | NH4 | 1.7 | 2.0
 | SO4 | 2.4 | 3.6

## Slide 14
Model Skill
Total ammonia underprediction during almost all periods and sites.
Shows as deficit in gas phase ammonia.
Nitrate underprediction during episodes.
Systematic OC underprediction (not shown) but offset by CMAQ other inorganics

## Slide 15
Reaction | Reactants | Products
R1 | NO2 + hν | NO + O
R3 | O3 + NO | NO2
R4 | O + NO2 | NO
R5 | O + NO2 | NO3
R6 | O + NO | NO2
R7 | NO2 + O3 | NO3
R14 | NO3 | NO2 + O
R15 | NO3 | NO
R16 | NO2 + NO | 2 NO2
R17 | NO3 + NO2 | NO + NO2
R18 | NO3 + NO2 | N2O5
R19 | N2O5 + H2O | 2 HNO3
R20 | N2O5 + H2O + H2O | 2 HNO3
R21 | N2O5 | NO3 + NO2
R22 | NO + NO + O2 | 2 NO2
R23 | NO + NO2 + H2O | HONO
R24 | NO + OH | HONO
R25 | HONO | NO + OH
R26 | OH + HONO | NO2
R27 | HONO + HONO | NO + NO2
R28 | NO2 + OH | HNO3
R29 | OH + HNO3 | NO3
R30 | HO2 + NO | OH + NO2
R31 | HO2 + NO2 | PNA
R32 | PNA | HO2 + NO2
R33 | OH + PNA | NO2
R46 | NO3 + O | NO2
R47 | NO3 + OH | HO2 + NO2
R48 | NO3 + HO2 | HNO3
R49 | NO3 + O3 | NO2
R50 | NO3 + NO3 | 2 NO2
R51 | PNA | 0.61HO2 + 0.61NO2 + 0.39OH + 0.39NO3
R52 | HNO3 | OH + NO2
R53 | N2O5 | NO2 + NO3
R89 | PAN | C2O3 + NO2
R90 | PAN | C2O3 + NO2
Integrated
Reaction
Rate
Analysis

## Slide 16: Nitrate formation analysis by process analysis
NO2 + OH  HNO3 (R1)
NO2 + O3  NO3 + O2 (R2)
NO3+NO2 ↔ N2O5 (R3)
N2O5  NO2 + NO3 (R4)
NO3 + VOC organic products (R5)
N2O5 + H2O  2HNO3 (R6)
RH and composition dependent accommodation
coefficient, uncertain
Daytime
Averages 0.075 ppb/hr in surface layer
Nighttime
Averages
0.044 ppb/hr
in surface layer

## Slide 17
Chart: Milwaukee
| 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
hom. hydrol. | 0.015293 | 0.01852 | 0.020133 | 0.020195 | 0.019311 | 0.016914 | 0.013969 | 0.010173 | 0.010173 | 0.008665
OH+NO2 | 0.026715 | 0.030247 | 0.033854 | 0.037399 | 0.04116 | 0.045651 | 0.050605 | 0.063367 | 0.063367 | 0.074753
het. hydrol. | 0.046584 | 0.055548 | 0.06197 | 0.063532 | 0.061584 | 0.056984 | 0.051976 | 0.041586 | 0.041586 | 0.034839
Chart: Mayville
| 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
hom. hydrol. | 0.010187 | 0.013898 | 0.017944 | 0.021802 | 0.024654 | 0.025012 | 0.022732 | 0.018079 | 0.012835 | 0.0097221
OH+NO2 | 0.017003 | 0.020471 | 0.023331 | 0.025925 | 0.027982 | 0.029708 | 0.031146 | 0.03281 | 0.034808 | 0.03752
het. hydrol. | 0.039844 | 0.054407 | 0.066156 | 0.076696 | 0.087127 | 0.09234 | 0.09469 | 0.095352 | 0.095283 | 0.093306

## Slide 18: Emissions Sensitivity: Emissions Scenarios
30% NOx from base case
30% NH3 from base case
2015 Proxy Case
  Simulate near-term changes in mobile NOx & simulate approximation of implementation of Cross State Air Pollution Rule (CSAPR) effect on coal-fired power plant NOx & SOx emissions
  -70% EGU SO2
  -10% EGU NOx
  -30% mobile NOx
Additional scenarios: add all-sector reductions to the 2015 Proxy Case
  - 30% NH3
  - 30% NOx
  - 30% NH3 & - 30% NOx

## Slide 19: Emissions Sensitivity Methods
Direct Sensitivity
Hybrid Box Model Sensitivity
  Input to sensitivity case box model?
  Measured T and RH
  Measured total sulfate, ammonia, and nitrate x fractional reduction in these species predicted by CMAQ model

## Slide 20
Thermodynamic Sensitivity / Model Skill
Chart: Direct CMAQ Sensitivities to Emissions versus ISORROPIA Model Hybrid of Modeled and Measured Values (During hours with > 27 µg m-3 measured PM2.5)
| 30% NOx | 30% NH3 | 2015 Proxy | 2015 Proxy + 30% NOx | 2015 Proxy + 30% NH3 | 2015 Proxy + 30% NOx, 30% NH3
Milwauk CMAQ | 1 | 19
Milwauk Hybrid | 2 | 20
Mayville CMAQ | 6 | 14
Mayville Hybrid | 3 | 21

## Slide 21
30% NOx Cut only reduces TNO3 by less than 12%
30% NH3 Cut reduces TNH3 by 22% or more
30% NH3 Cut reduces PM2.5 by 10-15%
PM ↓
PM ↑
Graphing % Reduction TNO3 Case: 30% NOx Cut
Graphing % Reduction TNH3 Case: 30% NH3 Cut
Graphing % Reduction PM2.5
Case: 30% NOx Cut
Graphing % Reduction PM2.5
Case: 30% NH3 Cut

## Slide 22
Conclusions – A refined conceptual model of wintertime episodes in the Upper Midwest
Composition: Confirming results from past studies. Database of time-resolved concentrations now available.
Urban-rural contrast: More episodes recorded at urban site. Urban primary pollutant enhancement quantified. Urban secondary enhancement <20% of inorganic total on average.
Primary sources? Local primary OC important. Role of primary local NOx under investigation with CMAQ.
Meteorology: Meteorology critical to episode occurrence and prediction. Stagnant low pressure systems, warmer than average temperatures, low wind speeds, low mixing heights. Snow cover, snow melt, and fog correlated with episodes.
Nitrate formation chemistry: Both daytime and nighttime pathways important.
Sensitivity of episodes: Direct modeled sensitivity from CMAQ is fairly accurate despite low NH3 bias. System responds to either reductions in total nitrate or total ammonia, but NOx controls inefficient at delivering total nitrate reduction in NOx source regions. Impact of local vs. regional NOx reductions under investigation.
3D Model skill: Fairly skilled, especially on average. Mixed skill for timing and intensity of individual episodes.

## Slide 23: Thank You!
Full reports on LADCO Winter Nitrate Study available at ladco.org and on Stanier group website
Questions?

## Slide 24: Nitrate formation analysis by process analysis
NO2 + OH  HNO3 (R1)
NO2 + O3  NO3 + O2 (R2)
NO3+NO2 ↔ N2O5 (R3)
N2O5  NO2 + NO3 (R4)
NO3 + VOC organic products (R5)
N2O5 + H2O  2HNO3 (R6)
RH and composition dependent accommodation
coefficient, uncertain
Daytime
Averages 0.075 ppb/hr in surface layer
Nighttime
Averages
0.044 ppb/hr
in surface layer

## Slide 26
Model Skill Continued… Gas Ratio Prediction Skill
Measurements 1.0 – 1.7. Model low on ammonia, but also low on sulfate and nitrate. Model range 1.1 – 1.5.

## Slide 27
Model Skill … Additional Evaluation Using Diurnal Patterns
Model Observations
Temp.
Nitrate
Sulfate

## Slide 28: Ammonia Availability
NH3 rich
NH3 poor

## Slide 29: Approach
Run ISORROPIA for every hour of the study using 400 different cases with varying reductions in
  Total ammonia (10), total sulfate (4), and total nitrate (10)
Make contour plots showing ammonia vs. nitrate sensitivity for constant sulfate cases.

## Slide 32
Comparison to Blanchard Midwest Ammonia Monitoring Project

## Slide 33
1A
2A
3A
4A
5A
1E
3E
4E
5E
Great River Bluffs MN (A=DJF avg; E=Feb 3, 2005 episode)
Mayville WI (A=DJF avg)
Lake Sugema IA (A=DJF avg; E=Feb 3, 2005 episode)
Bondville IL (A=DJF avg; E=Feb 3, 2005 episode)
Allen Park MI (A=DJF avg; E=Feb 3, 2005 episode)
a Mayville (JFM avg; no episodes)
b Mayville (JFM avg; all hours)
c Mayville (JFM avg; episodes)
d Milwaukee (JFM avg; no episodes)
e Milwaukee (JFM avg; all hours)
f Milwaukee (JFM avg; episodes)
a
b
d
e
c
f
Milwaukee (d-e-f)
Lake Sugema
Mayville study-study comparison
Mayville episodes

## Slide 34
1A
2A
3A
4A
5A
1E
3E
4E
5E
Great River Bluffs MN (A=DJF avg; E=Feb 3, 2005 episode)
Mayville WI (A=DJF avg)
Lake Sugema IA (A=DJF avg; E=Feb 3, 2005 episode)
Bondville IL (A=DJF avg; E=Feb 3, 2005 episode)
Allen Park MI (A=DJF avg; E=Feb 3, 2005 episode)
a Mayville (JFM avg; no episodes)
b Mayville (JFM avg; all hours)
c Mayville (JFM avg; episodes)
d Milwaukee (JFM avg; no episodes)
e Milwaukee (JFM avg; all hours)
f Milwaukee (JFM avg; episodes)
a
b
d
e
c
f
Milwaukee (d-e-f)
Lake Sugema
Mayville study-study comparison
Mayville episodes
I
II
III
IV
I nitrate sens > ammonia sens
II balanced sensitivity
III ammonia sens > nitrate sens
IV only sensitive to ammonia

## Slide 35: Future Work
Modeling episodes at 12 km with CMAQ
Look at sensitivity in model versus measured sensitivity
Look at skill for total ammonia and total nitrate
Investigate skill for total nitrate (and NOx and NOy) temporal and spatial patterns
Investigate link between O3 and nitrate formation

## Slide 36: Supporting slides

## Slide 42
January 22 (11 am) January 24 (11 am)
2009 2009

## Slide 45
Ammonia
PM
NOx
Local Reaction
NOx → Nitric Acid
Reacted NOx
Nitric Acid
Regionally Transported Pollutants
Emissions from Local Counties
PM NOx Ammonia
Gases
NOx
Ammonia
Nitric Acid
Nitrogen Leaving the Balance as Gas
Ammonium
Nitrate PM
Facility Specific
Emissions Within ~3 km
Human Exposure to Mixed PM
Regional “Other” PM – Ammonium Sulfate, Organics
Local Primary PM – e.g. Vehicle & Industry Emissions
weather
ammonia
Nitric acid

## Slide 46: Each winter is very different

## Slide 47
Species | Ox State | Compound Class
N2O5 | +5 | NOy
HNO3 | +5 | NOy
NO3- ion | +5 | NOy
PAN | +5 | NOy
NO3 radical | +5 | NOy
HONO | +3 | NOy
NO2 | +4 | NOx & NOy
NO | +2 | NOx & NOy
NH4+ ion | -3 | RN
NH3 | -3 | RN

## Slide 54: Monthly mean emissions (2001 NEI)
BC
NH3

## Slide 55: Monthly mean emissions (2001 NEI)
NOx
SO2