## Slide 1: RLINE: A Line Source Dispersion Model for Near-Surface Releases
Presented at the 12th Annual CMAS Conference, Chapel Hill, NC
October 28 – 30, 2013
Saravanan Arunachalam1, Michelle G. Snyder2, Akula Venkatram3,
David K. Heist2, Steven G. Perry2, Vlad Isakov2
1UNC/IE, 2U.S.EPA/NERL/AMAD, 3UCR

## Slide 2
Source: Rowangould, Transport Research Part D, 2013
Background
59.5 million people live within 500m of roads with > 25,000 Annual Average Daily Traffic (AADT)

## Slide 3
Illustrative AADT in Urban Area
Source: Michigan DOT

## Slide 4
Why was RLINE Developed?
Based on Science Advisory Board and the National Research Council recommendations, EPA-ORD initiated research on near-road air quality and health effects
Field measurements indicated that exposures to traffic-emitted air pollutants near roads can be influenced by complexities of roadway configurations (noise walls, depressed sections, etc.)
To improve exposure metrics for future health studies, ORD initiated model development project to account for these important parameters

## Slide 5
What is RLINE?
RLINE is EPA -ORD's research dispersion modeling tool for near roadway assessments
based on a steady-state Gaussian formulation
currently formulated for near-surface releases
contains new formulations for the vertical and lateral
dispersion rates
accounts for low wind meander
includes M-O similarity profiling of winds near the surface
uses the surface meteorology provided by AERMET
includes user-friendly input requirements for road network

## Slide 6
EPA-ORD: Model Development Focus
  Account for near-road complexities and very near road concentrations (i.e., within a few meters of the road)
  Design and conduct wind tunnel and field studies for development and evaluation of improved line source algorithms
  RLINE is
    initial modeling product of this development program
    research tool designed primarily to support risk assessments and health studies related to near-road pollutants

## Slide 7
What RLINE is NOT?
RLINE is not designed for regulatory applications (e.g., NAAQS enforcement, New Source Review, PM Hot Spot Conformity, SIP analyses, etc).
It is contained in a research platform and has not gone through the rigorous review and public comment required for inclusion in the list of recommended regulatory models

## Slide 8
Model Algorithm
Steady-state, Gaussian based plume model
Concentration at a receptor is the integrated contributions from points along the line using a Romberg Iteration Scheme.
where
and
For each point source within the integration, a wind-direction following plume is simulated.
Plume
For each point source within the integration, meander is handled in the same way as
AERMOD point source meander.
Meander
Snyder et al, Atmos. Environ, 2013

## Slide 9
Model Algorithm
RLINE uses the meteorological inputs from the AERMOD met. preprocessor (u*, w*, mixing height, Lmo, z0, Wspd, Wdir, heat flux, T) then corrects u* for light wind conditions.
Other surface parameters are then recalculated to be internally consistent with M-O theory.
This method was developed and evaluated by Qian and Venkatram (BLM 2011).
Meteorological Inputs
Concentration is a function of mean plume height (similar in nature to the effective parameter concept used in AERMOD).
Mean Plume Height
Snyder et al, Atmos. Environ, 2013

## Slide 10
Model Development Databases
Tracer Studies
  Idaho Falls 2008
  Prairie Grass
Wind Tunnel Studies
Field Studies
  Raleigh, Detroit, Phoenix

## Slide 11
How is RLINE being used?
The model can support health and risk assessments, epidemiology studies, and community based tools.
RLINE is designed to handle urban situations with thousands of line sources and receptors.
RLINE is used in a) “Near-Road EXposures to Urban air pollutants Study” (NEXUS) in Detroit examining the role of near-road exposures on asthmatic children who live near major roadways; b) Portland, ME and c) North Carolina Piedmont
RLINE can be used to estimate spatial variability in urban areas with many roadways.
See Talks by Snyder et al, and Chang et al, and Poster by Isakov et al.

## Slide 12
How does RLINE support community tools?
R-LINE algorithm is used in C-LINE, a decision support tool for evaluating effects of alternate transportation options on community health
EPA’s C-LINE Tool
See Poster by Barzyk et al

## Slide 13
Ongoing Development Work
The model framework is designed to accommodate algorithms for simulating near-source effects of complex roadway configurations (noise barriers, depressed roadways, roadway vegetation, etc).
These configurations could be used in mitigation, to reduce exposure near high emission roadways.
Finn et al., Atmos. Environ., 2010
_____ no barrier
------ barrier
Idaho Falls 2008 tracer study

## Slide 14
Field and wind tunnel studies show noise barriers and depressions reduce downwind concentrations under multiple stability conditions. These features are being added to the flat terrain RLINE model.
Field studies
Ongoing Development Work

## Slide 15
  4 models applied for 2 Tracer Studies
    Idaho Falls 2008
    CalTrans Highway 99
  All models showed ability to estimate majority of observations within a factor of 2
  Models performed best for near-neutral conditions in both tracer studies
    Mixed results in convective and stable conditions
Inter-comparison against other models
Heist et al, Trans. Res. D, 2013
AERMOD-A
AERMOD-V

## Slide 16
  Uses hourly meteorological data from AERMET v12345
    Similar to AERMOD applications
  Contains updated σy and σz formulations
    See Venkatram et al, 2013
  Can handle inputs in the form of activity (in AADT) or emissions (in g/m/s)
    AADT outputs can be post-processed with TAFs and species-specific emissions to obtain variable emissions
    Output in μg/m3
  Produces grouped source outputs
    Hourly (for entire simulation period or monthly)
    Daily average
Features in Release Version of RLINE

## Slide 17
  Analytical solution for near-source receptors
    Speeds up computation
  Input # lanes per roadway
    Spreads emissions over the lanes of traffic
  Solid/noise barrier algorithm
  Depressed roadway algorithm
Features Available as Beta Options

## Slide 18
  Summer 2013: Availability of pre-release version announced via Community Modeling & Analysis System (CMAS) website
  November 2013: Full public release expected via CMAS to include:
      Explanation of model code, use, and inputs required
      Documented evaluation and evaluation data
      Qualifications on appropriate use
  Spring/Summer 2014: Planned repository of tools and utilities for pre- and post-processing to support user community
Where to get RLINE from?

## Slide 19
Disclaimer: Although this work was reviewed by EPA and approved for publication, it may not necessarily reflect official Agency policy.

## Slide 20
Backup Slides

## Slide 21
Model Algorithm
New Dispersion Formulations
Vertical Dispersion
Venkatram et al, Atmos. Environ, 2013

## Slide 22
Lateral Dispersion
Model Algorithm
New Dispersion Formulations
Prairie Grass
Venkatram et al, Atmos. Environ, 2013

## Slide 23
Wind tunnel studies
Baldauf et al, 2009
Flat terrain
Downwind barrier
Depressed Roadway
Heist et al, Atmos. Environ, 2009
Ongoing Development Work
H = 6 m