## Slide 1: Developing a High Spatial Resolution Aerosol Optical Depth Product Using MODIS Data to Evaluate Aerosol During Large Wildfire Events
STI-5701
Jennifer DeWinter, Sean Raffuse, Michael McCarthy, Kenneth Craig, Loayeh Jumbam, Fred Lurmann
Sonoma Technology, Inc., Petaluma, CA
Scott Fruin
University of Southern California, Los Angeles, CA
Presented at the
12th Annual CMAS Conference
Chapel Hill, NC
October 29, 2013

## Slide 2: Outline
Background
Study objectives
Methods
  Data acquisition and preparation
  Surface reflectance ratios
  Aerosol optical properties
  Cloud filter
Results
Conclusions
Future applications

## Slide 3: Smoke and Air Pollution
Wildfires are a major source of air pollution, particularly in the western U.S. during summer/fall
Smoke from fires decreases visibility and exposes people to harmful air pollution such as PM2.5
Accurate estimation of PM2.5 concentrations during wildfires is important to quantify air pollution exposure and visibility
29%
2008 fire emissions inventory
sources of PM2.5
Background

## Slide 4: 2008 Fires in Northern California
  1.5 to 2 million acres burned
  600,000 to 800,000 tons of PM2.5 produced
  Stagnant meteorology and plumes mixed to the surface
  30-50 days of smoke impact
  Many days violated the National Ambient Air Quality Standards for PM2.5 and PM10
Fire locations in Northern California on June 25, 2008, as detected by MODIS
Image courtesy of NASA
Fire locations
Background

## Slide 5: Estimating the Spatial Distribution of PM2.5
Measurements, models, satellites
Data from satellites can provide information on the spatial distribution of pollution
Aerosol optical depth (AOD) is a unitless measure of the total scattering and absorption of light by aerosols in an atmospheric column
Correlation between AOD and hourly PM2.5 across United States
Engel-Cox J.A., Holloman C.H., Coutant B.W., Hoff R.M., 2004. Qualitative and quantitative evaluation of MODIS satellite sensor data for regional and urban scale air quality. Atmospheric Environment 38 (16), 2495-2509
R value
Background

## Slide 6: Our Study Objectives
  Develop a customized AOD product for wildfire conditions in the western U.S.
  High spatial resolution
  Localized aerosol and optical properties
  Improved cloud screening
  Estimate PM2.5 concentrations during wildfire events
Objectives

## Slide 7: Methods Overview
Obtain raw Level 1b MODIS radiance data and corresponding geolocation data
  http://ladsweb.nascom.nasa.gov/
  Raw data at 250 m, 500 m, 1-km spatial resolution
  Terra and Aqua satellites
  Time period: June 24 through July 31, 2008 (and 2009)
Modifications to NASA algorithm to develop our AOD product
  Develop localized surface reflectance properties
  Better characterize smoke aerosol
  Relax cloud filter algorithm
Total signal measured by satellite =
light reflected by ground + light reflected by aerosol column
MODIS measures reflectance in 36 spectral channels
Daily satellite-detected reflectance at 2.13 and 0.66 µm
Methods

## Slide 8: Local Surface Reflectance
Distinguish reflectance from aerosols in the atmospheric column vs. surface reflectance
Use MODIS top-of-atmosphere reflectance in two channels—0.66 and 2.13
Develop 0.66/2.13 surface reflectance ratio under clean conditions
Calculate the total column aerosol that would produce the observed 0.66 reflectance
Average surface reflectance ratio (0.66/2.13)
Methods

## Slide 9: Local Aerosol Properties
Omar Western aerosol model for western U.S. used in standard NASA AOD product
California biomass model has aerosol optical properties specific to California and biomass burning conditions
      Biomass model better characterizes smoke aerosol
Aerosol size distributions for different aerosol optical models
Methods

## Slide 10: Improved Cloud Filter
Implement a relaxed cloud filtering algorithm
Use reflectance from three MODIS channels
  0.47 (bright thick clouds)
  1.38 (thin cirrus clouds)
  2.12 (clouds only)
  Spatial variability and absolute value
Relaxed Cloud Mask
Original Cloud Mask
Methods

## Slide 11: Comparison of AOD Products
  Experimental AOD compared to the standard NASA product on June 27, 2008
Results

## Slide 12: Validating AOD with AOT
Observed aerosol optical thickness (AOT) from three coastal Aerosol Robotic Network (AERONET) sites in central and northern California
High resolution AOD is much better at matching observed AOT
  High resolution: R2 = 0.53
  Standard resolution: R2 = 0.08
Results

## Slide 13: Validating AOD with PM2.5
  Identify AOD pixels at ground monitor locations
  Calculate mean PM2.5 using ground measurements from 10 a.m. to 2 p.m.
  Calculate mean AOD using Terra and Aqua
Relationship between ground-based PM2.5 concentrations and high spatial resolution AOD that overlaps the ground monitors for June 24 to July 31, 2008.
Results

## Slide 14: Time-Series at Select Sites: PM2.5 & AOD
General shape of the pollution episodes is well captured
Results

## Slide 15: AOD-Estimated PM2.5
  Develop day-specific regression relationships (including all monitoring sites)
  Use the daily slope to predict PM2.5
Units: µg/m3
Results

## Slide 16: Conclusions
Developed a high spatial resolution AOD product specific to smoke aerosol
  Local surface reflectance properties
  Aerosol optical properties typical of California biomass burning aerosol
  Relaxed cloud filter preserved smoke pixels typically classified as clouds
Predicted PM2.5, particularly on days when smoke is well-mixed to the surface

## Slide 17: Future Applications
High resolution AOD product will be useful for
  Others studying the 2008 fire event
  Evaluating modeled smoke predictions
  Assimilation into air quality models to improve PM2.5 forecasts
Method can also be used in other areas
  Requires data processing to develop local AOD product
  Requires further improvements to surface reflectance ratios and cloud screening

## Slide 18: Contact
sonomatech.com
@sonoma_tech
Stephen Reid
sreid@sonomatech.com
Jennifer DeWinter
jdewinter@sonomatech.com
707.665.9900
35