## Slide 1: Improving Sources of Stratospheric Ozone and NOy and Evaluating Upper Level Transport in CAMx
Chris Emery, Sue Kemball-Cook, Jaegun Jung, Jeremiah Johnson, Greg Yarwood
and
Bright Dornblaser, TCEQ
13th Annual CMAS Conference
October 28, 2014

## Slide 2: Acknowledgements
This project was funded by the Texas Commission on Environmental Quality
The authors gratefully acknowledge the NOAA Air Resources Laboratory (ARL) for the provision of the HYSPLIT model and use of the READY website (http://www.ready.noaa.gov).

## Slide 3: Background
As the NAAQS become more stringent, understanding transport is increasingly important
O3 and some NOy are long-lived in the upper troposphere (UT) and lower stratosphere (LS)
  Can be transported for long distances
  Can mix downward and influence surface O3
Models used for O3 planning must accurately simulate O3 and NOy in the UT/LS
  Simulate impact of stratospheric air on background
  Comparison with column-integrated satellite data

## Slide 4: CAMx Vertical Grid
Model top 15 km
Downward motion brings LS air into modeling domain
Top BC is “Zero gradient” mixing ratio assumption
Figure: http://esrl.noaa.gov/csd/assessments/ozone/2006/chapters/Q1.pdf
TCEQ
Vertical
Grid

## Slide 5: Modeling with the Standard CAMx Top BC
Comparison of OMI vs. CAMx NO2 columns prompted deeper evaluation of CAMx in UT/LS
CAMx (red) underestimated UT/LS NO2 relative to INTEX-A aircraft profiles (black)
  Ad hoc top BCs for O3 and NOy improved comparison (purple)

## Slide 6: Layer Collapsing
CAMx is typically run with fewer layers than WRF for efficiency
Effect on surface ozone generally minimal
Test effect on UT/LS O3 and NOy
Layer
Collapsing
in UT
Surface
WRF
CAMx
No Layer
Collapsing

## Slide 7: GEOS-Chem Global Model
A common source for lateral BCs
  Spatially interpolate to CAMx grid
  Map species to CAMx list
Add new top BCs

## Slide 8: Example of New Top BC Extraction

## Slide 9: CAMx Model Performance Evaluation
3 CAMx runs
  Standard Zero Gradient Top BC, 28 layers
  GEOS-Chem Top BC, 28 layers
  GEOS-Chem Top BC, 38 layers (no layer collapsing)
Rider 8 modeling platform, June 2006 episode
  Lightning NOx emissions
  TCEQ AEM3 aircraft emission inventory
  CB6r2 chemical mechanism

## Slide 10: Ozonesonde at Huntsville, AL
Good agreement < 6 km
  No clear benefit from top BC or extra layers
GEOS-Chem matches observed profile well
  Though not at all US sites
Zero gradient run
  Diffusive, poor > 6 km
38 layer top BC run better than 28 layer top BC run > 6 km

## Slide 11: NO2 Profile with new Top BCs
Top BC improves UT/LS NO2 profile

## Slide 12: Effect of Layer Collapsing
Layer collapsing affects NO2 profile less than ozone

## Slide 13: Effect of Layer Collapsing on PAN Profile
CAMx has a low bias in middle and upper troposphere
PAN driven by BCs (GOES-Chem too low by >100 ppt)

## Slide 14: HYSPLIT Trajectory Analysis
Forward/backward trajectories from UT/LS vertical intrusion events
Prepared using 4 sets of inputs:
  WRF three-dimensional wind field
  WRF two-dimensional wind field
    HYSPLIT calculates vertical component using default divergence method
  CAMx three-dimensional wind field
    Vertical component calculated using CAMx algorithm
  EDAS three-dimensional wind field

## Slide 15: Diagnosing UT/LS Intrusion Events

## Slide 16: June 2, 2006

## Slide 17: Summary
New top BC improves performance in UT/LS
  Allows for column-integrated satellite comparisons
UT/LS O3 for 38 layer run was better than 28 layer run
  High vertical resolution needed for UT/LS transport
  Effects at surface intermittent and generally small
    28 layers sufficient for surface O3 in Texas summertime
    Larger effects expected in Intermountain West springtime
GEOS-Chem performance in UT/LS was variable
  Sometimes contributes to biases in CAMx
CAMx transport in UT/LS consistent with other models

## Slide 18: Thank You Questions?

## Slide 19: GEOS-Chem PAN
GEOS-Chem PAN (<100 ppt) lower than INTEX-A observations (300 ppt) near the tropopause

## Slide 20: Effect of Layer Collapsing on HNO3 Profile
Good (slightly high) simulation of HNO3 profile