## Slide 1: Evaluating the Cross State Transport of Ozone using CAMx & DISCOVER-AQ Maryland Observations
Presentation by:
Dan Goldberg
Co-authors: Tim Vinciguerra, Linda Hembeck, Sam Carpenter, Tim Canty, Ross Salawitch & Russ Dickerson
13th Annual CMAS Conference
Tuesday October 28, 2014

## Slide 2: Motivation for this study…
The state of Maryland owes a State Implementation Plan (SIP) in June 2015 to show future attainment of the Ozone NAAQS.
We are trying to verify that the regional air quality models are getting an accurate prediction of ozone for the right reasons in order to define the most effective attainment strategies.

## Slide 3: Motivation for this study…
The Ozone Design Values in Maryland have dropped dramatically in the past 3 years due to a combination of emissions reductions AND favorable meteorology
nonattainment (> 0.075 ppm)
nonattainment (> 0.085 ppm)
Marginal
Moderate
EPA CASTNET Sites
Maryland Ambient Air Quality Monitoring Network

## Slide 4: Comparison to Observations of Surface Ozone
There is excellent model agreement in predicting surface ozone when using the standard, “off-the-shelf” version of CAMx

## Slide 5: Comparison to Observations of Surface Ozone
July 2 – Under prediction due to 4th of July travel & transport aloft
July 21 – Over prediction due to bay breeze (He et al. 2014)
There is excellent model agreement in predicting surface ozone when using the standard, “off-the-shelf” version of CAMx

## Slide 6: Comparison to Observations of Surface Ozone
Is the model getting ozone right for the right reasons?
Let’s take a look at the precursors to ozone: NO2, VOCs, etc.
There is excellent model agreement in predicting surface ozone when using the standard, “off-the-shelf” version of CAMx

## Slide 7
NASA UC-12 (Remote sensing)
Continuous mapping of aerosols with HSRL and trace gas columns with ACAM
NASA P-3B (in situ meas.)
In situ profiling of aerosols and trace gases over surface measurement sites
Ground sites
In situ trace gases and aerosols
Remote sensing of trace gas and aerosol columns
Ozonesondes
Aerosol lidar observations
Three major observational components:
DISCOVER-AQ: Deriving Information on Surface conditions from Column and Vertically Resolved Observations Relevant to Air Quality
July 2011

## Slide 8: Ozone Precursors: CAMx v6.10 vs. Aircraft
NO2
Formaldehyde (HCHO)
NOy
Alkyl nitrates (NTR)

## Slide 9: Suggestions on how to reduce these biases
NO2 & NOy high biases:
  Reduce NOx emissions from on-road vehicles by 50% (Anderson et al., 2014, Fujita et al. 2012, Brioude et al. 2013)
Formaldehyde low bias:
  Use a new model for estimating biogenic emissions (trees, soil, etc)
    MEGAN v2.10 from BEIS v3.14
NTR high bias:
  Reduce the photolytic lifetime from 10 days to 1 days (Perring et al. 2013, Farmer et al. 2011)

## Slide 10: Making the aforementioned changes…
NOy
Alkyl nitrates (NTR)
NO2
Formaldehyde (HCHO)

## Slide 11: Baseline case
NO2
Formaldehyde (HCHO)
NOy
Alkyl nitrates (NTR)

## Slide 12: How about surface ozone agreement?
Reminder: The baseline case

## Slide 13: How about surface ozone agreement?
Didn’t change much! AND slightly better R-squared
Updated chemistry & emissions

## Slide 14: How about surface ozone agreement?
Didn’t change much! AND slightly better R-squared
Updated chemistry & emissions
Intermediate conclusion:
These changes have improved prediction of the precursors to ozone, while minimally impacting the prediction of surface ozone!

## Slide 15
July 2011: Ozone Source Apportionment
Fraction of total surface ozone attributed to the boundary conditions, Maryland, and everywhere else in the modeling domain
Modeling domain
Maryland accounts for only 30% of its air pollution!
Baseline

## Slide 16
With the updated chemistry & emissions, Maryland accounts for a slightly larger percentage of its pollution*
July 2011: Ozone Source Apportionment
Fraction of total surface ozone attributed to the boundary conditions, Maryland, and everywhere else in the modeling domain
Updated chemistry & emissions
Modeling domain

## Slide 17: *Changes in model attribute more pollution to power plants!
More ozone is attributed to sources that emit from smokestacks (mostly power plants, but also cement kilns, ships, etc.)
Surface pollution sources
Above surface pollution sources

## Slide 18: July 2011 Mobile Source Apportionment
Ozone from On-road Mobile (ppb)
% of Ozone from On-road Mobile
Baseline case (On-road mobile emissions likely overestimated)
Mobile emissions account for ~15 ppb of ozone at 5 PM in Baltimore, which is about 35% of total ozone as an average in July 2011

## Slide 19: July 2011 Mobile Source Apportionment
50% Mobile NOx case
Mobile emissions account for ~10 ppb of ozone at 5 PM in Baltimore, which is about 20% of total ozone as an average in July 2011
Ozone from On-road Mobile (ppb)
% of Ozone from On-road Mobile

## Slide 20: Importance of Boundary Conditions
Emissions outside of the state of Maryland, especially at the model domain boundaries, are becoming more important when trying to show future attainment
Synoptic set-up during July 9, 2007 & July 7, 2011 was very similar, see extra slides for more detail

## Slide 21: Conclusions
CAMx v6.10 has excellent agreement with prediction of 8-hour maximum surface ozone
  Mean bias: 1.06 ppb
Changes to the model improve the biases of the precursors while only minimally affecting prediction of surface ozone
  NOy high bias: from a factor of 2.0 to 1.5
  Formaldehyde low bias: from a factor of 0.57 to 1.15
Emissions from power plants account for a significantly larger percentage of ozone in the “improved” modeling scenario
  On-road mobile accounted for 35% of ozone, now only 20%
Ozone coming from the boundaries of the model domain has a non-trivial effect
  > 20 ppb surface ozone in Maryland

## Slide 22: Next steps
Update model simulations to the CB6r2 gas-phase chemistry
Assimilate O3 from TES and NO2 from OMI into the boundary conditions
Adjust dry deposition rates of some reactive nitrogen species which are hypothesized to be underestimated

## Slide 23: Conclusions
CAMx v6.10 has excellent agreement with prediction of 8-hour maximum surface ozone.
  Mean bias: 1.06 ppb
Changes to the model improve the biases of the precursors while only minimally affecting prediction of surface ozone.
  NOy high bias: from a factor of 2.0 to 1.5
  Formaldehyde low bias from a factor of 0.57 to 1.15
Emissions from power plants account for a significantly larger percentage of ozone in the “improved” modeling scenario.
  On-road mobile accounted for 35% of ozone, now only 20%
Ozone coming from the boundaries of the model domain has a non-trivial effect.
  > 20 ppb surface ozone in Maryland

## Slide 24: Synoptic Met: July 9, 2007

## Slide 25: Synoptic Met: July 7, 2011