## Slide 1: Source Attribution and Source Sensitivity Modeling Studies with CMAQ and CAMx
Prakash Karamchandani1, Jeremiah Johnson1, Tejas Shah1, Jaegun Jung1, Ralph Morris1, Susan Collet2, Toru Kidokoro3, Yukio Kinugasa3
1ENVIRON International Corporation, Novato, CA
2Toyota Motor Engineering and Manufacturing North America, Inc., Ann Arbor, MI
3Toyota Motor Corporation, Shizuoka, Japan
October 27-29, 2014
13th Annual CMAS Conference, Chapel Hill, NC

## Slide 2
Acknowledgement
This study was supported by Toyota Engineering and Manufacturing (TEMA) , North America and Toyota Motor Corporation (TMC), Japan

## Slide 3: Study Objectives
Determine source category contributions to future year air quality
  On-road mobile emissions (and sub-categories of on-road emissions)
  Off-road emissions
  Emissions from stationary sources (point, area)
  Natural emissions (biogenic, wild fire)
  Global contributions (boundary conditions)
Compare various approaches to determine source contributions and sensitivities:
  Different models (CMAQ vs CAMx): Brute force method (BFM)
  CAMx source attribution probing tools: OSAT for ozone and PSAT for PM2.5
  CAMx source sensitivity probing tool: HDDM for ozone
Calculate source category impacts on future year design values
Determine future year population exposures in non-attainment areas

## Slide 4: Study Components
Model performance evaluation for 2008 base year (CMAQ, CAMx)
Future year (2018, 2030) simulations (CMAQ, CAMx) with zero-out for relevant source categories
Future year CAMx OSAT and PSAT simulations
Future year CAMx-HDDM simulations and CAMx BFM simulations with 20% emission reductions
Analysis of results
Notes:   Analysis of measurements from 2009 Study of Houston Atmospheric Radical Precursor (SHARP) in the Houston area to identify missing HONO formation pathways and recommend parameterizations (UCLA and UH)
  Surface model
  CAMx surface model originally developed for persistent organic pollutants
  Extended in this work to include core model species, such as NO2, HNO3, and HONO
  Keeps track of accumulated mass deposited to surface
  Treats sorption and penetration into soil and vegetation; chemical degradation and transformation; and volatilization back to the air (re-emission)
  UNC
  CAMx Simulations and evaluation of results
  Process analysis
  Refinement
  Semi-empirical approach
  Analysis of evaluation results
  Adjust model parameters within range of plausible values

## Slide 5: Approach
Phased approach
Initial studies considered limited simulation periods (1 month in winter and 1 month in summer)
Understand differences in results predicted using various modeling tools
Latest study (ongoing) focuses on annual simulations with selected CAMx probing tools

## Slide 6: Modeling Domains
Nested Grid
  36 km resolution CONUS
  12 km resolution inner grids
Model Inputs
  Base year (2008) WRF meteorology
  Base and future year (2018 and 2030) emissions
  MOVES and EMFAC2007 used to adjust future year on-road mobile emissions for Tier 3/LEV III impacts
  36 km BCs from MOZART
  MEGAN for biogenic emissions

## Slide 7: Summary of 1-Month Simulation Studies
Model | Attribution Determining Method | Species | Emission Sources Tracked
CMAQ | Zero-Out Contributions | O3, PM | Off-road Mobile (US) Area (US) Point (US) Natural Boundary Conditions On-road Mobile (US) 4 sub-categories: LDGV HDGV LDDV HDDV
CAMx | Source Contributions: a) Zero-Out Contributions b) OSAT/PSAT Attributions | O3, PM | 
 | Source Sensitivities (20% Reductions): a) HDDM (First and second-order coefficients) b) BFM: 20% Reduction Applied to Base Emissions | O3 | 
Years: 2008 (Base), 2018 & 2030 (Future), Months: January (PM), July (O3, PM)

## Slide 8
Future Year CMAQ Daily Max 8-hour O3 and Change in Daily Max
Western US
Notes: Run A (base run) under-predicts observed HONO substantially
Run B (with direct HONO emissions) better, but still tends to under-predict; moreover predicted HONO:NO2 ratios are inconsistent with observations
Run H (with CAMx surface model) does a good job for most of the days, but over-predicts during the night on May 19 and 20, with the largest over-predictions on May 20
  HONO over-predictions associated with large NO2 over-predictions at night on May 19 and 20
  Focus on HONO:NO2 ratios as a way to assess model performance at night

## Slide 9
Future Year CMAQ Daily Max 8-hour O3 and Change in Daily Max
Eastern US
Notes: Run A (base run) under-predicts observed HONO substantially
Run B (with direct HONO emissions) better, but still tends to under-predict; moreover predicted HONO:NO2 ratios are inconsistent with observations
Run H (with CAMx surface model) does a good job for most of the days, but over-predicts during the night on May 19 and 20, with the largest over-predictions on May 20
  HONO over-predictions associated with large NO2 over-predictions at night on May 19 and 20
  Focus on HONO:NO2 ratios as a way to assess model performance at night

## Slide 10
O3 2008 DVCs and Future Year DVFs
0
20
40
60
80
100
120
SB, RS CA
LA CA
Ozone DV ppb
CMAQ
CA
AL
MI
WY
GA
NY
PA
SC
MD
X axis：Alphabetical Order, States => Counties
75
70
- 2030 DVFs < 75 ppb, except for 8 counties in CA
- 2030 DVFs < 70 ppb, except for 15 counties in CA and 1 county each in CO & MD
2008
DVB
2018
DVF
2030
DVF
Notes: Good agreement for April 21
NO2 is substantially over-predicted during the night on May 20

## Slide 11
O3 Non-Attainment Area Populations
More areas reach attainment in future years, resulting in lower population exposure
Millions of People
0
20
40
60
80
CMAQ
CAMx
59.2
58.9
20.9
21.0
11.5
14.2
19.7
20.7
18.4
18.8
11.4
13.3
2030
2018
2008
Notes: Good agreement for April 21
NO2 is substantially over-predicted during the night on May 20

## Slide 12: Comparison of Approaches
Approach | Pros | Cons
Zero-Out | Simple to understand Answers “what if” questions | Not a true source apportionment because of nonlinearity Expensive for more than a few source sectors or source regions
OSAT | Source apportionment under current or future conditions “Book-keeping” not affected by nonlinearity Efficient for a large number of source sectors or source regions | Not appropriate for “what if” scenarios with large emission perturbations because of nonlinearity
Source Attribution: OSAT vs Zero-Out
Approach | Pros | Cons
BFM | Simple to understand Answers “what if” questions for a particular scenario | Expensive for more than a few emission scenarios
HDDM | More efficient than BFM because it yields sensitivity coefficients that can be applied to a range of scenarios (multiple “what if” questions answered in a single simulation) | Expensive if only a small number of source scenarios required Large computer memory requirements
Source Sensitivity: HDDM vs BFM

## Slide 13
CMAQ vs CAMx Zero-Out: 2030 Max O3
On-Road Mobile Contributions
CMAQ
CAMx
CMAQ
CAMx
Western US
Eastern US
Notes: Run A (base run) under-predicts observed HONO substantially
Run B (with direct HONO emissions) better, but still tends to under-predict; moreover predicted HONO:NO2 ratios are inconsistent with observations
Run H (with CAMx surface model) does a good job for most of the days, but over-predicts during the night on May 19 and 20, with the largest over-predictions on May 20
  HONO over-predictions associated with large NO2 over-predictions at night on May 19 and 20
  Focus on HONO:NO2 ratios as a way to assess model performance at night

## Slide 14
CAMx Zero-Out vs OSAT: 2030 Max O3
On-Road Mobile Contributions
CAMx Zero-Out
CAMx OSAT
Western US
Eastern US
Notes: Run A (base run) under-predicts observed HONO substantially
Run B (with direct HONO emissions) better, but still tends to under-predict; moreover predicted HONO:NO2 ratios are inconsistent with observations
Run H (with CAMx surface model) does a good job for most of the days, but over-predicts during the night on May 19 and 20, with the largest over-predictions on May 20
  HONO over-predictions associated with large NO2 over-predictions at night on May 19 and 20
  Focus on HONO:NO2 ratios as a way to assess model performance at night

## Slide 15
Comparison of Source Attribution Approaches
Generally good agreement between CMAQ and CAMx zero-out results
OSAT generally predicts larger contributions of tracked anthropogenic source categories, particularly on-road mobile emissions, due to non-linearities which can be large with BFM
Chart: 
| CMAQ Z-OUT | CAMｘ Z-OUT | O-SAT | CMAQ Z-OUT | CAMｘ Z-OUT | O-SAT | CMAQ Z-OUT | CAMｘ Z-OUT | O-SAT | CMAQ Z-OUT | CAMｘ Z-OUT | O-SAT | CMAQ Z-OUT | CAMｘ Z-OUT | O-SAT | CMAQ Z-OUT | CAMｘ Z-OUT | O-SAT | CMAQ Z-OUT | CAMｘ Z-OUT | O-SAT | LA | SB | Ph | Den | DTW | Atl. | NY
Oｎ-Road Mobile | 8 | 10 | 23 | 4 | 10 | 21 | 16
HDGV | 0 | 0 | 1 | 1 | 2 | 2 | 0 | 0 | 0 | 0 | 2 | 2 | 1 | 1
HDDV | 2 | 2 | 4 | 3 | 11 | 10 | 0 | 0 | 1 | 3 | 7 | 7 | 3 | 3
LDGV | 1 | 1 | 4 | 2 | 9 | 9 | 1 | 0 | 2 | 4 | 6 | 6 | 5 | 5
LDDV | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Off-Road Mobile | 11 | 9 | 14 | 20 | 16 | 16 | 5 | 5 | 8 | 2 | 1 | 2 | 2 | 3 | 6 | 4 | 5 | 7 | 8 | 8 | 12
Point Sources | 3 | 2 | 7 | 6 | 5 | 8 | 3 | 4 | 6 | 12 | 10 | 11 | 8 | 20 | 19 | 16 | 15 | 22 | 9 | 11 | 16
Other Area | 7 | 9 | 10 | 13 | 16 | 18 | 4 | 5 | 6 | 4 | 1 | 6 | 1 | 3 | 5 | 4 | 5 | 7 | 7 | 8 | 11
BC | 17 | 16 | 25 | 12 | 20 | 30 | 13 | 12 | 20 | 24 | 34 | 45 | 20 | 11 | 18 | 15 | 8 | 15 | 13 | 13 | 22
Natural | 20 | 20 | 15 | 34 | 33 | 20 | 21 | 25 | 14 | 15 | 12 | 8 | 9 | 22 | 14 | 16 | 14 | 10 | 20 | 27 | 9
Non-Linear | 25 | 22 | 1 | 17 | 9 | 1 | 12 | 9 | 3 | 16 | 17 | 0 | 21 | 10 | 2 | 15 | 22 | 0 | 17 | 15 | 6
Calculated Ozone ppb
On-Road
2030 O3
Notes: Good agreement for April 21
NO2 is substantially over-predicted during the night on May 20

## Slide 16
CAMx O3 OSAT Apportionment-NOx vs VOC
Chart: 
| Point Sources | Other | Global BCs | Natural (bio+fires) | On-Road Mobile | Off-Road Mobile | Other Area | HD Gas | HD Diesel | LD Gas | LD Diesel
CAMx_SA_O3V | 0.014623 | 0.00044095 | 0.12901 | 0.163 | 0.020392 | 0.028622 | 0.10347
CAMx_SA_O3N | 0.066546 | 0.0044316 | 0.1584 | 0.030903 | 0.07787 | 0.12684 | 0.07365
Ozone Contributions %
Point
Source
Leftover
Emissions
Global
BCs
Natural
(Bio+Fires)
On-Road
Off-Road
Other Area
NOx
VOC
Notes: Surface model generally captures the observed diurnal variation in HONO:NO2 ratios
Base run and run with direct HONO emissions do not capture these features

## Slide 17
CAMx O3 OSAT Apportionment-NOx vs VOC
On-Road Mobile Contributions to 2030 O3
Western US
Eastern US
Notes: Surface model generally captures the observed diurnal variation in HONO:NO2 ratios
Base run and run with direct HONO emissions do not capture these features

## Slide 18
2030 HDDM Results: NOx vs. VOC
Effects of 20% Reductions in On-Road Mobile NOx or VOC Emissions
Notes: Surface model performs well on April 21, during both day and night
Over-predictions on May 20 are associated with NO2 over-predictions

## Slide 19
2030 HDDM Results: HDDM vs BFM
Effects of 20% Reductions in On-Road Mobile NOx and VOC Emissions
Notes: Surface model performs well on April 21, during both day and night
Over-predictions on May 20 are associated with NO2 over-predictions

## Slide 20
HDDM vs BFM Results
Effects of 20% Reductions in On-Road Mobile NOx and VOC Emissions
2030
HDDM
2030
BFM
Western US
Eastern US
Notes: Surface model performs well on April 21, during both day and night
Over-predictions on May 20 are associated with NO2 over-predictions

## Slide 21: Conclusions
Results from CMAQ and CAMx zero-out simulations are generally comparable
The sum of the source contributions in the zero-out simulations does not add up to the base value because of the inherent non-linearity in the system, resulting in sometimes large contributions of the so-called “unexplained” category with the brute force method
Because of the non-linearity, the zero-out method predicts generally lower source attributions of anthropogenic source categories than OSAT
Ozone responses to 20% reductions in NOx and VOC emissions calculated from HDDM sensitivity coefficients and BFM results are generally similar
Both apportionment (OSAT) and sensitivity (HDDM) approaches provide valuable information on source culpability at a lower cost than a large number of brute force calculations; the choice of the tool to be used depends on the study objectives
Notes:   Surface model Explicitly simulates HONO formation on ground surfaces by reactions of deposited HNO3 and NO2:
    Daytime photolysis of HNO3 and NO2
    Thermal NO2 reaction during night and day
  Daytime levels simulated well on most days
  Nighttime levels simulated well except when NO2 is over-predicted
  Observed and predicted HONO:NO2 ratios are in good agreement