## Slide 1: A Web-based Community Approach to Model Evaluation using AMET
Saravanan Arunachalam1, Nathan Rice2 and Pradeepa Vennam1
1Institute for the Environment
2ITS Research Computing Services
The University of North Carolina at Chapel Hill
Presented at the
13th Annual CMAS Users Conference, Chapel Hill
October 27 – 29, 2014

## Slide 2: Acknowledgements
U.S. EPA for providing AMET v1.2 and Observations from U.S. networks
FAA under PARTNER - a U.S. DOT Center of Excellence for partly sponsoring this work

## Slide 3: Motivation
Confidence needed in model outputs before they can be used to make policy
Both models and ambient datasets have grown in complexity
CMAS user community has grown and we have 1000’s of users who can run the CMAQ model
Tools needed to assist user community to evaluate, assess and interpret model performance
Atmospheric Model Evaluation Tool (AMET) released by EPA/CMAS in Feb 2008
Since then, only ~13% of CMAQ users have downloaded AMET
  Fairly steep learning curve to be able to install and use the tool

## Slide 4: Objective
Enhance AMET with a web-based front-end to assist users
Provide common infrastructure for multiple users to perform model evaluation
  Share “processed” ambient datasets
  Easily switch between model scenarios
  Compare performance across model iterations
  Leverage expertise in community

## Slide 5: Observational Datasets
AIRS (hourly) (~4000)
IMPROVE (every 3rd day) (~160)
CASTNET (hourly, weekly) (123)
NADP (weekly) (over 200)
EPA CSN (daily, every 6th day) (~225)
EPA Supersites (sub-hourly) (8)
EPA CSN (daily, every 6th day) (~225)
AERONET
Special field campaigns
  e.g. AIRMAP, ASACA, BRAVO, CCOS, CRPAQS,, SEARCH, SOS, TXAQS, etc.
  Aircraft Data
Remote Sensing Data
  MODIS AOD from Aqua, Terra; O3, NH3 from Aqua’s TES; NO2 from OMI, etc.

## Slide 6: AMET Approach
Source: Appel et al, Env. Mod. Software, 2011

## Slide 7: Software Tools: AMET on the Web
AMET v1.2 (Released via CMAS in July 2013)
  Uses MySQL, R and perl
JavaScript, JQuery and Angular JS
Python and Flask (web application framework written in Python)
Google Maps

## Slide 8: Approach 1: AMET Form

## Slide 9: AMET Form
Interactive approach to evaluating CMAQ
  Can perform custom analyses for user-defined set of networks, pollutants, time-periods, metrics
Uses canned AMET v1.2 scripts
Obs data stored on backend, but user needs to upload model-data, as “combine” outputs, via the web browser
Uses Forms to get user inputs to create AMET config files
AMET v1.2 scripts on back-end use the config files to perform analyses
Output files (plots, tables and logs) displayed on web browser

## Slide 10: AMET Form
Pros
  Relies on off-line AMET v1.2 scripts, hence consistent and full functionality
  GUI to choose network/pollutant/type of analyses
  Interface to review all analyses products and logs
  Can obtain paired CSVs as outputs for use in other software (!)
Cons
  Relies on off-line AMET v1.2 scripts
    Software dependencies in current AMET structure still remain
    Error messages not intuitive
  Current design limits file sizes of model outputs to 2 GB
    ~10 days of “combine” outputs for ConUS domain
    148 Cols x 112 Rows x 134 Species x 240 hours
  After finishing one set of plots, for any revised of plots, project name needs to be changed

## Slide 14: Approach 2: AMET Map

## Slide 15: AMET Map
Interactive approach to evaluating CMAQ
  Can perform custom analyses for user-defined set of networks, pollutants, time-periods, metrics
Uses pre-loaded obs-model data pairs based on “combine” outputs
Can easily repeat same analyses for multiple model iterations
Uses Map interface for user inputs
Does not use AMET v1.2 scripts for plots and analyses

## Slide 16: AMET Map
Pros
  Once obs-model pairs of multiple model iterations are paired and stored, AMET Map has immediate access to perform analyses
  Paired data of observations and any AQM is supported
  Map interface to select individual site(s) to assess model performance
  After species is selected, only relevant networks are shown
Cons
  Remote users need to have access to MySQL server on backend to be able to load obs-model pairs
  Not all of current AMET v1.2 functionality is provided

## Slide 21
Visualize bias and error

## Slide 22
Explore performance at individual (or subset of) sites

## Slide 24
Expected vs. observed concentration by Date
Timestep for Moving average

## Slide 25
Expected vs. observed concentrations
By Hour of the Day
By Day of the Week

## Slide 26
and by Day of the Week
and by Hour of the Day
Site Type: Uses EPA’s Designations for “Location Settings” for AQS Sites
Bias by Site Type

## Slide 27
Histogram of deviations from expected value

## Slide 28
Density Map

## Slide 29
PM2.5 Composition Analysis

## Slide 30: Next Steps
Complete “stress-testing” of both systems
Enable access to larger size datasets via AMET Form
Improve error reporting to make systems user-friendly
Expand scope to include
  Meteorological model evaluation
  Simultaneous analyses of emissions, meteorology and AQ

## Slide 31: Challenges
Moving this from from prototype to production version will take additional work
Computing resource needs for AMET Form and AMET Map will grow very fast to support community needs
  Creating acceptable use policy for AMET Map and AMET Form
  Explore creating “packages” of these that can be distributed for users to install locally?