## Slide 1: A Five-Year Performance Evaluation of Environment Canada’s Operational Regional Air Quality Deterministic Prediction System M.D. Moran1, J. Zhang1, R. Pavlovic2, and S. Gilbert2 1Air Quality Research Division, Environment Canada, Toronto, Ontario, Canada 2Air Quality Modelling Applications Section, Environment Canada, Montreal, Quebec, Canada
14th Annual CMAS Conference
October 5-7, 2015 Friday Center, UNC-Chapel Hill

## Slide 2: Talk Outline
Model Characteristics and Outputs
AQ Measurement Data Characteristics
AQ Measurement Data “Cleansing”
Selected 5-Year Evaluation Results for 2010-2014 Period
Summary and Conclusions

## Slide 3: GEM-MACH Model Description
GEM-MACH is a Canadian multi-scale chemical weather forecast model comprised of dynamics, physics, and in-line chemistry modules
  GEM-MACH15 with 15-km horizontal grid spacing and 58 vertical levels to 0.1 hPa became operational in Nov. 2009
  In Oct. 2012, GEM-MACH10 introduced as operational forecast model with 10-km horizontal grid spacing and 80 vertical levels to 0.1 hPa
  Seven changes made to piloting model, code, grid, and emissions during 5 year period from 2010 to 2014

## Slide 4: AQ Measurement Data Characteristics (1)
Used archived near-real-time hourly O3, PM2.5, and NO2 Canadian data and hourly O3, PM2.5, and NO2 U.S. data from AIRNow for 5-year period from 2010-14 (extracted as data pairs with accompanying model values from EC VAQUM evaluation system)
Many U.S. O3 monitors only operate during the “ozone season”
AIRNow started transmitting U.S. NO2 mmts in mid 2012
AIRNow performs some quality control (QC) and some QC is performed on Canadian data upon receipt at CMC Dorval
Included both urban and rural stations initially

## Slide 5: AQ Measurement Data Characteristics: Time Variation of Number of Observations
Chart: Number of Observations Per Month, 2010-14
| 40179 | 40210 | 40238 | 40269 | 40299 | 40330 | 40360 | 40391 | 40422 | 40452 | 40483 | 40513 | 40544 | 40575 | 40603 | 40634 | 40664 | 40695 | 40725 | 40756 | 40787 | 40817 | 40848 | 40878 | 40909 | 40940 | 40969 | 41000 | 41030 | 41061 | 41091 | 41122 | 41153 | 41183 | 41214 | 41244 | 41275 | 41306 | 41334 | 41365 | 41395 | 41426 | 41456 | 41487 | 41518 | 41548 | 41579 | 41609 | 41640 | 41671 | 41699 | 41730 | 41760 | 41791 | 41821 | 41852 | 41883 | 41913 | 41944 | 41974
O3 | 504806 | 473042 | 628819 | 793337 | 727115 | 813434 | 846699 | 840027 | 822470 | 787116 | 541880 | 514498 | 560729 | 505568 | 571033 | 732809 | 860407 | 831726 | 749245 | 865091 | 837968 | 825658 | 597484 | 584123 | 555320 | 503696 | 606347 | 721121 | 862892 | 835826 | 869408 | 803150 | 728577 | 814275 | 594676 | 574117 | 577603 | 545335 | 692506 | 829083 | 843164 | 858002 | 877517 | 892262 | 861113 | 812710 | 622778 | 600050 | 575716 | 553385 | 684909 | 830386 | 886136 | 861590 | 882549 | 890329 | 860527 | 818672 | 614278 | 594270
NO2 | 83592 | 80977 | 89933 | 86924 | 87946 | 85171 | 87038 | 87749 | 82777 | 85298 | 83759 | 87921 | 88714 | 83744 | 94630 | 92850 | 96948 | 93863 | 96057 | 95756 | 92826 | 97112 | 92913 | 95412 | 94940 | 98703 | 103077 | 108101 | 147331 | 143687 | 155198 | 150871 | 137121 | 156998 | 149282 | 156948 | 163517 | 151627 | 168060 | 165180 | 166060 | 170093 | 175891 | 176833 | 170791 | 176150 | 170636 | 175045 | 175484 | 161764 | 177641 | 172850 | 179396 | 172018 | 177788 | 183236 | 176443 | 180803 | 175994 | 181549
PM2.5 | 468992 | 440547 | 477830 | 466931 | 424981 | 471404 | 482422 | 483704 | 468151 | 483317 | 475588 | 498524 | 501871 | 437297 | 419279 | 441463 | 497947 | 475878 | 443565 | 504140 | 486907 | 503596 | 481593 | 508798 | 483933 | 433781 | 459232 | 458985 | 519058 | 498620 | 520980 | 486175 | 429183 | 507276 | 487161 | 500432 | 503923 | 468330 | 524298 | 512264 | 499860 | 509138 | 524309 | 536125 | 520592 | 525225 | 511810 | 525348 | 510413 | 474632 | 528469 | 510668 | 524170 | 506391 | 525579 | 532543 | 516918 | 529558 | 511710 | 527613

## Slide 6: AQ Data Characteristics: Station Distribution
Chart: O3 (1,334 stns)
| ECAN | WCAN | EUSA | WUSA
 | 131 | 78 | 819 | 306
Chart: NO2 (283 stns)
| ECAN | WCAN | EUSA | WUSA
 | 84 | 87 | 76 | 36
Chart: PM2.5 (871 stns)
| ECAN | WCAN | EUSA | WUSA
 | 112 | 102 | 406 | 251
EUSA
ECAN
WCAN
WUSA
Notes: 60% of O3 stations are in EUSA, 25% in WUSA, stations in ECAN is about twice as many as WCAN
60% of NO2 stations are in Canada, equally distributed in ECAN and WCAN. 40% in the USA, stations in EUSA is twice as many as in WUSA
Distribution of PM2.5 stations is similar to the O3 stations

## Slide 7: AQ Measurement Data Characteristics: O3 Extrema
Chart: O3 Observed Minimum by Station, 2010-2014
Chart: O3 Observed Maximum by Station, 2010-2014
150
0

## Slide 8: AQ Measurement Data Characteristics: NO2 Extrema
Chart: NO2 Observed Minimum by Station, 2010-2014
Chart: NO2 Observed Maximum by Station, 2010-2014
150
0

## Slide 9: AQ Measurement Data Characteristics: PM2.5 Extrema
Chart: PM2.5 Observed Maximum by Station, 2010-2014
Chart: PM2.5 Observed Minimum by Station, 2010-2014
200
0

## Slide 10: AQ Measurement Data “Cleansing” (1)
Further data “cleansing” is required before AQ measurement data are used to evaluate model performance
Step 1: Data completeness (representativeness data filter based on long-term availability of valid hourly measurements)
  O3 option 1 ‒ 75% completeness over 5 years
  O3 option 2 ‒ 75% completeness over 5 O3 seasons
  NO2 option 1 ‒ 75% completeness over 5 years
  NO2 option 2 ‒ 75% completeness over 2 years (2013-14)
  PM2.5 option 1 ‒ 75% completeness over 5 years
  If a station does not meet this check, all of its data pairs are removed from the 5-year evaluation data set

## Slide 11: AQ Measurement Data “Cleansing” (2)
Step 2: Daily range check (“non-flatness” data filter to avoid constant measurements throughout a day)
  O3 ‒ range > 1 ppbv per 24 hours
  NO2 ‒ range > 0 ppbv per 24 hours
  PM2.5 ‒ range > 0.1 ug m-3 per 24 hours
If a station reports constant or near-constant measurements for 24 hours, all 24 data pairs are excluded from the 5-year evaluation data set
The NO2 range check is very “tight” because some remote stations can measure very low NO2 concentrations for extended periods

## Slide 12: AQ Measurement Data “Cleansing” (3)
Step 3: Exceedance thresholds (extrema data filter)
  O3 ‒ exclude values < 0 ppbv or > 150 ppbv
  NO2 ‒ exclude values < 0 ppbv or > 150 ppbv
  PM2.5 ‒ exclude values < 0 ug m-3 or > 200 ug m-3
  Such values are rare and most are suspect, but they can have a material impact on statistical metrics
  Elevated PM2.5 values can occur due to both wildfires and dust storms, but the current RAQDPS does not consider either emissions source (but see FireWork: Environment Canadas North American Air Quality Forecast System with Near-Real-Time Wildfire Emissions, presented by Sophie Cousineau on Monday, Oct. 5)

## Slide 13: Impact of Data Completeness Check on Number of Stations Used in Evaluation
Species | All Stns | Option 1 | Option 2
O3 | 1,334 | 753 | 1,184
NO2 | 283 | 131 | 238
PM2.5 | 871 | 623 | N/A

## Slide 14: Impact of Range and Threshold Checks on Number of Data Pairs Used in Evaluation for Five-Year 75% Data Completeness Data Set
Species | Range Check | Threshold Check | Both Checks
O3 | -0.1813% | -0.0007% | -0.1820%
NO2 | -1.6737% | -0.0012% | -1.6749%
PM2.5 | -0.2031% | -0.0050% | -0.2081%

## Slide 15: Example of Impact of Data Filtering on a Single-Station 5-Year O3 Time Series
Chart: 2010-14 O3 Time Series at a U.S. Station Before Data Filtering
Chart: 2010-14 O3 Time Series at a U.S. Station After Data Filtering

## Slide 16
Impact on Statistics of Removal of 21 NO2 Observations > 200 ppb Out of 87,869 Observations
Chart: Original NO2 pairs for Aug. 2010
Chart: After removal of 21 Obs with NO2> 200 ppbv from two sites

## Slide 17: Evaluation Methods and Selected Results
By Forecast Lead Time
0-12h, 13-24h, 25-36h, and 37-48h
Spatial Stratification
1) By Region: East Canada, West Canada, East US, West US
2) By Land-Use: Urban and Rural
Temporal Stratification
Annual, Seasonal, Monthly, Weekly, and Diurnal
Spatial and Temporal Occurrences of Large Values
O3 > 100 ppbv, NO2 > 100 ppbv, and PM2.5 > 100 ug/m3
Evaluation tool
Mainly R (https://www.r-project.org) and its packages,
particularly the “openair” package (http://www.openair-
project.org/Default.aspx)

## Slide 18: Impact of Forecast Lead Time on Model Skill  First 12 Hours Have Best Scores on Average
Chart: RMSE - O3 by Year and Season, 2010-2014
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
0-12h | 14.1507 | 16.5497 | 13.1457 | 12.3073 | 13.6743 | 16.5413 | 13.4922 | 12.0189 | 13.3826 | 14.7492 | 12.3549 | 10.5634 | 13.0748 | 13.839 | 12.2124 | 11.5885 | 12.9354 | 13.415 | 12.1766 | 11.2064
13-24h | 13.9596 | 16.5637 | 13.1659 | 12.0561 | 13.5158 | 16.6792 | 13.513 | 11.7892 | 13.3498 | 14.8477 | 12.3786 | 10.4356 | 12.8326 | 13.9365 | 12.232 | 11.3048 | 12.6916 | 13.5188 | 12.1987 | 10.9803
25-36h | 14.0067 | 16.3646 | 13.175 | 12.0675 | 13.5206 | 16.4451 | 13.5111 | 11.8373 | 13.394 | 14.8903 | 12.4038 | 10.4837 | 12.8784 | 13.8707 | 12.2579 | 11.3093 | 12.7303 | 13.4163 | 12.1609 | 10.9787
37-48h | 14.0355 | 16.5908 | 13.3368 | 12.079 | 13.5771 | 16.6244 | 13.5869 | 11.8939 | 13.4293 | 14.9344 | 12.4697 | 10.5625 | 12.9364 | 14.0145 | 12.2822 | 11.3306 | 12.7816 | 13.5067 | 12.2107 | 11.0127
Chart: R - O3 by Year and Season, 2010-2014
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
0-12h | 0.60535 | 0.64926 | 0.66874 | 0.5907 | 0.5568 | 0.6673 | 0.6326 | 0.60447 | 0.616 | 0.69076 | 0.65306 | 0.62206 | 0.6014 | 0.65261 | 0.63514 | 0.63708 | 0.61175 | 0.66551 | 0.61708 | 0.62625
13-24h | 0.60094 | 0.64426 | 0.66412 | 0.59097 | 0.54802 | 0.65773 | 0.6286 | 0.60263 | 0.60494 | 0.68323 | 0.64536 | 0.61631 | 0.59568 | 0.6438 | 0.63027 | 0.63593 | 0.60663 | 0.65632 | 0.61152 | 0.62608
25-36h | 0.59463 | 0.63962 | 0.6607 | 0.58392 | 0.54207 | 0.65214 | 0.62521 | 0.59332 | 0.59872 | 0.67588 | 0.63954 | 0.60705 | 0.58812 | 0.6395 | 0.62602 | 0.62633 | 0.60085 | 0.65151 | 0.60975 | 0.61844
37-48h | 0.58863 | 0.63103 | 0.65171 | 0.57645 | 0.53612 | 0.64301 | 0.61833 | 0.58327 | 0.59569 | 0.67226 | 0.63362 | 0.59663 | 0.57977 | 0.62996 | 0.62258 | 0.61811 | 0.59608 | 0.6448 | 0.60338 | 0.61093
Notes: RMSE decreases over the 5-Year period.

## Slide 19: Trends in Full-Domain Seasonal R and RMSE Scores over 2010-14 Period for 0-12 H Forecasts
Chart: R - By Year and Season, 2010-2014
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
O3 | 0.60449 | 0.65658 | 0.64754 | 0.5933 | 0.56655 | 0.66712 | 0.62192 | 0.6042 | 0.61078 | 0.68743 | 0.66274 | 0.62462 | 0.60905 | 0.66701 | 0.64767 | 0.64713 | 0.61598 | 0.67668 | 0.6275 | 0.63343
NO2 | 0.55288 | 0.48577 | 0.56774 | 0.55901 | 0.51012 | 0.51748 | 0.52728 | 0.56781 | 0.51174 | 0.49417 | 0.61247 | 0.55945 | 0.5312 | 0.51641 | 0.61946 | 0.60554 | 0.55168 | 0.53841 | 0.5924 | 0.61533
PM2.5 | 0.3813 | 0.41723 | 0.43558 | 0.33408 | 0.29502 | 0.46702 | 0.39563 | 0.34898 | 0.37533 | 0.34813 | 0.36511 | 0.33255 | 0.32813 | 0.35202 | 0.41779 | 0.3308 | 0.37557 | 0.3049 | 0.35572 | 0.37258
Chart: RMSE - By Year and Season, 2010-2014
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
O3 | 14.2129 | 14.957 | 13.0633 | 12.2812 | 13.7969 | 15.3072 | 13.4061 | 12.0321 | 13.6105 | 14.2512 | 12.2116 | 10.5313 | 13.3667 | 13.3267 | 11.6437 | 11.5403 | 13.152 | 12.8978 | 11.8436 | 11.1655
NO2 | 9.0442 | 7.3034 | 7.6819 | 10.0624 | 9.1422 | 7.2993 | 8.3441 | 9.6858 | 8.8575 | 7.937 | 8.6218 | 9.1673 | 8.2702 | 7.6238 | 7.2167 | 9.1814 | 7.9149 | 6.9405 | 6.8838 | 8.7541
PM2.5 | 10.7598 | 11.9001 | 10.3815 | 12.8352 | 9.8625 | 11.551 | 11.0114 | 13.4929 | 9.8969 | 11.5603 | 11.5446 | 11.7697 | 8.3069 | 11.2868 | 9.6946 | 13.3668 | 8.121 | 11.0581 | 9.1461 | 10.2989
Notes: R improved for NO2 and RMSE improved for all three species, particularly O3.

## Slide 20
Correlation Coefficient (R) for Hourly O3, 2014 Seasonal
Notes: Higher correlation coefficient in the summer over the high O3 areas.

## Slide 21
Mean Bias (MB) for Hourly O3, 2014 Seasonal
Notes: Model overestimates O3 in the Summer and Fall seasons over the eastern continent, underestimates O3 in the Winter and Spring seasons for the most of the stations

## Slide 22: Variation of Seasonal Correlation Coefficient R for O3 by Region and Landuse, 2010-2014
Chart: R - O3 By Year, Season, and Canadian Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
ECAN_Urban | 0.58396 | 0.70395 | 0.6547 | 0.52955 | 0.50056 | 0.70464 | 0.66177 | 0.61182 | 0.55449 | 0.71887 | 0.68182 | 0.61403 | 0.49576 | 0.66077 | 0.64781 | 0.63032 | 0.51382 | 0.67397 | 0.6151 | 0.62851
ECAN_Rural | 0.50991 | 0.66284 | 0.58676 | 0.48685 | 0.43093 | 0.65085 | 0.58617 | 0.56675 | 0.48736 | 0.67736 | 0.62884 | 0.58226 | 0.49882 | 0.62445 | 0.54401 | 0.53891 | 0.55922 | 0.67804 | 0.52714 | 0.59297
WCAN_Urban | 0.54813 | 0.60328 | 0.50001 | 0.42481 | 0.48126 | 0.6373 | 0.55913 | 0.49924 | 0.51092 | 0.61072 | 0.55311 | 0.48688 | 0.4879 | 0.59294 | 0.54733 | 0.49806 | 0.46671 | 0.60466 | 0.4864 | 0.49825
WCAN_Rural | 0.4263 | 0.53183 | 0.4043 | 0.30809 | 0.35705 | 0.53944 | 0.39666 | 0.32692 | 0.36407 | 0.57082 | 0.48928 | 0.37869 | 0.3732 | 0.56944 | 0.49459 | 0.26906 | 0.39101 | 0.56553 | 0.49323 | 0.38108
Chart: R - O3 By Year, Season, and U.S. Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
EUSA_Urban | 0.62353 | 0.71406 | 0.70082 | 0.62876 | 0.6069 | 0.70615 | 0.642 | 0.60163 | 0.64077 | 0.72736 | 0.68895 | 0.65613 | 0.61807 | 0.71928 | 0.70824 | 0.66004 | 0.634 | 0.73076 | 0.6702 | 0.64159
EUSA_Rural | 0.59484 | 0.68861 | 0.66097 | 0.579 | 0.54989 | 0.68642 | 0.60531 | 0.58154 | 0.60325 | 0.71465 | 0.63456 | 0.62619 | 0.58636 | 0.68872 | 0.65287 | 0.63712 | 0.61425 | 0.69302 | 0.59278 | 0.63942
WUSA_Urban | 0.62981 | 0.69217 | 0.64865 | 0.55668 | 0.65862 | 0.70903 | 0.66535 | 0.57464 | 0.68286 | 0.70998 | 0.70219 | 0.58975 | 0.66606 | 0.69804 | 0.65576 | 0.61854 | 0.65365 | 0.7017 | 0.67016 | 0.58601
WUSA_Rural | 0.56531 | 0.62521 | 0.57454 | 0.49665 | 0.54899 | 0.61676 | 0.58838 | 0.49905 | 0.59072 | 0.61438 | 0.62992 | 0.52026 | 0.57312 | 0.60849 | 0.58601 | 0.54837 | 0.58233 | 0.6412 | 0.61129 | 0.53169
Notes: Correlation coefficient varies significantly by region and by landuse: urban better than rural, eastern stations better than western stations.

## Slide 23: Variation of Seasonal Mean Bias for O3 by Region and Landuse, 2010-2014
Chart: MB - O3 By Year, Season, and Canadian Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
ECAN_Urban | -6.3673 | 3.0872 | 3.2477 | -6.3272 | -3.969 | 2.6443 | 4.4806 | -4.1977 | -4.74 | -0.39054 | 1.0492 | -3.297 | -7.6689 | 0.16547 | 1.8456 | -5.7524 | -6.9256 | 0.95898 | 2.4405 | -5.6604
ECAN_Rural | -5.9289 | 4.4969 | 3.7899 | -7.7853 | -4.3497 | 4.108 | 5.2103 | -5.6119 | -4.3669 | 2.143 | 2.9643 | -4.0218 | -6.2882 | 3.7991 | 3.5893 | -6.4436 | -5.2289 | 3.8157 | 4.0637 | -6.2741
WCAN_Urban | -1.2291 | 1.3169 | 2.7954 | 1.5986 | -4.1732 | 0.030724 | 3.1454 | 0.13066 | -3.0667 | 0.74263 | 1.1095 | 0.59691 | -3.9077 | 0.23667 | 2.4739 | -1.6575 | -3.1803 | 1.5432 | 2.0924 | -0.73154
WCAN_Rural | -5.5839 | -0.22035 | -1.5393 | -3.7566 | -8.7969 | -0.8235 | -0.51498 | -5.1624 | -5.1226 | -0.10657 | -0.78211 | -3.4774 | -7.3604 | 0.19874 | 0.29775 | -5.8148 | -5.8202 | -0.33708 | 0.42695 | -4.5602
Chart: MB - O3 By Year, Season, and U.S. Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
EUSA_Urban | -4.7971 | 5.2678 | -0.9987 | -7.1614 | -2.3316 | 4.2196 | -1.3226 | -5.2675 | -2.6244 | 2.2643 | -1.11 | -3.4206 | -5.7706 | 3.2458 | 0.13508 | -5.3493 | -5.0878 | 3.4709 | 0.33863 | -4.9074
EUSA_Rural | -4.4678 | 6.5829 | -1.0061 | -7.525 | -2.8111 | 4.6208 | -1.0733 | -6.2746 | -2.6527 | 2.4375 | -1.0003 | -4.2572 | -5.5839 | 5.1316 | 1.4046 | -6.1459 | -4.8992 | 5.9467 | 1.674 | -5.3683
WUSA_Urban | -9.2933 | -6.9073 | -6.2989 | -5.9142 | -10.7031 | -7.9866 | -5.8308 | -5.4542 | -9.4839 | -7.9836 | -6.7256 | -5.2939 | -8.4398 | -5.939 | -6.161 | -5.9892 | -9.4923 | -5.5164 | -5.8233 | -5.194
WUSA_Rural | -8.9482 | -5.4254 | -6.6789 | -7.9749 | -10.7004 | -6.9527 | -6.2249 | -8.5327 | -10.1538 | -8.2845 | -6.8757 | -7.3827 | -8.2926 | -5.5485 | -5.2773 | -8.3659 | -8.2279 | -3.8069 | -4.2878 | -6.6349
0
0
Notes: Mean bias also varies significantly by region and by landuse

## Slide 24
Hourly Urban Sites
Monthly Urban Sites
Hourly Rural Sites
Monthly Rural Sites
Hourly, Weekly, and Monthly O3 by Landuse for Each Year
Weekday Urban Sites
Weekday Rural Sites
Notes: Overall model captured well the diurnal variation and also reasonably well the variation over the 7 days of a week. However, model failed to capture the peak O3 concentration in Spring. O3 peak predicted by model is in summer. Wasn’t model able to predict well the stratospheric O3 intrusion in Spring?

## Slide 25
Monthly ECAN Urban Sites
Monthly WCAN Urban Sites
Monthly O3 by Region and Landuse for Each Year (1)
Monthly ECAN Rural Sites
Monthly WCAN Rural Sites

## Slide 26
Monthly EUSA Urban Sites
Monthly WUSA Urban Sites
Monthly O3 by Region and Landuse for Each Year (2)
Monthly EUSA Rural Sites
Monthly WUSA Rural Sites
Notes: The disparity of O3 peak between model and observation happened mostly for the eastern stations, unlikely due to the stratospheric O3 intrusion in Spring. Should be other reasons.

## Slide 27: Variation of Seasonal Correlation Coefficient R for PM2.5 by Region and Landuse, 2010-2014
Chart: R - PM2.5 By Year, Season, and Canadian Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
ECAN_Urban | 0.32715 | 0.45741 | 0.52844 | 0.45658 | 0.38115 | 0.42002 | 0.46816 | 0.45042 | 0.41863 | 0.43439 | 0.56605 | 0.42288 | 0.37916 | 0.37029 | 0.49609 | 0.43085 | 0.41538 | 0.37507 | 0.39836 | 0.47515
ECAN_Rural | 0.1698 | 0.41037 | 0.63875 | 0.29195 | 0.47948 | 0.46053 | 0.57195 | 0.48087 | 0.45946 | 0.51046 | 0.56867 | 0.43289 | 0.32255 | 0.33568 | 0.34131 | 0.44101 | 0.38382 | 0.40002 | 0.45346 | 0.49227
WCAN_Urban | 0.17551 | 0.098764 | 0.21978 | 0.20027 | 0.14745 | 0.16159 | 0.18244 | 0.098078 | 0.16714 | 0.12172 | 0.22289 | 0.13913 | 0.25241 | 0.14632 | 0.18186 | 0.15335 | 0.20399 | 0.13959 | 0.29477 | 0.25022
WCAN_Rural | 0.21317 | 0.099939 | 0.19233 | 0.30936 | 0.062518 | 0.16099 | 0.20428 | 0.19848 | 0.16618 | 0.14746 | 0.24985 | 0.16913 | 0.20578 | 0.14999 | 0.20182 | 0.12755 | 0.24146 | 0.096539 | 0.23269 | 0.23927
Chart: R - PM2.5 By Year, Season, and U.S. Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
EUSA_Urban | 0.39595 | 0.42144 | 0.47915 | 0.40991 | 0.29257 | 0.44019 | 0.45779 | 0.3661 | 0.37886 | 0.33396 | 0.43555 | 0.37229 | 0.32951 | 0.37294 | 0.49917 | 0.4033 | 0.3717 | 0.34176 | 0.41163 | 0.40975
EUSA_Rural | 0.41607 | 0.45183 | 0.47359 | 0.38171 | 0.26439 | 0.42658 | 0.42511 | 0.378 | 0.28265 | 0.32977 | 0.41364 | 0.38504 | 0.31886 | 0.34793 | 0.52378 | 0.43643 | 0.34621 | 0.29831 | 0.40253 | 0.43322
WUSA_Urban | 0.24822 | 0.3151 | 0.28372 | 0.24744 | 0.23073 | 0.28891 | 0.28352 | 0.2948 | 0.27916 | 0.2737 | 0.28022 | 0.29756 | 0.27877 | 0.22978 | 0.3856 | 0.25566 | 0.26993 | 0.27407 | 0.30826 | 0.3338
WUSA_Rural | 0.19749 | 0.26341 | 0.17709 | 0.208 | 0.14054 | 0.24082 | 0.20872 | 0.26326 | 0.14931 | 0.1233 | 0.085835 | 0.1565 | 0.12949 | 0.11803 | 0.22561 | 0.27191 | 0.1635 | 0.18751 | 0.18167 | 0.16675
Notes: Eastern sites are between than western sites in terms of R

## Slide 28
Hourly Urban Sites
Monthly Urban Sites
Hourly Rural Sites
Monthly Rural Sites
Hourly, Weekly, and Monthly PM2.5 by Landuse
Weekday Urban Sites
Weekday Rural Sites
Notes: Significant overestimation of PM.25 for urban sites and underestimation of PM2.5 for rural sites particularly during the mid day

## Slide 29: Variation of Seasonal Correlation Coefficient R for NO2 by Region and Landuse, 2010-2014
Chart: R - NO2 By Year, Season, and Canadian Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
ECAN_Urban | 0.56089 | 0.47867 | 0.61516 | 0.57925 | 0.5429 | 0.50125 | 0.54247 | 0.60748 | 0.53069 | 0.45024 | 0.63663 | 0.5921 | 0.5003 | 0.47802 | 0.60147 | 0.62513 | 0.5492 | 0.52941 | 0.59832 | 0.62395
ECAN_Rural | 0.46301 | 0.45554 | 0.50068 | 0.53274 | 0.42569 | 0.4811 | 0.40757 | 0.59046 | 0.43406 | 0.50448 | 0.53482 | 0.48119 | 0.45705 | 0.46857 | 0.49185 | 0.62953 | 0.42241 | 0.48957 | 0.53793 | 0.54024
WCAN_Urban | 0.51268 | 0.4851 | 0.55 | 0.5247 | 0.46737 | 0.53269 | 0.49097 | 0.49329 | 0.50237 | 0.52256 | 0.58296 | 0.54589 | 0.54296 | 0.53221 | 0.6173 | 0.586 | 0.53234 | 0.55351 | 0.58074 | 0.59339
WCAN_Rural | 0.32785 | 0.14383 | 0.309 | 0.412 | 0.25298 | 0.15662 | 0.23418 | 0.31237 | 0.1635 | 0.14892 | 0.36204 | 0.36665 | 0.34436 | 0.25659 | 0.43215 | 0.40735 | 0.36034 | 0.25685 | 0.41023 | 0.46772
Chart: R - NO2 By Year, Season, and U.S. Region
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
EUSA_Urban | 0.49044 | 0.43725 | 0.59616 | 0.64315 | 0.5986 | 0.52635 | 0.59124 | 0.62453 | 0.59468 | 0.5488 | 0.58334 | 0.61925
EUSA_Rural | 0.48965 | 0.34066 | 0.33016 | 0.34518 | 0.3834 | 0.45205 | 0.4336 | 0.55356 | 0.4186 | 0.37116 | 0.45648 | 0.50609
WUSA_Urban | 0.42082 | 0.41427 | 0.46096 | 0.51255 | 0.42143 | 0.35744 | 0.50097 | 0.40387 | 0.44923 | 0.44077 | 0.46392 | 0.4996
WUSA_Rural | 0.39418 | 0.30013 | 0.45837 | 0.4062 | 0.40949 | 0.45234 | 0.56956 | 0.58293 | 0.44138 | 0.39235 | 0.54245 | 0.57664
Notes: Urban is better than rural and eastern is better than western for most of the stations

## Slide 30
Hourly Urban Sites
Monthly Urban Sites
Hourly Rural Sites
Monthly Rural Sites
Hourly, Weekday, and Monthly NO2 by Landuse
Weekday Urban Sites
Weekday Rural Sites
NO2 bias significantly reduced starting from 2012:
(1) US NO2 observation included in mid-2012
(2) New code version, new emissions introduced in Nov. 2011 and model resolution changed from 15km to 10km in Oct. 2012
Which one is the main reason?
Notes: Comparisons shows significant improvement in terms of bias after 2012. Two things happened in 2012: 1) New code version, new emissions introduced in Nov. 2011 and model resolution changed from 15km to 10km in Oct. 2012, and 2) added US NO2 measurements in mid 2012

## Slide 31
Hourly ECAN Urban Sites
Hourly WCAN Urban Sites
hourly NO2 by Region and Landuse for Canada
Hourly ECAN Rural Sites
Hourly WCAN Rural Sites
Probably due to model updates as indicated by the improvements to Canadian sites
Notes: Comparisons for Canadian sties indicate the reduced bias is likely due to updates to model

## Slide 32
Number of hours with O3 > 100ppb for 2010
Notes: O3 concentration larger than 100ppb occurs regionally over the polluted area and over water.

## Slide 33
Number of hours with PM2.5 > 100 ug/m3 for 2010
Notes: PM2.5 concentration larger than 100 ug/m3 occur locally near large sources

## Slide 34
Number of hours with NO2 > 100 ppbv for 2010
Notes: Similar to PM2.5, NO2 concentration larger than 100 ppb occur locally near large sources too

## Slide 35: Summary and Conclusions
A 5-year performance evaluation has been carried out for the operational Canadian AQ forecast model GEM-MACH for the period 2010-2014
Careful filtering should be applied to near-real-time measurements of O3, NO2, and PM2.5 for model evaluation
A trend towards improved model performance associated with model upgrades can be discerned, especially for R and RMSE scores
Regional differences and urban-rural differences are evident in all performance metrics
Overall model performs better over urban areas vs. rural areas and eastern vs. western North America
High NO2 concentrations occur mainly in areas near large emission sources, whereas high concentrations of O3 and PM2.5 occur at the regional scale over populated areas. High O3 concentrations over water bodies are also evident

## Slide 36: Thank you for your attention

## Slide 37: 2010 O3 Time Series, AQS Station in “Four Corners” Region of New Mexico

## Slide 38: Impact of Data Filtering on NO2 Seasonal RMSE Scores, 2010-2014
Chart: RMSE -NO2 by Year and Season, 2010-2014
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
Orignal | 8.9143 | 15.225 | 7.6481 | 9.9628 | 9.0086 | 7.5115 | 8.2741 | 9.6065 | 8.653 | 8.3966 | 9.1595 | 9.0833 | 8.2109 | 8.0332 | 7.8485 | 9.7211 | 8.0102 | 7.3554 | 7.5738 | 8.9605
5Y_75%_Filtering | 9.0442 | 7.3034 | 7.6819 | 10.0624 | 9.1422 | 7.2993 | 8.3441 | 9.6858 | 8.8575 | 7.937 | 8.6218 | 9.1673 | 8.2702 | 7.6238 | 7.2167 | 9.1814 | 7.9149 | 6.9405 | 6.8838 | 8.7541
2Y_75%_Filtering | 9.0691 | 7.2831 | 7.6946 | 10.1039 | 9.1565 | 7.301 | 8.3651 | 9.7291 | 8.6848 | 8.3699 | 9.0787 | 9.1735 | 8.2852 | 8.0921 | 7.8916 | 9.8324 | 8.0532 | 7.3515 | 7.6188 | 9.055

## Slide 39
Chart: R – NO2 by year and season
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
0-12h | 0.55413 | 0.18587 | 0.56755 | 0.56021 | 0.50938 | 0.48179 | 0.52571 | 0.56832 | 0.50778 | 0.47887 | 0.58194 | 0.56604 | 0.53532 | 0.51041 | 0.60722 | 0.59414 | 0.56103 | 0.53039 | 0.59146 | 0.61148
13-24h | 0.5351 | 0.17863 | 0.55517 | 0.54617 | 0.50055 | 0.46359 | 0.51365 | 0.55121 | 0.49799 | 0.46823 | 0.57654 | 0.55686 | 0.5211 | 0.50017 | 0.59863 | 0.59083 | 0.54227 | 0.51603 | 0.58423 | 0.59872
25-36h | 0.53387 | 0.1774 | 0.53534 | 0.52821 | 0.4995 | 0.46826 | 0.50586 | 0.53885 | 0.48678 | 0.4628 | 0.57472 | 0.54374 | 0.52301 | 0.48558 | 0.59596 | 0.58289 | 0.53956 | 0.50795 | 0.5781 | 0.58971
37-48h | 0.50852 | 0.17288 | 0.53033 | 0.51287 | 0.48524 | 0.45129 | 0.49279 | 0.52396 | 0.47967 | 0.45328 | 0.56578 | 0.52988 | 0.51262 | 0.48325 | 0.58987 | 0.57118 | 0.5275 | 0.50191 | 0.57087 | 0.58081
Chart: RMSE – NO2 by year and season
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
0-12h | 8.9143 | 15.225 | 7.6481 | 9.9628 | 9.0086 | 7.5115 | 8.2741 | 9.6065 | 8.653 | 8.3966 | 9.1595 | 9.0833 | 8.2109 | 8.0332 | 7.8485 | 9.7211 | 8.0102 | 7.3554 | 7.5738 | 8.9605
13-24h | 8.8498 | 15.2504 | 7.6865 | 10.0856 | 8.8833 | 7.5648 | 8.2804 | 9.7779 | 8.4456 | 8.2253 | 8.9131 | 9.0524 | 8.0862 | 7.7394 | 7.8076 | 9.6457 | 7.9577 | 7.1835 | 7.4598 | 9.0949
25-36h | 8.7298 | 15.2301 | 7.8476 | 10.289 | 8.7976 | 7.4417 | 8.2871 | 9.8989 | 8.4152 | 8.2514 | 8.7984 | 9.1935 | 7.9659 | 7.895 | 7.7721 | 9.7402 | 7.9138 | 7.1322 | 7.4724 | 9.1961
37-48h | 8.8464 | 15.3068 | 7.8417 | 10.3656 | 8.8138 | 7.3697 | 8.3988 | 10.0622 | 8.3287 | 8.2206 | 8.904 | 9.2844 | 8.0338 | 7.8266 | 7.786 | 9.8834 | 8.0023 | 7.1137 | 7.4967 | 9.3048

## Slide 40
Chart: RMSE - PM2.5 by year and season
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
0-12h | 11.9241 | 13.3119 | 10.9317 | 13.0415 | 11.4617 | 12.9429 | 11.9722 | 13.7336 | 10.4367 | 13.2581 | 11.7707 | 11.8722 | 8.4279 | 11.26 | 9.6654 | 13.0788 | 8.1102 | 11.1376 | 9.3261 | 10.2315
13-24h | 11.6824 | 13.2961 | 10.6744 | 12.7277 | 11.2815 | 12.8427 | 11.7441 | 13.509 | 10.2768 | 13.2561 | 11.404 | 11.6416 | 8.3199 | 11.2588 | 9.5943 | 12.7952 | 7.9894 | 11.1417 | 9.1648 | 10.2184
25-36h | 11.609 | 13.3269 | 10.6716 | 12.6741 | 11.1506 | 12.6185 | 11.7176 | 13.2934 | 10.1736 | 13.2316 | 11.208 | 11.5308 | 8.2504 | 11.2684 | 9.5154 | 12.7655 | 7.8927 | 11.0984 | 9.0837 | 10.2909
37-48h | 11.494 | 13.2532 | 10.6037 | 12.6006 | 11.0957 | 12.545 | 11.7054 | 13.2677 | 10.0868 | 13.1995 | 11.2157 | 11.4818 | 8.2281 | 11.1957 | 9.5189 | 12.7647 | 7.8945 | 10.9797 | 9.025 | 10.3352
Chart: R - PM2.5 by year and season
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
0-12h | 0.32896 | 0.34084 | 0.40114 | 0.32618 | 0.22849 | 0.38084 | 0.33996 | 0.33887 | 0.32239 | 0.25939 | 0.34044 | 0.32912 | 0.32111 | 0.34253 | 0.40618 | 0.32796 | 0.37024 | 0.28846 | 0.33489 | 0.36332
13-24h | 0.32975 | 0.3414 | 0.4017 | 0.32856 | 0.22542 | 0.37763 | 0.34118 | 0.33576 | 0.31881 | 0.25931 | 0.34156 | 0.32769 | 0.31759 | 0.33991 | 0.40594 | 0.32665 | 0.36346 | 0.28651 | 0.33596 | 0.35866
25-36h | 0.32848 | 0.33368 | 0.39738 | 0.32038 | 0.2239 | 0.3743 | 0.33996 | 0.3302 | 0.31549 | 0.25634 | 0.33655 | 0.32354 | 0.31411 | 0.33402 | 0.40662 | 0.32038 | 0.35805 | 0.2837 | 0.33393 | 0.34932
37-48h | 0.32149 | 0.32799 | 0.39084 | 0.30842 | 0.21695 | 0.36655 | 0.33648 | 0.32223 | 0.30967 | 0.25134 | 0.33089 | 0.31773 | 0.30492 | 0.32577 | 0.3999 | 0.30924 | 0.34762 | 0.28053 | 0.33053 | 0.34373

## Slide 41
Chart: MB - by year and season
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
O3 | -6.0405 | 1.5007 | -1.6516 | -6.4591 | -5.3513 | 0.32104 | -1.3708 | -5.4723 | -5.0884 | -1.0799 | -2.0551 | -4.132 | -6.6489 | 0.51188 | -0.80762 | -5.8751 | -6.3105 | 1.1158 | -0.47978 | -5.1742
NO2 | -1.1175 | -0.36918 | -1.5641 | -2.7636 | -1.2909 | 0.023312 | -1.1309 | -3.0828 | -0.6882 | 0.51422 | 0.6956 | -1.8071 | -0.28946 | 1.4095 | -0.19527 | -1.6023 | -0.17741 | 0.79914 | -0.48883 | -2.0847
PM2.5 | 0.55287 | 0.59863 | 1.039 | -0.55144 | -1.0846 | 1.2589 | 1.0786 | -0.51079 | 0.080304 | 1.0861 | 1.5469 | -0.55204 | -0.63222 | 1.3985 | 1.0761 | -0.46205 | -0.56277 | 0.70054 | 0.64245 | -1.3074
Chart: NMB - by year and season
| 2010-spring (MAM) | 2010-summer (JJA) | 2010-autumn (SON) | 2010-winter (DJF) | 2011-spring (MAM) | 2011-summer (JJA) | 2011-autumn (SON) | 2011-winter (DJF) | 2012-spring (MAM) | 2012-summer (JJA) | 2012-autumn (SON) | 2012-winter (DJF) | 2013-spring (MAM) | 2013-summer (JJA) | 2013-autumn (SON) | 2013-winter (DJF) | 2014-spring (MAM) | 2014-summer (JJA) | 2014-autumn (SON) | 2014-winter (DJF)
O3 | -0.17153 | 0.048947 | -0.063756 | -0.26619 | -0.15527 | 0.01007 | -0.053204 | -0.22697 | -0.14728 | -0.032488 | -0.081251 | -0.18003 | -0.18735 | 0.017058 | -0.032593 | -0.24122 | -0.17975 | 0.037674 | -0.019278 | -0.21584
NO2 | -0.13986 | -0.064038 | -0.19833 | -0.23937 | -0.16487 | 0.0041199 | -0.13976 | -0.27478 | -0.097889 | 0.091648 | 0.086742 | -0.17792 | -0.039683 | 0.26402 | -0.025348 | -0.14627 | -0.025 | 0.14723 | -0.067682 | -0.19267
PM2.5 | 0.068326 | 0.057693 | 0.12728 | -0.060225 | -0.1344 | 0.12871 | 0.12714 | -0.053794 | 0.010421 | 0.11741 | 0.18019 | -0.067073 | -0.084164 | 0.15521 | 0.13281 | -0.0485 | -0.073743 | 0.076598 | 0.082591 | -0.14461

## Slide 42: GEM-MACH vs. GEM-MACH15 vs. GEM-MACH10
GEM-MACH is a multi-scale chemical weather forecast model comprised of dynamics, physics, and in-line chemistry modules
GEM-MACH15 is a particular configuration of GEM-MACH chosen for operational AQ forecasting; its key characteristics include:
  introduced as operational forecast model in Nov. 2009
  limited-area-model (LAM) grid configuration for North America
  15-km horizontal grid spacing, 58 vertical levels to 0.1 hPa
  2-bin sectional representation of PM size distribution (i.e., 0-2.5 and 2.5-10 μm) with 9 chemical components
  output species include hourly fields of O3, NO2, and PM2.5 needed for Air Quality Health Index forecasts
  GEM-MACH10 is the same as GEM-MACH15 except with 10-km horizontal grid spacing and 80 vertical levels to 0.1 hPa
    introduced as operational forecast model in Oct. 2012
Notes: Emphasize that the presentation will, from now on, describe GEM-MACH 15

## Slide 43: Operational GEM-MACH Chronology: 2009-14 (Changes to Piloting Model, Code, Grid, Emissions)
Nov. 2009: GEM-MACH15 becomes operational
Mar. 2010: New emissions files introduced with modified
primary PM2.5 spatial distribution in Canada
Oct. 2010: Piloting model: GEM15  GEM-LAM15
Oct. 2011: New code version, new emissions (SET0)
Oct. 2012: GEM-MACH10 & GEM-LAM10 become
operational, new emissions (SET1)
Nov. 2012: Reversion to SET0 emissions
Feb. 2013: New code version, 3 bug fixes
Nov. 2014: New GEM code, new GEM-LAM10

## Slide 44
Correlation Coefficient R for Hourly O3, 2010-14 Period, All 75%-Data-Complete Stations

## Slide 45
Correlation Coefficient R for Hourly NO2, 2010-14 Period, All 75%-Data-Complete Stations

## Slide 46
Correlation Coefficient R for Hourly NO2, 2014 Seasonal

## Slide 47
Mean Bias MB for Hourly NO2, 2014 Seasonal

## Slide 48
Correlation Coefficient R for Hourly PM2.5, 2010-14 Period, All 75%-Data-Complete Stations

## Slide 49
Correlation Coefficient R for Hourly PM2.5, 2014 Seasonal

## Slide 50
Mean Bias MB for Hourly PM2.5, 2014 Seasonal

## Slide 51
Hourly ECAN Urban Sites
Hourly WCAN Urban Sites
hourly O3 by Region and Landuse for Each Year (1)
Hourly ECAN Rural Sites
Hourly WCAN Rural Sites

## Slide 52
Hourly EUSA Urban Sites
Hourly WUSA Urban Sites
Hourly O3 by Region and Landuse for Each Year (2)
Hourly EUSA Rural Sites
Hourly WUSA Rural Sites
Notes: Eastern sites are better than western sites, urban sites are better than rural sites.

## Slide 53
Monthly ECAN Urban Sites
Monthly WCAN Urban Sites
Monthly PM2.5 by Region and Landuse for Each Year (1)
Monthly ECAN Rural Sites
Monthly WCAN Rural Sites

## Slide 54
Monthly EUSA Urban Sites
Monthly WUSA Urban Sites
Monthly PM2.5 by Region and Landuse for Each Year (2)
Monthly EUSA Rural Sites
Monthly WUSA Rural Sites

## Slide 55
Hourly ECAN Urban Sites
Hourly WCAN Urban Sites
hourly PM2.5 by Region and Landuse for Each Year (1)
Hourly ECAN Rural Sites
Hourly WCAN Rural Sites

## Slide 56
Hourly EUSA Urban Sites
Hourly WUSA Urban Sites
Hourly PM2.5 by Region and Landuse for Each Year (2)
Hourly EUSA Rural Sites
Hourly WUSA Rural Sites

## Slide 57
Monthly ECAN Urban Sites
Monthly WCAN Urban Sites
Monthly NO2 by Region and Landuse for Each Year (1)
Monthly ECAN Rural Sites
Monthly WCAN Rural Sites

## Slide 58
Monthly EUSA Urban Sites
Monthly WUSA Urban Sites
Monthly NO2 by Region and Landuse for Each Year (2)
Monthly EUSA Rural Sites
Monthly WUSA Rural Sites

## Slide 59
Hourly EUSA Urban Sites
Hourly WUSA Urban Sites
Hourly NO2 by Region and Landuse for Each Year (2)
Hourly EUSA Rural Sites
Hourly WUSA Rural Sites