## Slide 1: Low-cost Sensor Packages for Roadside Emissions Factor Estimation
CMAS – 10/7/2015
Karoline K. Johnson, Michael H. Bergin, Duke University
Armistead G. Russell, Georgia Institute of Technology

## Slide 2: Overview
Advantages of low-cost sensing
Applications of interest to modeling
Emissions factors estimation

## Slide 3
Inexpensive ($10 - $6000)
Many models commercially available
Small
Lightweight
Low power consumption
Easier to use and maintain once assembled
Real-time fast response
Portable and robust
Advantages of Sensors
US Federal Equivalence Method
$40,000
Shinyei
particle sensor
$100
Img sources: Shinyei.co.jp, www.navajonationepa.org /aqcp/AirMonitoringSite.html
Notes: http://www.ecotech.com/gas-analyzers/co-analyzer
www.shinyei.co.jp

## Slide 4: Applications

## Slide 5: Spatial and Temporal Distribution
Low-cost and low upkeep allows more nodes
Real-time data
Portable
Identifying hot spots
  Find areas higher than expected
  Deploy more expensive equipment in specific locations of interest
Chart: PM2.5 µg m-3
PM2.5 comparison across campus (~1 mile)
Sensor Pilot – Georgia Tech
Notes: Integrated filter samples

## Slide 6: Health Studies
Estimating exposure
Can use network of sensors to estimate ambient concentrations throughout a community in microenvironments
Indoor and outdoor
Some sensors can be used as personal monitors

## Slide 7: Other applications
  Mobile monitoring
  Citizen science
  Not feasible at this time
  Litigation
  Regulatory compliance

## Slide 8: Emissions Factors
Locate sensors near roadways and other sources
Calculate based on pollutant and CO2 concentrations
Emissions factors variable regionally and over time

## Slide 9: Sensors & Modeling
  Benefits of sensors for modeling
  Additional data for inputs, training, and evaluation of models (especially important for fine-scale modeling)
  Custom emissions factors for models
  Benefits of modeling for sensors
  Combining sensor data into useful product (concentration over a city, etc.)
  Identifying problematic nodes in network

## Slide 10: Emissions Factors Estimation

## Slide 11
Railyard Emissions Factors: Conventional Instruments
(Galvis et al., 2013)

## Slide 12: Railyard Emissions Factors: Conventional Instruments cont.
(Galvis et al., 2013)

## Slide 13
COZIR
CO2 sensor
temperature and humidity sensor
Shinyei
PM sensor
Arduino-microcontroler
microAeth – black carbon
Sensor Package
Monitoring station and sensor package installation
(Atlanta, GA)
Road Emissions Factors: Low-cost Sensors

## Slide 14: Package Design for Emissions Monitoring
Shoebox-sized
Weatherproof design
Fan draws air through the box
Price: 1-2 orders of magnitude less expensive
  PM2.5, CO2, and microcontroller ~$400
  + Optional microAeth ~$6,000
  + Optional gas-phase sensors ~$200 each
    (CO, NO, NO2, O3-Alphasense)
Emissions Package Deployed at I-40
Durham NC
Notes: Different format for bullets

## Slide 15: How accurate are these measurements?
Comparison with reference methods:
PM2.5
  Atlanta roadside, R2 ~0.5
  India (high ambient concentrations), R2 ~0.9
  Ideal range ~20 - 300 µg m-3
CO2
  Atlanta roadside, R2 ~0.75

## Slide 16: Emissions Factor Application
Calculate: pollutant per unit fuel or unit activity
Baseline concentration
Identify a period where both CO2 and the pollutant of interest rise and fall together
Notes: Something weird happened to the image….?

## Slide 17: Emissions Factor Application
2. Integrate black carbon above background levels

## Slide 18: Emissions Factor Application
3. Integrate CO2 above background concentrations
4. Convert to kg gasoline

## Slide 19: Emissions Factor Application
5. Calculate Emissions Factor

## Slide 20: Emissions Factors Results
Sensors
Atlanta Roadside
(g kg-1)
Light Duty
Gasoline
(g kg-1)
Mid Duty and Heavy Duty Diesel
(g kg-1)
(Ban-Weiss et al., 2008)
(Dallmann et al., 2013)
PM2.5 0.038 0.39 1.4
Black Carbon 0.010 0.11 0.92

## Slide 21: Durham Emissions Factors: In Progress
Use wind data to determine when background vs when from road
PM concentrations slightly lower (~20%, 4 ug m-3)
I-40
N
RDU
Monitoring station
130° SW
22
Monitoring Station
Durham, NC
Sensor Package Deployed at I-40
Durham, NC

## Slide 22: Additional Applications for EFs
Other large sources like airports, railyards, etc.
Small sources such as biomass- or refuse burning
Trash Burning in India

## Slide 23: Summary
New low-cost sensors have many benefits over conventional methods
Many potential applications
Accuracy must be taken into account
Sensing and modeling can be used together to provide even more valuable information

## Slide 24: Acknowledgements
This work was made possible by the NSF PIRE grant 1243535 and EPA Star grant R83503901.
Thanks to Gayle Hagler at EPA, Jason Hu, Jaidevi Jeyaraman, Laura King, Jennifer Mountino, and Rodney Weber at Georgia Tech.
This presentation’s contents are solely the responsibility of the grantee and do not necessarily represent the official views of the US EPA or NSF. Further, US EPA or NSF do not endorse the purchase of any commercial products or services mentioned in this presentation.

## Slide 25: References
Ban-Weiss, G. A., J. P. McLaughlin, R. A. Harley, M. M. Lunden, T. W. Kirchstetter, A. J. Kean, A. W. Strawa, E. D. Stevenson, and Kendall, G. R.(2008) Long-term changes in emissions of nitrogen oxides and particulate matter from on-road gasoline and diesel vehicles, Atmospheric Environment, 42, 220-232, 2008.
Dallmann, T. R., Kirchstetter, T. W., DeMartini, S. J., and Harley, R. A.(2013): Quantifying on-road emissions from gasoline-powered motor vehicles: accounting for the presence of medium- and heavy-duty diesel trucks Environmental Science & Technology 46, 13873-13881.
Galvis, B., Bergin, M., and Russell, A., (2013) Fuel-based fine particulate and black carbon emission factors from a railyard area in Atlanta, Journal of the Air & Waste Management Association, 63:6, 648-658, DOI: 10.1080/10962247.2013.776507

## Slide 26: Questions?
Contact: Karoline.Johnson@duke.edu