## Slide 1
Rick Saylor1, Barry Baker1, Pius Lee2, Daniel Tong2,3, Li Pan2 and Youhua Tang2
1 National Oceanic and Atmospheric Administration
Air Resources Laboratory
Atmospheric Turbulence and Diffusion Division
Oak Ridge, TN 37830
2 National Oceanic and Atmospheric Administration
Air Resources Laboratory
College Park, MD 20740
3 Cooperative Institute for Climate and Satellites
University of Maryland
College Park, MD 20740
A Comparison of Particle Dry Deposition Algorithms in Air Quality Models
October 5-7, 2015
17th Community Modeling & Analysis System Annual Meeting
Chapel Hill, NC

## Slide 2: Dry Deposition of particles an important process

## Slide 4
“Dry deposited substances such as PM2.5 and selected PM chemical components exhibit the largest differences between the model simulations …”

## Slide 6
“Results show that the simulated dry deposition can lead to substantial differences among the models.”

## Slide 8
from Lee et al. (2013)

## Slide 13: CAMx and CMAQ algorithms
Zhang et al. 2001
Pleim and Ran 2011
Brownian Efficiency
Impaction Efficiency
Interception Efficiency

## Slide 14: Divergence of measurements and models for forest canopies

## Slide 15: Simulation Domain & Model Configuration
CAMx v6.00
NAQFC NMMB
NAQFC Emissions
CB05 Chemistry
8 Bin CMU sectional Aerosols
26 Land Use Types
4km Horizontal Resolution
308x244 grid cells
22 vertical layers
PPM Advection
EBI Chemistry
Simulation Period: June 10th -July 1st, 2013
Southern Atmosphere Study
SENEX (NOAA) and SOAS (NSF & USEPA)

## Slide 16
Inputs: National Air Quality Forecasting Capability (NAQFC) 2013 projected emissions, NMMB meteorological fields and boundary conditions derived from NAQFC simulations.
Chemistry and Aerosols: CB05 chemical mechanism; 8 bin CMU sectional aerosol (0.02-0.05, 0.05-0.10, 0.10-0.22, 0.22-0.46, 0.46-1.0, 1.0-2.15, 2.15-4.64, and 4.64-10 μm)
Simulations:
  Base – Zhang et al. [2001] particle dry deposition scheme (default in CAMx v6.00)
  ΔPleim & Ran [2011] – particle dry deposition scheme in CAMx replaced with Pleim & Ran [2011], which is the default scheme of the Community Multiscale Air Quality (CMAQ) model.
  ΔPetroff & Zhang [2010] – particle dry deposition scheme in CAMx replaced with Petroff & Zhang [2010].
  ΔEmpirical – particle dry deposition scheme in CAMx replaced with a modified Pleim & Ran [2011] scheme where size-dependent deposition velocity over all forest LUCs is forced to agree with historical measurements as shown in Figure 2. Deposition velocities over all other LUCs are calculated according to the original Pleim & Ran [2011] formulation.
CAMx v6.00 Simulations:
  Base – Zhang et al. [2001] particle dry deposition scheme (default in CAMx v6.00)
  Pleim & Ran [2011] – particle dry deposition scheme in CAMx replaced with Pleim & Ran [2011], which is the default scheme of the Community Multiscale Air Quality (CMAQ) model.
  Petroff & Zhang [2010] – particle dry deposition scheme in CAMx replaced with Petroff & Zhang [2010].
  Empirical – particle dry deposition scheme in CAMx replaced with a modified Pleim & Ran [2011] scheme where size-dependent deposition velocity over all forest LUCs is forced to agree with historical measurements. Deposition velocities over all other LUCs calculated according to the original Pleim & Ran [2011] formulation.

## Slide 17: Empirical-based algorithm for forest canopies

## Slide 18
CAMx Results – June 10th – July 1st, 2013 – Mean PM2.5 (μg/m3)

## Slide 20
CAMx Results – June 10th – July 1st, 2013 – Total PM2.5 Deposition (g/ha)

## Slide 21
CAMx Results – June 10th – July 1st, 2013 – Total PM2.5 Deposition (g/ha)

## Slide 22
CAMx Results – June 10th – July 1st, 2013 – PM2.5 SO42- Deposition (g/ha)

## Slide 23
Summary and Implications
Surface PM2.5 concentrations in AQ models can change significantly (~20%) by altering the dry deposition parameterization.
Pleim & Ran [2011] (CMAQ) predicts the lowest total PM2.5 deposition due to the exclusion of the vegetation interception term.
Pleim & Ran [2011] results in better surface concentrations but perhaps for the wrong reasons.
  Petroff and Zhang [2010] predicts similar overall particle deposition to Pleim & Ran [2011], but requires many more LUC-specific parameters.

## Slide 24
Summary and Implications (cont’d)
  Forcing deposition velocities to match ecosystem-level observations over forests (Empirical simulation) results in worse 3-D model comparisons to surface PM2.5 (compensating errors in 3-D models?).
  Simulation consistent with ecosystem-level measurements deposits up to 5 times more than the Zhang et al. [2001] scheme to forest LUCs and shifts total deposition from wet-dominated to dry-dominated.
  Regulations based on a ‘critical loads’ analysis using 3-D model deposition may be misleading if forest canopy deposition velocity measurements are correct.
  Recent observations show bi-directional particle fluxes over all surface types, rather than one-way deposition as in current models. Future 3-D models will need improved surface-atmosphere exchange modules. More canopy-scale particle flux measurements are needed to develop and evaluate these modules, especially over forests.

## Slide 25
Particulate
Matter
Deposition

## Slide 26
Farmer et al. (2013); Gordon et al. (2010); Vong et al. (2011); DeVentner et al. (2015); and many others.
Particulate
Matter
Bi-directional fluxes

## Slide 27
DeVentner et al. (2015)
Particulate
Matter
Bi-directional fluxes

## Slide 28
Summary and Implications (cont’d)
  Forcing deposition velocities to match ecosystem-level observations over forests (Empirical simulation) results in worse 3-D model comparisons to surface PM2.5 (compensating errors in 3-D models?).
  Simulation consistent with ecosystem-level measurements deposits up to 5 times more than the Zhang et al. [2001] scheme to forest LUCs.
  Regulations based on a ‘critical loads’ analysis using 3-D model deposition may be misleading if forest canopy deposition velocity measurements are correct.
  Recent observations show bi-directional particle fluxes over all surface types, rather than one-way deposition as in current models. Future 3-D models will need improved surface-atmosphere exchange modules. More canopy-scale particle flux measurements are needed to develop and evaluate these modules, especially over forests.

## Slide 29
Questions?

## Slide 30: Slinn (1982)
= gravitational settling velocity of the particle (cm s-1)
= aerodynamic resistance above the surface or canopy (s cm-1)
= resistance of the surface or canopy (s cm-1)

## Slide 31
CAMx Results – June 10th – July 1st, 2013 – PM2.5 NO3- Deposition (g/ha)

## Slide 32: Slinn (1982)
= wind speed at canopy top (cm s-1);
= friction velocity (cm s-1);
= shape factor for wind speed profile within a vegetative canopy;
= overall canopy particle collection efficiency.
For a vegetative canopy,

## Slide 33: Slinn (1982)
The particle collection efficiency of the canopy …
= collection efficiency due to Brownian diffusion of particles;
= collection efficiency due to interception of particles by canopy elements;
= collection efficiency due to impaction of particles on canopy elements;
= collection efficiency reduction due to particle “rebound”.