## Slide 1
Understanding and improving emissions information through atmospheric observations and models
Greg Frost
Chemical Sciences Division, Earth System Research Laboratory
National Oceanic & Atmospheric Administration, Boulder, Colorado, USA
Gregory.J.Frost@noaa.gov, http://www.esrl.noaa.gov/
Acknowledgements: Ravan Ahmadov, Jessica Gilman, Joost de Gouw, Claire Granier, Si-Wan Kim, Brian McDonald, Megan Melamed, Paulette Middleton, Jeff Peischl, Gabrielle Petron, Tom Ryerson, Colm Sweeney, Christine Wiedinmyer

## Slide 2: Successes and Challenges of US Clean Air Act
www3.epa.gov/airtrends/aqtrends.html
Current US Non-Attainment Areas for O3 and PM
US Clean Air Act and subsequent regulations have reduced emissions of criteria pollutants for decades.
At the same time, population, economy, vehicle use, and energy consumption increased
US counties representing a significant fraction of US population remain in non-attainment of O3 and PM standards
2000
2004
2010
1985
2002
2006
2014
2008
2012
1998
1998
1995
1970
Notes: FIGURE 2.2 Percent changes from values in 1970 for gross domestic product, vehicle miles traveled,
population, energy consumption, CO2 emissions, and aggregate emissions from the six most widespread
air pollutants (carbon monoxide, ozone, lead, nitrogen dioxide, particulate matter, and sulfur dioxide)
through 2014 nationally over the United States. The graph shows decreasing air pollutant emissions over
time since passage of the Clean Air Act, despite growth in U.S. population, economy, energy use, and
miles driven. SOURCE: https://www3.epa.gov/airtrends/aqtrends.html.

## Slide 3: Global impacts of air pollution
Green: good Yellow: moderate
Red: unhealthy Brown: hazardous
Asia
aqicn.org
www.who.int/phe/health_topics/outdoorair/
Bad air quality is still a serious issue in many parts of the world
Air pollution is a leading cause of illness and mortality worldwide
Other nations look to the US for guidance on understanding and solving these problems

## Slide 4: Environmental actions and decisions focus on emissions
Research
Analysis
Prediction
Long-range transport
Air quality
Climate change
Regulation
Atmospheric modeling
Human exposure
Permitting & compliance
Standards attainment
Public reporting
Economics
Emissions trading
Control implementation
Diplomacy
Assessments
Pollution conventions
Data sharing
Emissions data addresses multiple mandates and has many uses

## Slide 5: Bottom-Up Inventory Methods
Inventories are simple in structure but complex in application
EX = ΣS [EFX,S  AS  (1 – CEX,S)]
Emissions factor = mass of compound X emitted by source S per unit activity
Activity of source S, e.g., amount of fuel burned
Effectiveness of control measures for compound X at source S
Sum up all sources S
Total mass of compound X emitted
Calculated for…
Specific region
Specific time
Also need…
Spatial allocation
Temporal variation
Speciation
Inventories are fundamental
Process-level understanding
High granularity
Comprehensive view
Key model inputs
Quantify changes
Prediction
Connect disciplines
Key decision-making tools
Complexity
Insufficient data
Long costly development cycle
Diverse data sources, traceability
Proprietary data
Inconsistencies
Unknown or missing sources
Super-emitting or sporadic sources
Uncertainties difficult to estimate
Inventories face challenges

## Slide 6: Top-down Emissions Approaches
Rely on high quality atmospheric observations of atmospheric abundance
Use chemical-transport models of varying complexity to convert atmospheric abundance into emissions
Hybrid approach: use atmospheric measurements in bottom-up inventory
Top-down deliverables:
Total emissions
Spatial mapping
Temporal variation
Sector partitioning
We cannot manage what we can’t measure – John Burrows
Top-down methods complement bottom-up inventories, helping to improve the scientific basis of emissions.
Bottom-Up Inventories
Top-Down Approaches
Reconciliation
Synthesis to Benefit Stakeholders
Improvement
Some benefits of top-down methods:
Quantifiable uncertainties
Quantify super-emitting or sporadic sources
Detect cheating
Complementary methods give confidence

## Slide 7
National Academies of Sciences, Engineering, and Medicine. 2016. The Future of Atmospheric Chemistry Research: Remembering Yesterday, Understanding Today, Anticipating Tomorrow.
Recommendations
Science Priorities
2016 National Academies Report
Notes: Priority Science Area 2: Quantify emissions and deposition of gases and particles in a
changing Earth system.
Emission and deposition processes govern concentrations and spatial distributions of
gases and particles in the atmosphere. A predictive capability of these distributions is key for
assessing the impacts of atmospheric processes on human and ecosystem health, weather, and
climate. Research is needed to reduce uncertainties in emissions for known sources and constrain
emissions of poorly understood constituents (e.g., bioparticles), as well as to understand
deposition processes that remove reactive species. Sources of atmospheric constituents change as
humans make new decisions about technology, energy systems, pollution control, agriculture,
and transportation. Natural sources respond to meteorological conditions, changes in land use,
longer-term changes in climate, and biogechemical and ecosystem feedbacks.
Actions needed to address these key scientific gaps include:
A. Better determine emissions from both anthropogenic and natural sources and their spatial
and temporal variations and trends.
B. Identify mechanisms and measure rates by which wet and dry deposition removes aerosol
particles and trace gases from the atmosphere.
C. Determine the role of meteorology, including temperature, precipitation, and extreme
events, on emissions and removal of atmospheric species.
D. Determine the role of global change and societal choices (including changes in climate,
energy choices, and land use) on the emissions and removal of atmospheric species.

## Slide 8: Two Examples Today
US motor vehicles
US oil and natural gas basins
Other NOAA examples I won’t have time for:
Power generation
Refineries
US vs European motor vehicles
Well blowouts
Agriculture
Wildfires

## Slide 9
Quantify on-road CO2 emissions
State-level taxable gasoline and diesel fuel sales reports
Public and annual
Map on-road CO2 emissions
Using traffic count data
Basis for scaling co-emitted combustion byproducts
McDonald et al. (J. Geophys. Res. 2014)
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
Fuel-Based Inventory of Vehicle Emissions (FIVE)

## Slide 10
Use of Roadway Studies for Emission Factors
Roadside monitoring data
Measures in-use vehicles
Captures high-emitters
Regulatory models typically rely on chassis dynamometer tests
Figure from Univ. of Denver FEAT System
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
Brian McDonald

## Slide 11
0
2
4
6
8
10
12
14
NO2 (ppb)
NOAA P-3 Aircraft
WRF-Chem Model
Si-Wan Kim et al. (J. Geophys. Res. 2016)
Simulated for California Nexus Study (CalNex) in 2010
Los Angeles is good test case of transportation emissions (~2/3 of NOx budget)
Test of Fuel-Based Emissions Approach

## Slide 12
Long-Term Trends in U.S. On-Road NOx Emission Factors
Gasoline EF high by factor of ~2
Diesel EF within ~20%
Figure updated from McDonald et al. (J. Geophys. Res. 2012)
MOVES = EPA’s Vehicle Emission Model

## Slide 13
Long-Term Trends in U.S. On-Road CO Emission Factors
Gasoline EF high by factor of ~3
Figure updated from McDonald et al. (Environ. Sci. Technol.. 2013)
MOVES = EPA’s Vehicle Emission Model

## Slide 14
Comparing U.S. Mobile Source NOx Emissions by Sector
McDonald et al. (in preparation)

## Slide 15
Comparing U.S. Mobile Source CO Emissions by Sector
McDonald et al. (in preparation)

## Slide 16
Comparing Fuel-Based & NEI/MOVES in Regional Model
McDonald et al. (in preparation)
NEI 2011
CO
NOy
WRF-Chem modeling compared to summer 2013 observations at SEARCH network site in downtown Atlanta
Model using fuel-based motor vehicle emissions captures ambient NOy and CO in urban areas better than EPA MOVES

## Slide 17
Comparing Fuel-Based & NEI/MOVES in Regional Model
McDonald et al. (in preparation)
NOy
CO
WRF-Chem modeling compared to vertical profile observations collected by the NOAA P-3 aircraft in Nashville in summer 2013
Model using fuel-based motor vehicle emissions captures ambient NOy and CO in urban areas better than EPA MOVES

## Slide 18
Comparing Fuel-Based & NEI/MOVES in Regional Model
McDonald et al. (in preparation)
Mean bias (model-obs) in summer 2013 daily 8-hr O3 max modeled with NEI 2011 vs. AQS data
Model using fuel-based motor vehicle emissions captures regional maximum O3 levels better than EPA MOVES
Change in model-obs bias for daily 8-hr O3 max
(∆bias = |model(NEI 2011)-obs|-|model(FIVE) – obs|)
FIVE is better 
 FIVE is worse

## Slide 19
Comparing Fuel-Based & NEI/MOVES in Regional Model
McDonald et al. (in preparation)
Mean bias (model-obs) in 2013 O3 exceedance days (>70 ppb) modeled with NEI 2011 vs. AQS data
Model using fuel-based motor vehicle emissions captures regional O3 exceedance days better than EPA MOVES
Change in model-obs bias for O3 exceedance days
(∆bias = |model(NEI 2011)-obs|-|model(FIVE) – obs|)
FIVE is better 
 FIVE is worse

## Slide 20
Quantifying Impacts of Oil and Gas Production
NOAA ESRL research is focused on:
A. Climate Emissions of radiative forcing agents (methane, black carbon, CO2, ozone)
B. Air quality
  Emissions of ozone and PM2.5 precursors Understanding ozone formation Emissions of air toxics (e.g. benzene)
ESRL research aircraft quantified methane (CH4) emissions from regions accounting for
  32% of U.S. oil production
  40% of U.S. natural gas production
  70% of U.S. shale gas production
Joost de Gouw
www.esrl.noaa.gov/csd/news/topics/oilandgas.html

## Slide 21
CH4 emissions = (wind speed • mixing height • measured plume CH4 enhancement)
Mass balance flights directly measure CH4 emissions rate
NOAA WP-3D
NOAA Twin Otter
Scientific Aviation Mooney
Jeff Peischl

## Slide 22
Substantial regional variability in oil/gas CH4 emissions
Regional emissions variability is high. Drivers include:
dry vs. wet gas formations, production activity, economic and regulatory framework
Interannual emissions variability appears low – at least on basin-wide scales.
Petron et al. JGR 2012; Petron et al. JGR 2014; Karion et al. GRL 2013; Peischl et al. JGR 2015; Peischl in prep

## Slide 23: Using VOC/CH4 Ratios to Quantify VOC Emissions
Jessica Gilman, in preparation
C2H6/CH4
15
10
5
0
VOC (ppbv)
1940
1920
1900
Methane (ppbv)
VOC | ER[VOC]/[CH4} | r | MWVOC
Ethane | 0.43 ± 0.06 | 0.94 | 30
Propane | 0.38 ± 0.04 | 0.96 | 44
n-Butane | 0.21 ± 0.03 | 0.94 | 58
Flux(VOC) = Flux(CH4) * ER(VOC/CH4) * MW(VOC)/MW(CH4)
VOCs and CH4 are highly correlated with in a basin
VOC/CH4 enhancement ratios (ERs) provide a chemical fingerprint of oil/gas activity
VOC/CH4 ERs are basin specific
Combine CH4 emissions derived from mass balance with VOC/CH4 ERs to quantify emissions of different VOC species in a basin

## Slide 24
Emission datasets | Source | Methane (tons/year) | Non methane VOCs (tons/year) | NOx (tons/year)
Bottom-up | EPA National Emission Inventory (NEI-2011) | 100,279 | 101,184 | 16,448
Top-down | Based on the measurements | 482,130 | 184,511 | 4,158
Total top-down based methane flux estimate from Karion et al., 2013
Total methane and other VOC emissions in NEI-2011 are lower by a factor of 4.8 and 1.8
than in the top-down estimates, respectively
Conversely, NOx emissions are 4 times higher in the NEI-2011 inventory
Implications for air quality regulations and for climate and air quality impacts
Atmospheric Measurements Improve Oil/Gas Emissions in Uintah Basin
Ahmadov, R., et al. (2015) Atmos. Chem. Phys.

## Slide 25
(NEI-2011)
Measurement-Based Emissions Improve WRF-Chem O3 Predictions in Uintah Basin
Multi-day buildup of surface O3 during stagnation episodes
Model using official bottom-up emissions inventory can’t reproduce observed high O3 levels
Ahmadov, R., et al. (2015) Atmos. Chem. Phys.

## Slide 26
(NEI-2011)
Measurement-Based Emissions Improve WRF-Chem O3 Predictions in Uintah Basin
Multi-day buildup of surface O3 during stagnation episodes
Model using official bottom-up emissions inventory can’t reproduce observed high O3 levels
Measured emissions case explains high O3 levels
High O3 in this basin driven mostly by oil/gas emissions
Ahmadov, R., et al. (2015) Atmos. Chem. Phys.

## Slide 27: Better Collaboration Can Improve Inventories
Some examples:
NOAA
NASA
AQRS
GEIA

## Slide 28
NOAA’s Emissions Research Benefits Stakeholders
What NOAA provides:
Connect research to models
Inform inventory development
Synthesize information
Nurture community of experts
NOAA Stakeholders
A
C
A
D
E
M
I
A
Forms of outreach:
Journal articles
Conferences
Assessments
Direct outreach

## Slide 29: NASA Air Quality Applied Sciences Team
aqast.org
Conveying NASA’s science information to regulatory agencies

## Slide 30
Office of Science and Technology Policy’s National Science and Technology Council
Air Quality Research Subcommittee (AQRS)
Co-chairs:
Dan Costa National Program Director, ORD’s Air, Climate, and Energy Research Program
John Daniel Deputy Director, Chemical Sciences Division, NOAA Earth System Research Lab
Goals: To enhance the effectiveness and productivity of U.S. air quality research and to improve information exchange on air quality issues, including the scientific knowledge base for air quality standards and compliance assessment.
Ongoing topics of interagency discussion and coordination:
Ozone transport (tropospheric and stratospheric) and the NAAQS
Wildfires: Future field experiments to improve understanding of emissions, chemical transformations, transport, and impacts
Appropriate response to the report by the National Academies of Sciences, Engineering, and Medicine on the future of atmospheric chemistry research
Committee on Environment, Natural Resources, and Sustainability (CENRS)
Federal Interagency Cooperation on Air Quality

## Slide 31
International Emissions Efforts
Analysis
Identifying priorities, facilitating research, and synthesizing findings to improve the scientific basis of emissions
China Working Group
Latin America/ Caribbean WG
VOC WG
Assessing Emissions Quantification
using
Inverse Modeling
(joint with IGAC)
www.geiacenter.org
Community
Strengthening the emissions community by connecting developers and users
GEIA member(s)
SSC member(s)
2000 people worldwide
Access
Creating easier, more open access to emissions data and information
www.globalchange.umd.edu/ceds/
Community Emissions Data System
Notes: Open information
Freely available
Open to all members of the GEIA community
Strengthening community
GEIA supports network of 1800 people worldwide
GEIA organizes bi-annual conferences
Through IGAC and other sponsors, GEIA provides travel support and encourages participation of early career scientists and scientists from emerging countries
Research priorities, e.g.: Land Use, Fires, Energy Production, Agriculture, Urban Areas, Historical Emissions
GEIA Working Groups, including 2 that focus on building understanding of regional emissions
China WG: Organizing East Asian Emissions Assessment, includes many papers in a multi-year ACP special issue
Latin America/Caribbean WG: Building database of emissions experts in LAC nations. Organizing workshops and other community activities.
VOCs
Urban
GEIA demonstrates approaches for quantifying emissions that can be applied worldwide
GEIA synthesizes and conveys emissions science for the benefit of global emissions stakeholders

## Slide 32: Some Final Thoughts
Emissions are critical to decision making
Inventories are fundamental datasets with many challenges
Atmospheric observations and models complement inventories and help inform emissions understanding
Reconciling approaches improves scientific basis
Structures exist to work together nationally and globally
Guiding principles:
  Humility
  Flexibility
  Communication
  Collaboration