## Slide 1: Organic Aerosol Sources and Partitioning in CMAQv5.2
Office of Research and Development
National Exposure Research Laboratory; Research Triangle Park, NC
2016 CMAS Annual Meeting
Benjamin N. Murphy
Matthew Woody, Jeff Young and Havala O. T. Pye
National Exposure Research Laboratory, US Environmental Protection Agency

## Slide 2: Organic aerosol background
Organic aerosol in the atmosphere:
is a significant contribution to mass throughout the world
is becoming relatively more important for PM2.5 predictions as PM sulfate and nitrate concentrations fall
has been shown to evaporate with dilution from near-source to ambient conditions
(Lipsky et al., Environ Sci Technol, 2006, Grieshop et al., ACP, 2009, May et al., Atmos. Environ, 2013)
is primarily comprised of oxygenated compounds
(Ng et al., ACP, 2010; Zhang et al., Anal Bioanal Chem, 2011)
Organic aerosol in CMAQv5.1:
is dominated by primary, nonvolatile organic mass
underestimates the response of OA to photooxidation in urban areas (Woody et al., ACP, 2016)
overestimates OA observations in winter (due to high POA concentrations)
underestimates OA observations in summer (due to low SOA concentrations)
Primary Secondary
OA OA

## Slide 3: A sample of chemical transport models that have considered semivolatile POA
United States
Robinson et al., Science, 2007
Lane et al., AE, 2008
Shrivastava et al., JGR, 2008
Murphy et al., JGR, 2010
Ahmadov et al., JGR, 2012
Koo et al., AE, 2014
Hodzic et al., GRL, 2014
Jathar et al., ACP, 2015
Woody et al., ACP, 2016
Mexico
Tsimpidi et al., ACP, 2010
Shrivastava et al., JGR, 2011
Shrivastava et al., JGR, 2013
Europe
Hodzic et al., ACP, 2010
Fountoukis et al., ACP, 2011
Murphy et al., ACP, 2012
Bergström et al., ACP, 2012
Karnezi et al., 2015
Ciarelli et al., ACP, 2016
Asia
Matsui et al., ACP, 2014
Zhao et al., Sci. Reports, 2016
Global
Farina et al., JGR, 2010
Pye and Seinfeld, ACP, 2010
Jathar et al., ACP, 2011
Jo et al., AE, 2013
Spracklen et al., ACP, 2013
Tsimpidi et al., GMD, 2014
Tsigaridis et al., ACP, 2014
Notes: Many studies have looked at this in various domains
A few have done winter studies
They all find better results when treating semivolatile POA
Have to include some other source in their model to overcome underprediction – usually aging of anthropogenic SOA

## Slide 4: Sources of uncertainty in OA formation parameterizations
POA evaporation in CTMs causes massive underprediction of total OA
Where does the missing SOA come from?
POA
SOA
SOG
VOC Emissions
Toluene, Xylene, Benzene,
Alkanes, Alkenes, etc
·OH, O3,
NO3·
LV-POA
SV-POA
LV-POG
SV-POG
VOC Emissions
Toluene, Xylene, Benzene,
Alkanes, Alkenes, etc
SOG
SOA
·OH, O3,
NO3·
IVOC
·OH
Aged SOG
·OH
Aged SOA
Missing Vapors from Chamber Walls
Organic-Water Interactions
1
2
3
4
Potential Combustion SOA (pcSOA)
nvPOA
svPOA
Semivolatile POA
SOG – secondary organic gas
LV-POG – low volatility primary organic gas
SV-POG – semivolatile primary organic gas
IVOC – intermediate volatility organic compounds
Both of these configurations are available in CMAQv5.2

## Slide 5: Organic aerosol updates
Semivolatile POA:
  Consistent with 1.5-Volatility Basis Set implementation (Koo et al., Atmos. Environ., 2014)
  POA aging:
    Explicit functionalization and fragmentation
    kOH = 4 x 10-11 cm3 molec-1 s-1
Volatility Distribution for POA Emissions |  |  |  |  |  | 
Volatility - C*(298 K) µg m-3 |  | ≤ 0.1 | 1 | 10 | 100 | 1000
POA Emissions Factor |  | 0.09 | 0.09 | 0.14 | 0.18 | 0.5
pcSOAparticle
pcSOAvapor
(C* = 10-5 µg m-3)
pcVOC
kOH =
1.25 x 10-11
cm3 molec-1 s-1
+ OH
emissions
EF =
9.6 g pcVOC/ gPOA
Sensitivity Suite: EF [g pcVOC / g POA] = 6.5 – 12
kOH [cm3 molec-1 s-1] = 1.0 – 2.0 x 10-11
  Potential Combustion SOA (pcSOA):
LVOC SVOC IVOC
Inspired by the “SIMPLE” method:
Spracklen et al., 2011
Hodzic and Jimenez, 2011
Hayes et al., 2015
Woody et al., 2016

## Slide 6: Evaluated new model against observations in several domains
California at the Nexus of Air Quality and Climate Change (CalNex):
May-June 2010
Pasadena, CA
Bakersfield, CA
Carbonaceous Aerosol and Radiative Effects Study (CARES):
June 2010
Sacramento, CA
Cool, CA
CMAQ Configuration:
t-SOA: Odum method with yields from Griffin et al. (1999)
Anthropogenic Emiss: NEI 2011
Biogenic Emiss: BEIS 3.14
Southern Oxidant and Aerosol Study (SOAS):
May-June 2013
Centreville, AL
Look Rock, TN
Continental US:
CSN, IMPROVE, SEARCH
Jan-Dec, 2011
Jan, July 2002
4 km
12 km
12 km

## Slide 7: Diel-averaged profiles at continuous observation sites
California Domain
Eastern US Domain
Obs
nvPOA
svPOA (BASE)
svPOA (Low pcVOC Emission)
svPOA (High pcVOC Emission)

## Slide 8: Base module captures extent of oxygenation and inferred volatility distribution
Chart: Centreville Volatility Distribution
| -3 | -2 | -1 | 0 | 1 | 2
Obs-TD | 1.4694 | 0.64399 | 1.0068 | 1.4059 | 0.62585
CMAQv5.2 | 2.0594 | 0 | 0.15747 | 0.14433 | 0.25453 | 0.12758
WRF-Chem | 0.19048 | 0.072562 | 1.161 | 0.43537 | 0.13605
Pasadena (CalNex)
Saha et al., Quantifying the volatility of organic aerosol in the southeastern U.S., ACPD, 2016
LVOC SVOC
≤
mobs = 0.146
mbase = 0.103
mnvPOA = 0.007

## Slide 9: Performance sensitivity to pcSOA parameters
CalNex/CARES Sites:
Normalized Mean Bias Factor (NMBF) and Normalized Mean Error Factor (NMEF) calculated for data pairs at each site and then aggregated together.
CONUS Jan/July 2011:
Optimal Case: Low Emission Factor, Base Reaction rate (LEBR)
NMBF and NMEF calculated for data pairs at each site and month and then aggregated together.
12
10
8
6
12
10
8
6
12
10
8
6
12
10
8
6
1 1.5 2 x10-11
1 1.5 2 x10-11
1 1.5 2 x10-11
1 1.5 2 x10-11
Yu et al., Atmospheric Science Letters, 2006.

## Slide 10: CONUS domain: Annual (Jan-Dec) 2011 summary

## Slide 11: Seasonal and regional performance indicators for CONUS 2011 simulation

## Slide 12: Seasonal and regional performance indicators for CONUS 2011 simulation

## Slide 13: Year-to-year trends
Missing residential wood burning emissions

## Slide 14: 2011 and 2002 bias correlations with observed pollutants at CSN sites during summer
Aerosol-water interactions?
Organic nitrates?

## Slide 15: Take-Home Points and Next Steps
CMAQv5.2 predicts more realistic partitioning and photochemical dependence of OA formation
  Wintertime OC overprediction is nearly resolved (statistically)
  Diel-averaged profiles in urban conditions are faithfully reproduced. Performance is enhanced in nearly all US regions and seasons in 2011 scenario
  The model does not capture decrease in summertime urban daily-averaged OC concentrations from 2002 to 2011
  See talk by Wyat Appel: Wednesday at 9:50 for the effect on PM2.5
The OA representation will be continually updated with emerging science in order to improve accuracy and reduce the contribution of pcSOA
  Explicit IVOC emissions and yields
  Refine biomass burning OA with insights from field observations
  Revised SOA yields accounting for chamber wall losses of low volatility vapors
  Organic-water interactions
  Constrain vertical predictions with aircraft and remote sensing data

## Slide 17: Unbiased symmetric metrics
Yu et al., Atmospheric Science Letters, 2006.
Normalized mean bias factor
Normalized mean error factor

## Slide 20
Annual Winter Summer

## Slide 21
Annual Winter Summer

## Slide 22: Change in POA
Annual Winter Summer

## Slide 23: Change in POA vs [POA + Recycled POA + pcSOA]
Annual Winter Summer

## Slide 24: References
Koo et al., 1.5-Dimensional volatility basis set approach for modeling organic aerosol in CAMx and CMAQ, Atmos. Environ., 2014.
Ryerson et al, The 2010 California research at the nexus of air quality and climate change (CalNex) field study, Journ. Geophys. Res., 2013.
Woody et al., Understanding sources of organic aerosol during CalNex-2010 using the CMAQ-VBS, Atmos. Chem. Phys., 2016.
Yu and Luo, Modeling of gaseous methylamines in the global atmosphere: impacts of oxidation and aerosol uptake, Atmos. Chem. Phys., 2014.
Zaveri et al, Overview of the 2010 carbonaceous aerosols and radiative effects study (CARES), Atmos. Chem. Phys., 2012.

## Slide 25: CMAQ-NPF: New particle formation in CMAQ
Pasadena
Bakersfield
Sacramento
Cool
Median (and 25-75 percentiles) over noon to early evening hours
Size distributions during CalNex and CARES
Features:
Dedicated aerosol nucleation mode
New condensation sink calculation for treating sub-10 nm particles
SEVEN simultaneously occurring NPF pathways
  Binary H2SO4-H2O (Vehkamaki et al., 2002)
  Ternary H2SO4-NH3-H2O (Almeida et al., 2013)
  H2SO4-Amine (Olenius et al., 2013)
  Organic-H2SO4 (Paasonen et al., 2010)
  Pure Organic (Kirkby et al., 2016)
  Ion-mediated H2SO4 (Yu et al., 2009)
  Ion-mediated Organic (Kirkby et al., 2016)
  Performance:
Observations
CMAQ-NPF
CMAQv5.2
1 x 106
10,000
100
1