## Slide 1
Updates on Soil NOx parametrization in CMAQ v 5.1
Quazi Z. Rasool1, Jesse O. Bash2, Rui Zhang1, Ellen J. Cooter2, Benjamin Lash1, Daniel S. Cohan1 and Lok N. Lamsal3
1Department of Civil engineering, Rice University
2Computational Exposure Division, NERL, US Environmental Protection Agency
3NASA Goddard Space Flight Center
15th Annual CMAS Conference, UNC-Chapel Hill
October 25, 2016

## Slide 2: Outline: Soil N emissions in CMAQ
Updated parametrized approach to soil NO
  Replaces Yienger & Levy scheme in CMAQ
  Emissions are function of soil N, biome, and meteorology
  Soil N from EPIC agricultural model
Impact of soil NO on ozone and PM2.5
New mechanistic approach
  Consistent representation of multiple N species (NO, HONO, N2O, NH3)
  Accounts for soil processes (nitrification, denitrification)

## Slide 3: Soil NO Parameterization
Available Soil N
Biome
Fertilizer3
Deposition2
Meteorological model
Land Surface Model
Soil Temperature (T) and moisture (θ)
Canopy reduction factor
Pulsing = f (rain, dry period)
Emission Factor for each biome1
Soil NO
1Stienkamp & Lawrence (2011)
2 In-line from CMAQ
3 From Potter et al. (2010) or EPIC agricultural model

## Slide 4: Rasool GMD paper header

## Slide 5: Soil biome/Land Cover Dataset Enhancements
GEOS-Chem (0.25° x 0.25°)
CMAQ (12 km x 12 km)
GEOS-Chem
24 MODIS land cover categories
Too coarse for regional modeling
CMAQ
Mapped 40 NLCD categories from Pleim-Xiu to 24 MODIS categories
Köppen-Geiger climate zones
Sub-grid fractionation of biomes

## Slide 6
Environmental Policy Integrated Climate (EPIC) agricultural model
Fertilizer quantity: USDA Agricultural Resource Management Survey database, validated with fertilizer sales data
Fertilizer timing: Determined by plant nutrient stress
Can simulate varied agricultural practices (e.g., tillage, fertilizer type)
Fertilizer Emission Scenario Tool for CMAQ (FEST-C) incorporates EPIC simulated soil N into CMAQ runs
[Source: Cooter et al., 2012]
Notes: HUSC to Schedule Vegetable Plantings, Predict Harvest Dates and Manage Crops
Temperature controls the development of many organisms that don’t have complex thermoregulatory systems. This allows us to predict the development of different organisms by accurately using development or phenology models which are based on the accumulation of heat units (i.e. degree days) during a growing season.

## Slide 7
CMAQ with
soil NO parameterization
Biogenic Emissions Land use Database v4 (BELD4)
(Land cover, Crop type fractions per grid)
EPIC agricultural model#
Soil N
N Deposition
FEST-C*
*modified for CONUS run (based on Bash et al., 2013)
#modified for CONUS run (based on Cooter et al., 2012)
FEST-C integrates EPIC with CMAQ
Rasool et al., 2016 [GMD]
WRF meteorology
SMOKE
Other
Emissions

## Slide 8: Impact of Potter vs EPIC Fertilizer Data on Soil NO
Fertilizer
Application (kgN/ha)
Potter
EPIC
Difference in
Soil NO (g/s)
EPIC - Potter
*Averaged over July 2011

## Slide 9: Impact of Soil NO scheme on Ozone
Daily Average 8-hourly max. Ozone (Updated Parametrization – Base CMAQ v5.1)

## Slide 10: Impact of Soil NO scheme on PM
Daily Average PM2.5 (Updated Parametrization – Base CMAQ v5.1)

## Slide 11: Parameterized  Mechanistic approach
Parameterization quantifies only soil NO
  Not integrated with NH3 scheme
  Neglects other N species (HONO, N2O)
Need mechanistic approach to represent Soil N biogeochemistry
  Nitrification and denitrification processes
Challenge: Scarcity of observational data

## Slide 12: Soil-Atmosphere reactive N exchange
NH3
NH3
NH4+
NO N2O
N2
NO N2O HONO
NO3-
N2
N2O
NO
HNO3
HNO3
NO2-
NO2-
Atmosphere
Soil
HNO2
H+
NO2
NO2
H+
Fertilizer, Deposition
Adapted from Su et al., 2011; Pilegaard, 2013 and Medinets et al., 2015
N (-3)
N (+5)
Nitrification
Denitrification
Org N
NO
N2O

## Slide 13: Mechanistic approach including other N species*
Nitrification Rate
Soil NH4+
Water-filled pore space (WFPS)
Soil temperature
Soil texture
*Parton et al., 2001, Del Grosso et al., 2000, Oswald et al., 2013, Su et al., 2011
Denitrification Rate
Soil NO3−
WFPS
Labile Carbon
Soil texture
Optimum HONO
HONO
NH4+ / NO2-
(HONO + NO )/ N2O
vs
WFPS
N2O
NO

## Slide 14: Conclusions and Next Steps
Enhanced parameterization of soil NO in CMAQ
  Significant impact on PM and Ozone compared to base CMAQ
  Not consistent with bi-directional NH3 scheme
Developing mechanistic representation of soil biogeochemistry to model multiple N species consistently
Next steps:
  Better represent speciation of deposited N
  Bi-directional flux for other N species as for NH3
Broader goal: Model how soil N emissions and air quality vary with agricultural practices
  Potential to mitigate air pollutant and greenhouse gas emissions via best management practices
  Choices of tillage, fertilizer timing, biochar, etc

## Slide 15: Acknowledgements
NASA AQAST TIGER Soil NOx Project funding
CED, NERL at US EPA for the opportunity as a visiting researcher

## Slide 16: References
Bash, J., Cooter, E., Dennis, R., Walker, J., and Pleim, J. (2013). Evaluation of a regional air-quality model with bidirectional NH 3 exchange coupled to an agroecosystem model, Biogeosciences, 10, 1635-1645.
Cooter, E., Bash, J., Benson, V. and Ran, L. (2012). Linking Agricultural Crop Management and Air Quality Models for Regional to National-Scale Nitrogen Assessments. Biogeosciences Discussions, 9: 6095-6127.
CMAS FEST-C 2015: User’s Guide for the Fertilizer Emission Scenario Tool for CMAQ (FEST-C) Version 1.2, Institute of Environment, The University of North Carolina at Chapel Hill, Chapel Hill, NC, available at: https://www.cmascenter.org/fest-c/documentation/1.2/FESTC1_2_userManual.pdf.
Dinnes, D. L., Karlen, D. L., Jaynes, D. B., Kaspar, T. C., Hatfield, J. L., Colvin, T. S., and Cambardella, C. A. (2002). Nitrogen management strategies to reduce nitrate leaching in tile-drained Midwestern soils, Agronomy journal, 94, 153-171.
Hudman, R. C., Moore, N. E., Mebust, A. K., Martin, R. V., Russell, A. R., Valin, L. C., and Cohen, R. C. (2012). Steps towards a mechanistic model of global soil nitric oxide emissions: implementation and space based-constraints, Atmos. Chem. Phys., 12, 7779-7795, doi:10.5194/acp-12-7779-2012.
Medinets, S., Skiba, U., Rennenberg, H., & Butterbach-Bahl, K. (2015). A review of soil NO transformation: Associated processes and possible physiological significance on organisms. Soil Biology and Biochemistry, 80, 92-117.
Pilegaard, K. (2013). Processes regulating nitric oxide emissions from soils. Philisophical Transactions of the Royal Society: Biological Sciences, (368). Retrieved from http://dx.doi.org/10.1098/rstb.2013.0126.
Pleim, J. E. X. A. (1811). Development of a Land Surface Model. Part II: Data Assimilation. Journal of Applied Meteorology. Dec2003, 42(12).
Potter, P., N. Ramankutty, E.M. Bennett, and S.D. Donner. 2010. Characterizing the Spatial Patterns of Global Fertilizer Application and Manure Production. Earth Interactions 14 (2): 1-22. http://dx.doi.org/10.1175/2009EI288.1.
(S&L) Steinkamp, J., & Lawrence, M. G. (2011). Improvement and evaluation of simulated global biogenic soil NO emissions in an AC-GCM. Atmospheric Chemistry and Physics, 11(12), 6063–6082. doi:10.5194/acp-11-6063-2011
Rasool, Q. Z., Zhang, R., Lash, B., Cohan, D. S., Cooter, E. J., Bash, J. O., and Lamsal, L. N.: Enhanced representation of soil NO emissions in the Community Multiscale Air Quality (CMAQ) model version 5.0.2, Geosci. Model Dev., 9, 3177-3197, doi:10.5194/gmd-9-3177-2016, 2016.
Yienger, J. J., & Levy, H. (1995). Empirical-Model Of Global Soil-Biogenic Nox Emissions. Journal of Geophysical Research-Atmospheres, 100(D6), 11447-11464. doi: 10.1029/95jd00370.
Vinken, G. C. M., Boersma, K. F., Maasakkers, J. D., Adon, M., & Martin, R. V. (2014). Worldwide biogenic soil NOx emissions inferred from OMI NO2 observations. Atmospheric Chemistry and Physics, 14(18), 10363–10381. doi:10.5194/acp-14-10363.

## Slide 17: Extra Slides

## Slide 18: Inline BDSNP: Three WRF-BEIS-CMAQ simulation cases
YL - EPA standard configuration with YL95 soil NO scheme
BDSNP (Potter with old Biome) – BDSNP soil NO scheme with GEOS-Chem soil biome classification and Potter at al. (2010) fertilizer data
BDSNP (EPIC with new Biome) – BDSNP soil NO scheme with NCLD40 Global soil biome and EPIC fertilizer data

## Slide 19: Updated Parametrized approach
Source: Rasool et al., 2016 [GMD]

## Slide 20: Mechanistic approach including other N species
Parton et al., 2001, Del Grosso et al., 2000:
NOx to N2O Nitrification ratio:
HONO -> fraction of Nitrification NO+HONO
  (Oswald et al., 2013)
Nitrification N2O flux (Parton et al, 2001 , DayCENT) = K2 * FNO3 (gNm-2d-1)
  K2 = 0.02 (2%) (parton et al., 2001)  fraction of nitrified N lost as N2O flux

## Slide 21: Mechanistic approach (2)
Denitrification N2 to N2O ratio:
) * f (WFPS)
K= soil texture dependent parameter (Del Grosso et al., 2000)
[k controls the max. value of )]
Soil heterotrophic respiration (HR) is a proxy for labile C (electron donor) in denitrification

## Slide 23: Impact of Soil NO scheme on PM
Daily Average PM2.5 (Updated Parametrization – Base CMAQ v5.1)

## Slide 24
Total daily soil N (= NH4+-N + NO3--N + Organic N ) for BDSNP
[Weighted sum as per grid –wise crop usage fraction]
Crop usage fraction per grid cell consistent with NLCD40 LU/LC)
Grid-wise daily soil N
(Fertilizer + Deposition N)
(classified as separate NH4+-N , NO3--N , Organic N pools)
+
WRF
Bi-directional CMAQ modeling system + BDSNP
BELD4: Grid Crop Data
(NLCD 40 MODIS 24 types)
Non-Fertilizer NEI (CONUS)
EPIC agricultural model#
(25 year spin-up for biogeochemical processes)
(reanalysis)
(Inherent EPIC datasets)
Fertilizer N
N Deposition
FEST-C*
*modified for CONUS run (based on Bash et al., 2013)
#modified for CONUS run (based on Cooter et al., 2012)
Soil data
Spatial data for CONUS (12 km grid with crop data)
Meteorology
EPIC-BDSNP-CMAQ interphase
Source: Rasool et al., 2016 [GMD]

## Slide 25: Monthly Mean (July 2011) Soil NO
YL
BDSNP (Potter with Old Biome)
BDSNP (EPIC with New Biome)

## Slide 26: Model validation
PM2.5 (Daily) Observed data from IMPROVE sites1
Ozone Observed data from EPA’s AIRS AQS (Air Quality System) network2
Aggregated performance metrics for sites showing higher sensitivities between 3 cases (including sites exceeding EPA standard in case of Daily max. 8-hr ozone)
1http://www3.epa.gov/airquality/airdata/
2http://views.cira.colostate.edu/fed/Datasets/Default.aspx

## Slide 27: Model performance
For MDA8 Ozone:
  F ratio > Fcritical and P-value << 0.05 from ANOVA analysis
  difference between 3 schemes are statistically significant.
For PM2.5 (daily mean):
  F-ratio < Fcritical and p-value > 0.05 in comparisons among the 3 cases
  differences are not that statistically significant.
MDA8O3 modeled vs observed (CASTNET), July 2011

## Slide 28: Variability in soil conditions effects modeled N emissions
-Bias in modeled precipitation not too indicative -Need to include other N species in models
Modeled estimates for Dry forest sites
& Wet agricultural/ prairie sites perform differently
Soil moisture (vol.) for July 2011 (mean)
Precip. Bias (%) for July 2011 (mean)

## Slide 29: Monthly mean(July 2011) Daily Max. 8 hr. O3
YL
BDSNP (Potter with Old Biome)
BDSNP (EPIC with New Biome)

## Slide 30: Monthly mean(July 2011) Daily Avg. PM 2.5
YL
BDSNP (Potter with Old Biome)
BDSNP (EPIC with New Biome)

## Slide 31: PM2.5 (daily mean) modeled vs observed July 2011

## Slide 32: MDA8O3 modeled vs observed July 2011

## Slide 33: Model performance (3 cases inline with CMAQ, July 2011 scenario)

## Slide 34: Fractional Land use in BDSNP
Minor enhancement in BDSNP soil biome to improve sub-grid calculation

## Slide 35: Biochar as N emission amendment
47-67 %reductions in NO emissions (Nelissen et al, 2014) when biochar is applied to agricultural soils

## Slide 36
Chart: CASTNET agricultural/praire site's MDA8 O3 field observation (ppbv)
Chart: CASTNET forest/National Park site's MDA8 O3 field observation (ppbv)