## Slide 1: Future changes in land use-related emissions and their impacts on air/water quality and reactive nitrogen deposition
Yilin Chen, Huizhong Shen, Armistead G. Russell, Talat Odman, Jhih-Shyang Shih, Juha Siikamäki, Dallas Burtraw, Charles Driscoll, Richard Smith, Shuai Shao
Speaker: M. Talat Odman
Community Modeling and Analysis System Conference
Chapel Hill, NC

## Slide 2: Land Use Change and Air Quality
Why land use change matters to air and water quality:
  Emissions/discharge linkages
    Increasing component as industrial and mobile sources are reduced
  Heating/cooling (e.g., urban heat island)
  Directly affected by future global change
Impacts on PM, Ozone, NOx, reactive nitrogen deposition …
  Health
  Welfare
    Often overlooked
  Acidic deposition (N&S)
  Terrestrial nitrogen
  enrichment (NR)

## Slide 3: Study Objectives
Identify the future changes in emissions from land use-related source changes and the impacts of global change with a focus on reactive nitrogen (NR);
  Cropland NH3 emissions
  Forest nitrogen (e.g., fires)
  Biogenic emissions
Develop an integrated modeling framework to investigate the potential impacts of land-use and climate-related changes on air pollution, atmospheric deposition and associated impacts on water quality and sensitive ecosystems;
  Identified as a need in last NOX-SOX secondary NAAQS review
Identify effective mitigation strategies with benefits in multiple environmental media.

## Slide 4
CMAQ with FEST-C and BEIS
  FEST-C: Fertilizer Emission Scenario Tool for CMAQ, estimates cropland NH3 emissions;
  BEIS: Biogenic Emission Inventory System, estimates biogenic emissions;
  CMAQ: air quality modelling, provide deposition fields for SPARROW and PnET-BGC inputs.
SPARROW: USGS SPAtially Referenced Regressions On Watershed attributes
  Water quality assessment
  Nationwide application, watershed level scale
  PnET-BGC: an integrated biogeochemical model to simulate forest and aquatic ecosystems
  Two hotspots: Adirondacks and Great Smokey Mountain
  Stream chemical composition
Models applied

## Slide 5
Climate projections
  Two sets of meteorological fields under both Representative Concentration Pathway 4.5 (RCP4.5, a scenario with moderate temperature increase) and RCP8.5 (a scenario with intensive temperature increase) scenarios
    MCIP: 36km spatial resolution, based on output from the Community Earth System Model (CESM1) downscaled using WRF spectral nudging
    MACA (Multivariate Adaptive Constructed Analogs) dataset: major components at a high spatial resolution (6 km) and monthly temporal resolution
      Multi-model projections (17 climate models)
      Components: temperature (T, Tmax, and Tmin), wind speed, precipitation, humidity, evaporation
Data Preparation
2028-2032
2048-2052
2098-2099
2008-2012
MACA: 2006-2100, monthly
2100
2010
2080
2030
2040
2050
2060
2070
2090
2020
2006
MCIP: four periods
CMAQ
SPARROW PnET-BGC
RCP4.5
RCP8.5

## Slide 6: Modeling Framework: Future projection
Note:
CCSM: Community Climate System Model
SSP: Shared Socioeconomic Pathway

## Slide 7
Primary results shown
  Climate change impacts on NH3 emissions from soil and plants (ESPNH3), mainly over cropland, and implications for crop production and nitrogen deposition.
Project in progress: Preliminary Results

## Slide 8
Model Configurations and Evaluation
  CMAQv5.0.2 with FEST-C v1.1
  Considering recent updates, will rerun using CMAQv5.3 and FEST-C v1.4.
  Both CMAQ with and without NH3 BIDI exchange were applied, model with the module reduces model bias for the compounds directly related with NH3.
NMB | Base | BiDi | Observed | CMAQ-BIDI | units
NO2 CONC | -3% | -2% | 9.1 | 8.9 | ppbV
NH3 CONC | -52% | -30% | 2.0 | 1.4 | ppbV
HNO3 DRY DEP | 66% | 65% | 3.4 | 5.6 | kg/ha/yr
NH4 DRY DEP | -14% | -5% | 0.25 | 0.24 | kg/ha/yr
NO3 DRY DEP | 499% | 518% | 0.24 | 1.51 | kg/ha/yr
NH4 WET DEP | -47% | -32% | 2.7 | 1.8 | kg/ha/yr
NO3 WET DEP | -36% | -36% | 6.9 | 4.4 | kg/ha/yr
Total NO3 DEP | 10% | 9% | 10 | 11 | kg/ha/yr
Total NH4 DEP | -41% | -25% | 2.8 | 2.1 | kg/ha/yr
Model Evaluation and Version Comparison

## Slide 9
NH3 emission intensity in cropland and other land cover types
  higher emission intensities over croplands
  higher emission-to-temperature sensitivities over other land cover types
NH3 emission from soil and plants (ESPNH3)
NH3 emissions from soil and plants (ESPNH3) over different land use types
Notes: Cropland shows much higher emission intensities than non-agricultural land (such as forest, grass, urban, etc.) except wetland, which is higher than wheat field. The highest emission intensities are found for rice (1870 kgkm-2year-1) and cotton fields (1200 kgkm-2year-1) due to large N fertilizer demand for growth of these two types of crops (Gerik, Oosterhuis et al. 1998, Chauhan, Jabran et al. 2017); The lowest is found over forest (17 kgkm-2year-1) likely due to mechanisms preventing N loss—substantial plant uptake of nitrogen and leaf absorption of NH3 as well as low volatilization due to low skin temperature (Finzi, Norby et al. 2007, González-Pedraza and Dezzeo 2014). Overall, cropland contributes to about 80% of the total ESPNH3 at the national scale.
We calculate the ratios of the FEST-CMAQ-BIDI-based ESPNH3 to the regression model-based ESPNH3 and find that the ratios are log-normally distributed with a spatial gradient increasing from the north to the south (Figure SX8). After log-transformation, the ratios are positively correlated with 2-metre temperature (T) (r = 0.76, p ~ 0, Figure SX8), which largely explains the latitudinal gradient—higher ratios in the south due to warmer climates. In addition, the ratios show a positive correlation with near-surface wind speed (W, 10-m wind speed) (r = 0.05, p ~ 0, Figure XX) and a negative correlation with total precipitation (P) (r = -0.21, p ~ 0, Figure XX) mainly because higher wind speeds facilitate volatilization, and higher precipitation enhances NH3 penetration into deeper soil layers preventing volatilization (Riddick 2012). This warrants including meteorological variables in the regression model. We employ an exponential term (Equation X) as the climate-adjustment factor to account for T, W, and P (Methods) (Sutton, Reis et al. 2013, Riddick, Blackall et al. 2017). The enhanced model (MC, refers to the LC-based model with the climate-adjusted factor) explains 84% of the variance and enables us to reproduce the future ESPNH3 changes as projected by FEST-CMAQ-BIDI on a 36km×36km grid level (Figure SX9). By decomposing the effects of LC and the three climate components (T, W, and P), we find the projected increase in T being the dominant driving factor leading to the ESPNH3 increase. Under the RCP4.5 scenario, increased T in 2050 leads to a net increase of 11% in ESPNH3, while the projected increases in W and P have opposite and relatively minor impacts (+2.0% and -1.5%, respectively). Cropland has an ESPNH3-T sensitivity (SE,T) of 10.3% K-1 which is lower than other land types such as grassland and forest (?? and ??, respectively) (Table SI). The difference between cropland and non-agricultural lands suggests that agricultural management likely reduces the ESPNH3 sensitivity to warming. Overall, the absolute increase in emissions is from croplands (75%) due to the much higher emission intensity.

## Slide 10
Observed evidence
  NH3 concentration peaked in 2012 in the Midwest United States
    likely due to abnormal climate conditions (highest temperature in the last 123 year and dryer-than-normal conditions)
    Attributed to multiple factors (emissions, gas-particle partitioning, deposition)
The year-to-2012 ratios of annual mean NH3 concentrations in the Midwest reported by Ammonia Monitoring Network
Climate change impacts on NH3 emissions from soil and plants (ESPNH3)

## Slide 11
Used FEST-C-CMAQ to investigate how climate impacts NH3 emissions and atmospheric levels and to see how well the model captures the observations
  By comparing the model (FEST-C-CMAQ-BIDI) results in 2011 and 2012
    sensitivities of NH3 concentration to temperature (+0.18 ppbK-1 in the Midwest; +0.33 ppbK-1 at the site locations) in line with observations (+0.15 ppbK-1 and +0.34 ppbK-1, respectively)
  By replacing ESPNH3 in 2012 with that in 2011
    cropland NH3 emissions contributed 40% of the concentration increase.
Modelled increases in NH3 concentrations between 2011 and 2012
a. All factors (emissions, gas-particle partitioning, removal processes)
b. Only emissions
Climate change impacts on NH3 emissions from soil and plants (ESPNH3)

## Slide 12
Optimizing agricultural management can reduce emission-to-temperature sensitivity in cropland in warmer conditions
  ESPNH3~T function for natural landscapes, often adopted for cropland:
Relationship obtained from natural circumstances
Relationship over cropland considering impacts of agricultural management
ESPNH3~ change in annual mean T
Sensitivity ~ change in annual mean T
Climate change impacts on NH3 emissions from soil and plants (ESPNH3)
Notes: In most studies as well as in MC, it is assumed that the long-term T-dependency of ESPNH3 over cropland follows a similar function as that of natural circumstances (Eq (X), Methods) (Sutton, Reis et al. 2013, Riddick, Blackall et al. 2017). SE,T which is the derivative of the ESPNH3~T function is inversely proportional to T2 (SE,T = α / T2), indicating that ESPNH3 will become less sensitive to T at higher T levels (Figure X1). MC gives an α value of 8690 K for unirrigated crop, equivalent to a SE,T of 10% K-1 at 18 ℃ and a slightly lower SE,T (9.8% K-1) at 25 ℃. The cropland SE,T directly calculated from FEST-CMAQ-BIDI via a year-by-year comparison (Method) shows a very similar SE,T (10.2% K-1) at 18 ℃ but a much lower SE,T (4.7% K-1) at 25 ℃ (Figure X1). The difference between FEST-CMAQ-BIDI-based and MC-calculated SE,T suggests that MC may be overly sensitive to T changes at higher T levels (Figure X1). For non-agricultural land, on the other hand, the SE,T obtained from MC and FEST-CMAQ-BIDI match each other at a wide T spectrum (for MC, 9.9%—14.8% and 9.5%—14.1% for different LC types at 18 ℃ and 25 ℃, respectively; for FEST-CMAQ-BIDI, 12.0% and 11.4%, respectively). The functional difference at higher T levels between cropland and non-agricultural lands implies heterogeneous responses of ESPNH3 to warming and that the true response for cropland could be oversimplified if directly employing the semi-empirical relation. Investigation into the various aspects of the projected agricultural management under RCP8.5 finds a decrease of 5.5% in annual crop yield (expressed as N yield) in 2100 compared with 2010 (Figure X), whereby the uptake of the applied N fertilizer is reduced by 11.9%. An important consequence of such a decrease in applied N fertilizer uptake (specifically NH3 fertilizer) is a lower soil NH4+ content which ultimately lessens the ESPNH3 increase. This provides an important pathway, which is often omitted, of how management, interacting with climate, will factor into ESPNH3 under extremely warm conditions―proper management practices in response to climate change can prevent cropland N loss. To confirm the management impact, we reconduct the RCP8.5 2100 simulation but, this time, fix the applied N to the 2010 level. The simulation without the management impact shows the ESPNH3 increase being 17.1% higher than the standard simulation, in line with the MC response, and proves the potential of management (more specifically N application in response to climate change) in lessening ESPNH3 increase in warm conditions.

## Slide 13
Multi-model projections
  Regression models considering land cover types and climate variables (T, wind speed, and precipitation) established based on the integrated model outputs.
  Multi-model projections using the outputs of 17 climate models
Climate change impacts on NH3 emissions from soil and plants (ESPNH3)
Notes: Based on the MC adjusted by the management-induced lessening impact (MC-adj, Method) and climate projections of 18 climate models (Table SX) (Abatzoglou and Brown 2012, Taylor, Stouffer et al. 2012), we evaluate the future trends of multi-projection ESPNH3 and isolate the impacts of T, which is expected to provide a broader view of how projected warming will affect ESPNH3 (Fig. X2). All ESPNH3 projections show increasing trends at the national scale (Fig. X2), with the increased rates by the end of the twenty-first century ranging from +4.3% (based on GFDL-ESM2G) to +58.0% (HadGEM2-CC365) in RCP4.5 and from +36.4% (GFDL-ESM2G) to +120% (HadGEM2-CC365) in RCP8.5 (Fig. X2 and Fig. SXX). Excluding the impacts of T lead to increased rates being close to nil and significantly narrows the variation across projections which largely fall within ±5% (Fig. SXX), indicating the dominant impact of T.

## Slide 14
Spatial distributions of ESPNH3 changes reflected by the multi-model means
  Overall increase in ESPNH3 between 2010 and 2100:
    30% (26-33% as 95% confidential interval) in RCP4.5;
    99% (90%-108%) in RCP8.5.
Spatial changes in ESPNH3 by the end of the twenty-first century due to climate change only.
Climate change impacts on NH3 emissions from soil and plants (ESPNH3)
Notes: 16 out of 18 projections show increases of ≥ 50% in at least two thirds of the CONUS land area under RCP8.5 (Fig. X2), but the changes are not spatially consistent because of the disparity in climate projections (Table SX). Means of the multi-projection ensemble derived at the grid level give a tighter spatial estimate, which suggests that, in relative terms, regions with larger fractions of non-agricultural land (e.g. the Mountain States and Appalachia regions) have a tendency towards a higher increase (Fig. X3c,d) due to a higher T sensitivity for natural land, while in absolute terms, the increase is dominated by cropland (e.g. in the Northern and Southern Plains) (Fig. X3a,b). The multi-projection means show higher ESPNH3 increases than the estimate driven by a single climate projection of CESM. The ESPNH3 under RCP4.5 is estimated to increase by 310±80 Gg/year (as the mean and semi-interquartile range, respectively) by the end of the twenty-first century, while the increase is up to 980±200 Gg/year under RCP8.5, which is 54% higher than the single-projection estimate. Our assessments of the management impact finds that agricultural management practices should further increase the ESPNH3 by 16 and 110 Gg in 2100 under RCP4.5 and RCP8.5, respectively. That leads to overall increases of 30% (26%–33% as the 95% confidential interval of the multi-projections meanfor RCP 4.5) and 99% (90%–108%, RCP 8.5) in ESPNH3 compared to current levels. In 2010, cropland ESPNH3 has an 8% loss of synthetic N fertilizer, which increases to 14% in 2100 (RCP8.5) with current agricultural practices and no further mitigation measures.

## Slide 15
Implications
  Loss of synthetic N fertilizer: from 8% in 2010 to 14% in 2100 (RCP8.5);
  Crop yield loss: 460 Gg N/year;
  Atmospheric burden of NH3/NH4+: increases by 20%
  N deposition over sensitive regions: increases by 10%
Mitigation measures
  Replacement of urea with non-urea fertilizers (RU): 500 Gg/year reduction in ESPNH3;
  Urea application with irrigation (UIR): -180 Gg/year
  Application of urea inhibitor (UIN): -280 Gg/year
  Deep placement of fertilizers (DP): -700 Gg/year
The most effective strategy combining RU and DP measures with best management practices is estimated to reduce the ESPNH3 by ~50% (1020 Gg/year), fully compensating for the negative impacts of warming-induced ESPNH3 increase on the atmosphere and ecosystems
Climate change impacts on NH3 emissions from soil and plants (ESPNH3)

## Slide 16
Summary
  Multiple causes of potential NH3 (and NR) changes
    Land use
    Climate
      CMAQ-FEST-C appears to capture NH3 sensitivity to meteorology, Modeled vs Observed:
        Midwest: +0.18 ppbK-1 vs +0.15 ppbK-1
        Site locations: +0.34 ppbK-1 vs +0.33 ppbK-1
  Cropland NH3 emissions expected to significantly increase in response to
    Climate warming,
    Land use change
  Changes impact
    N cycle
    Sensitive ecosystems
    Threaten food security

## Slide 17
Acknowledgement
  EPA grant number R835880
  Contacts:
    Armistead G. Russell: ted.russell@gatech.edu
    Yilin Chen: ychen870@gatech.edu
    Huizhong Shen: hshen73@gatech.edu
  R835880
This presentation was made possible in part by USEPA. Its contents are solely the responsibility of the grantee and do not necessarily represent the official views of the funding sources and those sources do not endorse the purchase of any commercial products or services mentioned in the publication.