## Slide 1
Impact of Severe Drought on Air Quality in California
Huazhen Liu
PhD Student
Gillings School of Global Public Health
Department of Environmental Sciences and Engineering
Jared H. Bowden, Timothy Glotfelty, Jordan Kern, J. Jason West

## Slide 2
Impacts of Drought
Interactions and feedbacks among climate, meteorology, hydrology, emissions, pollution, technology, and ecosystems
Higher temperature & lower humidity
Reduced precipitation
(wet deposition)
Meteorology
Increased stagnation
Reduced runoff and hydropower
Hydrology
Increased electricity demand
Society
Increased fossil electricity generation
Anthropogenic emissions
Increased wildfire
Ecosystems
Reduced stomatal uptakes
Biology
Deteriorated air pollution

## Slide 3
Drought and Air Quality
Most studies identified drought affecting air quality via natural processes, seldom focusing on the change in anthropogenic emissions during drought periods.
Statistical analysis on observations was widely used by these studies. Some of them also employed global models, such as GEOS-Chem. However, regional models like WRF-Chem were rarely used in this research field.
A review of previous studies on relationships between drought and air quality
[Wang et al., 2015; Wang et al., 2017; Achakulwisut et al., 2018; Demetillo et al., 2019; Hu et al., 2019; Lin et al., 2020; Lei et al., 2022]

## Slide 4
Objectives
1
2
Analyze relationships between drought and air pollution in California using observations.
Quantify the contributions of different processes leading to these relationships using WRF-Chem model.
Motivation
Advance our holistic understanding of the dynamic connections and feedbacks among climate change, meteorology, drought, power plant emissions, and air pollution.

## Slide 5
Drought Conditions in California
[Source: https://droughtmonitor.unl.edu/DmData/TimeSeries.aspx]
U.S. Drought Monitor: a combination of Palmer Drought Severity Index, CPC Soil Moisture Model, USGS Weekly Streamflow, Standardized Precipitation Index, and Objective Drought Indicator Blends.

## Slide 6
Climate Divisions in California
California Climate Divisions
PDSI: Palmer Drought Severity Index
Category | Extreme Drought | Severe Drought | Moderate Drought | Mid-Range | Moderately Moist | Very Moist | Extremely Moist
PDSI Value | -4.00 and lower | -3.00 – -3.99 | -2.00 – -2.99 | -1.99 – 1.99 | 2.00 – 2.99 | 3.00 – 3.99 | 4.00 or greater

## Slide 7
Air Quality in California
Distribution of air pollutants monitoring stations

## Slide 8
Air Quality During Drought Periods
Climate division | Start date | End date | Duration (months) | Mean PDSI | Mean PM2.5 (μg/m3) | Mean ozone (ppb)
C1 | 03/2015 | 11/2015 | 9 | -3.544 | 7.076 | 35.185
 | 03/2021 | 12/2021 | 10 | -4.154 | 12.293 | 33.596
 | Non-drought periods |  |  | 0.027 | 7.963 | 32.112
Climate division | Start date | End date | Duration (months) | Mean PDSI | Mean PM2.5 (μg/m3) | Mean ozone (ppb)
C2 | 03/2015 | 11/2015 | 9 | -3.524 | 7.748 | 46.327
 | 12/2020 | 09/2021 | 10 | -4.481 | 12.164 | 43.531
 | Non-drought periods |  |  | 0.332 | 8.869 | 41.717
Climate division | Start date | End date | Duration (months) | Mean PDSI | Mean PM2.5 (μg/m3) | Mean ozone (ppb)
C3 | 11/2013 | 04/2015 | 18 | -4.137 | 4.693 | -
 | 09/2020 | 09/2021 | 13 | -4.155 | 15.405 | 49.544
 | Non-drought periods |  |  | 0.711 | 4.552 | -

## Slide 9
Climate division | Start date | End date | Duration (months) | Mean PDSI | Mean PM2.5 (μg/m3) | Mean ozone (ppb)
C4 | 04/2013 | 12/2015 | 33 | -5.222 | 7.922 | 35.988
 | 04/2021 | 09/2021 | 6 | -4.492 | 7.746 | 37.865
 | Non-drought periods |  |  | 0.167 | 8.347 | 35.406
Climate division | Start date | End date | Duration (months) | Mean PDSI | Mean PM2.5 (μg/m3) | Mean ozone (ppb)
C5 | 03/2013 | 03/2016 | 37 | -5.657 | 12.641 | 47.862
 | 11/2020 | 11/2021 | 13 | -4.908 | 13.665 | 44.368
 | Non-drought periods |  |  | 0.674 | 11.583 | 46.272
Air Quality During Drought Periods

## Slide 10
Climate division | Start date | End date | Duration (months) | Mean PDSI | Mean PM2.5 (μg/m3) | Mean ozone (ppb)
C6 | 06/2012 | 12/2016 | 55 | -5.815 | 11.308 | 44.004
 | 11/2017 | 12/2018 | 14 | -5.069 | 11.552 | 43.480
 | 02/2021 | 12/2021 | 11 | -4.725 | 10.756 | 45.530
 | Non-drought periods |  |  | 0.715 | 11.051 | 44.048
Climate division | Start date | End date | Duration (months) | Mean PDSI | Mean PM2.5 (μg/m3) | Mean ozone (ppb)
C7 | 01/2014 | 11/2014 | 11 | -3.974 | 10.478 | 53.307
 | 05/2016 | 11/2016 | 7 | -3.437 | 8.997 | 52.881
 | 04/2018 | 09/2018 | 6 | -3.717 | 10.546 | 58.459
 | 11/2020 | 12/2021 | 14 | -3.931 | 9.277 | 46.157
 | Non-drought periods |  |  | 0.167 | 7.725 | 47.658
Air Quality During Drought Periods

## Slide 11
WRF-Chem Simulation
Separate the contributions of meteorological and biological processes and increased anthropogenic emissions.
Increased fossil electricity generation
Increased electricity demand
Reduced hydropower

## Slide 12
Study Periods
Drought Regimes | Periods
Drought | April 2021 – November 2021
 | December 2013 – March 2014
Wet | January 2005 – December 2005
Neutral | October 2019 – January 2020
 | February 2010 – September 2010
Composite Year Periods Representing the Full Annual Cycle of Different Climate Regimes in California
Meteorology
Anthropogenic emissions
Biogenic emissions
Simulation 1
Simulation 2
Simulation 3
Simulation 4
Simulation 5
Simulation 6
Simulation 7
Drought
Non-Drought
WRF-Chem Simulation Experiments

## Slide 13
Simulation Area
Spatial resolution: 12km-4km
Meteorological data: ERA5

## Slide 14
WRF Model Evaluation
Comparison between WRF simulations with observations MADIS during the “Extreme Drought of 2021”
Temperature at 2m
20210401-20211130
Mixing ratio of water vapor
20210401-20211130
Too warm
Too dry
KE16 (20210601-20210630)
2m Mixing Ratio (g/kg)
2m Temperature (K)
2m Relative Humidity (%)
Surface Pressure(mb)
Observations
WRF simulations
Observation-Model Time Series

## Slide 15
Future work
Improve WRF performance.
Separate the contributions of different processes using WRF-Chem model.
Results
There are some differences between the air quality of drought and non-drought periods in California, but a more robust analysis is required to understand and isolate those differences.
When simulating meteorology during drought periods in California, WRF model overestimated temperature while underestimated humidity by failing to cool down and catch high humidity.
1
2
3
Test and evaluate WRF-Chem simulations.
4
Further analyze observations to infer changes in air quality during droughts, and relationships with meteorological, hydrological, electric power, and emissions data

## Slide 16
Acknowledgements
Advisor
Jason West
Collaborators
Jared Bowden (NCSU)
Timothy Glotfelty (NCSU)
Jordan Kern (NCSU)
Funding Source
NSF

## Slide 17
Thanks for your attention!
Questions?