## Slide 1: Spatiotemporal Trends in PM2.5 Chemical Composition in the Continental U.S. during 2006-2021
Bin Cheng1, Saravanan Arunachalam1 and Kiran Alapaty2
1Institute for the Environment, The University of North Carolina at Chapel Hill, NC, USA
2U.S. Environmental Protection Agency, Research Triangle Park, NC, USA
Presented at
The 21st Annual CMAS Conference, Chapel Hill, NC
October 17-19, 2022
Disclaimer: The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA.

## Slide 2: Introduction: PM2.5 chemical compositions in the U.S.
Fine particulate matter (PM2.5):
One of the six criteria pollutants
Adverse health and environmental impacts
National monitoring network since late 1990’s
  Air Quality System (AQS)
  Chemical Speciation Network (CSN)
  Interagency Monitoring of Protected Visual Environments (IMPROVE)
Major chemical compositions of PM2.5
Sulfate (SO42-), ammonium (NH4+), nitrate (NO3-), organic carbon (OC), elemental carbon (EC), and a spectrum of elements and ions (Bell et al., 2007)
Attributed to a variety of emissions sources and atmospheric processes
Toxicity of PM2.5 chemical components
The PM2.5 components may not have the same toxicity (Levy et al., 2012; Krall et al., 2013)
EC and organic compounds associated with higher risks of emergency hospitalization
Visibility degradation of PM2.5
PM2.5 related ammonium sulfate [(NH4)2SO4] and organic compounds are the main contributors to the light extinction in the SE U.S.
Other components (EC, NH4NO3, crustal materials) also responsible for visibility impairment

## Slide 3: Introduction: PM2.5 chemical compositions in the U.S.
Spatial and temporal variations of PM2.5 chemical compositions
PM2.5 conc. have been significantly reduced in the U.S. (Cheng et al., 2019)
Stringent state and local control measures lead to emission reduction
Dynamic changes of PM2.5
Fate and transport of various primary and secondary pollutants
Spatial heterogeneity of various emission sources & local meteorological conditions
Emissions control strategies implemented along the time
Comprehensive explanation of adverse impacts of PM2.5
Detailed analysis of spatiotemporal trends of PM2.5 chemical compositions
Aid in tracking progress of regulatory actions
Understanding the relationship between changes in emissions & ambient conc.
Research objectives
Investigate the dynamic contributions of various chemical compositions to the PM2.5 mass conc. in spatial and temporal scales in the continental U.S.
Provide basic information of atmospheric chemical condition
Implicate the potential development of PM2.5 control strategies

## Slide 4: Methodology
PM2.5 and chemical composition monitoring network
PM2.5 mass conc. and chemical speciation data were downloaded from U.S. EPA Air Quality System database (USEPA, 2021)
Regions within the contiguous United States
Nine climatically consistent regions were identified within the continental U.S.: Northeast, Upper Midwest, Ohio Valley, Southeast, Northern Rockies and Plains, South, Southwest, Northwest, and West
Atmospheric chemical condition analysis
The ammonium availability index, J = (Chu et al., 2004)
  J < 1, NH4+ deficit; J = 1, neutralization; J > 1, NH4+ surplus
Data adjustment
Organic matter (OM) = 1.4 × (OCM – OCFB)
  OCM = measured organic carbon; OCFB = field blank organic carbon
Statistical analysis
Tukey’s honest significant difference (HSD) test
Theil Sen regression
Kendall’s tau statistics

## Slide 5: Annual average PM2.5 concentrations
ΔPM2.5 (2006 minus 2020)
Higher in CA, Eastern U.S.
Spikes in CA, reduction in Eastern U.S.
Greater reductions in areas with higher PM2.5 conc. in 2006; increase in CA
2020 CA wildfires

## Slide 6: Temporal trend of PM2.5 and PM2.5 chemical compositions concentrations
1. PM2.5 significant reduction, 11.38 ± 2.94 µg m-3 (2006) to 8.20 ± 2.76 µg m-3 (2020)
2. The reductions in inorganic PM2.5 (i.e., NH4+, NO3-, and SO42-) are the major contributors
3. PM2.5 peak in summer before 2008 and peak in winter after 2008
4. NO3- and EC tended to peak in winter, while SO42- tended to peak in summer
5. Less seasonal variation of SO42- in recent years
PM2.5
NH4+
NO3-
SO42-
EC
OM
↑ winter, ↓ summer
↑ winter, ↓ summer
↑ summer, ↓winter

## Slide 7: Emission trend of NH3, NOx, SO2, primary PM2.5, and VOC
Significant & spatially consistent reductions in the emissions of NOx & SO2
National SO2 emissions decreased by 85.6% & national NOx emissions decreased by 59.6% (2006-2021)
The Tier 2 & 3 emission standards
The Clean Air Interstate Rule (CAIR) implemented in 2005
Financial crisis during around 2008-2009
The Cross-State Air Pollution Rule (CSAPR) replaced CAIR in 2015
Improved vehicle technology
Transition of gasoline/diesel vehicles to electric vehicles
NOx
SO2
NH3
Pri-PM2.5
VOC

## Slide 8: Spatiotemporal trend of SO42-
1. SO42- conc. were higher in Ohio River Valley region, Great Lake Basin, and southeastern U.S. in 2006
2. Significant reduction of SO42- during 2006-2020 and greater reductions occurred in eastern U.S. (3.5-4.0 µg m-3)
3. Less spatial heterogeneity in 2020
Higher in Eastern U.S.
ΔSO42- (2006 minus 2020)
Reduction across U.S.

## Slide 9: Spatiotemporal trend of NO3-
1. NO3- conc. were higher in California & Great Lake Basin in 2006
2. NO3- conc. were significantly reduced during 2006-2020
3. Larger reduction in area with higher NO3- in 2006, the highest reduction was 1-3.9 µg m-3
3. Less spatial heterogeneity in 2020
Higher in CA & Great Lake Basin
ΔNO3- (2006 minus 2020)
Reduction across U.S.

## Slide 10: Spatiotemporal trend of OM
1. Increase in CA, 4.72 µg m-3
2. Decrease in SEUS, 5.9 µg m-3
ΔOM (2006 minus 2020)
Higher in CA & SE U.S
Increase or decrease in certain areas
2020 CA wildfires
↑
↓

## Slide 11: Monthly PM2.5 mass closure profile
1. The declining trend of PM2.5 in four periods (Tukey test) mainly attributed to the reductions in 3 inorganic components, SO42-, NO3-, and NH4+
2. The carbonaceous fraction (OM + EC) amounted to ~ 38–50% of PM2.5 during 2016-2020, the major contributors to PM2.5
3. Since SO42-, NO3-, and NH4+ have almost levelled off in recent years, further air quality improvements may require targeting carbonaceous species
4. Before 2008, PM2.5 tended to peak in summer, while after 2008, PM2.5 tended to peak in winter; the considerable reduction of SO2 emissions led to the weaker seasonal variation of SO42- in recent years

## Slide 12: Trend in extrema
1. Fewer high PM2.5 conc. occurred during 2006-2020, which indicated that the heavily polluted days (heavy hitters) occurred less in recent years
2. The 98th percentile of PM2.5 conc. in each period are: 34.1 μg m–3 during 2006-2008; 27.7 μg m–3 during 2009-2011; 24.6 μg m–3 during 2012-2015; 23.2 μg m–3 during 2016-2020, which were all below the primary and secondary 24-hr PM2.5 NAAQS (35 μg m-3)
3. Reduction in the occurrence of extrema PM2.5 conc. can be mainly attributed to the reductions of SO42-, NH4+, and NO3- rather than OM and EC
PM2.5
SO42-
NH4+
NO3-
EC
OM

## Slide 13: Ammonium availability index-J
1. J values (0.80 ± 0.10 to 0.48 ± 0.10) exhibited a reduction trend during 2006-2020, acidic particles
2. The reduction trend in J was inconsistent with the temporal changes of ↑NH3, ↓NOx, and ↓SO2 emissions
J =

## Slide 14: Summary
PM2.5 was significantly reduced, 11.38 ± 2.94 µg m-3 (2006) to 8.20 ± 2.76 µg m-3 (2020) mainly attributed to the reductions in inorganic PM2.5 (i.e., NH4+, NO3-, and SO42-)
The largest air quality improvements occurred in areas with the worst baseline air quality (Ohio Valley & SE U.S.)
Spikes in PM2.5 in CA were due to higher EC & OM from 2020 wildfires
Control strategies on SO2 and NOx led to significant emissions reductions
SO42-, NO3-, and NH4+ almost levelled off in recent years, further air quality improvements may require targeting carbonaceous species
The heavily polluted days (heavy hitters) occurred less in recent years
Particles are acidic
This analysis provided insights to target specific precursors to aid in the development of PM2.5 control strategies in the future

## Slide 15: Selected References
This project was funded by New York State Energy Research and Development Authority (NYSERDA)
Great thanks to Dr. Brett Gantt and Liz Naess for helpful discussions
Great thanks to Dr. Wyat for providing the useful information for the EC and OC data correction
Acknowledgments
Bell, ML, Dominici, F, Ebisu, K, Zeger, SL, Samet, JM. Spatial and temporal variation in PM2.5 chemical composition in the United States for health effects studies. Environmental Health Perspectives. 2007;115(7):989-995.
Cheng, B., Wang-Li, L., Meskhidze, N., Classen, J., Bloomfield, P. Spatial and temporal variations of PM2.5 mass closure and inorganic PM2.5 in the Southeastern U.S. Environ. Sci. Pollut. Res. 2019, 26, 33181–33319.
United States Environmental Protection Agency (USEPA). 2021. Air Data: Air Quality Data Collected at Outdoor Monitors Across the US.. https://aqs.epa.gov/aqsweb/airdata/download_files.html
Krall, JR, Anderson GB, Dominici F, Bell ML, Peng RD. 2013. Short-term exposure to particulate matter constituents and mortality in a national study of U.S. urban communities. Environ Health Perspect. 121(10):1148-53.

## Slide 16
Thank you!
Any questions?
Mike Lewelling/National Park Service
Jessica Wentz and Romany Webb

## Slide 17: Extra Results (animation)
PM2.5 mass concentration (2006-2020)
SO42- (2006-2020)
NO3- (2006-2020)
OM (2006-2020)

## Slide 18: Spatiotemporal trend of NH4+ & EC
ΔNH4+ (2006 minus 2020)
ΔEC (2006 minus 2020)
NH4+ (2006 to 2020)
EC (2006 to 2020)

## Slide 19: Topography
CA topography
USA topography
San Joaquin Valley