## Slide 1: Simple urban parameterization for WRF-CMAQ.
Jonathan Pleim and Robert Gilliam
USEPA

## Slide 2: Motivation
Urban/suburban areas are generally warmer and more turbulent than surroundings
Less stable boundary layers at night and during morning and evening transitions mix surface emissions more quickly
Rate of morning PBL growth and entrainment from residual layers are critical for photochemisty in urban areas
Effects of built environments disproportionately important for AQ because of high emissions in these areas

## Slide 3: Problem
Without realistic treatment of urban effects:
  PBL too stable during morning and evening transitions and overnight
  Overprediction of ground emitted primary species (e.g. CO, NOx, Primary PM)
July 2006 – CMAQ 12 km CO
Birmingham (SEARCH)

## Slide 4: Potential Solutions
Meteorological models and parameterizations for urban areas vary greatly in complexity and data requirements.
Currently WRF has several urban parameterizations: Bulk, single-layer, and multi-level BEP-BEM NUDAPT all tied to the NOAH LSM
Need for a simple scheme considers the effects of development at the local (1-4 km) and regional (12 km) grid scales that works with the PX LSM that we use for WRF-CMAQ.

## Slide 5: A New Bulk Approach for PX LSM
Leverage very high resolution National Land Cover Database (NLCD) with multi-level urban classifications
  PX LSM considers subgrid LU fractions
Utilize NLCD-based Impervious surface data directly in land-surface model to scale surface heat capacity
Increase surface roughness for urban LU classes to better represent developed areas
Decrease albedo in urbanized areas to account for sky-view and radiation trapping effects
Reduce deep soil temperature nudging strength

## Slide 6: Impervious Fraction (%) for 12 km Grid

## Slide 7: Impervious Fraction (%) for 4km Grid

## Slide 8
Impervious Fraction (%) for 1 km Grid
Shopping malls in Sugarland

## Slide 9: Skin Temperature on Aug 24,2006 at 10Z
Base – NLCD 2006
Urban

## Slide 10: 1 km WRF August 2006: Urban - Base
Albedo
T2m (Aug 31, 6AM LT)

## Slide 11: Evaluation Using Tethersonde Profiles
Tethersondes were launched on selected evening and nights in September through November at U of Houston
Profiles from 2 model runs : Base (NoImp) --- no impervious, NLCD 2006
Urban (Imp2) – Impervious, increased roughness, decreased albedo and weaker deep soil temp nudging
Tethersonde data provided by Bernhard Rappenglueck (UH)

## Slide 12: September 7, 20 LT (1Z)
qv
WS

## Slide 13: September 7, 23LT (4Z)

## Slide 14: September 7, Midnight LT (5Z)

## Slide 15: September 8, 2LT (7Z)

## Slide 16: September 8, 3LT (8Z)

## Slide 17: September 8, 4LT (9Z)

## Slide 18: September 8, 6LT (11Z)

## Slide 19: September 8, 8LT (13Z)

## Slide 20: CMAQ urban treatment
To compensate for inadequate treatment of enhanced turbulent mixing in urban areas CMAQ sets the minimum eddy diffusivity according to fraction of urban LU:
  In CMAQv4.7.1 and earlier: Kzurb = 2.0 and Kzrur = 0.5 m2/s
  In CMAQv5.0 and later: Kzurb = 1.0 and Kzrur = 0.01 m2/s
We hope to eliminate the need for this arbitrarily large Kzmin in urban areas by improving urban model in WRF

## Slide 21: CMAQ Runs
Four runs for 4 km Texas domain – Aug 23 – September 9
Unmodified CMAQ 5.0.1
  Base run using WRF-NLCD2006
  Urban run using impervious data and other urban mods
Modified CMAQ 5.0.1 with minimum Kz set to 0.01 m2/s everywhere
  Base run
  Urban run

## Slide 22: Base – Urban at 13Z (8AM LT) Aug 31, 2006
NOx
PM
O3
Large differences in primary pollutants at night and morning
Substantial differences in O3 but at a time when concentrations are low
No urban minimum Kz (Kzmin = 0.01)

## Slide 23: NOx: August 24 – September 8, 2006
12 AQS sites
6 AQS sites
Way too high at night in Houston for all runs
Both the Urban mods and the high minimum Kz reduce over prediction of NOx
3 AQS sites

## Slide 24: PM2.5: August 24 – September 8, 2006
Urban mods effective for Dallas in lowering nocturnal PM2.5
High minimum Kz more effective for Houston
Model too low at San Antonio except for morning Rush

## Slide 25: Conclusions
New bulk urban scheme for the PX-LSM shows much improved PBL structure in evening, overnight, and morning compared to Houston tethersonde measurements
4 km CMAQ runs show reduced high bias for primary pollutants but still too high
Removing urban Kzmin makes over-prediction worse
Further improvements should be evaluated meteorologically since nocturnal emissions may have significant errors

## Slide 26: Next steps
Enhancements to the Urban parameterization:
  Add anthropogenic heating based on population and housing unit density
  Add NLCD canopy fraction data for accurate accounting of tree cover in all areas including urban.
Comprehensive evaluation of meteorology and AQ at all scales

## Slide 27: Extras

## Slide 28: Why AQ model at 4 km resolution grossly overpredicts NOx in Houston
AQS site near Houston ship channel
2 km

## Slide 29: 4 km modeling for Houston – August 2006
WRF Potential temperature (blue) in Houston at 7 PM shows premature surface inversion
CMAQ v4.7 and 5.0 overpredict CO especially during morning and evening rush hours

## Slide 30: Ozone at 00Z (7PM LT) Sept 1, 2006
Substantial ozone differences in evening when concentrations are high
Base - Urban
Urban

## Slide 31: Ozone: August 24 – September 8, 2006
Difference among the 4 runs are less for Ozone than for NOx
Run with least nocturnal mixing (highest over-prediction of NOx) is closest to Obs for Dallas and San Antonio.
All runs too low for Houston.

## Slide 32: NOx: August 24 – September 8, 2006
3 AQS sites
2 AQS sites
Daytime modeled NOx compares well for San Antonio
Urban effects are small for Austin