## Slide 1: Sensitivity analysis of influencing factors on PM2.5 nitrate simulation
the 11th Annual CMAS Conference
October 16, 2012
This research was supported by the Environment Research and Technology Development Fund (C-1001) of the Ministry of the Environment, Japan.
○ Shimadera H.1, Hayami H.1, Chatani S.2, Morino Y.3,
Mori Y.4, Morikawa T.5, Yamaji K.6, Ohara T.3
1 Central Research Institute of Electric Power Industry
2 Toyota Central R&D Labs., Inc.
3 National Institute for Environmental Studies
4 Japan Weather Association
5 Japan Automobile Research Institute
6 Japan Agency for Marine-Earth Science and Technology

## Slide 2: Introduction
Fine particulate matter (PM2.5) has adverse health effects
In Japan, air quality standard for PM2.5 is not attained in many areas*1
Air quality models (AQMs) are essential tools to seek effective measures
Current air quality models cannot sufficiently reproduce concentrations of PM2.5 and its components in Japan*2
*1Ministry of the Environment (2012) http://www.env.go.jp/press/press.php?serial=14869
*2Morino et al. (2010) J. Jpn. Soc. Atmos. Environ. 45, 212-226
Urban air quality Model Inter-Comparison Study (UMICS) has been conducted to improve AQM

## Slide 3: UMICS: Urban air quality Model Inter‐Comparison Study
Phase | Target period | Target process | Target component | Influencing factor |  |  | 
 |  |  |  | Module | Met. | Emiss. | React.
UMICS1 (FY2010) | Summer 2007 (FAMIKA) | Transport | EC | ○ | ○ | ○ | ×
UMICS2 (FY2011) | Winter 2010 Summer 2011 | SIA production | SO42-NO3-NH4+ | △ | △ | ○ | ◎
UMICS3 (FY2012) | Winter 2010 Summer 2011 | SOA production | OC | △ | △ | ◎ | ◎
Focuses on PM2.5 components in the Kanto region of Japan
Uses common meteorological, emission and boundary data
Participants conduct sensitivity runs in their fields of expertise
– Observation vs. Baseline Simulation of UMICS2 – Sensitivity analyses to improve SIA simulation

## Slide 4: Simulation domain
Elevation (m)
Observation sites for PM2.5 components
D1
D3
D2
Tsukuba
Komae
Saitama
Kisai
Maebashi
Horizontal D1: East Asia (64-km grids, 96x80)
D2: East Japan (16-km grids, 56x56)
D3: Kanto region (4-km grids, 56x56)
Vertical 30 layers (surface – 100 hPa)
Common dataset for UMICS2

## Slide 5: Meteorological field
Meteorological model: WRF-ARW v3.2.1
Simulation period Winter 2010: Nov. 15 – Dec. 5, 2010
Summer 2011: Jul. 11 – Jul. 31, 2011
 | Configurations
Terrain | USGS (30sec)
Initial/Boundary | NCEP FNL (1deg, 6hr) NCEP/NOAA RTG_SST_HR (1/12deg, daily)
Nesting | No feedback
Cumulus | Kain-Fritsch (D1, D2)
Microphysics | WSM5
Radiation | Dudhia/RRTM
PBL | ACM2
Land surface | Pleim-Xiu LSM
Analysis nudging | Gt, q, uv = 1.0x10-4 s-1 (D1, D2)
Common dataset for UMICS2

## Slide 6: Emission data
Based on database described by Chatani et al.*
Anthropogenic
D1: INTEX-B (SO2, NOX, CO, PM, VOC), REASv1.11 (NH3)
D2, D3: Estimate model by JATOP (Vehicle), G-BEAMS (Others)
Ship
D1: SAPA201112 by NMRI
D2, D3: Emission inventory by OPRF
Biogenic VOC
MEGAN v2.04 with common meteorological field
Volcanic SO2
Volcanic activity reports by JMA
*Chatani et al. (2011) Atmos. Environ. 45, 1383-1393
Common dataset for UMICS2

## Slide 7: Boundary concentration
D1: MOZART-4 results
http://www.acd.ucar.edu/gctm/mozart/subset.shtml
D2, D3: CMAQ v4.7.1 with common dataset
(Baseline case for UMICS2: M0)
 | Configurations
Advection | yamo
Vertical Diffusion | acm2
Photolysis rate | table
Gas phase | saprc99 (ebi)
Aerosol phase | aero5
Cloud phase | acm
Common dataset for UMICS2

## Slide 8: Time series at Kisai
Winter 2010
(μg m-3)
(μg m-3)
(μg m-3)
HNO3
PM2.5 NO3-
NH3
PM2.5 NH4+
PM2.5 SO42-
PM2.5 OA
PM2.5 EC
PM2.5
Observation vs. Baseline Simulation

## Slide 9: Mean concentration at observation sites
Winter 2010
(μg m-3)
(μg m-3)
Observation vs. Baseline Simulation

## Slide 10: Time series at Kisai
Summer 2011
(μg m-3)
(μg m-3)
(μg m-3)
HNO3
PM2.5 NO3-
NH3
PM2.5 NH4+
PM2.5 SO42-
PM2.5 OA
PM2.5 EC
PM2.5
Observation vs. Baseline Simulation

## Slide 11: Mean concentration at observation sites
Summer 2011
(μg m-3)
(μg m-3)
Observation vs. Baseline Simulation

## Slide 12: Summary
PM2.5: mean concentrations were agreed, but temporal variations were not reproduced
PM2.5 EC and SO42-: approximately reproduced
HNO3: diurnal variations were reproduced
PM2.5 OA: clearly underestimated
  Being discussed in UMICS3
PM2.5 NH4+: overestimated as NH4NO3
NH3 and PM2.5 NO3-: clearly overestimated
  Sensitivity analysis for influencing factors will be presented
Observation vs. Baseline Simulation

## Slide 13: Inter-comparison of baseline Sim. cases
Target period
  Winter 2010: Nov. 22 – Dec. 5, 2010
  Summer 2011: Jul. 18 – Jul. 31, 2011
Target area
  1st layer on land area < 200m ASL in D3 ( )
 | M0 | M1 | M2 | M3 | M4
AQM | CMAQ v4.7.1 | CMAQ v4.7.1 | CMAQ v4.6 | CMAQ v4.7.1 | CMAQ v5.0
Domain | D1, D2, D3 | D3* | D3* | D1, D2, D3 | D3*
H Adv. | yamo | yamo | yamo | ppm | yamo
V Adv. | yamo | yamo | yamo | ppm | wrf
H Diff. | multiscale | multiscale | multiscale | multiscale | multiscale
V Diff. | acm2 | acm2 | acm2 | acm2 | acm2
Photolysis rate | table | inline | table | inline | inline
Gas phase | saprc99 (ebi) | saprc99 (ebi) | saprc99 (ros3) | saprc99 (ebi) | saprc99 (ebi)
Aerosol phase | aero5 | aero5 | aero4 | aero5 | aero5
Cloud phase | acm | acm | radm | acm | acm
D3
*Using D2 result of M0 for boundary concentration

## Slide 14: Time series of spatial mean Conc.
Winter 2010
Summer 2011
PM2.5 NO3-
PM2.5 NH4+
(μg m-3)
(μg m-3)
(μg m-3)
(μg m-3)
PM2.5 NO3-
PM2.5 NH4+
Inter-comparison of baseline simulation cases
Using common dataset, temporal variation patterns in M0–M4 are very similar to each other

## Slide 15: Difference of mean Conc. from M0
Winter 2010
Summer 2011
Difference from M0 (%)
M1, M3: relatively small difference between CMAQ v4.7.1 runs
  phot_table→Inline reduce HNO3 and PM2.5 NO3- in summer
  M3: yamo→ppm Adv. scheme increase ground-level Conc.
M2: CMAQ v4.6, ros3, aero4, radm, offline VD Calc. …
M4: Smaller Min. KZ in CMAQ v5.0 increase nighttime Conc.
Inter-comparison of baseline simulation cases

## Slide 16: Sensitivity analysis
NO3
NO2
NO
HNO3
N2O5
NH3
NH4NO3
NOX Emiss.
NH3 Emiss.
T & RH
Dry Dep.
Semi volatile
+
Daytime
Nighttime
Het. Chem.
Processes involved in PM2.5 NO3- production

## Slide 17: T & RH (M0, D3)
Sensitivity analysis
Winter 2010
Summer 2011
Difference from baseline case of M0
(%)
Uniformly changed T in aerosol module by ±2 K
Uniformly changed RH in aerosol module by ±10%
  T&RH affect not only gas/aerosol partitioning
  RH is within the range of 0.5 – 99%

## Slide 18: NOX emission (M1, D3)
Uniformly changed NOX emission by from -40 to +40%
  Uncertainty in total NOX emission is probably smaller
Sensitivity analysis
Winter 2010
Summer 2011
Difference from baseline case of M1
(%)

## Slide 19: NH3 emission (M0, D2-D3)
Total emission changed by +52% in winter and -42% in summer in D3
Chart: 
 | 0.070821 | 0.066686 | 0.072888 | 0.07909 | 0.099764 | 0.10012 | 0.10174 | 0.094714 | 0.075694 | 0.079888 | 0.083225 | 0.075369
Monthly emission ratio
summer
winter
Common data
Modified
according to process for N2O emission estimate in Japan
according to EMEP/CORINAIR EF
Sensitivity analysis
Winter 2010
Summer 2011
Difference from baseline case of M0
(%)

## Slide 20: HNO3 & NH3 dry deposition VD (M2, D3)
Uniformly multiplied HNO3 & NH3 VD by 5 and 0.2
*Neuman et al. (2004) JGR 109, D23304
Baseline VD (cm s-1)
Neuman et al.* estimated higher daytime
HNO3 VD (8 – 26 cm s-1) from measurement
of power plant plumes
Sensitivity analysis
Winter 2010
Summer 2011
Difference from baseline case of M2
(%)

## Slide 21: N2O5 heterogeneous reaction (M0, D3)
Constant ΓN2O5 values: 0 (No React.) and 0.1 (Upper estimate)
Parameterization method of aero3 and aero4 (Baseline: aero5)
N2O5 reaction probability
Sensitivity analysis
Winter 2010
Summer 2011
Difference from baseline case of M0
(%)

## Slide 22: Mod. of multiple factors (M0, D1-D3)
Photolysis rate: photo_table → photo_inline
  PM2.5 NO3-: +3% in winter, -6% in summer
Modified seasonal variation of NH3 emission
  PM2.5 NO3-: +11% in winter, -24% in summer
HNO3 & NH3 VD: 5 times
  PM2.5 NO3-: -39% in winter, -46% in summer
N2O5 Het. Chem.: aero5 → aero3
  PM2.5 NO3-: -6% in winter, -4% in summer
M0_Base → ModMulti
  PM2.5 NO3-: -39% in winter, -74% in summer
applied
simultaneously
Winter
Summer
Difference from baseline case of M0 (%)
Sensitivity analysis

## Slide 23: Mean concentration at observation sites
Winter 2010
Summer 2011
(μg m-3)
(μg m-3)
Modification of multiple factors (M0)

## Slide 24: Summary
UMICS2 was conducted to improve AQM performance for simulating SIA, particularly PM2.5 NO3-
Using common dataset, results of CMAQ runs with different configurations were similar to each other
HNO3 & NH3 dry deposition and NH3 emission can be key factors for improvement of PM2.5 NO3- simulation
  Accumulation of Obs. data of HNO3 & NH3 Conc.
  Development of better NH3 emission inventory
  Drastic modification of AQM may be required
Sensitivity analysis