## Slide 1: Advanced Land Surface Processes in the Coupled WRF/CMAQ with MODIS Input
Limei Ran1, Robert Gilliam1, David Wong1, Hosein Foroutan2, Jonathan Pleim1, George Pouliot1, Wyat Appel1, Matthew Woody3, Benjamin Murphy1, Kirk R. Baker3, Daiwen Kang1, Shawn Roselle1, Brian Eder1, Ellen Cooter1
1Computational Exposure Division, USEPA/ORD/NERL, Research Triangle Park, NC, USA
2Department of Biomedical Engineering and Mechanics, Virginia Tech, Blacksburg, VA, USA
3Office of Air Quality Planning and Standards, USEPA, Research Triangle Park, NC, USA

## Slide 2: 1. Background and Objective
LSM: important for WRF/CMAQ
Meteorology: heat, moisture and momentum (e.g. LH, soil water, 2-m T and Q, PBLH)
Air quality: dry deposition and dust emissions
Updated: WRF3.4 bias difference: MODIS – Base
2-m Q
200608
MODIS improves 2-m Q in the north-central states
Better:
63.85% sites
Efforts on improving land surface processes
Evaluated and updated WRF v3.4 with MODIS vegetation product for offline CMAQ v5.0.1 (Ran et al., 2015 and 2016, JGR-Atmos.)
Implemented a photosynthesis approach in the PX LSM box model (Ran et al., 2017, JGR-Atmos.)
MODIS input helps reduce 2-m Q bias during growing season from April to September
Monthly average mean bias (MB) and error (MAE)
2006

## Slide 3: 1. Background and Objective
Bias Difference: Updated CMAQ – Base CMAQ
Bias reduction across domain, particularly southwest - > sparsely vegetated land (average 2.1 ppb)
O3
200608
Sites in > 50% irrigated grid cells show bigger improvements
Efforts on improving land surface processes
Updated CMAQ v5.0.1 for O3 dry deposition soil resistance and developed a simple irrigation scheme in updated WRF v3.4 (Ran et al., CMAS 2016)
2-m T
2010 05-06
MODIS: Irrigation – Base
Goal: evaluate the updated coupled model - WRF/CMAQ
  CMAQ 12km (April and August 2016)
  CA 4km with the simple irrigation scheme (May - June, 2010)
Coupled WRF v3.8/CMAQ v5.2 with the previous updates and new changes
  MODIS vegetation input
  Soil treatment
CIMIS Site Metrics vs. Grid Irrigated Land Percent

## Slide 4: 2. MODIS Data and Soil Treatment
Real-time LAI
MODIS LAI/FPAR V6 products at 500m:
Inconsistent values – jumping due to contaminations in image acquisition
LAI is lower in the peak growing day in August than that in June
MCD15A2H V6 LAI: 2016-06-25
MCD15A2H V6 LAI: 2016-08-04
MOD15A2GFS V5 LAI: 06-25
MOD15A2GFS V5 LAI: 08-04
4 year averaged LAI (2004-2007)
North American Carbon Program (NACP) MODIS gap-filled and smoothed products at 1km (Gao et al., 2008, IEEE):
LAI is consistent, but different from real-time product
WRF and CMAQ dust model

## Slide 5: 2. MODIS Data and Soil Treatment
WRF PX LSM updated on:
Soil texture: Menut et al., 2013, JGR-Atmos
Soil parameters: Noilhan & Mahfouf et al., 1996, GPC, ECMWF TESSEL
Soil residual water: fitted function using soil texture based on Rawls et al., 1982, Trans. ASAE
Consistent soil and vegF treatment for:
WRF PX LSM (Pleim and Xiu, 1995, JAM)
CMAQ dust model (Foroutan et al., 2017, JAMES)
Residual soil water for 11 soil types
Base CMAQ: soil categories
CMAQ dust model updated on:
WRF vegetation fraction (MODIS FPAR)
WRF Soil texture:
  Very similar – PX LSM soil categories do well
  More fine and medium sand in the east and less in the west from WRF
Fine and medium sand percent at 12km grid cells
Modified CMAQ: WRF
1 : 1

## Slide 6: 3. WRF/CMAQ Evaluation – Model Configuration
Configuration
No feedback
NCEP 12km NAM analysis and reanalyzed with OBS data using OBSGRID
Indirect soil nudging from 2-m T and Q (SFDDA) in the PX LSM
    2010 and April 2016: standard NCEP NAM 12km every 3 hours
    August 2016: hourly UnRestricted Mesoscale Analysis (URMA) 2.5km
CB05e51 gas-phase chemistry, AE6 modal aerosols
In-line biogenic and dust emissions
Others: standard EPA options (Ran et al., 2016, JGR-Atmos.)
Two domains
CONUS 12km April and August 2016: two scenarios
  BASE: standard released WRF and CMAQ with PX LSM table
  MODIS: updated system with averaged LAI/FPAR
  Emissions: NRT emissions from projected USEPA NEI
CA 4km May to June 2010: two scenarios
  MODIS: updated system with averaged LAI/FPAR
  MODIS IRR: with a simple irrigation scheme
  Emissions: same as what is used by Woody et al., 2016, ACP
Forest Percent for CONUS 12km NLCD(2011)/MODIS(2016)
Forest and Agricultural Percent for CA 4km NLCD(2011)/MODIS(2010)
Updated coupled WRF-ARW v3.8/CMAQ v5.2

## Slide 7
3. WRF/CMAQ Evaluation – CONUS 12km
Base
MODIS
2016-04
2-m T (K)
2-m Q (g/kg)
2-m T (K)
2-m Q (g/kg)
Every 3 hours - NCEP NAM 12km PX LSM soil nudging input
Cold and wet bias reduction during the day, particularly late afternoon
2016-08
Every 1 hour - URMA 2.5km PX LSM soil nudging input
2-m T and Q perform really well for both cases
MODIS improves daytime cold and wet bias slightly
Diurnal Comparison against MADIS Observations
Diffusion soil resistance used in the MODIS case (Sakaguchi and Zeng, 2009 JGR; Pleim et al., 2013 JGR-Atmos.) : tends to make night wetter (Swenson and Lawrence, et al., 2014, JGR) than the β soil approach (Lee and Pielke, 1992 JAM) in the base
Base
MODIS

## Slide 8
3. WRF/CMAQ Evaluation – CONUS 12km
Base
MODIS
2016-04
2-m Q (g/kg)
Every 3 hours – NCEP NAM 12km PX LSM soil nudging input
MODIS reduced cold and wet bias in the northern east
2016-08
Every 1 hour – URMA 2.5km PX LSM soil nudging input
2-m T: similar with slightly reduced cold bias in the west and FL in MODIS
MODIS reduced wet bias in central Plains and FL, but worse for many in the west
Base
MODIS
MODIS - Base
Bias Spatial Comparison against MADIS Observations
MODIS - Base
Better:
57% sites
Better:
66% sites
Better:
47% sites
Better:
53% sites
2-m T (K)
2-m T (K)
2-m Q (g/ka)
Hourly URMA nudging input: dominant influence
  MODIS impacts different from 3 hour nudging in August from Ran et al., 2016, JGR-Atmos.

## Slide 9
3. WRF/CMAQ Evaluation – CONUS 12km
2016-04
MODIS case slightly better in early days of April
MODIS case reduces errors for sites in the north
2016-08
MODIS and Base perform similarly on daily average domain-wide
Better most of the east, northwest, southwest for MODIS
Worse in FL, around IL, around the Central Valley for MODIS
Bias: MODIS - Base
Daily Maximum 8-h Average O3 (ppb) against AQS sites
Error: MODIS - Base

## Slide 10
3. WRF/CMAQ Evaluation – CONUS 12km
2016-04
MODIS case tends to reduce dust emissions further during the dust events
Reduced dust emissions helps PM2.5 from the SW to Great Lakes states
2016-08
MODIS and Base perform similarly on daily average domain-wide
Many sites in the east tend to be better with reduced high bias
Daily PM2.5 (ug/m3) evaluation against AQS sites
Bias: MODIS - Base
Bias: MODIS - Base
2016-04-16: Base
2016-04-16: MODIS

## Slide 11
California Irrigation Management Information System (CIMIS) Stations (http://www.cimis.water.ca.gov/)
3. WRF/CMAQ Evaluation – CA 4km
Comparison against CIMIS
  Irrigation data for crop and pasture: MIrAD-US at 250m (http://earlywarning.usgs.gov/USirrigation)
  Irrigation scheme: PX LSM deep soil water content is modified based on:
    Max. allowable water depletion (Hanson et al., 2004; Sorooshian et al., 2011, JGR; Ozdogan et al., 2010, AMS)
  MADIS site evaluations: similar results
Irrigated agricultural land (%)
at 4km grid cells
Agricultural land (%) and CIMIS stations at 4km grid cells
CIMIS sites (May 10 to June 30, 2010) : MODIS IRR - MODIS vs. grid irrigated land Percent
CIMIS sites in > 50% irrigated grid cells (34 sites) show some improvements

## Slide 12
3. WRF/CMAQ Evaluation – CA 4km
20-Z average and average difference from May 10 to June 30, 2010
LH (W/m2): MODIS
LH: MODIS IRR
LH: MODIS IRR - MODIS
LH increases in the Central Valley
2-m T and PBLH decrease accordingly
2-m T (K): MODIS
2-m T: MODIS IRR - MODIS
PBLH (m): MODIS
PBLH: MODIS IRR - MODIS

## Slide 13
3. WRF/CMAQ Evaluation – CA 4km
2010-05-10 to 06-31
Irrigation treatment reduces errors for the Central Valley and southeastern area
During the ozone event, irrigation reduces the daily averaged mean bias and error in the Central Valley slightly
Bias: MODIS IRR - MODIS
Daily Maximum 8-h Average O3 (ppb) against AQS sites
MAError: MODIS IRR - MODIS
Ozone event: 2010-06-01 to 06-07
Bias: MODIS IRR
MAError: MODIS IRR - MODIS

## Slide 14
3. WRF/CMAQ Evaluation – CA 4km
2010-05-10 to 06-31
Irrigation reduces bias and error of PM2.5 and PM10 slightly
Daily PM (ug/m3) evaluation against AQS sites
Bias: MODIS IRR - MODIS
MAError: MODIS IRR - MODIS
Bias: MODIS IRR
PM10
PM2.5

## Slide 15: Conclusions and Future Work
Conclusions
  Updated coupled WRF/CMAQ performs reasonably well with averaged MODIS vegetation
    Reduces cold and wet bias during the daytime; but tends to make the model wetter late at night
    Surface ozone is slightly better and PM is improved particularly during the dust events
  The simple irrigation scheme helps improve the system in general
    Reduces hot and dry bias for CIMIS sites which are dominated by irrigated agricultural land
    Influences LH, 2-m T, and PBLH in the Central Valley
    Improves ozone and PM in the Central Valley
Future Work
  Complete two manuscripts with detailed description and analysis
  Implement the photosynthesis approach in the updated system
  Help implement the updates in the WRF and CMAQ releases

## Slide 16: Disclaimer
While this work has been reviewed and cleared for presentation by the U.S. EPA, the views expressed here are those of the authors and do not necessarily represent the official views or policies of the Agency.