## Slide 1: Searching for missing carbonaceous aerosols sources in Bogotá: Sensitivity analysis using WRF-Chem
Maria Paula Pérez-Peña, MSc. 1
Ricardo Morales Betancourt, PhD. 1
1 – Universidad de los Andes, Bogotá, Colombia.
Chapel Hill, NC
2018

## Slide 2
CONTEXT
Bogotá is a fast-growing megacity.
~8M inhabitants
~2M vehicles (73% privately owned)
Introduction
Our study area: Bogotá, Colombia
PM10 [µg m-3]
AQ monitoring network data in Bogotá
PM10 : 49.1 [µg m-3]
PM2.5 : 29.1 [µg m-3]
Annual average concentrations
MAIN CONCERN
Particulate matter
Notes: Annual average pm10 c=49.1
Annual average p¿m2.5 c= 29.1
UNCERTAINTIES
Composition of particulate and gaseous species in the atmosphere

## Slide 3
A
B
C
D
PM10 composition in Bogotá
(Vargas & Rojas, 2007)
 | Organic Matter |  | Sulfate (SO42-)
 | Elemental Carbon |  | Nitrate (NO3-)
 | Crustal/Mineral/Soil |  | Trace
 | Ionic |  | Others (un-speciated)
 | Secondary Inorg. Aer. |  | 
Conference (Pachón et al., 2017)
PM Species
(Ramírez et al., 2018)
Introduction
Chart: 
 | 39.2 | 12.6 | 38.2 | 9.8 | 0.3
Chart: 
 | 43.4 | 14.5 | 38.2 | 4.3 | 0.5
Chart: 
 | 37.7 | 25.3 | 16.2 | 10.5 | 1.4
Chart: 
 | 32 | 26 | 30 | 10 | 1
Chart: 
 | 42 | 8.7 | 23 | 7.3 | 3.3 | 0.4 | 15
Chart: 
 | 39.2 | 12.6 | 38.2 | 9.8 | 0.3
Chart: 
 | 43.4 | 14.5 | 38.2 | 4.3 | 0.5
Chart: 
 | 37.7 | 25.3 | 16.2 | 10.5 | 1.4
Chart: 
 | 42 | 8.7 | 23 | 7.3 | 3.3 | 0.4 | 15
Chart: 
 | 32 | 26 | 30 | 10 | 1
A
B
C
D
E
Bogotá
Notes: Remove name of places, set them as a side note
Suba, caervajal, tunal, inmisión, u.libre

## Slide 4
Gas phase measurements in Bogotá
(Franco, Pacheco, Belalcázar & Behrentz, 2015)
Alkanes are 80% of total VOCs
Max. total VOC concentration:
Majority of measured VOCs are emitted by vehicular sources
Introduction
11 Air Quality monitoring stations (∆) in Bogotá
CO, NOx, SO2 and O3 are measured
VOC Characterization
Bogotá AQMN
Notes: Bogotá has measurements of O3, CO, NOx and SO2
While PM10 has been measured in more occasion, only one peer reviewed work has been published where the gaseous phase has been characterized

## Slide 5: Previous AQ modelling studies in Bogotá
On-road traffic sources represent a significant contribution of the EI
TAPOM/FVM
(Zárate et al., 2007)
Resuspended dust from paved and unpaved roads is a significant source of PM in the city.
CMAQ
(Nedbor-Gross et al., 2018)
Sensitivity analysis show the best gas-phase chemical mechanism to use (RADM2)
WRF-Chem
(Kumar et al., 2016)
Introduction

## Slide 6: Our goal
Introduction
Our methods
To be able to explain the observed levels of carbonaceous airborne species in the city by means of chemical transport modelling
Determine optimal model configuration (i.e., static fields, physics, gas-phase chemistry, aerosol schemes…)
Test out different emissions inventories: Sensitivity analysis
Identify potential weaknesses in emission sources and emissions speciation
Notes: Our goal: To be able to reproduce the observed levels of carbonaceous airborne species observed in the city by means of chemical transport modelling, and further assess its impact on a regional level.
Select inventories
Select configuration (physc chem)
Find missing sources
Select our goals

## Slide 7
Simulation and challenges
500 m
4000 m
WRF-Chem V3.9.1
3 Nested domains
D01: 27 x 27km
D02: 9 x 9km
D03: 3 x 3km
D03
Complex Topography
Notes: Our modelling domain:
Our challenges
Geographic location of our domain
What is our downscaling

## Slide 8
Building a base case Bsc
Methods
(Nedbor-Gross, 2018)
STATIC FIELDS
CHEMISTRY RELATED
Land use: MODIS
Topography: ASTER
Anthropogenic EI
Local EI for cities
  Bogotá (RPM estimates)
Global EI
  EDGAR V4.3.1
  EDGAR-HTAP
BC and IC:
MOZART4-GEOS5 for d01
Biogenic emissions:
MEGAN
online
Chem. options:
RACM and
MADE/VBS
Urban areas
Notes: There have been developments of EI for some cities in Colombia

## Slide 9
Global emissions Vs. Local emissions
Mobile emissions inventory
Methods
Gas Phase Emissions
Particle Emissions
Notes: Considering such discrepancies, we decided to test out first the global emissions inventories

## Slide 10: Choosing the global inventory for our base case
EDGAR-HTAP
EDGARv4.3.1
PM2.5
Power plant 1
Power plant 2
[µg/m3]
Methods
Overestimation of energy sector emissions by EDGAR-HTAP

## Slide 11
BC and IC:
MOZART4-GEOS5 for d01
Building a base case Bsc
Methods
(Nedbor-Gross, 2018)
STATIC FIELDS
CHEMISTRY RELATED
Land use: MODIS
Topography: ASTER
Biogenic emissions:
MEGAN
online
Anthropogenic EI
Chem. options:
RACM and
MADE/VBS
We choose EDGARv4.3.1 adding local RPM

## Slide 12: Meteorology evaluation
Observations
Model
TEMPERATURE
Attainance of benchmarks
Results
AQ monitoring network (RMCAB)

## Slide 13: Chemistry performance
O3 [ppb]
NO [ppb]
Results
[ppb]
Mod
Obs
PBLH

## Slide 14: Chemistry performance
Fine particles underestimated in north of the city (misplaced emissions?)
Coarse mode particles are underestimated all over Bogotá
PM2.5
PM10
PM2.5
/ PM10
[µg/m3]
[µg/m3]
Results

## Slide 15: OA contribution to PM10
Organic fraction in PM10
Results
ASOA fraction in PM10
2.7% ASOA/PM10 within Bogotá
18% Organic/PM10 within Bogotá
(Ramírez et al., 2018)
Chart: 
 | 42 | 8.7 | 23 | 7.3 | 3.3 | 0.4 | 15
Observed composition PM10
Notes: We know our simulations are good, but what about the composition and the contribution of organic species to the simulated PM? Well …

## Slide 16: OA contribution to fine PM
Organic fraction in PM2.5
Results
ASOA fraction in PM2.5
3% ASOA/PM2.5 within Bogotá
22% OM/PM2.5 within Bogotá
Modeled composition PM2.5
Notes: We know are simulations are good, but what about the composition and the contribution of organic species to the simulated PM? Well …

## Slide 17
CO (Ton/yr)
Results
Using the local mobile emissions
> 10X VOC
4X CO
5X NOx
1X PM
EDGARv4.3.1
Local emissions 2012
Vs.
Notes: So what if we now tested the local emissions inventory, which though having higher magnitudes, spatially show a more accurate pattern of emissions

## Slide 18: Modeled PM performance
Local mobile emissions inventory produces a significant change on particle estimates
Results
PM10
PM2.5
|18
Results
PM10
PM2.5
Overestimation of fine particles
Base case
Using mob loc EI

## Slide 19: Using the local emissions: What happens with the gaseous phase?
Results
CO [ppb]
Mod
Obs
PBLH
Base case
With local mobile emissions

## Slide 20: Particle composition
Results
But gas phase pollutants are overestimated!
Average Observed PM2.5
PM10
With MADE/VBS regional sources don’t explain the OM

## Slide 21: Concluding remarks
Even with high concentration of SOA precursors, OM is not well represented
EC is underrepresented in all simulations, irrespective of emission inventory used
Our results suggest that missing OM and EC could be caused by:
  Too little POM and EC in the local/global emissions inventory
  Need of speciation of re-suspended particles emitted in the city (Work developed by Jorge Pachón’s group)
  Do we have a misrepresentation of regional sources? Biomass burning aerosols from wildfires?
Take home message

## Slide 22: Speciation of PM2.5
Measurements campaigns of fine PM
Ongoing work
PM2.5 27.9 [µg m-3]
Chart: 
| OC | EC | SO4 | NO3 | NH4 | Cl | Na | Otros
 | 16.8129 | 2.6225 | 7.2767 | 2.0495 | 46.8712 | 0.24208 | 0.25089 | 23.8743

## Slide 23: Acknowledgements
This work was funded by the FAPA program from the Office of the vice-dean for Research from Universidad de los Andes, Bogotá, Colombia.
We thank the local authority Secretaría Distrital de Ambiente SDA for providing the local emissions inventory for 2012.
We acknowledge use of the WRF-Chem preprocessor tools anthro_emiss, bio_emiss and mozbc provided by the Atmospheric Chemistry Observations and Modelling Lab (ACOM) of NCAR.
To the air quality group from CIIA . . .

## Slide 24: Thank you!!! Questions ?
Maria Paula Pérez-Peña, MSc. 1
Ricardo Morales Betancourt, PhD. 2
1 – mp.perez@uniandes.edu.co
2 – r.moralesb@uniandes.edu.co

## Slide 25: Back-up slides
Maria Paula Pérez-Peña, MSc. 1
Ricardo Morales Betancourt, PhD. 2
1 – mp.perez@uniandes.edu.co
2 – r.moralesb@uniandes.edu.co

## Slide 26: Pollutant dependency to PBLH estimates
Results
…. Too low night-time PBLH

## Slide 27: Base case modelling results: chemistry performance
NO [ppb]
OBSERVATIONS
PREDICTIONS
PREDICTIONS

## Slide 28: Concluding remarks
The results of our simulations indicate that PM2.5 and PM10 levels can be represented well with the emission inventories explored in the study.
The contribution of both, Elemental Carbon and Organic Aerosols is highly underestimated.
Secondary inorganic aerosol contribution is overestimated by all model simulations.
Organic aerosol contribution is only well represented when using the local inventories, which grossly overestimates other species such as CO and VOC.
Secondary inorganic aerosol contribution is overestimated by all model simulations