## Slide 1: Model-Measurement Comparison of Ozone and Precursors Along Land-Water Interfaces during the 2017 LMOS Field Campaign
Liljegren, J; Baker, K.; Valin, L; Szykman, J; Henderson, B.; Judd, L.; Al-Saadi, J; Janz, S.; Sareen, N.; Possiel, N

## Slide 2
https://www.nasa.gov/sites/default/files/thumbnails/image/lmos_2.jpg
Elevated ozone episodes along the shores of Lake Michigan
Several monitors exceed the National Ambient Air Quality Standards (NAAQS)
“lake breeze” airflow can influence ozone production and transport
More info including a white paper can be found at:
https://www-air.larc.nasa.gov/missions/lmos/
Motivation for the Lake Michigan Ozone Study
Notes: Study involved aircraft, ground based and ship based measurements of ozone and its precursor compounds

## Slide 3
No routine measurements over the lake; persistent nonattainment status for ozone
1989 the four Lake Michigan states (IL, IN, WI, MI) formed the Lake Michigan Air Director’s Consortium (LADCO) to coordinate a 3-year Lake Michigan Ozone Study (LMOS 1991)
  later the 1994-2003 LADCO Aircraft Project (LAP)
  Cleary et al. 2015 ferry-based ozone measurements and analysis
Figures from White Paper: Lake Michigan Ozone Study 2017 (LMOS 2017) Peirce et al. 2016
History
Notes: Cleary results using measurements from 2008-2010 showed that NAM CMAQ at the time consistently overpredicts [O3] over lake as compared to measurements on the ferry but ferry measurements were on average about 4 ppb higher than O3 measurements along the shoreline
Cleary First study of CMAQ model bias over the water of Lake Michigan (11-16 ppb) greater bias than over the surrounding land (6-9 ppb)
Version of CMAQ??? Paper says National Air Quality Forecast Model (NAQFM) was developed with the collaboration of the National Oceanic and Atmospheric Administration (NOAA) and the Environmental Protection Agency (EPA) (Eder, 2009). The NAQFM is made up of two components: the National Center for Environmental Prediction’s (NCEP) North American Mesoscale (NAM) meteorological model and the EPA’s Community Multiscale Air Quality (CMAQ) modeling system

## Slide 4
LMOS 2017 May 22‐June 22, 2017
1 high ozone episode prior to the start of the LMOS study
June 2
June 10-12
June 14-16
3 high ozone episodes during LMOS
May 16-17
Sheboygan
Chicago area
Ozone Area Design Values (2016-2018)
Notes: High ozone episodes with hourly ozone values >70 ppb
Figure is a map of the routine ozone monitoring locations, the Sheboygan shoreline monitor and the Kenosha Wisconsin monitor north of Chicago are typically the nonattainment monitors for the study area

## Slide 5
Model: CMAQv5.3 as released via GitHub
Emissions: EPA’s 2016 beta platform w/ 2017-specific
Mechanism: cb6r3_ae7_aq
Meteorology: WRF v3.8
Domain: Lake Michigan 4km 35 layers
Maximum daily 8-hour averaged ozone (MDA8)
May 12 – June 23, 2017
Notes: We also ran 4km CMAQv5.3

## Slide 6
NOx Zion IL
Ozone Zion IL

## Slide 7
NOx Sheboygan WI
Ozone Sheboygan WI

## Slide 8
Sheboygan
May 12- June 23
Chicago area
May 12- June 23
Ozone Performance
May 12- June 23
Mean Bias of Average MDA8
Sheboygan
Chicago area

## Slide 9
Ozone Performance—June 2
Monitor Location | Observed (ppb) | Modeled (ppb) | Obs/Mod Time
Sheboygan | 76 | 65 | 11am/1pm
Chicago Area (Kenosha WI) | 84 | 64 | 2pm/1pm
Chicago area
May 12- June 23
MDA8 Mean Bias June 2, 2017
Sheboygan
Chicago
area
Sheboygan
May 12- June 23

## Slide 10
June 2, 2017, ozone, fires, and smoke
https://www.airnowtech.org/navigator/

## Slide 11
Zero-out (fires only contribution) on June 2, 2017
12km CMAQv5.2.1 CONUS

## Slide 12
Focus on June 2, 2017 episode
6:00 CST
14:00 CST
shift in wind direction indicative of lake breeze
https://www.airnowtech.org/navigator/
Notes: Hourly ozone and wind barbs 6 AM and 2 PM on June 2

## Slide 13
Observed (top) and Predicted (bottom) Ozone over Lake Michigan
EPA ORD/NOAA Research Vessel LMOS Data Repository
June 2
June 11
June 12
June 13
June 15

## Slide 14
Hourly Nitrogen Dioxide (NO2)
NO2 Performance
May 12 – June 23, 2017
Mean Bias of Average Hourly NO2
May 12 – June 23, 2017

## Slide 15
NO2 Performance
Milwaukee1
Milwaukee2
Chicago1
Chicago2
Milwaukee2
Milwaukee1
Chicago1
Chicago2
May 12 – June 23, 2017
Mean Bias of Average Hourly NO2

## Slide 16
NO2 Performance
Milwaukee1
Milwaukee2
Chicago1
Chicago2
Mean Bias of Average Hourly NO2
for June 2, 2017 ONLY
May 12 – June 23, 2017 (x = June 2 only)
Milwaukee2
Milwaukee1
Chicago1
Chicago2

## Slide 17
GeoTASO high res column NO2 measurements from sub-orbital flights
  aggregated to hourly, and
  projected to the 4 km CMAQ model domain
GeoTASO hourly flight segments were then aggregated to a multi-hour composite for comparison with CMAQ total column NO2
Pandora ground-based total column NO2 measurements are also depicted
GeoTASO & Pandora Spectrometer System
GeoTASO = Geostationary Trace Gas and Aerosol Sensor Optimization
https://pandora.gsfc.nasa.gov//index.html
https://twitter.com/nasa_langley/status/462244232732762112

## Slide 18
GeoTASO-Pandora & CMAQ NO2 column
Observed
Modeled
June 2
2pm – 6pm

## Slide 19
GeoTASO-Pandora & CMAQ NO2 column
Observed
Observed
Observed
Observed
Predicted
Predicted
Predicted
Predicted
8-10am
8-10am
11-2pm
11-2pm
3-5pm
3-5pm
June 1 to June 2
2-6pm
2-6pm

## Slide 20
Modeling-Based Evidence of Regional NOx Sensitivity
Modeling of individual hypothetical sources in the Lake Michigan region shows NOx emissions generally have a greater ozone impact than VOC emissions
CAMx modeling based on 2011 platform
https://www3.epa.gov/ttn/scram/guidance/guide/EPA454_R_16_006.pdf
Precursor | Emissions (tons per year) | Stack release height (low or high) | Maximum downwind ozone impact (ppb)
NOx | 500 | H | 1.15
NOx | 500 | L | 1.18
NOx | 1000 | H | 2.04
NOx | 3000 | H | 2.81
VOC | 500 | L | 0.42
VOC | 1000 | H | 0.78
VOC | 1000 | L | 0.81
VOC | 3000 | H | 2.00
Hypothetical Source 1 Emissions and O3 Impact
https://www.epa.gov/sites/production/files/2017-05/documents/national_modeling.advance.may_2017.pdf

## Slide 21
NOx- sensitive
transitional
VOC- sensitive
Ratio of Hourly Averaged Formaldehyde (FORM) to NO2 at Sheboygan
Indicator Ratios of Ozone Sensitivity — Sheboygan
Measurements at Spaceport Sheboygan EPA ORD LMOS Data Repository

## Slide 22
Indicator Ratios of Ozone Sensitivity — Zion
Sillman 1995
H2O2/HNO3
> 0.4 NOx sensitive
0.3 - 0.5 transitional
< 0.4 VOC sensitive
In general,
higher values for the O3/HNO3 ratio indicate NOx-sensitivity
lower values VOC-sensitivity
12-16 transitional
CIMS measurements
Tim Bertram et al.
LMOS Data
Repository

## Slide 23
Model again with 2016v1 platform (current modeling was done with the 2016 beta) updated any 2017-specific emissions where available
Analyze the other high ozone episodes that occurred in 2017
Look at other key data from LMOS 2017
Ongoing Analyses

## Slide 24
Questions
&
Thank You
Liljegren, J; Baker, K.; Valin, L; Szykman, J; Henderson, B.; Judd, L.; Al-Saadi, J; Janz, S.; Sareen, N.; Possiel, N

## Slide 25
Additional Slides

## Slide 26
Sillman 1995
H2O2/HNO3
< 0.4 VOC sensitive
> 0.4 NOx sensitive
0.3 - 0.5 transitional
Sillman 1995 indicator approach to ozone sensitivity has drawbacks
Relationship btwn sensitivity and indicator species may shift with changes in initial emission rates (i.e. depend on model assumptions)
Based on assumption of accuracy in model-based indicator species correlation
Figure 5 from Sillman 1995 Predicted reductions in peak O3 from 35% reduction in emis rate for anthro VOC (crosses) and NOx (circles) plotted against H2O2/HNO3 coincident with the ozone peak in the simulation for Lake Michigan base case.
Indicator Ratios of ozone sensitivity

## Slide 27
Change in monthly max MDA8 with 50% VOC cut
Change in monthly max MDA8 with 50% NOx cut

## Slide 28
Hourly Ozone June 2nd
10 am – midnight
ppb

## Slide 29
Hourly NO2 June 2nd
ppb
1 am – midnight

## Slide 30
Emissions information for 2017 model runs
Platform Sector abbreviation | Notes about the sector
ptegu | 2016 beta except replace with 2017 CEMS where applicable and apply known shutdowns. Derive and apply temporal profiles based on 2017 CEMS data using methods consistent with 2016 beta. Process all EGUs as elevated sources.
pt_oilgas | 2016 beta.
ptnonipm | 2016 beta.
ag | 2016 beta for livestock and fertilizer. Use 2017 met-based temporalization for both livestock and fertilizer.
ptagfire | 2017 Pouliot data (convert to FF10)
afdust_adj | 2016 beta with 2017 met-based adjustments.
beis | 2017 BEIS with water corrections
cmv_c1c2 | 2016 beta (projected from 2014)
cmv_c3 | 2016 beta (projected from 2014) as 12km points
rail | 2016 beta (from ERTAC)
nonpt | 2016 beta (portions projected from 2014)
np_oilgas | 2016 beta (ERG+state) with 2016 temporal profiles and spatial surrogates.
rwc | 2016 beta projected from 2014 with temporal allocation based on 2017 met
nonroad | 2016 beta adjusted to 2017 using national factors from OTAQ
onroad | 2016 beta adjusted to 2017 using national factors from OTAQ
onroad_ca_adj | 2017 CARB
ptfire | 2017 NEI draft fires – confirm Flint Hills looks appropriate
ptfire_othna | 2017 FINN fires
othafdust | 2016 beta (2015 Canada) adjusted with 2017 met data
othpt | 2016 beta
othar | 2016 beta
onroad_can | 2016 beta
onroad_mex | 2017 MOVES-Mexico

## Slide 31
EPA’s WRF configuration
Version | WRF ARW v3.8
Meteorological initial and boundary fields retrieved from | 12km North American Mesoscale Forecast system (NAM)
Horizontal resolution | 4 km
Vertical resolution | 35 layers between the surface and 50 mb with thinner layers closer to the surface
Cumulus Parametrization | Kain-Fritsch (new Eta)
Shallow Convection | no shallow convection
Microphysics | Morrison 2-moment
Longwave radiation | RRTMg
Shortwave radiation | RRTMg
PBL Scheme | ACM2 (Pleim)
Surface Layer Scheme | Pleim
Land-Surface Scheme | Pleim-Xiu Land-Surface Model
Urban Model | No urban physics
Land Use Classification | NLCD40
3D analysis nudging | grid
SFC analysis nudging | off
obs nudging | off
sea surface temperature (SST) | default
typically used for regulatory modeling e.g. CONUS transport

## Slide 32: Speciated PM2.5 and NH3
Model tends to underestimate regional ammonia compared to AMON
Good agreement for sulfate, EC, and OC compared with IMPROVE/CSN monitors
Nitrate a little underpredicted and soil components were systematically overestimated

## Slide 33
Sheboygan
Chicago
Ozone Area Design Values (2016-2018)
81 ppb
79 ppb
Preliminary 2017-2019 DV Sheboygan and Chicago
both 75 ppb

## Slide 34: Region 5 2008 Ozone Nonattainment Areas
2008 ozone NAAQS = 0.075 ppm (75 ppb)
Have come into attainment and been redesignated
Cleveland
Columbus
Cincinnati
St. Louis
Did not reach attainment by attainment date and were bumped up to classification of “moderate” nonattainment
Chicago
Sheboygan
Did not reach attainment by attainment date and bumped up to “serious” nonattainment
  Chicago
Sheboygan qualified for and requested a 1-year extension, but Sheboygan did not attain by the 1-year extension date and would need to be bumped up to serious if not redesignated based on 2019 clean data
Notes: Attainment date for Moderate areas: July 20, 2018
Statutory deadline for issuing final determinations: January 20, 2019
NPRM published November 14, 2018
  EPA proposed determinations of attainment/failure to attain (and reclassification to Serious), and 1-year attainment date extensions based on 2015-17 DV for 11 areas
  Proposal also included due dates for attainment plans and RACT implementation
Final notice anticipated in late spring 2019

## Slide 35: Region 5 2015 Ozone Nonattainment Areas
14 areas in Region 5 are “marginal” nonattainment
Chicago IL/IN/WI
Northwest Milwaukee/Ozaukee County Shoreline WI
Sheboygan County (partial) WI
Manitowoc County (partial) WI
Door County (partial; Rural Transport Area) WI
St. Louis IL/MO
Berrien County MI
Allegan County (partial) MI
Muskegon County (partial) MI
Detroit MI
Cleveland OH
Columbus OH
Cincinnati OH
Louisville IN/KY
Bold areas still violating based on prelim 2019 data
Non-bolded areas clean and/or redesignated

## Slide 36
NO2

## Slide 41
GeoTASO-Pandora & CMAQ NO2 column
Observed
Observed
Observed
Observed
Predicted
Predicted
Predicted
Predicted
8-10am
8-10am
11-2pm
11-2pm
3-5pm
3-5pm
June 1 to June 2
2-6pm
2-6pm

## Slide 42
Observed (top) and Predicted (bottom) Ozone over Lake Michigan
EPA ORD/NOAA Research Vessel LMOS Data Repository
June 2
June 11
June 12
June 13
June 15