## Slide 1: UNCERTAINTIES INFLUENCING HEALTH-BASED PRIORITIZATION OF OZONE ABATEMENT OPTIONS
9th Annual CMAS Conference
11-13th October, 2010
Daniel S. Cohan, Antara Digar & Wei Tang
Rice University
Michelle L. Bell
Yale University

## Slide 2: Decision Support Context
Two objectives of ozone attainment planning
  Attain standard at monitors
  Benefits to human health, agriculture, ecosystems
Health benefits rarely quantified, but could inform prioritization of control measures
Uncertainties in health benefit estimates
  Uncertain model sensitivities (∆Emissions  ∆O3)
  Uncertain epidemiological functions (∆O3  ∆Health)

## Slide 3: Context: AQ model uncertainties
Sensitivities cannot be directly evaluated
Three sources of uncertainty
  Structural: Numerical representation of physical and chemical processes
  Parametric: Input parameters for emission rates, reaction rate constants, deposition velocities, etc.
  Model/User error
New methods to efficiently quantify parametric uncertainty (Tian et al., 2010; Digar and Cohan 2010)

## Slide 4
Probability distribution of pollutant response (ΔC) to emission control (ΔE)
Emis NOx
Emis AVOC
Emis BVOC
RJs
R(NO2+OH)
R(NO+O3)
BC (O3)
BC (NOy)
Parametric Uncertainty of Sensitivities
Reduced form models for efficient Monte Carlo
ΔE
ΔC

## Slide 5: Context: Health effect uncertainties
Ozone linked to respiratory illness, hospital admissions, and mortality
  Mortality link established by three meta-studies (Epidemiology, 2005)
Various concentration-response functions
  Typical form:
  Magnitude and uncertainty of β vary by study
  Reported on 1-, 8-, and 24-hour metrics
No clear evidence of thresholds (Bell et al., 2006)

## Slide 6: Linking Uncertain Sensitivities and C-R Functions
Uncertain
Pollutant Reduction
Uncertain
Beta Distribution
Averted Mortalities per ΔE
Uncertain Health Impact
Uncertain health impact due to uncertain ozone impact (∆C) and C-R function (β)
C

PC,t

## Slide 7: Two Case Studies
Georgia
Episode: July 30 – Aug 15, 2002/9
ΔE: -1 tpd NOx only (ΔO3/ΔEVOC small)
5 Emission Regions: Atlanta, Macon, Rest of Georgia, and 2 power plants
Texas
Episode: Aug 30 – Sept 5, 2006
ΔE: -1 tpd NOx or VOC
4 Emission Regions: Houston Ship Channel (elevated/surface), and Rest of Houston (elevated/surface)

## Slide 8: Input Parameter Uncertainties (φk)
Parameter | Uncertainty | Sigma | Reference
Domain-wide NOx |  40% (1) | 0.336 | a
Domain-wide Anthropogenic VOC |  40% (1) | 0.336 | a
Domain-wide Biogenic VOC |  50% (1) | 0.405 | a
All Photolysis Rates | Factor of 2 (2) | 0.347 | b
R(All VOCs+OH) |  10% (1) | 0.095 | a, b
R(OH+NO2) |  30% (2) | 0.131 | c
R(NO+O3) |  10% (1) | 0.095 | b
Boundary Cond. O3 |  50% (2) | 0.203 | a
Boundary Cond. NOy | Factor of 3 (2) | 0.549 | a
Note: All distributions are assumed to be log-normal
References: aDeguillaume et al. 2007; bHanna et al. 2001; cJPL 2006

## Slide 9: Computing sensitivity under uncertainty
Compute concentrations & sensitivities in base case
Use Taylor series expansions with cross-sensitivities to adjust sensitivities for uncertain inputs:
10,000 Monte Carlo samplings of ϕk to generate probability distribution of sj(1)*
(Cohan et al., ES&T 2005)
(Digar and Cohan, ES&T 2010)

## Slide 10: Computing ΔHealth due to ΔO3
Averted mortality is function of ozone change (ΔC), , and baseline mortality Mt:
Estimates of  and its uncertainty taken from ozone-mortality meta-analysis (Bell et al., JAMA 2004)
Baseline mortality incidence rates Mt (US CDC) and population distributions extracted from BenMAP
Scale by 153/365 for ozone season only benefits
10,000 Monte Carlo samplings of 
Metric | β (ppb-1) | σ(β) (ppb-1)
Daily (24-hour) | 5.18E-04 | 1.25E-04
Daily 1-hour maximum | 3.33E-04 | 6.32E-05
Daily 8-hour maximum | 4.22E-04 | 7.76E-05

## Slide 11: Probability Distribution of Health Benefits
Averted mortalities per ozone season per -1 tpd ΔE
(results averaged over episode and integrated over domain; 8-hour metric)
Results Based on 8-hour max
Uncertain AQ model parameters (phi) generate more uncertainty than uncertain C-R function (β) if temporal metric fixed.
Probability density (averted mortalities-1)
Houston Ship Channel surface NOx
Atlanta NOx

## Slide 12: Rankings on spatial O3 and health metrics
1
3
2
4
5
1
2
3
4
5
Impacts based on 8-hour metric
Atlanta
Macon
Rest of Georgia
Plant McDonough
Plant Scherer
Ranking
Ranking
25%
5%
50%
75%
95%
Deterministic
Spatial Impact Health Impact

## Slide 13: Uncertainty Of Health Benefits
Uncertainties are large relative to median impacts
Outliers driven by uncertainty in ENOx, EbioVOC, and photolysis rates
(Results based on 8-hour metric, with uncertain φ and β)
Houston NOx
Georgia NOx
Houston VOC
Averted mortalities per O3 season per tpd

## Slide 14: Choice of temporal metric influences rankings
Atlanta
Macon
Rest of Georgia
Plant McDonough
Plant Scherer
Atlanta
Macon
Rest of Georgia
Plant McDonough
Plant Scherer
Atlanta
Macon
Rest of Georgia
Plant McDonough
Plant Scherer
24-hr
8-hr
1-hr
1
2
5
3
4
1
2
4
3
5
5
2
1
4
3
Ranking
Averted mortalities per ozone season per 1 tpd ΔE

## Slide 15
Why does temporal metric matter??
Diurnal trends in ozone sensitivities
Cohan et al., ES&T 2005
Urban NOx can titrate surface ozone at night in populated area, reducing 24-hour impacts and leading to the ranking reversals
VOC and elevated or rural NOx yield little nocturnal disbenefit

## Slide 16: Conclusions
Jointly considered how uncertainty in AQ model (parametric) and C-R functions generate uncertainty in ozone health benefit estimates
AQ model uncertainties are leading driver of overall uncertainty in benefit estimation
  Key parameters: ENOx, EbioVOC, and photolysis rates
Urban NOx emissions tend to have larger and more uncertain health impacts
Choice of temporal metric for C-R function can reverse the rankings of per-ton benefits

## Slide 17: Acknowledgments
Funding:
Baseline modeling and emissions data provided by Georgia Environmental Protection Division (B.-U. Kim and J.W. Boylan) and University of Houston (D.W. Byun)
U.S. EPA – Science To Achieve Results (STAR) Program
Grant # R833665