## Slide 1
Standard images are available on the intranet
For more specific images please contact Matthew Hart
For PowerPoint help please contact Elizabeth Leishman
Air Quality Forecasting using WRF and CMAQ
Andrea Fraser, Geoff Dollard, Paul Willis, Trevor Davies, Justin Lingard
AEA, Harwell, UK
9th CMAQ conference October 2010

## Slide 2: Overview
AEA - Air Quality Forecasting
WRF-CMAQ UK Air Quality Forecasting
Summary

## Slide 3
AEA - Air Quality Forecast
AEA have been providing daily forecasts since 1990.
Defra and the Devolved Administrations require a daily UK Air Quality Forecast to both protect public health and to meet specific EC Directive Requirements.
The Directive requires publication of:
  The likely geographical extent of periods of high concentrations.
  The expected change in pollution (improvement, stabilisation or deterioration) and reasons for those changes.

## Slide 4
AEA - Air Quality Forecast
In 2009 a new 3-year contract was let to AEA to provide these daily forecasts.
The new proposal included developing a WRF-CMAQ forecasting model.
Other aspects of the contract include the need to:
  Keep abreast of advances in forecasting air quality and advise Defra and the DAs on possible approaches to improve the forecasts.
  Enhance understanding of the value and role of air quality forecasting in air quality management and public information services

## Slide 5
AQ Forecast Methodology
AEA’s approach is to use a team of air quality experts to compile the forecasts based on a portfolio of inputs.
The team use a daily forecasting protocol and a web-based portal to deliver forecasts 365 days a year.
The inputs include:
  UK optimised AQ forecasting models.
  Pan-European model results.
  Latest UK & European monitoring data.
  Weather forecasts.
  Satellite imagery.
  Expert judgement based on analyses of historical air pollution episodes.

## Slide 6
UK Air Quality Forecast Models
AEA currently uses the WRF- CMAQ to produce daily air quality forecasts for Ozone, PM10, PM2.5, NO2, SO2 and CO. PM2.5 is not yet formally part of the UK AQ Forecasting service.
96 hour air mass back-trajectories are automatically obtained from HYSPLIT each day for UK and cross-channel locations. To assist with source attribution of pollutants during long-range transport episodes.
The UK forecast is compared daily for consistency with the forecasts produced by other European groups.
Ozone Daily max

## Slide 7
Check current conditions
Latest weather forecasts may be 12 hours or more after those used to initiate the model runs so divergence from an earlier forecast is not unexpected.
UK and European monitoring data for the current conditions and the previous 24 hrs. May indicate any unexpected divergence from forecasts which require more investigation

## Slide 8
Satellite Imagery
Useful for identifying the likely source of a pollution episode, or tracking the progress of any unusual events towards the UK.

## Slide 9: Communication
Forecasts are disseminated via the internet , media bulletins and a freephone information service.
Websites are maintained for:
  UK
  Devolved Administrations of Scotland, Wales and N. Ireland
  Local Authorities e.g. Kent and Surry Heath
The forecast is based on the Air Quality Index (1-10) for low-moderate-high- very high
Alert Service

## Slide 10: Communication
Forecasts are disseminated via the internet , media bulletins and a freephone information service.
Websites are maintained for:
  UK
  Devolved Administrations of Scotland, Wales and N. Ireland
  Local Authorities e.g. Kent and Surry Heath
The forecast is based on the Air Quality Index (1-10) for low-moderate-high- very high
Alert Service

## Slide 11: Communication - UK

## Slide 12: Communication - UK

## Slide 13: Communication
Forecast for mobile phones Scotland
Kids corner N. Ireland

## Slide 14
Rapid Response to “Emergency” Situations
Dedicated e-mail and phone contacts for the team.
Carrying out ad-hoc model runs and analysis to investigate the situation
Assisting in drafting press notices or dealing with press enquiries as they happen.
Post event analysis and reporting through short reports for the AQ Archive.

## Slide 15: WRF – CMAQ UK Air Quality Forecast

## Slide 16: WRF – CMAQ UK Air Quality Forecast
AIM:
  10:00 Update the AQ forecast for Today
  14:00 AQ forecast for tomorrow
Operation:
  May 2009 European (48km) 24hr and 48hr forecast
  October 2009 European (48km) and UK (12km) 24hr and 48hr forecast
  January 2010 Started the 50km European and 10km UK forecast
  February 2010 Daily forecasts for both configurations

## Slide 17: WRF-CMAQ Air Quality modelling system
Meteorology Data produced using WRF
(Weather Research and Forecasting) Model
Original 48km and 12km resolution for Europe and the UK.
Now 50km and 10km resolutions
All with 48 vertical layers.
Using GFS initial and boundary conditions
Emissions data
Europe – EMEP - 50km
UK - NAEI - 1km
Biogenic Potential Inventory - 50km
CMAQ (Community Multiscalar Air Quality) Model
  Version 4.7
  CB05 Chemistry with aerosol and aqueous extensions
  Boundary conditions are from the STOCHEM global model
  CMAQ uses the same resolution as WRF, with a slightly smaller grid
  and 25 vertical layers, with 12 layer below 800M
Extract values at monitoring stations
Daily and Monthly evaluation with monitoring data
Create Images
Animations and plots of daily maximum
– O3 NO2 SO2 CO PM10 PM2.5
Ozone Daily max
PM10 Daily Max
SO2 Daily Max
Notes: GFS – global forecast system – a US model available through NCAR

## Slide 18: European Grid – Surface Conditions
48km European Grid 50km European Grid

## Slide 19: European Grid – PM10
48km European Grid 50km European Grid
2006 emissions 2007 emissions

## Slide 20: UK Grid - Ozone
12km UK Grid - 2006 emissions 10km UK Grid – 2007 emissions
Low
Moderate
High
V. High
AQ Index
10 V. High
9
8 High
7
6
5 Moderate
4
3
2 Low
1

## Slide 21: Evaluation of CMAQ AQ Forecast
Daily
  To provide a daily update on model performance for the duty forecaster
  A line plot of provisional observations vs. model for the previous 7 days along with the 24hr and 48hr forecast
  A skill plot to show how well CMAQ has performed in the previous 14 days
  For Rural, Urban Background and Urban monitoring sites.
Monthly
  A monthly evaluation of model performance over the previous month based on provisional observations.
Quarterly
  A repeat of the monthly evaluation based on ratified observations.
  The Monthly and Quarterly evaluations build up a seasonal profile.

## Slide 22: Daily Evaluation
NO2 – Urban Background Sites

## Slide 23: Monthly Evaluation
Rural Ozone - June 2010

## Slide 24: Monthly Evaluation
Rural Ozone - June 2010
UK - 12km resolution, 2006 emissions
UK - 10km resolution 2007 emissions

## Slide 25: PM10 – Urban Background sites
June 2010

## Slide 26: WRF-CMAQ summary
To date
  AEA run a daily 24hr and 48hr WRF-CMAQ Air Quality Forecast
  This is used by the duty forecaster as one of the tools to produce the UK Air Quality Forecast on behalf of Defra and the DA’s
  The evaluation shows that there is a tendency to overestimate ozone and underestimate PM10.
Next stage
  Currently moving to a new cluster
  Update the emission processes
    Inline emissions
    Point sources emissions
    A method to introduce additional sources of emissions
  Extended evaluation
    Europe, speciated PM, and deposition
Look at other opportunities to use the forecast
  Options to downscale the forecast to ADMS or Aermod
  Extend to more days at times of poor air quality

## Slide 27: Summary
AEA have been producing the UK AQ forecast for 20 years.
It is an ‘expert’ forecast using several sources of information.
WRF- CMAQ forecasts for O3, SO2, NO2, CO, PM10 and PM2.5 is one of the tools used by the duty forecaster.

## Slide 28: Thanks to:
The air quality forecasting team
Defra and the DA for there support
Models and Data:
  CMAQ
  WRF
  NCEP – GFS
  EMEP
  UK – NAEI

## Slide 29
Standard images are available on the intranet
For more specific images please contact Matthew Hart
For PowerPoint help please contact Elizabeth Leishman
Thank you
Any Questions?
Andrea Fraser
andrea.fraser@aeat.co.uk

## Slide 30: Monthly Evaluation
Urban Background NO2 – June 2010