## Slide 1
Direct radiative forcing of aerosols and tropospheric ozone from specific emissions sectors and locations
CMAS
10/11/2010
Daven K Henze
University of Colorado at Boulder
Farhan Akhtar, Rob Pinder, Dan Laughlin, US EPA
Robert Spurr, RT Solutions
Kevin Bowman, Adetutu Aghedo, Susan Kulawik NASA JPL
Helen Worden, NCAR
Monika Kopacz, Princeton University
Kumaresh Singh, Virgina Tech
With support from US EPA GLIMPSE and
NASA New Investigator Program.

## Slide 2: Short Lived Climate Forcing Agents
Past: Important for pre-industrial to present radiative forcing
AR4, Forster et al.,
2007
Focus on
direct effects of
- black carbon
- sulfate
- ozone (trop)
Future: Addressing SLCFAs important for immediate
mitigation efforts as well as air quality.

## Slide 3: Systems for modeling air quality & climate change

## Slide 4: Refining the RF bar chart
Sector specific contributions: Fuglestvedt et al., 2008
Unger et al., 2008
Sector and regional specific contributions: Unger et al., 2008

## Slide 5: Systems for modeling air quality & climate change

## Slide 6: Radiative Forcing Transfer Functions
How to calculate the radiative forcing change for
a given change in emissions?
Using transfer function T:

## Slide 7: Radiative Forcing Transfer Functions
How to calculate the radiative forcing change for
a given change in emissions?
Using transfer function T:
Approximate T using adjoint:

## Slide 8: Aerosols and Radiative Forcing
Sensitivities from every sector and region:
Calculated very efficiently using GEOS-Chem adjoint
(Henze et al., 2007 and LIDORT (Spurr, 2002)

## Slide 9: Important Approximations
Macro
- Clear sky
- Only direct effects
- Only SO4-NO3-NH4-H2O and BC aerosol
Micro
- Refractive index of SO4-NO3-NH4-H2O is that of SO4.
- Assumed dry size
- External mixture
Conveniance
- Only July conditions

## Slide 10: Radiative Forcing potential
The % change in radiative forcing per change in emission:
note: per change in any emission. This shows variation
in efficiency of emissions forcing.
%RF / [kg box]
%RF / [kg box]

## Slide 11: Radiative Forcing sensitivities
Results for different SO2 emissions, Ei, for July 2008:
anthropogenic SO2
[%]
anthropogen NH3
The sensitivity of pre-industrial to present RF
with respect to scaling factors for individual emission
sectors

## Slide 12: Radiative Forcing sensitivities
Results for different BC emissions, Ei, for July 2008:
fossil fuel BC
[%]
biofuel BC
The sensitivity of pre-industrial to present RF
with respect to scaling factors for individual emission
sectors

## Slide 13: Applying to global future scenarios: regional and sector-based analysis
% of aerosol direct RF
(CLE 2030 – present) owing to BC emissions
Consider future CLE scenario for 2030 (Kloster et al., 2008)

## Slide 14: Applying to detailed US scenarios see Farhan Akhtar’s poster
Chart: BASE
| 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
Coal | 7560.04 | 7721.68 | 8364 | 9094.94 | 9759.53 | 9804.24 | 10003.47 | 10710.59 | 10974.14
Coal w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas | 3482.65 | 3873.73 | 3677.06 | 3870.3 | 4249.56 | 5202.31 | 6055.07 | 6663.92 | 7721.53
Natural Gas w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Oil | 31.07 | 20.98 | 25.2 | 11.73 | 8.59 | 0 | 0 | 0 | 0
Nuclear | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6
Biomass | 2.8 | 1.88 | 7.47 | 2.59 | 0.78 | 0 | 0 | 0 | 0
Municipal Solid Waste | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 62.04 | 65.1 | 65.1 | 85.28 | 66.66 | 60.54 | 60.54 | 60.54 | 60.54
Hydro | 1145.18 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19
Wind | 155.16 | 157.07 | 158.53 | 191.24 | 160.38 | 185.37 | 174.04 | 181.33 | 188.59
Solar | 9.99 | 12.49 | 12.65 | 12.81 | 1.6 | 1.73 | 1.91 | 1.91 | 1.91
Chart: RCP4.5
| 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
Coal | 7323.05 | 6955.36 | 6991.44 | 7004.59 | 6474.94 | 4912.37 | 3443.89 | 1075.09 | 0
Coal w/CCS | 0 | 0 | 0 | 0 | 0 | 191.13 | 959.46 | 2749.84 | 2655.67
Natural Gas | 3411.99 | 4091.03 | 4326.16 | 4217.74 | 4882.96 | 6400.41 | 7316.69 | 8041.33 | 5615.22
Natural Gas w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 557.95 | 4543.99
Oil | 28.56 | 14.36 | 18.28 | 14.87 | 8.59 | 0 | 0 | 0 | 0
Nuclear | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6 | 2674.6
Biomass | 13.88 | 7.82 | 10.88 | 15.76 | 0.78 | 0 | 0 | 9.42 | 9.42
Municipal Solid Waste | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 62.91 | 65.97 | 65.97 | 176.97 | 404.62 | 544.92 | 544.92 | 544.92 | 544.92
Hydro | 1120.43 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19
Wind | 194.74 | 197.69 | 199.86 | 1089.03 | 1326.99 | 1646.57 | 2371.98 | 2736.42 | 3747.66
Solar | 9.99 | 12.49 | 12.65 | 12.81 | 1.6 | 1.73 | 1.91 | 1.91 | 1.91
Chart: RCP4.5GC
| 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
Coal | 7302.25 | 6847.83 | 5586.75 | 5926.35 | 5534.28 | 3655.2 | 2702.9 | 785.62 | 0
Coal w/CCS | 0 | 0 | 1908.06 | 2231.38 | 2365.22 | 3491.48 | 3592.46 | 5820.46 | 7606.75
Natural Gas | 3403.01 | 4332.45 | 4162.32 | 4194.56 | 4641.02 | 5814.16 | 6374.9 | 6694.24 | 5898.35
Natural Gas w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Oil | 28.75 | 13.71 | 14.14 | 14.87 | 8.59 | 0 | 0 | 0 | 0
Nuclear | 2697.98 | 2712.25 | 2735.24 | 2772.25 | 2831.87 | 2927.89 | 3082.53 | 3331.57 | 3732.66
Biomass | 14.07 | 8.45 | 8.32 | 2.59 | 0.71 | 0 | 0 | 0 | 64.62
Municipal Solid Waste | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 62.91 | 65.97 | 65.97 | 176.97 | 404.62 | 544.92 | 544.92 | 544.92 | 544.92
Hydro | 1119.12 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19 | 1133.19
Wind | 168.02 | 170.26 | 171.97 | 320.37 | 629.54 | 779.28 | 1362.64 | 1410.51 | 2130.53
Solar | 9.99 | 12.49 | 12.65 | 12.81 | 1.6 | 1.73 | 1.91 | 1.91 | 1.91
Consider estimates of US energy usage from MARKAL
Chart: RF (mW/m2)
| 2000.0 | 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
BASE | -79.1225 | -77.1545 | -70.3069 | -68.6805 | -67.2627 | -66.9607 | -67.1938 | -66.9806 | -66.4586 | -66.8625 | -66.873
RCP4.5 | -79.1225 | -77.6801 | -70.7369 | -68.9958 | -67.6046 | -67.0544 | -66.4104 | -65.2162 | -64.1649 | -62.8972 | -62.5951
RCP4.5GC | -79.1225 | -77.3445 | -70.3833 | -68.744 | -66.8926 | -66.0017 | -65.6496 | -64.8656 | -64.2846 | -64.0965 | -64.594
RCP4.5GCBC | -79.1225 | -77.3445 | -70.3833 | -69.0665 | -67.4701 | -66.8006 | -66.616 | -65.9884 | -65.6322 | -65.506 | -66.0603
WARMING
COOLING
Apply RF estimates to BC and SO2 sources

## Slide 15: Validation

## Slide 16: Radiative forcing of tropospheric ozone
3rd most important GHG for pre-industrial to present
radiative forcing
This estimate (0.35 +/-0.15 W/m2) relatively
unchanged since 2nd IPCC
AR4, Forster et al.,
2007

## Slide 17: O3 radiative effect observed from TES
All-sky tropospheric Instantaneous Radiative Forcing
Kernel, IRFK, is change in OLR per change in O3 [ppb]
see Helen Worden’s papers (2008 Nature Geo; JGR submitted)
Aug 2006, land, daytime

## Slide 18: Radiative forcing of tropospheric O3: uncertainty
Variability in model estimated O3 at 511 hPa:
(Aghedo et al., under review JGR)
AM2-Chem
ECHAM5-MOZ
GISS
TES
leads to large biases in OLR relative to TES
AM2-Chem
ECHAM5-MOZ
GISS

## Slide 19: Ozone radiative effect sensitivities
Combine TES IRFK’s with GEOS-Chem sensitivities
GC-adjoint (Henze et al., 2007)
TES
IRFK
results for different emissions, Ei, for Aug 2006:
anthropogenic NOx
[%]
aircraft NOx (x 10)
Notes: \frac{\partial \mbox{radiative effect}}{\partial E_i(x)}=\frac{\partial \mbox{O}_3(z)}{\partial E_i(x)} \times \frac{\mbox{radiative effect}}{\partial \mbox{O}_3(z)}

## Slide 20: Radiative effect efficiencies
Results show amount by which anthropogenic NOx influences O3 that is radiatively important:
Combine O3 sensitivities with RE sensitivities to map
efficiency
Aug, 2006

## Slide 21: Future applications
Consider additional months, seasons.
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> integrate with GLIMPSE screening tool

## Slide 22: Final Remarks
GLIMPSE:
Farhan Akhtar
Rob Pinder
MARKAL:
Dan Loughlin
GEOS-Chem/LIDORT Adjoint:
Daven Henze
GEOS-Chem Adjoint
LIDORT radiative transfer model
Integrated with
MARKAL for the purpose of
Scenario
Exploration
Application of rapid screening tools can help us
understand the relationship between specific policy actions
and the radiative forcing from short lived species.

## Slide 23: the end
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> potential as screening tool

## Slide 24: Validation: BC
CLE 2030 – 2000 perturbation
Looks good

## Slide 25: Validation: SO2
CLE 2030 – 2000 perturbation
Looks OK, but adjoint-approach biased?

## Slide 26: Validation: SO2
10% perturbations
CLE 2030 – 2000 perturbation
Check: does reducing perturbation reduce nonlinearity?
Yes. The adjoint code is accurate.

## Slide 27: Validation: SO2
RF
ESO2
E2000
E’2030
|ADJ| > |FD|
E’’2030
|ADJ| < |FD|
Can we anticipate bias?

## Slide 28: Validation: SO2
CLE 2030 – 2000 perturbation
E2030 > E2000 (China, India)
E2030 < E2000 (Europe )
Yes, bias can be anticipated.
Also, overall ordering remains the same.
Conclusion: adjoint sensitivities provide a rapid means of exploring the effect of specific emissions changes on aerosol DRF.

## Slide 29: Ozone sensitivities using GEOS-Chem adjoint
For example, sensitivity w.r.t. anthropogenic NOx emissions:
Quickly calculate sensitivity of model response w.r.t.
numerous parameters (Henze et al., 2007)
- response J = global average tropospherice O3 column
- parameters Ei = all emissions in all locations
indicate regions of largest influence
source attribution for small changes to emissions
[%]

## Slide 30: Refining the RF bar chart
Sector specific contributions:
Fuglestvedt et al., 2008

## Slide 31: Refining the RF bar chart
Sector and regional specific contributions:
Unger et al., 2008