## Slide 1: Improving transport in AQ models using alternative FDDA techniques
Rob Gilliam, Jim Godowitch and ST Rao
Office of Research and Development
National Exposure Research Lab, Atmospheric Modeling and Analysis Division, Atmospheric Model Development Branch
October 25, 2011

## Slide 2
Even a perfectly designed air quality model will produce poor solutions if meteorological transport fields have excessive uncertainty.
Nocturnal jets and residual layer winds are important features in regional pollution transport that have often been inadequately simulated in the past, thus, a main focus of this study.
An example of the impact: the ozone formed over urban areas during the day can be transported quite differently overnight depending on the meteorological transport.
Why focus on transport?

## Slide 3: Current Transport Issues in WRF
Godowitch et al. (2011)
Recent evaluations of modeled winds in the lower troposphere (<1000 m), have clearly shown biases in wind, which is likely injecting considerable uncertainty in CMAQ’s transport.
Godowitch et al. (2011)

## Slide 4
Can we improve these modeling problem by altering our current nudging techniques? Can new or unused observations improve WRF if used in our FDDA?

## Slide 5
10 m wind
SURFACE ANALYSIS NUDGING Obsgrid: 12 km NAM Analysis (3-hourly) + 10 m wind obs (U10m,V10m)
P-X Soil Nudging Obsgrid: 12 km NAM Analysis (3-hourly) + T2m + Q2m - adjustment of soil moisture and temperature
3-D ANALYSIS NUDGING Obsgrid: 12 km NAM Analysis (3-hourly) + twice daily RAOB, vars --U, V, T, Q
PBL Height

## Slide 6: Unused wind profiler observation are available that could improve FDDA
Velocity Azimuth Display (VAD) Pros: Consistent and full US spatial coverage, sub-hourly and easily accessible Cons: Coarse vertical resolution, can be influenced by birds and precip
UHF Profiler Pros: high vertical (10’s of m) and temporal resolution (sub-hourly), good coverage in the more critical air sheds Cons: inconsistent spacing

## Slide 7: Sensitivity Comparisons
**From Stull (1988)
Main metric is CHANGE in layer-average error
WRF Version 3.3,12 km CONUS, 34 levels, standard US EPA model physics
4 day case, Aug 11-14, 2002
Six sensitivity model simulations
East US high ozone case examined by Godowitch et al. (2011)

## Slide 8: SENS1 vs. BASE Impact of Surface Analysis Nudging
Frequency distribution of wind speed error difference at sites in spatial plots to the left

## Slide 9: SENS3 vs. SENS1 Impact of UHF Nudging

## Slide 10: SENS4 vs. SENS1 Impact of VAD Nudging

## Slide 11: SENS6 vs. SENS5 Impact of RAOB, UHF & VAD Nudging

## Slide 12: Jun-Aug 2006
Wind Speed RMSE (300-1000 m)
Error difference (NewAssim-AQMEII) (300-1000 m)

## Slide 13: Jun-Aug 2006
Wind Speed Bias (300-1000 m)
Change in Bias (300-1000 m)

## Slide 14: Jun-Aug 2006
Wind Dir. MAE (300-1000 m)
NewAssim-AQMEII MAE (300-1000 m)
Change in WD bias (300-1000 m)

## Slide 15: Jun-Aug 2006 Diurnal Statistics
RMSE Wind Speed BASE NewAssim
RMSE Wind Speed
Bias Wind Speed
BASE NewAssim
Bias Wind Speed

## Slide 16: Conclusions
Assimilation of UHF and VAD winds above the PBL were independently shown to improve model representation of the nocturnal jet and residual layer.
Convective boundary layer winds were improved by eliminating all PBL nudging and refining the geostropic forcing at the top of the PBL using UHF and VAD observations; a top down approach.
No PBL nudging will allow PBL models to interact with the land-surface model freely without the artificial nudging.

## Slide 17: Future Work
Investigate other sources of wind and temperature profiles - Aircraft wind, temperature and moisture profiles - Satellite wind - Satellite sounding and radiance data - mesoscale analyses
Show that improvements translate to better air quality model results
Independent verification of our approach from other groups is necessary. Feel free to contact me for detail on data preprocessing.

## Slide 18: Supplementary Slides

## Slide 19: Nudging Sensitivities
4 day case, Aug 11-14, 2002
East US high ozone case examined by Godowitch et al. (2011)
SAN Surface analysis nudging
3D AN 3D Analysis Nudging

## Slide 20: Observational Uncertainty
Observations from RAOB and VAD sites that were in close proximity (39 are collocated) paired in time at the ~500, 750 and 1000 m levels
RMSE, Bias and Index of agreement (IOA) were computed to provide a level of inherent observation uncertainty

## Slide 21: SENS5 vs. SENS1 Impact of UHF & VAD Nudging