## Slide 1: Modeling emission trends for scenarios of the future using MARKAL
Dan Loughlin, Chris Nolte, Bill Benjey
Farhan Akhtar and Rob Pinder
U.S. EPA Office of Research and Development
Daven Henze
University of Colorado
Presented at the 10th Annual CMAS Conference, UNC-CH, Oct. 24-26, 2011

## Slide 2: Purpose of presentation
Describe the use of the MARKet ALlocation (MARKAL) energy system model to develop long-term emission projections for alternative scenarios of the future

## Slide 3: Notes
Abbreviations are defined in the extra slides at the end of the presentation
Results are provided for illustrative purposes only
DISCLAIMER:
  The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. Environmental Protection Agency or the University of Colorado

## Slide 4: Presentation outline
Part 1. Overview of MARKAL
  Assumptions
  Scope and detail
  Outputs
  Use
Part 2. Generating CMAQ-ready future emissions
  Translation of MARKAL emissions into growth-and-control factors
  Use of growth-and-control factors in developing future air quality modeling inventories
Part 3. On the horizon: GLIMPSE
  Example results

## Slide 5
Part 1. Overview of MARKAL

## Slide 6: Overview of MARKAL
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact
Modeling U.S. energy system scenarios with MARKAL

## Slide 7: Overview of MARKAL: Assumptions
Outputs
Technology pathway
Fuel use
Criterial air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact
MARKAL
energy system model
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Baseline assumptions
Data sources include:
U.S. EIA:
Annual Energy Outlook 2010
Commercial Building Energy Consumption Survey
Residential Energy Consumption Survey
Transportation Energy Data Book
U.S. EPA:
eGRID database
AP-42 emission factors
Greenhouse Gas Inventory
Speciate database
Regulatory impact assessments
MOVES model
Other:
Argonne’s GREET model
Scientific literature

## Slide 8: Overview of MARKAL: Scope and detail
Outputs
Technology pathway
Fuel use
Criterial air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact
MARKAL
energy system model
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Primary
energy
Processing and conversion of energy carriers
End-use sectors
Energy system in MARKAL

## Slide 9: Overview of MARKAL: Scope and detail
Outputs
Technology pathway
Fuel use
Criterial air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Energy system in MARKAL
The full energy system diagram represented in MARKAL is much larger than this. For example, the U.S. EPA 9-Region MARKAL database includes:
  98 energy service demands (x9, one for each region)
  346 residential and commercial technologies (x9)
  149 transportation technologies (x9)
  527 industrial technologies across 12 industries (x9)
  48 electricity production technologies (x9)
  38 other conversion technologies (x9)
  462 resource extraction steps
  More than 11,000 components
MARKAL is also an inter-temporal model, representing the energy system in time steps over the 2005-to-2055 time horizon. This allows the evolution of the system to be modeled over a multi-decadal period.

## Slide 10: Overview of MARKAL: Scope and detail
Outputs
Technology pathway
Fuel use
Criterial air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Why energy?
Air quality
Contributions to U.S. anthropogenic emissions:
NOx – 95%
SO2 – 89%
CO – 95%
Hg – 87%
Climate change
Contributes 94% of U.S. anthropogenic CO2 emissions
Water supply and quality
89% of U.S. electricity production uses water for steam or cooling
Represents 39% of U.S. water withdrawals
(agriculture ~ 41%; domestic ~ 12%)

## Slide 11: Overview of MARKAL: Output
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact
Modeling U.S. energy system scenarios with MARKAL
Chart: Electricity production by technology
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal to Existing Steam | 1922.9432 | 2105.1934 | 2187.2351 | 2164.849 | 2137.985 | 2160.6045 | 2214.3045 | 2265.1129 | 2282.5129 | 2298.6185 | 2329.6185
Coal to Existing Steam-CCS Retro | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal to New Steam | 0 | 1.0472 | 1.0472 | 1.0472 | 1.0472 | 1.0472 | 1.0472 | 1.0472 | 1.0472 | 1.0472 | 0
Coal to New Steam-CCS Retro | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal to IGCC | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal to IGCC-CCS Retro | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal to IGCC-CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
NGA to Steam Electric | 103.689 | 5.2056 | 2.775 | 4.0472 | 0.99167 | 0.99167 | 0 | 0 | 0 | 0 | 0
NGA to Combustion Turbine | 4.2194 | 102.9806 | 107.7529 | 109.3973 | 113.8473 | 118.7834 | 123.4973 | 134.5029 | 143.5362 | 151.1362 | 144.6168
NGA to Combined-Cycle | 794.7145 | 621.5172 | 598.4227 | 645.9061 | 773.0117 | 895.6729 | 1042.3147 | 1200.3732 | 1398.0345 | 1611.5235 | 1831.5848
NGA to Combined-Cycle-CCS Retro | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
NGA to Combined-Cycle-CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Coal
Natural gas
Nuclear
Solar
Wind
Hydro
Illustrative results

## Slide 12: Overview of MARKAL: Output
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Regional output
Electricity production by technology
R1 New England
R2 Middle Atlantic
R5 South Atlantic
R6 East South Central
R7 West South Central
R3 East North Central
R4 West North Central
R8 Mountain
R9 Pacific
Illustrative results
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact

## Slide 13: Overview of MARKAL: Output
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Chart: Light duty vehicle technology penetrations
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Conventional GSL-ICE Vehicles | 2642.79 | 2703.63 | 1937.14 | 1276.32 | 211.41 | 0 | 0 | 0 | 0 | 0 | 0
Moderate GSL-ICE Vehicles | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Advanced GSL-ICE Vehicles | 0 | 0 | 672.22 | 1461.57 | 2688.33 | 3108.29 | 3107.74 | 3063.49 | 3060.98 | 3041.69 | 3020.45
Hybrid GSL-ELC Vehicles | 0 | 29.11 | 29.11 | 29.11 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plugin-10 Hybrid Vehicles | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plugin-20 Hybrid Vehicles | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plugin-40 Hybrid Vehicles | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
E85-ICE Vehicles | 7.87 | 5.52 | 3.24 | 1.25 | 0.62 | 0 | 0 | 0 | 0 | 0 | 0
Moderate E85-ICE Vehicles | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Advanced E85-ICE Vehicles | 0 | 0 | 143.15 | 252.25 | 252.25 | 179.89 | 70.79 | 70.79 | 0 | 0 | 0
Hybrid E85-ELC Vehicles | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Plugin-10 E85 Hybrid Vehicles | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Advanced
gasoline
Conventional
gasoline
Electric
E85
E85 plugin hybrid
Diesel
Illustrative results
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact

## Slide 14: Overview of MARKAL: Output
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Chart: Residential efficiency improvements vs. 2005
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Freezing | 0 | 6.5133 | 12.6622 | 18.1167 | 18.1089 | 18.0922 | 18.1256 | 18.1578 | 18.1389 | 18.11 | 18.1078
Lighting | 0 | 1.8133 | 34.6689 | 51.8589 | 55.3578 | 59.2422 | 62.8156 | 66.3278 | 69.7756 | 73.2133 | 76.6667
Electric Appliances | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas Appliances | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Refrigeration | 0 | 8.5156 | 16.7878 | 24.2211 | 25.1 | 28.14 | 31.8778 | 34.7111 | 35.5233 | 35.5178 | 35.5211
Space Cooling | 0 | 3.7522 | 8.8322 | 14.8244 | 18.4656 | 21.0267 | 21.5311 | 20.5333 | 23.0556 | 23.4611 | 23.8444
Space Heating | 0 | 1.0956 | 2.98 | 4.95 | 7.45 | 9.3756 | 11.1478 | 10.8444 | 12.3889 | 12.8978 | 13.2322
Water Heating | 0 | 3.4544 | 4.7189 | 6.0256 | 7.4356 | 8.5944 | 7.2833 | 5.6878 | 5.1778 | 4.7389 | 4.6211
Lighting
Refrigeration
Cooling
Illustrative results
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact

## Slide 15: Overview of MARKAL: Output
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Chart: Residential fuel use
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Fuel Oil-High S | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Fuel Oil-Low S | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Distillate Oil | 877.09 | 792.73 | 768.07 | 779.09 | 773.88 | 755.27 | 695.73 | 663.92 | 634.45 | 606.06 | 548.69
Natural Gas | 5170.66 | 5051.31 | 4947.23 | 5074.87 | 5089.1 | 5055.95 | 5142.64 | 5343.45 | 5288.62 | 5286.82 | 5324.55
LPG | 331.77 | 318.97 | 336.59 | 369.32 | 392.68 | 384.41 | 353.21 | 324.32 | 287.83 | 260.91 | 226.06
Kerosene | 80.06 | 73.98 | 72.38 | 74.36 | 74.67 | 75.38 | 72.18 | 69.72 | 67.39 | 64.99 | 62.57
Biomass | 433.74 | 433.74 | 433.74 | 433.74 | 433.74 | 433.74 | 433.74 | 433.74 | 348.49 | 334.55 | 320.61
Solar | 0 | 8.55 | 37.98 | 45.54 | 46.71 | 48.06 | 49.59 | 64.53 | 83.88 | 108.99 | 141.66
Electricity | 4855.42 | 5051.92 | 5018.63 | 5110.05 | 5387.8 | 5621.44 | 5774.51 | 5847.12 | 6035.93 | 6251.53 | 6476.7
Chart: Commercial fuel use
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Heavy Fuel Oil | 122.07 | 62.87 | 92.73 | 90.05 | 90.3 | 90.87 | 91.51 | 94.97 | 98.54 | 102.24 | 106.08
Light Fuel Oil | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Distillate Oil | 470.64 | 386.27 | 366.61 | 370.9 | 380.6 | 486.95 | 512.55 | 704.2 | 906.68 | 1300.97 | 1456.28
Natural Gas | 2957.72 | 3033.33 | 2900.26 | 3062.39 | 3196.99 | 3254.28 | 3613.21 | 3658.46 | 3737.88 | 3719.04 | 3919
LPG | 93.79 | 82.19 | 90.04 | 91.58 | 93.44 | 95.33 | 97.02 | 99.7 | 102.41 | 105.23 | 108.11
Kerosene | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Biomass | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Solar | 0 | 31.14 | 34.92 | 35.91 | 37.17 | 39.15 | 42.21 | 54.81 | 71.28 | 92.7 | 120.51
Electricity | 5945.12 | 6039.45 | 6139.61 | 6324.67 | 6575.51 | 6997.94 | 7370.26 | 7960.94 | 8565.29 | 9237.74 | 9983.62
Chart: Industrial fuel use
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal | 1183.15 | 1004.3 | 1288.22 | 1270.98 | 1365.71 | 1392.17 | 1311.77 | 1283.07 | 1178.31 | 1187.32 | 1095.54
Fuel Oil-High S | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Fuel Oil-Low S | 287.73 | 236.95 | 288.71 | 303.78 | 383.02 | 387.31 | 443.92 | 448.87 | 446.43 | 480.13 | 352.57
Fuel Oil-Ultra Low S | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Distillate Oil | 107.2 | 89.1 | 104 | 107.51 | 109.45 | 137.25 | 112.7 | 112.46 | 117.26 | 254.19 | 440.79
Gasoline | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas Liquids | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas | 6328.26 | 4438.88 | 5188.01 | 5517.05 | 5130.91 | 4882.24 | 4766.32 | 4940.03 | 4997.79 | 4887.95 | 5182.11
LPG | 2326.64 | 1995.46 | 2229.72 | 2290.67 | 2286.11 | 2310.33 | 2295.66 | 2270.64 | 2300.49 | 2388.19 | 2462.88
Kerosene | 743.88 | 477.92 | 525.77 | 557.53 | 591.46 | 596.94 | 592.11 | 591.61 | 607.54 | 606.12 | 595.36
Other | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Biodiesel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Transportation fuel use
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Diesel | 7760.88 | 7423.88 | 8845.03 | 9451.1 | 9987.07 | 10359.36 | 10829 | 11339.63 | 11945.99 | 12733.9 | 13588.29
Biodiesel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Gasoline | 18319.55 | 18161.45 | 15549.7 | 14591.13 | 12613.66 | 12361.69 | 12242.36 | 12048.62 | 12173.13 | 12362.25 | 12651.76
Ethanol | 315.89 | 440.36 | 1418.09 | 1495.67 | 1714.52 | 1629.41 | 1629.41 | 1714.52 | 1629.42 | 1629.42 | 1629.41
CNG | 61.16 | 60.06 | 65.33 | 92.21 | 126.02 | 169.45 | 218.75 | 248.72 | 283.04 | 314.39 | 348.89
LPG | 49.21 | 37.37 | 30.97 | 25.68 | 24.6 | 23.61 | 24.8 | 26.24 | 27.75 | 29.37 | 31.06
Methanol | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Fuel Oil | 96.2 | 79.23 | 84.59 | 89.39 | 93.56 | 97.65 | 101.63 | 105.67 | 109.86 | 114.19 | 118.72
Jet Fuel | 2777.36 | 2968.99 | 3194.35 | 3422.51 | 3597.05 | 3776.39 | 3945.18 | 4218.22 | 4510.17 | 4822.32 | 5156.06
Bio-Jet Fuel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Electricity | 22.13 | 23.2 | 23.91 | 24.97 | 129.41 | 336.61 | 724.94 | 985.47 | 1183.11 | 1356.21 | 1521.95
Hydrogen | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Electricity
Natural gas
Gasoline
Diesel
Illustrative results
Electricity
Natural gas
Natural gas
Electricity
Biomass
LPG
Jet Fuel
Ethanol
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact

## Slide 16: Overview of MARKAL: Output
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Chart: Air pollutant emissions relative to their 2005 values
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
NOX Total | 1 | 0.82851 | 0.641 | 0.57189 | 0.53712 | 0.50064 | 0.47379 | 0.48444 | 0.49579 | 0.51305 | 0.53025
SO2 Total | 1 | 0.60502 | 0.42339 | 0.34338 | 0.33586 | 0.32121 | 0.31641 | 0.3243 | 0.33409 | 0.3576 | 0.36888
PM10 Total | 1 | 0.96236 | 0.92929 | 0.89433 | 0.87284 | 0.85864 | 0.85136 | 0.86623 | 0.82816 | 0.84355 | 0.85411
PM25 Total | 1 | 0.93954 | 0.87525 | 0.82386 | 0.79821 | 0.78361 | 0.77409 | 0.77958 | 0.689 | 0.69008 | 0.68148
VOC Total | 1 | 0.84705 | 0.66315 | 0.50214 | 0.41313 | 0.36272 | 0.34725 | 0.344 | 0.32527 | 0.32418 | 0.32522
CO Total | 1 | 0.82401 | 0.63535 | 0.50771 | 0.47002 | 0.45071 | 0.4516 | 0.45596 | 0.45322 | 0.45698 | 0.4618
Illustrative results
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact

## Slide 17: Overview of MARKAL: Output
MARKAL
energy system model and
U.S. EPA MARKAL database
Scenario assumptions
Population growth
Economy
Climate change
Technology development
Behavior
Policies
Modeling U.S. energy system scenarios with MARKAL
Chart: GHGs and SLCF emissions relative to their 2005 values
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
CO2 Net | 1 | 0.99594 | 0.99835 | 1.0048 | 0.99018 | 1.002 | 1.028 | 1.0635 | 1.1006 | 1.1475 | 1.1977
SO2 Total | 1 | 0.60502 | 0.42339 | 0.34338 | 0.33586 | 0.32121 | 0.31641 | 0.3243 | 0.33409 | 0.3576 | 0.36888
N2O Total | 1 | 0.87811 | 0.81366 | 0.76062 | 0.73926 | 0.73425 | 0.75422 | 0.77827 | 0.78622 | 0.81281 | 0.83849
CH4 Total | 1 | 0.93766 | 0.89624 | 0.89213 | 0.91241 | 0.94035 | 0.97936 | 1.0252 | 1.0675 | 1.124 | 1.1815
BC Total | 1 | 0.87607 | 0.80344 | 0.64741 | 0.46032 | 0.36286 | 0.2858 | 0.2872 | 0.27964 | 0.29069 | 0.30252
OC Total | 1 | 0.91565 | 0.91027 | 0.86646 | 0.84998 | 0.83774 | 0.82005 | 0.81788 | 0.73212 | 0.72906 | 0.71198
CO2
SO2
N2O
CH4
BC
OC
Illustrative results
Outputs
Technology pathway
Fuel use
Criteria air pollutant
emissions
Greenhouse gas (GHG)
emissions
Short-lived climate
forcer (SLCF) emissions
and radiative impact

## Slide 18: Overview of MARKAL: Application
Use of MARKAL:
What is the technology/fuel pathway that meets energy demands and constraints (e.g., emission limits) at least cost?
What are the resulting fuel use and emission impacts?
How do the least cost pathway, fuel use, and emissions change when scenario assumptions change?
- Alternative assumptions about economic growth
- Adoption of a new policy
Example:
Examining the response to a hypothetical CO2 policy resulting in 35% reduction from 2005 levels by 2050

## Slide 19: Overview of MARKAL: Application
Chart: CO2 emissions
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Transportation | 2192.54 | 2174.13 | 2115.45 | 2106.35 | 2010.27 | 2027.25 | 2063.85 | 2108.56 | 2184.28 | 2282.03 | 2394.84
Residential | 385.07 | 370.58 | 363.89 | 374.18 | 376.13 | 372.35 | 370.32 | 377.01 | 369.1 | 364.86 | 360.07
Commercial | 218.22 | 210.25 | 204.29 | 213.58 | 222 | 233.59 | 255.83 | 273.61 | 294.16 | 324.03 | 347.72
Industry | 775.29 | 658.72 | 748.46 | 789.03 | 796.24 | 812.55 | 818.68 | 851.11 | 890.77 | 947.98 | 1011.46
Electricity Production | 2604.19 | 2736.56 | 2733.02 | 2721.98 | 2710.02 | 2742.07 | 2839.25 | 2957.02 | 3058.1 | 3167.16 | 3282.14
Chart: Electricity production by fuel and type
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal | 6922.59 | 7582.46 | 7877.81 | 7797.22 | 7700.51 | 7781.94 | 7975.26 | 8158.17 | 8220.81 | 8278.79 | 8386.62
Coal w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas | 3923.74 | 3299 | 3200.03 | 3381.47 | 3803.56 | 4271.58 | 4826.58 | 5451.55 | 6229.74 | 7075.4 | 7898.08
Natural Gas w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Oil | 2 | 36.77 | 20.57 | 27.79 | 16.21 | 1.55 | 0 | 0 | 0 | 0 | 0
Nuclear | 2847.63 | 2805.24 | 2847.63 | 2824.3 | 2847.63 | 2847.63 | 2847.63 | 2847.63 | 2847.63 | 2847.63 | 2847.63
Biomass | 0 | 5.98 | 16.51 | 21.49 | 17.2 | 3.7 | 13.34 | 39.24 | 39.24 | 39.24 | 40.91
Municipal Solid Waste | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 75.6 | 45.14 | 81.81 | 85.3 | 122.51 | 179.41 | 181.62 | 181.62 | 181.62 | 181.62 | 181.62
Hydro | 1095.76 | 883.54 | 878.34 | 930.46 | 967 | 1060.71 | 1095.59 | 1106.8 | 1106.8 | 1106.8 | 1106.8
Wind | 477.15 | 541.08 | 903.26 | 958.59 | 1098.57 | 1235.46 | 1249.69 | 970.93 | 1008.65 | 1045.68 | 1045.68
Solar | 12.15 | 51.61 | 85.98 | 94.66 | 97.29 | 89.03 | 93.62 | 121.33 | 157.15 | 203.68 | 264.16
Chart: Fuel inputs to system
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal | 24694.4 | 26782.5 | 28065.9 | 27608.3 | 27650.8 | 27929.8 | 28623 | 29212.7 | 29355.3 | 29661.9 | 29989.9
Natural Gas | 26347.3 | 22689.8 | 21747.5 | 22467.5 | 22615.8 | 23274.4 | 24779.3 | 26592.1 | 28358 | 30003.8 | 32285.3
Natural Gas Liquids | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Crude Oil | 32867.8 | 32759.3 | 31576 | 31575.9 | 29602.3 | 30025.3 | 30692.3 | 31489.6 | 33150.3 | 35575.6 | 38203.9
Petroleum Products | 4655.9 | 3544.2 | 3791.5 | 3696.6 | 4055.3 | 3577.3 | 3014.3 | 2892.3 | 2435.4 | 2033.6 | 1643.8
Uranium | 8603.58 | 8475.49 | 8603.58 | 8533.07 | 8603.58 | 8603.58 | 8603.58 | 8603.58 | 8603.58 | 8603.58 | 8603.58
Renewables | 5163 | 4216.3 | 4927.1 | 5231.7 | 6029.8 | 6858 | 7026.9 | 6126.1 | 6059 | 6142.5 | 6202.9
Other | 9.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Emissions relative to their 2005 values
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
NOX Total | 1 | 0.82851 | 0.641 | 0.57189 | 0.53712 | 0.50064 | 0.47379 | 0.48444 | 0.49579 | 0.51305 | 0.53025
SO2 Total | 1 | 0.60502 | 0.42339 | 0.34338 | 0.33586 | 0.32121 | 0.31641 | 0.3243 | 0.33409 | 0.3576 | 0.36888
PM10 Total | 1 | 0.96236 | 0.92929 | 0.89433 | 0.87284 | 0.85864 | 0.85136 | 0.86623 | 0.82816 | 0.84355 | 0.85411
N2O Total | 1 | 0.87811 | 0.81366 | 0.76062 | 0.73926 | 0.73425 | 0.75422 | 0.77827 | 0.78622 | 0.81281 | 0.83849
CH4 Total | 1 | 0.93766 | 0.89624 | 0.89213 | 0.91241 | 0.94035 | 0.97936 | 1.0252 | 1.0675 | 1.124 | 1.1815
BC Total | 1 | 0.87607 | 0.80344 | 0.64741 | 0.46032 | 0.36286 | 0.2858 | 0.2872 | 0.27964 | 0.29069 | 0.30252
A base scenario
NOx
SO2
PM10
N2O
CH4
BC
Illustrative results
-35%
Electric sector
Transportation
Industrial
Coal
Natural gas
Nuclear
Hydro
Wind
Coal
Natural gas
Oil
Renewables

## Slide 20: Overview of MARKAL: Application
Chart: CO2 emissions
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Transportation | 2192.54 | 2167.68 | 2072.85 | 2009.38 | 1919.33 | 1944.83 | 1990.61 | 2000.58 | 2044.89 | 2106.79 | 2205.12
Residential | 385.07 | 370.05 | 362.96 | 375.33 | 377.81 | 371.8 | 365.93 | 361.62 | 351.12 | 339.16 | 321.29
Commercial | 218.22 | 210.3 | 205.38 | 210.34 | 222 | 235.43 | 251.78 | 258.79 | 261.81 | 264.83 | 252.92
Industry | 775.3 | 713.61 | 729.14 | 759.01 | 771 | 782.07 | 782.74 | 804.86 | 834.69 | 858.19 | 852.19
Electricity Production | 2593.44 | 2698.25 | 2520.45 | 2267.62 | 2062.4 | 1749.27 | 1423.24 | 1119.32 | 783.56 | 438.01 | 375.47
Chart: Electricity production by fuel and type
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal | 6927.75 | 7471.24 | 7151.43 | 6323.18 | 5472.43 | 4542.1 | 3075.09 | 1316.81 | 0 | 0 | 0
Coal w/CCS | 0 | 0 | 0 | 255.11 | 85.59 | 85.59 | 357.51 | 1051.34 | 1840.41 | 1776.5 | 1892.54
Natural Gas | 3864.26 | 3267.87 | 3291.91 | 3498.84 | 4372.71 | 4488.9 | 5016.24 | 5886.58 | 6643.56 | 3772.31 | 3360.16
Natural Gas w/CCS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3094.64 | 3962.15
Oil | 5.05 | 35.82 | 19.53 | 35.33 | 10.98 | 1.55 | 0 | 0 | 0 | 0 | 0
Nuclear | 2847.63 | 2801.07 | 2866.83 | 2655.19 | 3011.06 | 3110.83 | 3271.52 | 3530.31 | 3947.09 | 3947.09 | 3947.09
Biomass | 0 | 5.68 | 15.58 | 36.92 | 24.18 | 9.7 | 20.29 | 20.8 | 27.01 | 34.38 | 59.67
Municipal Solid Waste | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Geothermal | 74.84 | 40.09 | 75.67 | 197.74 | 253.93 | 189.56 | 181.62 | 181.62 | 181.62 | 179.09 | 181.62
Hydro | 1093.89 | 911.25 | 900.23 | 961.56 | 1029.83 | 1073.59 | 1106.8 | 1106.8 | 1106.8 | 989.3 | 953.2
Wind | 477.15 | 530.47 | 976.84 | 979 | 1244.65 | 2750.99 | 2840.47 | 2771.99 | 3089.8 | 4480.68 | 6387.47
Solar | 12.15 | 51.61 | 85.98 | 94.66 | 97.26 | 89.03 | 1137.12 | 2097.62 | 2133.44 | 2179.97 | 2240.45
Chart: Fuel inputs to system
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
Coal | 24679.7 | 26259.1 | 25379.4 | 22643.7 | 19875.1 | 17145 | 14789.5 | 12757.9 | 12020.7 | 11015.6 | 11582.8
Natural Gas | 26143.2 | 22845.1 | 22623.9 | 23794.8 | 25053.5 | 25170.9 | 26365.8 | 28202.9 | 29921 | 31314.9 | 31722.1
Natural Gas Liquids | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Crude Oil | 32867.9 | 33164.7 | 31576 | 31576 | 29602.4 | 30089.1 | 30759.4 | 31453.7 | 32861.1 | 35152 | 37712.1
Petroleum Products | 4666.2 | 3034.1 | 3202.9 | 2726.7 | 2800 | 2262.1 | 1962.5 | 1756.4 | 1567.4 | 1428.6 | 1318
Uranium | 8603.58 | 8462.9 | 8648.27 | 8000.82 | 9062.9 | 9343.26 | 9794.86 | 10522.18 | 11693.5 | 11693.5 | 11693.5
Renewables | 5152.8 | 4249.7 | 4975.4 | 6269.3 | 7542.2 | 8532.1 | 9718.3 | 9930.4 | 10149.7 | 11224.1 | 13115
Other | 9.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Emissions relative to their 2005 values
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
NOX Total | 1 | 0.8308 | 0.64076 | 0.55483 | 0.51456 | 0.46363 | 0.41633 | 0.42832 | 0.45684 | 0.46354 | 0.46196
SO2 Total | 1 | 0.60528 | 0.4233 | 0.32614 | 0.28158 | 0.24262 | 0.21074 | 0.16152 | 0.091347 | 0.069969 | 0.060634
PM10 Total | 1 | 0.96012 | 0.91191 | 0.86162 | 0.81158 | 0.77007 | 0.73424 | 0.72417 | 0.67558 | 0.68119 | 0.66536
N2O Total | 1 | 0.88807 | 0.8082 | 0.7488 | 0.71984 | 0.68654 | 0.70763 | 0.70856 | 0.70323 | 0.70153 | 0.70145
CH4 Total | 1 | 0.93593 | 0.88197 | 0.86047 | 0.89443 | 0.88247 | 0.91742 | 0.9476 | 0.97515 | 0.99915 | 1.0286
BC Total | 1 | 0.8768 | 0.80922 | 0.64967 | 0.46028 | 0.36461 | 0.30003 | 0.27322 | 0.2018 | 0.18238 | 0.17441
A hypothetical CO2 policy scenario
NOx
SO2
PM10
N2O
CH4
BC
Illustrative results
Electric sector
Transportation
Industrial
Coal
Natural gas
Nuclear
Hydro
Wind
Coal
Natural gas
Oil
Renewables
Solar
CCS

## Slide 21
Part 2. Generating CMAQ-ready future emissions
Methodology described and demonstrated in:
Loughlin, D.H., Benjey, W. G., and C.G. Nolte (2011). “ESP v1.0: methodology for exploring emission impacts of future scenarios in the United States.” Geoscientific Model Development, 4, 287-297, doi:10.5194/gmd-4-287-2011.

## Slide 22: Generating CMAQ-ready future emissions
Chart: Regional NOx emissions (kTonnes/yr)
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
EGUs-Coal | 844.309 | 545.215 | 297.102 | 281.763 | 276.097 | 274.496 | 277.062 | 275.937 | 272.331 | 263.586 | 271.241
EGUs-Gas | 21.383 | 41.52 | 29.691 | 32.935 | 37.711 | 41.635 | 38.394 | 39.298 | 43.273 | 51.493 | 51.473
EGUs-Oil | 22.883 | 22.89 | 19.9 | 17.888 | 0.638 | 0.638 | 0 | 0 | 0 | 0 | 0
EGUs-Other | 0 | 0 | 0 | 0 | 0 | 0 | 0.143 | 0.394 | 0.394 | 0.394 | 0.439
Commercial-Gas | 13.554 | 14.149 | 14.665 | 15.746 | 17.027 | 18.246 | 20.145 | 21.643 | 21.667 | 23.234 | 24.763
Commercial-Oil | 3.574 | 2.333 | 2.671 | 2.677 | 2.739 | 4.429 | 5.192 | 5.854 | 9.088 | 10.539 | 12.165
Commercial-LPG | 0.615 | 0.557 | 0.628 | 0.655 | 0.684 | 0.712 | 0.739 | 0.773 | 0.807 | 0.841 | 0.876
Residential-Gas | 19.195 | 19.595 | 19.492 | 19.919 | 21.023 | 21.724 | 22.58 | 27.431 | 28.349 | 28.808 | 29.329
Residential-Oil | 2.798 | 2.654 | 2.657 | 2.787 | 2.852 | 2.861 | 2.85 | 2.789 | 2.729 | 2.661 | 2.589
Residential-Wood | 3.448 | 3.448 | 3.448 | 3.448 | 3.448 | 3.448 | 3.448 | 3.448 | 3.307 | 3.226 | 3.138
Residential-LPG | 5.114 | 4.99 | 4.919 | 5.028 | 5.026 | 4.926 | 4.786 | 4.673 | 4.549 | 4.532 | 4.275
Residential-Kerosene | 4.266 | 4.044 | 4.044 | 4.238 | 4.333 | 4.342 | 4.321 | 4.229 | 4.137 | 4.036 | 3.925
Region 5 (South Atlantic) NOx emissions by MARKAL source category
EGU-Coal
Heavy duty - diesel
Heavy duty - gasoline
Off highway
- diesel
Illustrative results
Rail

## Slide 23: Generating CMAQ-ready future emissions
Step 1.
Annual emissions are summed for each combination of:
  pollutant species
  MARKAL emission category
  Census Division

## Slide 24: Generating CMAQ-ready future emissions
Step 2.
A cross-walk is used to link MARKAL emissions categories to aggregated Source Classification Codes (SCCs)
The MARKAL emissions are allocated fully to each of the matching aggregated SCCs

## Slide 25: Generating CMAQ-ready future emissions
Crosswalk linking MARKAL emission categories with SCC codes
Notes:
“?” is a wildcard that signifies a match with any digit
The crosswalk can be made more specific for shorter-term projections by using less aggregation

## Slide 26: Generating CMAQ-ready future emissions
Step 3. For each aggregated SCC, multiplicative emission growth factors are calculated by dividing future-year emissions by base-year emissions

## Slide 27: Generating CMAQ-ready future emissions
Step 4. Copies of the resulting growth factors are made for each matching combination of:
  pollutant
  SCC
  state within the region
The resulting emissions growth factors are placed in a projection packet in a SMOKE growth-and-control file

## Slide 28: Generating CMAQ-ready future emissions
Step 5. SMOKE is used to apply the growth factors to the base-year inventory to develop a CMAQ-ready future-year inventory
Alternatively, these factors can be used within EPA’s CoST model to develop a projected emissions inventory

## Slide 29: Generating CMAQ-ready future emissions
Results for a baseline scenario, South Atlantic Census Division
Regional growth factors – 2005 to 2055
Changes in daily NOx emissions
Changes in daily PM10 emissions
Illustrative results

## Slide 30: Generating CMAQ-ready future emissions
Important considerations:
How do you apply growth factors to a technology that does not exist in the base year?
How do you site new emission sources?
We address these issues by interpreting MARKAL-projected changes as long-term trends, not source-specific changes
Aggregating by SCC allows us to capture trends by emission category, with the assumptions that (i) all sources in a category will follow the trend of that category, and (ii) new sources in the category will be co-sited with existing sources

## Slide 31
Part 3. On the horizon: GLIMPSE

## Slide 32: What is GLIMPSE?
Goals:
  Screening tool for simultaneous analysis of climate change (radiative forcing) and air quality/health effects of GHGs and short-lived pollutant species
  Rapidly consider tradeoffs between the environmental and climate impacts with mitigation options and costs
Framework links economic and atmospheric models:
  Energy use and production market model of emissions growth and mitigation using MARKAL
  GEOS-Chem/LIDORT Adjoint model for determining the radiative forcing impacts and air quality effects of spatial emissions of SLCFs
GEOS-Chem Adjoint
LIDORT radiative transfer model
Integrated with
MARKAL for the
Purpose of
Scenario
Exploration
Collaborators:
Rob Pinder (EPA/ORD/NERL)
Farhan Akhtar (EPA/ORD/NERL)
Daven Henze (Univ. of Colorado)
Dan Loughlin (EPA/ORD/NRMRL)

## Slide 33: Modifications to MARKAL
Added 20- and 100-year global warming potentials
  for CO2, NOx, SO2, VOC, CO, BC, OC, CH4 and N2O
Added regional direct radiative forcing factors
  for SO2, BC and OC
To do:
  - Add air quality impact factors from CMAQ adjoint
  - Add health impact factors

## Slide 34: Example application of GLIMPSE
Baseline scenario
Chart: Relative to 2010 modeled emissions
| 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
CO2 | 0 | 0.0045834 | 0.031215 | 0.020426 | 0.034572 | 0.06662 | 0.097294 | 0.1363 | 0.18687 | 0.24817
NOX | 0 | -0.085432 | -0.22671 | -0.37764 | -0.46084 | -0.51179 | -0.50089 | -0.48271 | -0.46026 | -0.4291
SO2 | 0 | -0.18049 | -0.40565 | -0.41344 | -0.42039 | -0.43261 | -0.43439 | -0.43445 | -0.43233 | -0.60193
CM | 0 | -0.23646 | -0.30815 | -0.3578 | -0.37861 | -0.36797 | -0.35838 | -0.3528 | -0.34388 | -0.33275
VOC | 0 | -0.2169 | -0.4057 | -0.51111 | -0.56913 | -0.58452 | -0.58577 | -0.5957 | -0.59562 | -0.59555
PM10 | 0 | -0.038913 | -0.10723 | -0.16226 | -0.18808 | -0.21082 | -0.19898 | -0.22109 | -0.21729 | -0.24159
PM25 | 0 | -0.051515 | -0.13466 | -0.2245 | -0.2677 | -0.29984 | -0.29216 | -0.32548 | -0.32485 | -0.33956
CH4 | 0 | -0.041133 | -0.054769 | -0.012423 | 0.02977 | 0.074085 | 0.12961 | 0.17635 | 0.2343 | 0.3018
N2O | 0 | -0.07963 | -0.14078 | -0.16533 | -0.1707 | -0.14571 | -0.12319 | -0.10198 | -0.072767 | -0.040211
BC | 0 | -0.082182 | -0.24989 | -0.48502 | -0.59742 | -0.68356 | -0.68146 | -0.68476 | -0.67565 | -0.66741
OC | 0 | -0.03022 | -0.076751 | -0.065698 | -0.070666 | -0.083044 | -0.070376 | -0.12266 | -0.13098 | -0.18513
Regulated pollutants decrease relative to 2010. Others tend to increase.
CO
Illustrative results

## Slide 35: Example application of GLIMPSE
CO2 policy scenario
Chart: Relative to 2010 modeled emissions
| 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0 | 2055.0
CO2 | 0 | -0.042186 | -0.084371 | -0.12655 | -0.16874 | -0.21092 | -0.25311 | -0.29529 | -0.33748 | -0.33748
NOX | 0 | -0.098661 | -0.24438 | -0.42214 | -0.51516 | -0.5395 | -0.53494 | -0.56236 | -0.57289 | -0.56482
SO2 | 0 | -0.20926 | -0.60325 | -0.59699 | -0.66798 | -0.55968 | -0.64922 | -0.60111 | -0.59122 | -0.986
CM | 0 | -0.23662 | -0.33911 | -0.40102 | -0.43272 | -0.43143 | -0.42988 | -0.43867 | -0.44228 | -0.43901
VOC | 0 | -0.21726 | -0.40644 | -0.51198 | -0.57044 | -0.58616 | -0.58925 | -0.60398 | -0.61558 | -0.62371
PM10 | 0 | -0.06788 | -0.17155 | -0.21587 | -0.25575 | -0.12664 | -0.15224 | -0.15187 | -0.17303 | -0.13403
PM25 | 0 | -0.067565 | -0.16928 | -0.25879 | -0.31185 | -0.27514 | -0.28983 | -0.32457 | -0.35449 | -0.35549
CH4 | 0 | -0.040549 | -0.0032941 | 0.042275 | 0.047608 | 0.095137 | 0.090275 | 0.094667 | 0.14957 | 0.22698
N2O | 0 | -0.075218 | -0.078067 | -0.12498 | -0.15871 | -0.12346 | -0.14777 | -0.1483 | -0.14314 | -0.1021
BC | 0 | -0.082362 | -0.25575 | -0.48794 | -0.59929 | -0.67172 | -0.67347 | -0.73584 | -0.76281 | -0.79234
OC | 0 | -0.05951 | -0.1397 | -0.072233 | -0.068301 | 0.17142 | 0.14637 | 0.16479 | 0.13877 | 0.1939
Different species react differently to the application of the CO2 policy
CO
Preliminary results

## Slide 36: Example application of GLIMPSE
Chart: CO2 equivalent (annual kTonnes)
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
BC | 1213.22 | -479.84 | -542.32 | -4663.52 | -2387.28 | -1513.37 | 8636.33 | 5827.22 | -37966.36 | -64608.89
CH4 | 588.47 | -325.06 | -305.76 | 164.19 | 181.47 | -171.01 | -155.08 | -728.31 | -1131.41 | -1178.86
CM | -3323.63 | -280.39 | -308.16 | -18260.23 | -25395.96 | -31744.99 | -37195.95 | -41892.32 | -50281.38 | -57591.05
N2O | 38.86 | -373.25 | -205.74 | 1710.23 | 989.9 | 81.13 | 398.09 | -1132.6 | -1842.29 | -2638.52
NOX | -3058.61 | -3996.94 | -6362.23 | -6705.71 | -11595.4 | -13272.31 | -7623.68 | -8961.86 | -18364.34 | -25203.29
OC | -589.61 | 1672.62 | 2350.88 | 3112.53 | 1725.56 | 1496.28 | -4801.84 | -3840.77 | -5688.83 | -5262.75
SO2 | 74179.69 | 38365.77 | 48667.41 | 151279.22 | 138869.42 | 183091.64 | 107678.79 | 171936.89 | 140598.4 | 135102.65
VOC | -9.69 | -40.12 | -43.74 | -49.19 | -49.14 | -62.2 | -73.09 | -135.96 | -299.9 | -700.17
Chart: CO2 equivalent (annual kTonnes)
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
BC | 348.8 | -137.94 | -155.93 | -1340.76 | -686.34 | -435.08 | 2482.93 | 1675.32 | -10915.33 | -18575.04
CH4 | 204.32 | -112.86 | -106.18 | 57 | 63.01 | -59.37 | -53.84 | -252.87 | -392.85 | -409.35
CM | -1202.81 | -101.47 | -111.54 | -6608.46 | -9190.91 | -11488.66 | -13461.41 | -15161.02 | -18197.07 | -20842.46
N2O | 40.08 | -384.88 | -212.15 | 1763.51 | 1020.76 | 83.66 | 410.46 | -1167.84 | -1899.69 | -2720.69
NOX | 299.67 | 391.59 | 623.32 | 656.99 | 1136.03 | 1300.33 | 746.9 | 878.02 | 1799.19 | 2469.25
OC | -160.8 | 456.15 | 641.14 | 848.85 | 470.61 | 408.07 | -1309.58 | -1047.5 | -1551.49 | -1435.32
SO2 | 18544.93 | 9591.45 | 12166.85 | 37819.82 | 34717.36 | 45772.91 | 26919.69 | 42984.2 | 35149.61 | 33775.65
VOC | -9.69 | -40.12 | -43.74 | -49.19 | -49.14 | -62.2 | -73.09 | -135.96 | -299.9 | -700.17
Change in annual GWP20
(CO2 policy – baseline)
Change in annual GWP100
(CO2 policy – baseline)
Changes in these emissions have a net warming effect…
CO
CO
Preliminary results
Net
warming
Global warming potential of non-CO2 emissions
Preliminary results

## Slide 37: Example application of GLIMPSE
Chart: CO2 equivalent
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
BC | 1213.22 | -479.84 | -542.32 | -4663.52 | -2387.28 | -1513.37 | 8636.33 | 5827.22 | -37966.36 | -64608.89
CH4 | 588.47 | -325.06 | -305.76 | 164.19 | 181.47 | -171.01 | -155.08 | -728.31 | -1131.41 | -1178.86
CM | -3323.63 | -280.39 | -308.16 | -18260.23 | -25395.96 | -31744.99 | -37195.95 | -41892.32 | -50281.38 | -57591.05
CO2 | -306915.23 | -359662.56 | -630810.15 | -1036939.31 | -1213955.94 | -1543654.95 | -1982939.54 | -2413810.25 | -2895722.47 | -3448372.11
N2O | 38.86 | -373.25 | -205.74 | 1710.23 | 989.9 | 81.13 | 398.09 | -1132.6 | -1842.29 | -2638.52
NOX | -3058.61 | -3996.94 | -6362.23 | -6705.71 | -11595.4 | -13272.31 | -7623.68 | -8961.86 | -18364.34 | -25203.29
OC | -589.61 | 1672.62 | 2350.88 | 3112.53 | 1725.56 | 1496.28 | -4801.84 | -3840.77 | -5688.83 | -5262.75
SO2 | 74179.69 | 38365.77 | 48667.41 | 151279.22 | 138869.42 | 183091.64 | 107678.79 | 171936.89 | 140598.4 | 135102.65
VOC | -9.69 | -40.12 | -43.74 | -49.19 | -49.14 | -62.2 | -73.09 | -135.96 | -299.9 | -700.17
Chart: CO2 equivalent
| 2005.0 | 2010.0 | 2015.0 | 2020.0 | 2025.0 | 2030.0 | 2035.0 | 2040.0 | 2045.0 | 2050.0
BC | 348.8 | -137.94 | -155.93 | -1340.76 | -686.34 | -435.08 | 2482.93 | 1675.32 | -10915.33 | -18575.04
CH4 | 204.32 | -112.86 | -106.18 | 57 | 63.01 | -59.37 | -53.84 | -252.87 | -392.85 | -409.35
CM | -1202.81 | -101.47 | -111.54 | -6608.46 | -9190.91 | -11488.66 | -13461.41 | -15161.02 | -18197.07 | -20842.46
CO2 | -306915.23 | -359662.56 | -630810.15 | -1036939.31 | -1213955.94 | -1543654.95 | -1982939.54 | -2413810.25 | -2895722.47 | -3448372.11
N2O | 40.08 | -384.88 | -212.15 | 1763.51 | 1020.76 | 83.66 | 410.46 | -1167.84 | -1899.69 | -2720.69
NOX | 299.67 | 391.59 | 623.32 | 656.99 | 1136.03 | 1300.33 | 746.9 | 878.02 | 1799.19 | 2469.25
OC | -160.8 | 456.15 | 641.14 | 848.85 | 470.61 | 408.07 | -1309.58 | -1047.5 | -1551.49 | -1435.32
SO2 | 18544.93 | 9591.45 | 12166.85 | 37819.82 | 34717.36 | 45772.91 | 26919.69 | 42984.2 | 35149.61 | 33775.65
VOC | -9.69 | -40.12 | -43.74 | -49.19 | -49.14 | -62.2 | -73.09 | -135.96 | -299.9 | -700.17
Change in annual GWP20
(CO2 policy – baseline)
Change in annual GWP100
(CO2 policy – baseline)
… but this effect is dwarfed by the impact of CO2 reductions
CO
CO
Net
cooling
Global warming potential of all tracked emissions
Preliminary results
Preliminary results

## Slide 38: Next steps
Use GLIMPSE to identify emission control strategies that simultaneously address criteria pollutants, GHGs and SLCFs goals
Identify synergies in technological pathways that efficiently address all three, accounting for regional differences in resources and impacts

## Slide 39: Questions?
For more information…
  Dan Loughlin:
    Loughlin.Dan@epa.gov
    919-541-3928
Also…
  CMAS poster on GLIMPSE by Farhan Akhtar et al.
  Loughlin, D.H., Benjey, W. G., and C.G. Nolte (2011). “ESP v1.0: methodology for exploring emission impacts of future scenarios in the United States.” Geoscientific Model Development, 4, 287-297, doi:10.5194/gmd-4-287-2011

## Slide 40: Extra Slides

## Slide 41: U.S. EPA MARKAL database development team
Name | Roles | Contact Information
Cynthia Gage | Transportation, refrigeration, energy demands | Gage.Cynthia@epa.gov
Tyler Felgenhauer | Integrated assessment modeling, adaptation | Felgenhauer.Tyler@epa.gov
Tim Johnson | Regional assessments, geographic and systems, uncertainty analysis, biofuels | Johnson.Tim@epa.gov
Dan Loughlin | Co-team lead, emissions, light duty vehicles, sensitivity analysis, scenarios | Loughlin.Dan@epa.gov
Carol Shay Lenox | Co-team lead, energy efficiency, database management, model calibration | Lenox.Carol@epa.gov
Rebecca Dodder | Biofuels, renewables, energy & water linkages | Dodder.Rebecca@epa.gov
Ozge Kaplan | Industrial sector, waste-to-energy, biofuels | Kaplan.Ozge@epa.gov
Tai Wu | Software development, GIS | Wu.Tai@epa.gov
William Yelverton | Electric sector, renewables, energy & water linkages | Yelverton.William@epa.gov

## Slide 42: Recent EPA MARKAL database developments
Expanded pollutant provide energy system coverage for:
  CO2, NOx, SO2, PM10, PM2.5, CO, CH4, N2O, VOCs, BC and OC
Reviewing and updating emission factors to be more consistent with recent EPA regulations and modeling
Add factors to track water withdrawals and consumption from electricity production activities
Adding additional biofuels production technologies and improving biomass resource characterization
Revamping characterization of heavy duty transportation technologies (incl. trucks, buses, airplanes, trains, shipping)
Binning existing coal plants by plant age and size, and characterizing emission control options for each bin
Improving characterization of climate change impacts on heating and cooling demands

## Slide 43: Recent and ongoing MARKAL applications
Developing air pollutant emission scenarios for the ORD Global Change Air Quality Assessment
Evaluating alternative biofuels production technologies, and examining tradeoffs associated with using biomass for liquid fuels or in electricity production
Examining the performance requirements and potential impacts of breakthrough technologies
Assessing specific technologies:
  Hydrogen fuel cell vehicles
  Plug-in hybrids
  Advanced nuclear power
  Coal gasification with CCS
  Outdoor wood hydronic heaters
Investigating the role of energy efficiency in meeting greenhouse gas mitigation targets
Examining how technology growth limits impact mitigation pathways and natural gas demands

## Slide 44: Abbreviations
Models and databases:
AP-42 – U.S. EPA compilation of air pollutant emission factors
CMAQ – Community Multiscale Air Quality modeling system
CoST – Control Strategy Tool model
eGRID – Emissions and Generation Resource Integrated Database
GEOS-Chem – 3-D chemical transport model (CTM), driven by input from the Goddard Earth Observing System (GEOS)
GLIMPSE – GEOS-Chem adjoint LIDORT Integrated with MARKAL for the Purpose of Scenario Exploration
GREET – Greenhouse gases, Regulated Emissions, and Energy use in Transportation model
LIDORT – Linearized Discrete Ordinate Radiative Transfer model
MARKAL – MARKet ALlocation energy system model
MOVES – Motor Vehicle Emission Simulator model
SMOKE – Sparse Matrix Operator Kernal Emissions modeling system

## Slide 45: Abbreviations, cont’d
Pollutants and related metrics:
BC – black carbon
CH4 - methane
CO – carbon monoxide
CO2 – carbon dioxide
GHGs – greenhouse gases
GWP20 – 20-yr global warming potential
GWP100 – 100-yr global warming potential
NOx – nitrogen oxides
N2O – nitrous oxide
OC – organic carbon
PM10 – particulate matter of 10 micrometers or less
PM2.5 – particulate matter of 2.5 micrometers or less
SLCFs – short-lived climate forcers
SO2 – sulfur dioxide
VOC – volatile organic compounds

## Slide 46: Abbreviations, cont’d
Technologies and fuels:
CCS – carbon capture and sequestration
CHP – combined heat and power technologies
CNG – compressed natural gas
EGU – electricity generating unit
E85 – blend of approximately 85% ethanol, 15% gasoline
HDV – heavy duty vehicles
IGCC – integrated gasification and combined cycle using coal
LDV – light duty vehicles
LPG – liquid petroleum gas
NGA – natural gas
NGCC – natural gas combined cycle
PV – photovoltaic
Other:
U.S. EIA – U.S. Energy Information Administration
SCC – Source classification code