## Slide 1: Implementing APT Plume-in-Grid and Volatility Basis Set (VBS) Algorithms in CMAQ 5.0
    Bonyoung Koo, Prakash Karamchandani, Greg Yarwood and Jeremiah Johnson
    ENVIRON International Corporation, Novato, CA
    Eladio Knipping and Naresh Kumar
    EPRI, Washington, D.C. and Palo Alto, CA
    10th Annual CMAS Conference, October 24-26, 2011
    Chapel Hill, North Carolina

## Slide 2: Acknowledgements
This work was supported by the Electric Power Research Institute
The U.S. EPA Atmospheric Modeling Development Branch provided access to early alpha and beta versions of CMAQ 5.0 to facilitate community contributions to this new release

## Slide 3: Background
External (community) alternative science contributions to CMAQ usually lag behind official CMAQ release by one or two versions
Example: APT Plume-in-Grid and MADRID aerosol treatments were released in CMAQ 4.6 in August 2009, while CMAQ 4.7 became available in September 2008
With CMAQ 5.0, EPA intends to allow more timely contributions by providing access to early versions of the code to interested model developers
Community contributions can now be part of the initial official release or interim releases

## Slide 4: Scope of Study
Implement Advanced Plume Treatment (APT) for sub-grid scale treatment of point source plumes in CMAQ 5.0
  Available as a community-contributed option in CMAQ up to Version 4.6
  Existing version incompatible with CMAQ re-design for 5.0
Implement Volatility Basis Set (VBS) approach as an alternative option for organic PM
Testing and evaluation of new modules using EPA-provided modeling datasets (ongoing)
Submission of new code and evaluation results to EPA/CMAS for review (pending)
Include as new options in next interim release after submission is approved

## Slide 5: APT Implementation
Update embedded plume model to the most recent version of SCICHEM (v2100, Karamchandani et al.-CMAS, 2010)
Update plume model gas-phase chemistry, aerosol, and aqueous modules for consistency with CMAQ 5.0 beta default options (CB05TUCL, AE6)
Rewrite model interfaces to deal with structural changes to CMAQ (new modules for specification of model species, code re-engineering to increase modularity)
  SCICHEM now uses CMAQ modules and derived data types to build species lists and species properties
  Much tighter integration between CMAQ and SCICHEM
  Updates for future CMAQ versions likely to require less coding effort as long as CMAQ is not re-engineered again
Update host and plume models for point source treatment
  SCICHEM now reads CMAQ in-line point source files directly
  CMAQ does not treat point sources that are simulated with SCICHEM

## Slide 6: VBS Implementation for CMAQ 5.0
Volatility Basis Set Approach
  New approach to modeling organic aerosol formation which uses consistent set of semi-volatile organic aerosol species (the basis set) to represent organic aerosols formed from different precursors
Implementation Issues
  Initial implementation in AERO5 that tracks primary organic mass (POA)
  New AERO6 module tracks POC (carbon mass of POA) and PNCOM (primary non-carbon mass) separately
  Implementation in AERO6 using presumed OM/OC ratios for volatility bins  allocation of POA onto volatility bins not based on emission factors from laboratory data
Emission Input Preparation
  Users need to prepare separate POA emissions for resolved source categories

## Slide 7: VBS Implementation for CMAQ 5.0
Three Volatility Basis Sets
SV_AVB1
SV_AVB2
SV_AVB3
SV_AVB4
SV_BVB1
SV_BVB2
SV_BVB3
SV_BVB4
SV_FVB1
SV_FVB2
SV_FVB3
SV_FVB4
A_AVB1
A_AVB2
A_AVB3
A_AVB4
A_BVB1
A_BVB2
A_BVB3
A_BVB4
A_FVB1
A_FVB2
A_FVB3
A_FVB4
Volatility
Gas-phase
Aerosol-phase
Anthropogenic
Biogenic
Fires
(Aromatics & POA)
(Isoprene, monoterpenes & sesquiterpenes)
(POA from biomass burning)

## Slide 8: VBS Partitioning Properties
Volatility Bin | Molecular Weight | Saturation Concentration (µg/m3) | Enthalpy of Vaporization (kJ/mol)1
1 | 220 | 1 | 30
2 | 205 | 10 | 30
3 | 190 | 100 | 30
4 | 175 | 1000 | 30
4 volatility bins ranging from 1 µg/m3 to 103 µg/m3 in c*
Increasing MW to account for mass gains from aging
1Phthak et al. (2007) Atmos. Chem. Phys., 7, 3811-3821.

## Slide 9: Precursor Oxidation & Chemical Aging
NOx-dependent Aerosol Yields
For aromatics, isoprene & monoterpenes:
E.g., XYLRO2 + NO  NO + 0.001 SV_AVB1 + 0.084 SV_AVB2
+ 0.139 SV_AVB3 + 0.218 SV_AVB4
XYLRO2 + HO2  HO2 + 0.030 SV_AVB1 + 0.129 SV_AVB2
+ 0.173 SV_AVB3 + 0.264 SV_AVB4
Chemical Aging
SV_AVBn + OH  OH + SV_AVBn-1 k = 10-11 cm3 molec-1 s-1
SV_FVBn + OH  OH + SV_FVBn-1 k = 10-11 cm3 molec-1 s-1
No aging for biogenic SOA1
1Murphy and Pandis (2009) Environ. Sci. Technol., 43, 4722-4728.

## Slide 10: POA Emission Factors by Source Category
A_AVB1
A_AVB2
A_AVB3
A_AVB4
A_FVB1
A_FVB2
A_FVB3
A_FVB4
Source Category
POA_GV
POA_DV
POA_OP
POA_BB
Gasoline Vehicle
Diesel Vehicle
Other POA
Biomass Burning
POA emissions (AERO5) from each source category are allocated to volatility bins based on emission factors determined from laboratory experiments for the source
Users need to provide pre-merged POA emissions (POA_??) for each source category
If only merged POA emissions are provided, i.e., emissions inputs include only POA instead of separate POA_??, default emission factors (those of POA_OP) are applied

## Slide 11: Alternate POA Allocation for AERO6
With AERO6, POA emissions are separated into POC (carbon mass of POA) and PNCOM (primary non-carbon mass)
POA emissions (=POC+PNCOM) are allocated to volatility bins based on their POA/POC ratios
Volatility Bin | Assumed OM/OC ratio
1 | 2.0
2 | 1.7
3 | 1.4
4 | 1.1
E.g., If 1.4 ≤ POA/POC < 1.7
x POA  Bin 3 x = ( 2.38 POC / POA – 1.4 ) / 0.3
(1-x) POA  Bin 2
Chemical aging will increase OM/OC ratio

## Slide 12: Challenges/Issues
CMAQ 5.0 alpha received in January 2011
CMAQ 5.0 beta received in May 2011
Significant differences between alpha and beta versions, resulting in some additional code revisions for APT and VBS
Final version of CMAQ 5.0 not yet released; extent of additional code changes, if any, is TBD
The EPA test case, received in August 2011, is very large (CONUS with 12 km resolution: 299 rows, 459 columns, 34 layers)
  Initial efforts to run the Base CMAQ 5.0 beta (w/o APT or VBS) for this domain on two 12-core machines with hyper-threading (48 virtual cores) and 48GB RAM on each machine have been unsuccessful-model crashes in first hour of simulation
  Slower simulation for large domain expected, but crashing is not
  More success in running a windowed domain
  Currently working with EPA to resolve these issues

## Slide 13: Future Steps
Updates for official CMAQ 5.0 release
Resolve issues with base CMAQ CONUS 12-km grid application (if still an issue with official CMAQ 5.0)
Complete testing, debugging and evaluation of APT and VBS modules
Submit to EPA for approval and inclusion in next interim release