## Slide 1: Application of SCICHEM-2012 for 1-Hour NO2 Concentration Assessments
Prakash Karamchandani, Ralph Morris, Greg Yarwood, Bart Brashers, S.-Y. Chen
ENVIRON International Corporation
Eladio Knipping
Electric Power Research Institute
Biswanath Chowdhury, Ian Sykes
Sage Management
11th Annual CMAS Conference, Chapel Hill, NC, October 16, 2012

## Slide 2: Acknowledgements
This work was supported by the Electric Power Research Institute (EPRI)
The American Petroleum Institute (API) provided the AERMOD modeling data sets for the Wainwright, Alaska simulations

## Slide 3: SCICHEM
State-of-the-science reactive puff model, which combines the Second Order Closure Integrated Puff model (SCIPUFF) with a full treatment of gas, particle, and aqueous-phase chemistry comparable to the treatments in CMAQ
Application of model and comparison of model results with aircraft measurements presented at previous CMAS conferences and published (Karamchandani et al., 2000, ES&T)
A version of SCICHEM is embedded in CMAQ 5.01 to provide capability for treating sub-grid scale plumes (presented in yesterday’s session on Model Development)

## Slide 4: SCICHEM-2012
Latest version of model (currently in beta)
Enhancements to the model and testing for reactive species (NOx, O3) as well as long-range tracer transport experiments described by Biswanath Chowdhury earlier in this session
Has capability for both short-range and long-range assessments for primary and secondary pollutants from single sources and multiple sources
Has been adapted to read AERMOD-style input files for short-range assessments and to handle multiple source types (point, area, volume)
Accounts for the effects of building downwash on point source plumes

## Slide 5: Scope of Study
Test SCICHEM-2012 capability for AERMOD-type analysis, focusing on 1-hour NO2 concentrations (this presentation)
Test SCICHEM-2012 capability for single-source air quality assessment for secondary pollutants (ongoing):
  Consequence analysis for ozone, PM2.5, other criteria pollutants
  Comparison of results with those from CALPUFF and CAMx

## Slide 6: 1-Hour NO2 Concentration Assessments
Conducted with both AERMOD and SCICHEM
AERMOD run with and without PVMRM to get NO2 and NOx concentrations for calculating NO2/NOx ratios
SCICHEM calculates NO2 and NOx in a single run
  NO-NO2-O3 chemistry for near-source applications:
  1 [NO2] -> [NO] + [O]
  2 [O] -> [O3]
  3 [O3] + [NO] -> [NO2]
  4 [NO] + [NO] -> (2.0) [NO2]
1-hour NO2 concentrations and NO2/NOx ratios from the two models compared for the simulation period.

## Slide 7: Case Study 1: Wainwright
Power plant located in the North Slope of Alaska
Single monitoring station sited 500 m from the local power plant
NO2, O3 and meteorological variables measured for 12.5 months
Generally low observed O3 concentrations: max hourly O3 is 46 ppb
AERMOD results with PVMRM show no violation of the 1-hour NO2 standard
In-stack NO2/NOx ratio = 0.2
13-month simulation

## Slide 8: AERMOD-Type SCICHEM Input File for Wainwright
****************************************
** AERMOD Control Pathway
****************************************
CO STARTING
TITLEONE Wainwright
TITLETWO hourly O3 data
MODELOPT dfault conc
AVERTIME 1
POLLUTID TRAC
FLAGPOLE 0.00
RUNORNOT RUN
DOMAIN 462129.3 462832.4 7837619. 7837956. 2500.
STARTEND 2009 9 1 1 2010 9 30 1
DELPRJFI NO
MAXPUFFS 25000
MAXMET1D 100
MAXSURFG 25000
TIMEREF LOCAL
MAXTSTEP 900
CO FINISHED
MA STARTING
MA MATCLASS trac Gas
MA DESCRPTN This is ignored
MA DENSITY trac 1.2
MA GASDEPOS trac 0.0
MA DECAYMIN trac 0
DECAYAMP trac 0
MA IMCFILE 'ae5_amb.imc'
MA FINISHED
****************************************
** AERMOD Source Pathway
****************************************
SO STARTING
LOCATION STCK1 POINT 462247.547 7837899.026 11.500
MULTCOMP NO2 NO
SRCPARAM STCK1 1.0e3 9.322 762.928 91.18399 0.229
** Building Downwash **
……..Building parameters (not shown)
HOUREMIS scichem.scn
SRCGROUP ALL
SO FINISHED
****************************************
** AERMOD Receptor Pathway
****************************************
RE STARTING
RE SAMPFILE 'wwright.sam'
DELTSAMP 3600.
RE FINISHED
****************************************
** AERMOD Meteorology Pathway
****************************************
ME STARTING
SURFFILE new_2009-10.SFC
PROFFILE new_2009-10.PFL
SURFDATA 27503 2009 Wainwright 462513.71 7837202.87
UAIRDATA 27502 2009 BARROW/W_POST-W_ROGERS_ARPT
SITEDATA 0 2009
PROFBASE 10.0 METERS
ME FINISHED

## Slide 9: NO2/NOx Ratios vs NOx Concentrations for Wainwright
Chart: AERMOD
Chart: SCICHEM

## Slide 10: CFDs of NO2/NOx Ratios for Wainwright
Chart: NO2/NOx
| 0-0.1 | 0.1-0.2 | 0.2-0.3 | 0.3-0.4 | 0.4-0.5 | 0.5-0.6 | 0.6-0.7 | 0.7-0.8 | 0.8-0.9 | 0.9-1.0
AERMOD | 0 | 0.0016393 | 0.18033 | 0.68197 | 0.89016 | 0.97213 | 0.9918 | 0.99836 | 1 | 1
SCICHEM | 0 | 0.0013661 | 0.21721 | 0.76776 | 0.94809 | 0.97268 | 0.98634 | 0.99044 | 0.99727 | 1

## Slide 11: Case Study 2
Natural gas-fired facility with a Heat Recovery Steam Generator (HRSG) and typical controls
Located in Washington State, adjacent to a major freeway, flat terrain
About 300 m between NOx source and property boundary
Max hourly O3 is nearly 120 ppb
In-stack NO2/NOx ratio = 0.15
Maximum annual 1-hour NO2 concentrations predicted by AERMOD with PVMRM exceed the standard at a fence-line receptor

## Slide 12: NO2/NOx Ratios vs NOx Concentrations for Case Study 2
Chart: AERMOD
Chart: SCICHEM

## Slide 13: CFDs of NO2/NOx Ratios for Case Study 2
Chart: NO2/NOx
| 0-0.1 | 0.1-0.2 | 0.2-0.3 | 0.3-0.4 | 0.4-0.5 | 0.5-0.6 | 0.6-0.7 | 0.7-0.8 | 0.8-0.9 | 0.9-1.0
AERMOD | 0 | 0.0017929 | 0.052891 | 0.077544 | 0.11295 | 0.1515 | 0.20753 | 0.25101 | 1
SCICHEM | 0 | 0.26984 | 0.47619 | 0.62434 | 0.73016 | 0.86772 | 0.95238 | 0.99471 | 1

## Slide 14: Summary of Results
 | AERMOD | SCICHEM
Max. NOx (ppb) | 298 | 240
Max. NO2 (ppb) | 68 | 75
NO2/NOx at Max | 23% | 31%
Average NO2/NOx | 38% | 36%
NOx-weighted average NO2/NOx | 35% | 32%
Wainwright
 | AERMOD | SCICHEM
Max. NOx (ppb) | 109 | 94
Max. NO2 (ppb) | 98 | 16
NO2/NOx at Max | 90% | 18%
Average NO2/NOx | 80% | 36%
NOx-weighted average NO2/NOx | 80% | 29%
Case Study 2

## Slide 15: Conclusions
Successful annual applications of SCICHEM for near-source 1-hr NO2 concentrations using AERMOD inputs
SCICHEM and AERMOD results comparable for Wainwright case study
Very different SCICHEM and AERMOD predictions of 1-hour NO2 concentrations and NO2/NOx ratios for Case Study 2 but NOx concentrations are comparable
SCICHEM predicts significantly lower conversion of NO to NO2 in Case Study 2
Applications for other case studies will provide more data points for comparison