## Slide 1: Analysis of Ultra-Fine Particle (UFP) Measurements of Urban and Rural Sites in Delaware
11th Annual CMAS Conference
October 15-17, 2012
Mohammed A Majeed1, Golam Sarwar2, Michael McDowell1, Betsy Frey1, Ali Mirzakhalili1
1Delaware Dept. of Natural Resources & Environmental Control, Division of Air Quality
2U.S. Environmental Protection Agency, Office of Research & Development

## Slide 2: Outline
Trends in UFP number concentrations
  At MLK and Lewes in Delaware
  Descriptive statistics
  Temporal and spatial variability
    Diurnal variations
    Weekday vs. weekend
    Seasonal
Preliminary analysis of nucleation events
Summary & Future work

## Slide 3: Ultrafine Particles
UFPs are particles
  Diameter < 100 nm
  Occur in large number, but hardly any mass
Most common source
  Dominated by vehicle exhaust in urban areas
Adverse health effects may be closely related to UFPs
Long range transport
  Affect particle number & mass concentrations in urban areas
  Accumulation particles can transport long distances
Nucleation particles
  Survive only a few hours due to coagulation and growth
  Spatial scale of a max of few hundred kilometers
Meteorological conditions and seasonal changes
  Can influence particle number concentrations

## Slide 4: Idealized Schematic for Atmospheric Particle Number Size Distribution
(Hussein, 2005)

## Slide 5: European Union UFP Standards
In 2005 the EU adopted “Clean Air for Europe” program
For light duty vehicles with diesel engines
  6 x 1011 particles/km
  Phased in - 2010 to 2012

## Slide 6
MLK
Lewes

## Slide 7: UFP Monitor (TSI Model 3031-1) & Sampling
TSI 3031-1 Ultrafine Particle Monitor and sampling system
Photo: Ted Allen

## Slide 8
Monitoring Period
  MLK: 11/2009 - 07/2011
  Lewes: 01/2012 - 06/2012
Measurements made in six channels at 15-min intervals
  Channel 1 : 20-30 nm  N30
  Channel 2 : 30-50 nm  N50
  Channel 3 : 50-70 nm  N70
  Channel 4 : 70-100 nm  N100
  Channel 5 : 100-200 nm  N200
  Channel 6 : 200-500 nm  N500
UFP Measurements at MLK & Lewes

## Slide 9: Descriptive Statistics for Similar Periods
MLK 2011 | 25th Percentile | Median | 75th Percentile | Max | Mean | SD
Jan | 26,700 | 36,500 | 54,300 | 127,900 | 41,900 | 21,000
Feb | 20.500 | 32,400 | 49,400 | 174,300 | 38,000 | 24,900
Mar | 12,200 | 19,400 | 29,700 | 187,300 | 23,000 | 15,400
Apr | 12,900 | 19,300 | 28,200 | 79,600 | 22,400 | 13,800
May | 15,200 | 23,000 | 28,300 | 75,600 | 25,400 | 13,100
Jun | 20,500 | 27,300 | 35,600 | 85,900 | 29,800 | 13,100
Lewes 2012 | 25th Percentile | Median | 75th Percentile | Max | Mean | SD
Jan | 5,900 | 9,900 | 15,700 | 47,100 | 11,200 | 6,900
Feb | 8,300 | 12,100 | 16,700 | 32,100 | 12,900 | 6,200
Mar | 6,500 | 9,600 | 15,100 | 54,500 | 11,800 | 7,300
Apr | 12,900 | 12,900 | 19,500 | 64,500 | 15,000 | 9,000
May | 5,800 | 9,100 | 19,500 | 58,300 | 11,800 | 9,000
Jun | 9,200 | 15,900 | 25,800 | 60,000 | 17,900 | 11,100
Total Number Concentration, cm-3.h-1

## Slide 10: Particle Number Comparisons

## Slide 11: Diurnal Pattern of Particle Number Concentration
Hour of Day

## Slide 12
Hour of Day
June 2012
Seasonal Pattern of Particle Number Concentration for Weekdays
Hour of Day
Hour of Day
June 2012

## Slide 13
Hour of Day
Hour of Day
Seasonal Pattern of Particle Number Concentration for Weekends
June 2012
June 2012

## Slide 15: Event Types
Noon Event: 2/07/2010
Three Peaks: 1/18/2010
Morning & Afternoon peaks: 1/27/2010

## Slide 16: Classification of Events
Short - lived
Weak – dN30/dt: 5,000 cm-3 h-1
Moderate – 5,000 < dN30/dt < 10,000 cm-3 h-1
Strong - dN30/dt > 10,000 cm-3 h-1
Event Days at MLK |  |  | 
Year | Month | Moderate | Strong
2011 | Jan | 13 | 10
 | Feb | 10 | 8
 | Mar | 11 | 5
 | Apr | 9 | 3
 | May | 7 | 3
 | Jun | 6 | 4
 | Jul | 2 | 2
Event Days at Lewes |  |  | 
Year | Month | Moderate | Strong
2012 | Jan | 1 | 0
 | Feb | 1 | 0
 | Mar | 1 | 1
 | Apr | 2 | 2
 | May | 1 | 1
 | Jun | 1 | 1

## Slide 17: MLK: Evolution of Number Conc. on Strong Nucleation Days

## Slide 18
Lewes: Evolution of Number Conc. on Strong Nucleation Days
26th May 2012 (Saturday)

## Slide 19: Summary & Future Work
MLK and Lewes data exhibit urban and rural differences in UFP counts
MLK number concentrations are impacted by motor vehicle emissions
  Morning and afternoon peaks are evident
  Weekday and weekend differences are also evident
UFP counts at urban site outnumber those at rural site
Summer UFP counts at Lewes are most likely impacted by motor vehicle emissions
Future Work
Further analysis on classification of events
Meteorological influences on nucleation
Apply the CMAQ model to simulate number concentration