## Slide 1: Integrating source and receptor models for the purpose of emissions inventory improvement: Application to residential wood combustion in the Southeast.
Sergey L. Napelenok, Ram Vedantham,
George A. Pouliot, Prakash V. Bhave, Roger Kwok
U.S. Environmental Protection Agency
Research Triangle Park, NC
11th Annual CMAS Conference
Notes: PVB: I added Michael’s first name and fixed spelling of Sheesley

## Slide 2: Why Residential Wood Combustion?
Primary carbon emissions from this source contribute significantly to PM2.5.
This sector has been identified by NEI developers as one of their top concerns.
Our own modeling shows room for improvement in total carbon (TC) predictions.
Winter bias = 0.10
Summer bias = -2.08
Spring bias = -0.83
Autumn bias = -0.91

## Slide 3: Why Southeast?
Region with highest concentration of carbonaceous PM2.5 in the U.S.
Extensive measurement campaign in 2007
  PM, trace metals, organic tracers, etc.
15 EPA FRM sites available with a fairly complete record of observations of levoglucosan (nsamples = 817)
  Zhang, X., Hecobian, A., Zheng, M., Frank, N. H., Weber, R. J. (2010). Biomass burning impact on PM(2.5) over the southeastern US during 2007: integrating chemically speciated FRM filter measurements, MODIS fire counts and PMF analysis. Atmos Chem Phys 10(14): 6839-6853.

## Slide 4: Summary of Current NEI Total Carbon Emissions
The 2008 NEI has nine distinguishable sources of biomass-combustion-produced carbon emissions.
Fires (wildland + prescribed) dominate the emissions from all 3 states of interest.
Alabama
Georgia
South Carolina
105
103
10
102
104
TC Emissions in 2007 (kg/day)

## Slide 5: Air Quality Model: CMAQ-ISAM
CMAQ v4.7.1 has been equipped with Integrated Source Apportionment Method (ISAM)
  Tracks primary and inorganic secondary particulate matter species by sector, geographical region, and/or chemical precursor.
  Performs very well for primary sources like EC/OC
  Presentation by Roger Kwok – Wednesday 11:20.
Simulation information
  Episode: 1 January – 31 December 2007.
  Inputs: Standard WRF, 2008 NEI, GEOS-Chem boundaries.
  Track the nine carbon sources using CMAQ-ISAM.

## Slide 6: Levoglucosan Source Profiles
To approximate levoglucosan concentrations from CMAQ TC, speciation profiles from emission source tests are used:
  Wood Bark
  Industrial 0.1134 μg levoglucosan / μg C
  Wood Stove (Fine et al., 2002)
  Fire Place
  Waste Leaf
  Land Clear 0.0658 μg levoglucosan / μg C
  House Waste (Lee et al., 2005)
  Fire
  Crop Residue 0.0935 μg levoglucosan / μg C
              (Hays et al., 2002)

## Slide 7
CMAQ-ISAM Apportioned Levoglucosan

## Slide 8: CMAQ-ISAM Apportioned Levoglucosan (2)

## Slide 9: Evaluation of Model Predicted Levoglucosan
 | Mean Obs (ng/m3) | Mean CMAQ (ng/m3) | Mean Bias (ng/m3)
Winter (DJF) | 171.1 | 152.3 | -13.9
Spring (MAM) | 182.1 | 111.4 | -69.0
Summer (JJA) | 20.0 | 34.4 | 15.6
Autumn (SON) | 57.7 | 103.7 | 46.7
Model appears to consistently under predict total PM2.5 from biomass combustion sources at most sites
It would be helpful to split the bias among the various categories of biomass combustion – in other words to apportion the observations

## Slide 10: Unmix 6.0
Receptor models apportion observations to sources.
Unmix version 6.0.
  Constrained multivariate receptor model.
  Input: speciated concentrations.
  Output: source profiles, source contributions, diagnostics, and uncertainties.
  Local, urban, and regional sources.
Traditional applications of Unmix focus on identifying source types with the goal of maximally explaining total PM mass.
  Inputting measured concentrations of levoglucosan and other species (mannosan, galactosan, xylose, potassium, magnesium, nitrate, sulfate, oxalate, WSOC) in a standard application results in one or two sources that can only be explained as “Biomass related.”
    Not too helpful…
  Need to distinguish different sources of biomass burning without source specific molecular markers.

## Slide 11: Unmix Application
We can use CMAQ-ISAM apportioned levoglucosan in addition to total observed levoglucosan as independent species in Unmix to see what the distribution of sources might look like:
Unmix is able to apportion the majority of the observed levoglucosan using 7 distinct factors
Sources of WoodStove and FirePlace are indistinguishable as one factor (1)
Sources of WasteLeaf, LandClear, and HouseWaste are indistinguishable and split between two sources (5 + 7)
The other 4 sources appear to be independent of one another as resolved by Unmix
Source | Factor 1 | Factor 2 | Factor 3 | Factor 4 | Factor 5 | Factor 6 | Factor 7
WoodBark | 2 | 88 | 0 | 0 | 1 | 5 | 4
WasteLeaf | 9 | 1 | 0 | 0 | 30 | 0 | 60
LandClear | 8 | 1 | 0 | 5 | 67 | 5 | 15
Industrial | 2 | 0 | 0 | 0 | 7 | 83 | 9
WoodStove | 92 | 0 | 0 | 3 | 0 | 2 | 2
HouseWaste | 3 | 2 | 0 | 1 | 0 | 12 | 82
FirePlace | 99 | 0 | 0 | 0 | 1 | 0 | 0
CropResidue | 0 | 1 | 1 | 96 | 1 | 0 | 0
Fire | 9 | 0 | 87 | 2 | 1 | 0 | 1

## Slide 12: Bias in Sector Specific Levoglucosan Predictions

## Slide 13: Bias in Sector Specific Levoglucosan Predictions (2)

## Slide 14: Bias in Sector Specific Levoglucosan Predictions (3)

## Slide 15: Bias in Sector Specific Levoglucosan Predictions (4)

## Slide 16: Summary
A new approach for evaluating sector specific emissions
  Combines AQM source apportionment and observation-based source apportionment.
  Allows to further explore possible refinement to various categories of biomass burning in the NEI.
Results are very preliminary, but the method looks promising.
  Too early to make recommendations
  Quantify uncertainty in Unmix output
  Gain confidence in the results by applying other SA models (PMF)

## Slide 17
Contact information:
napelenok.sergey@epa.gov

## Slide 18: Appendix: Unmix Application
samples
species
samples
sources
sources
species
Standard
Unmix
Current
Application
obs
Src
Cont
Source
Profile
ISAM
Src
Cont
Source
Factors
levo
obs