## Slide 1: Potential role of isoprene epoxydiols in organic aerosol formation over the United States
Havala O. T. Pye1, Rob Pinder1, Ying Xie1, Deborah Luecken1, Bill Hutzell1, Golam Sarwar1, Jason Surratt2
1 US Environmental Protection Agency
2 University of North Carolina at Chapel Hill
Office of Research and Development
National Exposure Research Laboratory, Atmospheric Modeling and Analysis Division
15 October 2012

## Slide 2: Current CMAQ Performance
CMAQ underestimates OC compared to surface networks
(especially in summer)
CMAQ 4.7 [Carlton et al. 2010]
Notes: The SOA treatment in CMAQ v5.0 remains largely unchanged from 4.7.1 and indicates a significant underestimate in aerosol phase organic carbon.
CMAQ underestimates OC compared to surface networks in the summer, esp in southeast
tracer based evaluation (Prakash CMAS 2009?) indicates isoprene SOA in particular is underestimated
  check on Carlton CalNex tracer eval (CMAS 2011)
  check on Napelenok Midwest tracer eval (CMAS 2011)
modern vs fossil measurements in a variety of locations emphasize role of modern C
CMAQ underestimate is not necessarily unique: other models have very similar SOA pathways

## Slide 3: Current CMAQ Performance
CMAQ underestimates OC compared to surface networks
(especially in summer)
CMAQ 4.7 [Carlton et al. 2010]
CMAQ 5.0 [Pye and Pouliot 2012]
Notes: CMAQ underestimates OC compared to surface networks in the summer, esp in southeast
tracer based evaluation (Prakash CMAS 2009?) indicates isoprene SOA in particular is underestimated
  check on Carlton CalNex tracer eval (CMAS 2011)
  check on Napelenok Midwest tracer eval (CMAS 2011)
modern vs fossil measurements in a variety of locations emphasize role of modern C
CMAQ underestimate is not necessarily unique: other models have very similar SOA pathways

## Slide 4: Isoprene is a significant contributor to SOA
Isoprene is the largest non-methane VOC emission
Even a small aerosol yield makes isoprene an important SOA source
Isoprene tracers found to account for 7.9% of ambient OC in Yorkville, GA [Lin et al. 2012]
Chart: 
| Isoprene Tracers
2-methyltetrols | 0.33
C5 alkene triols | 0.29
organosulfates | 0.077
dimers | 0.0005
Chart: 
| Total OC | Isop tracer OC
 | 3.96 | 0.34
Total OC
Notes: 725 ng/m3 isoprene tracers

## Slide 5: Isoprene is a significant contributor to SOA
Isoprene is the largest non-methane VOC emission
Even a small aerosol yield makes isoprene an important SOA source
Isoprene tracers found to account for 7.9% of ambient OC in Yorkville, GA [Lin et al. 2012]
Objectives
Explore a new way of modeling isoprene SOA based on recent developments
Determine how the new parameterization differs from the standard parameterization
Chart: 
| Isoprene Tracers
2-methyltetrols | 0.33
C5 alkene triols | 0.29
organosulfates | 0.077
dimers | 0.0005
Chart: 
| Total OC | Isop tracer OC
 | 3.96 | 0.34
Total OC
Notes: 725 ng/m3 isoprene tracers

## Slide 6: CMAQ v5.01 Isoprene SOA (same as v4.7 Carlton et al. 2010, ES&T)
Isoprene + OH
SVISO1
SVISO2
AISO1
AISO2
Odum 2-product
Notes: Figure showing standard pathways to isoprene SOA (same as 4.7.1)
  isoprene + OH leads to initial product formation (no NOx dependence)
  AISO1,2 absorptive partitioning
  AISO3 acid enhancement
  oligomerization

## Slide 7: CMAQ v5.01 Isoprene SOA (same as v4.7 Carlton et al. 2010, ES&T)
Isoprene + OH
SVISO1
SVISO2
AISO1
AISO2
AOLGB
AISO3
H+
H+
Odum 2-product
Acid Enhanced
Oligomerized
Notes: Figure showing standard pathways to isoprene SOA (same as 4.7.1)
  isoprene + OH leads to initial product formation (no NOx dependence)
  AISO1,2 absorptive partitioning
  AISO3 acid enhancement
  oligomerization

## Slide 8: IEPOX as Precursor to SOA
[Surratt et al. 2010, PNAS]
Notes: Recognition of new chemistry: IEPOX
  produced under low-NOx conditions
  Poulot Science 2009
  Surratt PNAS, linkage to 2-methyl tetrols
  acid catalyzes ring-opening of IEPOX (Eddingsaas 2010, McNeill 2012)
  role for water and/or acidity?
  Hlaw vs Kp
other things like high-NOx pathways will not be discussed

## Slide 9: IEPOX as Precursor to SOA
[Surratt et al. 2010, PNAS]
Notes: Recognition of new chemistry: IEPOX
  produced under low-NOx conditions
  Poulot Science 2009
  Surratt PNAS, linkage to 2-methyl tetrols
  acid catalyzes ring-opening of IEPOX (Eddingsaas 2010, McNeill 2012)
  role for water and/or acidity?
  Hlaw vs Kp
other things like high-NOx pathways will not be discussed

## Slide 10: Aerosol from IEPOX Uptake
Why heterogeneous uptake?
  Vapor pressure of IEPOX relatively high (C* > 104 μg m−3)
  Henry’s Law coefficient for IEPOX is large
 | Henry’s Law Coefficient [M atm−1]
HNO3 | 2.1 × 105
Glyoxal | 3.6 × 105
IEPOX | 1.9 × 107 to 9.6 × 108 [Chan et al. 2010]
Notes: Less than a tenth of a percent of iepox partiioning to the aerosol phase under most atmospherically relevant conditions (M<22 ug/m3)
Protonation of the epoxide ring followed by ring opening is likely what leads to tracer compounds like tetrols and triols

## Slide 11: Aerosol from IEPOX Uptake
Why heterogeneous uptake?
  Vapor pressure of IEPOX relatively high (C* > 104 μg m−3)
  Henry’s Law coefficient for IEPOX is large
  Acid catalyzed particle phase reactions can be irreversible
 | Henry’s Law Coefficient [M atm−1]
HNO3 | 2.1 × 105
Glyoxal | 3.6 × 105
IEPOX | 1.9 × 107 to 9.6 × 108 [Chan et al. 2010]
[Eddingsaas et al. 2010]
Notes: Less than a tenth of a percent of iepox partiioning to the aerosol phase under most atmospherically relevant conditions (M<22 ug/m3)
Protonation of the epoxide ring followed by ring opening is likely what leads to tracer compounds like tetrols and triols

## Slide 12: Aerosol from IEPOX Uptake
  CMAQ implementation
    SAPRC07TC chemistry updated to include IEPOX formation as well as greater speciation of nitrates [Xie et al. 2012, ACPD in press]
    Heterogeneous uptake of IEPOX onto accumulation mode aerosol
  g = 0.0029 [Liggio et al. 2005; Lin et al. 2012]
  Simulations for late July-August 2006
IEPOX
AIEPOX

## Slide 13: CMAQ IEPOX Predictions
Gas-Phase IEPOX
Standard Isoprene Aerosol
mgC/m3
Notes: Figure 1: plot of gas-phase IEPOX from gas-only simulation
Figure 2: plot of standard CMAQ isoprene SOA
Same scale: ugC/m3
note the difference in spatial distribution
  IEPOX forms under low NOx conditions and is higher outside urban areas
  standard CMAQ SOA is driven by absorptive partitioning (generally in POA which is higher in urban areas)
  If we make SOA out of IEPOX, what is it’s spatial distribution and how is it influenced by our choice of parameterization?

## Slide 14: CMAQ IEPOX Predictions
Concentration of gas-phase IEPOX indicates significant SOA potential
IEPOX not necessarily highest in locations where we currently predict the most isoprene SOA
  For example: Atlanta, Charlotte
  IEPOX requires low-NOx conditions to form
Gas-Phase IEPOX
Standard Isoprene Aerosol
mgC/m3
Notes: Figure 1: plot of gas-phase IEPOX from gas-only simulation
Figure 2: plot of standard CMAQ isoprene SOA
Same scale: ugC/m3
note the difference in spatial distribution
  IEPOX forms under low NOx conditions and is higher outside urban areas
  standard CMAQ SOA is driven by absorptive partitioning (generally in POA which is higher in urban areas)
  If we make SOA out of IEPOX, what is it’s spatial distribution and how is it influenced by our choice of parameterization?

## Slide 15: Total IEPOX Increase with Uptake
Fractional Increase (With Uptake - Without)/Without
Notes: large fractional increases seen away from IEPOX source regions (aerosol species cannot react with OH so it lives longer)
Atlanta and Charlotte around 150% increase in total IEPOX

## Slide 16: Total IEPOX Increase with Uptake
Total IEPOX (gas+aerosol) increases due to protection against OH reaction
  Lifetime of gas-phase IEPOX against OH ~ couple hours
  Lifetime of gas-phase IEPOX against uptake ~ less than 30 min at peak
Fractional Increase (With Uptake - Without)/Without
Notes: large fractional increases seen away from IEPOX source regions (aerosol species cannot react with OH so it lives longer)
Atlanta and Charlotte around 150% increase in total IEPOX

## Slide 17: New Parameterization Increases total Aerosol OC
Likely to result in improved model performance (reduces underestimate in OC)
Given g uncertainty, not clear if model is improved for the right reason
OC [mgC/m3]
Change in total OC compared to standard isoprene SOA simulation
Notes: california hot spot is in location of fire—large amount of surface area for Iepox uptake

## Slide 18: A Closer Look at the Southeast
IEPOX SOA
[mg/m3]
SouthEastern Aerosol Research and Characterization (SEARCH) Network
http://www.atmospheric-research.com/studies/SEARCH/index.html
Notes: background is IEPOX SOA
Note that Charlotte is a local max in IEPOX SOA even though it was a min in gas-phase production

## Slide 19: Diurnal Variation Different
normalized concentration
Notes: plots normalized to median value at each location
The diurnal variation in the standard and heterogenous pathways is distinctly different
het peaks in morning and declines throughout day (sometimes a PM peak in Alabama sites)
standard generally increases throughout day and peaks around 4-7pm

## Slide 20: Diurnal Variation Different
Heterogeneous SOA typically peaks in AM then decreases, sometimes with an evening peak at the AL sites
Standard SOA increases throughout day and peaks in afternoon/evening
normalized concentration
Notes: plots normalized to median value at each location
The diurnal variation in the standard and heterogenous pathways is distinctly different
het peaks in morning and declines throughout day (sometimes a PM peak in Alabama sites)
standard generally increases throughout day and peaks around 4-7pm

## Slide 21: Diurnal Variation in Standard SOA
normalized concentration
Total semivolatile 2 (AISO2+SVISO2)
Standard Isoprene SOA
POC
Notes: peak late in the day dictated by AISO2 (the lower volatility product) when sun sets, semivolatile from the daytime is still around (more limited removal mechanisms for SV)
IEPOX is removed by OH, note that SV_ISO2 is only removed through deposition so a greater pool or SOA precursor can exist at the end of the day
both het and trad reflect competition between POC/surface area which is minimum in middle of day and photochemical production of precursors which is maximum during the middle of day/afternoon. how the patterns line up dictates where the maximum is

## Slide 22: Diurnal Variation in Standard SOA
influences: (1) production of second semivolatile product, (2) POA, (3) temperature
normalized concentration
Total semivolatile 2 (AISO2+SVISO2)
Standard Isoprene SOA
POC
Notes: peak late in the day dictated by AISO2 (the lower volatility product) when sun sets, semivolatile from the daytime is still around (more limited removal mechanisms for SV)
IEPOX is removed by OH, note that SV_ISO2 is only removed through deposition so a greater pool or SOA precursor can exist at the end of the day
both het and trad reflect competition between POC/surface area which is minimum in middle of day and photochemical production of precursors which is maximum during the middle of day/afternoon. how the patterns line up dictates where the maximum is

## Slide 23: Diurnal variation in IEPOX SOA
normalized concentration/surface area
IEPOX gas
IEPOX SOA
J-mode surface area
Notes: note: AOLGB shows a very similar pattern to AIEPXJ and surface area
AH2OJ decreases significantly throughout day
surface area and APOC show similar pattern

## Slide 24: Diurnal variation in IEPOX SOA
normalized concentration/surface area
influences: (1) aerosol surface area and (2) photochemical production of precursors
IEPOX gas
IEPOX SOA
J-mode surface area
Notes: note: AOLGB shows a very similar pattern to AIEPXJ and surface area
AH2OJ decreases significantly throughout day
surface area and APOC show similar pattern

## Slide 25: Summary
Adding the heterogeneous pathway
  increases total IEPOX compared to a gas-only simulation
  reveals that IEPOX aerosol is important even in urban areas
  leads to more isoprene derived aerosol than standard CMAQ

## Slide 26: Summary
Adding the heterogeneous pathway
  increases total IEPOX compared to a gas-only simulation
  reveals that IEPOX aerosol is important even in urban areas
  leads to more isoprene derived aerosol than standard CMAQ
Heterogeneous uptake differs from the traditional SOA parameterization in terms of
  magnitude of isoprene SOA predicted
  diurnal variation of isoprene SOA
Future work should refine parameters used here and capture additional dependencies