## Slide 1: Application and Evaluation of 2006 NLCD and MODIS in the WRF/CMAQ System Part I: Meteorology Simulations
Limei Ran1,2, Robert Gilliam3, Jonathan Pleim3, Adel Hanna1 , William Benjey3
  1Center for Environmental Modeling for Policy Development, Institute for the Environment
  University of North Carolina at Chapel Hill, NC USA
  2Ph.D. program, Curriculum for the Environment and Ecology, UNC-Chapel Hill
  3Atmospheric Modeling and Analysis Division, ORD NERL/USEPA, Research Triangle Park, NC

## Slide 2: Outline
Background and Objectives
NLCD/MODIS Processing Tools
WRF Simulations and Analysis with:
  Four Landcover Data Sets
  Two different nudging strengths
Conclusion and Future Work

## Slide 3: Background
Consistent and accurate land cover data plays an important role in meteorology and air quality modeling systems such as WRF/CMAQ
Land cover data is used in:
  Land surface models (LSMs) for meteorology modeling to estimate the exchanges of heat, moisture, and momentum between the land surface and the atmosphere
  Bi-directional ammonia flux and dry deposition
  Biogenic emission modeling
  Emission spatial allocation for air quality simulations

## Slide 4: Background
Issue:
Different land cover data sets result in different LU class fractions in modeling grids
Land cover data sets available to WRF/CMAQ:
USGS GLCC data (WRF, BELD3) – global, 1992-1993 AVHRR, at 30-second (~1 km), Anderson LCCS (Loveland et al. 2000)
MODIS IGBP land cover data (2001 in WRF)– global, yearly, 500m and 1km (Friedl et al. 2001)
NLCD 1992, 2001, 2006, US, 30m, modified Anderson LCCS, 30m (Vogelmann et al. 2001, Homer et al. 2004, Fry et al. 2011)
NLCD 2011 is scheduled for release in 12/2013
Houston 1km Domain Grids

## Slide 5: NLCD/MODIS Processing Tools
Current Spatial Allocator release
  2001 USGS-NOAA NLCD/BU-MODIS tool
    Land cover, canopy, and imperviousness, one MODIS file from BU
    Output: 50 land cover classes
New tools developed
  BELD4 Tool: 2001 USGS-NOAA NLCD/BU-MODIS, FIA, NASS, SC-CA
    Land cover, canopy, and imperviousness, one MODIS
    Output: 50 land cover classes, 194 Tree and 42 rainfed /irrigated crop fractions
  2006 NLCD/NASA-MODIS tool
    USGS NLCD and tiled NASA MODIS data in HDF format as input
    Output: 40 land cover classes
Goal: one consistent land use data set
  USGS NLCD, NASA tiled MODIS, FIA, NASS, SC-CA, and other spatial data (e.g. eco-regions, population for better LSM in different regions and urban areas )
  40 land cover classes and tree /crop fractions
  Output data to WPS GeoGrid output file – for WRF simulation

## Slide 6: Objectives
Assess the impacts of different land cover data sets on the WRF/CMAQ modeling system using the PX LSM during the August 2006 TexAQS period
Key features of PX LSM
  Fractional land cover within a grid cell
  Soil moisture and deep soil T nudging
  Connected to CMAQ dry deposition, NH3 bi-directional models
Science questions:
  How sensitive is the WRF system to:
    Land cover data sets with different classification and resolution
    Different nudging strength
  How does CMAQ respond to changes in land cover classification

## Slide 7: Modeling Domains and Configuration, Land Cover Data Sets
Four land cover data sets for each domain:
1992-1993 USGS GLCC land cover data within WRF
2006 NLCD and MODIS Terra and Aqua land cover 500-m (MCD12Q1) IGPB data
2006 MODIS Terra and Aqua land cover 500-m (MCD12Q1) IGPB data
1992 NLCD and 2006 MODIS Terra and Aqua land cover 500-m (MCD12Q1) IGPB data
Observation data:
NOAA’s Meteorological Assimilation Data Ingest System (MADIS) for NA
AQS air quality network data
WRF:
  WRF–ARW V3.4: NCEP 12km NAM analysis and reanalyzed with OBS data using WPS OBSGRID
  Regular and weaker nudging schemes for analysis nudging (W, T, Q) above the PBL and indirect soil moisture and T nudging from 2-m T and Q in the PX LSM (Pleim & Xiu 2003, Pleim & Gilliam 2009)
  Modified the PX LSM for 2006 NLCD and MODIS land cover categories
  Other physics options: ACM2 PBL scheme, the RRTMG radiation model for SW and LW radiation, the Morison cloud microphysics scheme, and the Kain-Fritsch cumulus scheme only on the 12 km and 4 km domains
CMAQ:
  CMAQ v5.0.1 with CB05 gas-phase chemistry, AE6 modal aerosols, 2006 emissions and BELD3 data
  Modified for 2006 NLCD/MODIS and 2006 MODIS land over data

## Slide 8: Meteorology Results: Statistic Summary 2006 - 08/10-09/09

## Slide 9: Meteorology Results: 2006 NLCD (regular nudging)
2m Q: 4km
10m WS: 1km
2m T: 12km
Diurnal Statistics
Mean Bias
2m T: 12km
2m Q: 4km
10m WS: 1km

## Slide 10: 12km Albedo Comparison: 2006-08-31-18Z (2006243)
NLCD:
Too high albedo for
Grassland and Pasture (25, 23)
2006 NLCD
2006 MODIS
MODIS MCD43C3 Albedo, 2006241
NLCD shows more detailed patterns in SW, consistent with MODIS albedo
White sky (Diffuse) SW: 0.3-5.0 µm
Black sky (Direct) SW: 0.3-5.0 µm

## Slide 11: 4km Meteorology Comparison: 2006-08-31-18Z Regular Nudging
ST: 2006 NLCD – 2006 MODIS
2006 NLCD
2006 MODIS
NLCD is cooler with forest cover
Google image

## Slide 12: 1km Meteorology Comparison: 2006-08-31-18Z Regular Nudging
ST: 2006 NLCD – 2006 MODIS
NLCD is much warmer along the coast:
1. Difference of wetland cover
2. Treatment of wetland in the PX LSM
ST: 2006 NLCD – USGS GLCC
PBLH: 2006 NLCD – USGS GLCC
2006 NLCD
2006 MODIS
USGS GLCC
Woody and Herbaceous Wetland

## Slide 13: 4km Meteorology Comparison, 2006-08-31-18Z Weaker Nudging
2006 NLCD: Forest
Changes from same land cover data, different years:
Landuse change
Different sensors and algorithms
Albedo: 2006 NLCD – 1992 NLCD
1992 NLCD: Forest
LAI: 2006 NLCD – 1992 NLCD
Lower albedo for expanded urban areas
Lower LAI and higher albedo due to lower forest fractions

## Slide 14: Conclusions
All WRF simulation evaluation statistics well within typical model performance benchmarks
Land use data sets do matter both spatially and temporally, although nudging (particularly PX LSM soil T and moisture nudging) overpowers some differences
Improve NLCD parameters (e.g. albedo)
Improve wetland treatments in soil moisture modeling
Re-evaluate the modified model
Complete CMAQ simulation and analysis
Release completed Raster Tools through the CMAS and modified LSM through WRF to the community
Assimilate MODIS dynamic vegetation products (e.g. fPAR, EVI, LAI) as well as albedo for better ET estimation
Future Work

## Slide 15: Acknowledgements
Development of the Land use processing tools are funded by:
U.S. EPA under the Contract No. EP-W-09-023, “Operation of the Center for Community Air Quality Modeling and Analysis (CMAS)”