## Slide 1: Quantifying CMAQ Simulation Uncertainties of Particulate Matter in the Presence of Uncertain Emissions Rates
Wenxian Zhang, Marcus Trail, Alexandra Tsimpidi, Yongtao Hu, Athanasios Nenes, and Armistead Russell
CMAS Annual Conference
Oct 17, 2012

## Slide 2: Acknowledgements
U.S. EPA
Southern Company/
Georgia Power
Phillips 66
RD83479901

## Slide 3: Overview
Uncertainties in regional air quality models
Method for uncertainty analysis
- Monte Carlo method
- Reduced-form model based on high-order DDM sensitivity analysis
Quantification of uncertainties in simulated PM2.5 concentrations due to uncertain emissions
Quantification of uncertainties in model response to emissions control in the presence of uncertain emissions
Quantification of uncertainties in first-order sensitivities of PM2.5 due to emission uncertainties

## Slide 4: Uncertainties in Air Quality Models

## Slide 5: How to Quantify Uncertainties?
Original AQM
Concentration 1
Concentration 2
Concentration 3
.
.
.
Concentration N
Sample 1
Sample 2
Sample 3
.
.
.
Sample N
Computationally Expensive!
Uncertainty
Traditional: Monte Carlo Method
Nonroad
Mobile
EGU
Area
Biogenic

## Slide 6
RFM
Concentration 1
Concentration 2
Concentration 3
.
.
.
Concentration N
Sample 1
Sample 2
Sample 3
.
.
.
Sample N
New approach: Monte Carlo Method with reduced-form model (RFM)
Uncertainty
Nonroad
Mobile
EGU
Area
Biogenic

## Slide 7: Reduced-Form Model
CMAQ HDDM-3D
CMAQ
Input
Parameters
Pollutant
Concentrations
RFM
- Constructed based on sensitivity coefficients
- Directly reflects pollutant-parameter response
- Substantially reduces the computational cost

## Slide 8: Evaluation of RFM
[Zhang et al., 2012 GMD]
Nitrate concentration with
50% reductions in domain-wide NOx
Nitrate concentration with
50% reductions in domain-wide SO2

## Slide 9: Air Quality Modeling in Houston Region
36x36 km
12x12 km
4x4 km
Modeling domain
- Nested 4x4km grids
- Houston region, border of
Texas and Louisiana
Episode
- July 12 – 23, 2006
Modeling system
- SMOKE v2.6
- WRF v3.0
- CMAQ v4.7.1 with HDDM

## Slide 10: Model Performance
PM2.5 concentration
July 23, 2006 24-h average
9525 1/2 Clinton Dr
1262 1/2 Mae Drive
4510 1/2 Aldine Mail Rd
Date (July 2006 CDT)
PM2.5 Concentrations (μg m-3)
Model Evaluation
July 12-23, 2006 hourly average
Pollutants | O3 | PM2.5
MOC | 54.8 ppb | 12.8 μg m-3
MB | 1.8 ppb | -1.8 μg m-3
MNB | 7.28% | 10.5%
MNE | 23% | 66.2%
FB | 3.38% | -24.4%
FE | 22.26% | 51%
Performance Metrics

## Slide 11: Emission Uncertainties and Sampling
Log-normal distribution
Emission uncertainty factors
[ E / f, E x f ]
Random sampling with
N = 1000
Source Categories
Source Categories | Uncertainty Factors | References
EGU | 1.03 | Napelenok, 2011
Mobile | 2 | Hanna et al., 2001
Non-road | 1.5 | Chi et al., 2010
Area | 2 | Hanna et al., 2001
Biogenic | 3 | Hanna et al., 2005
E/E0
Sampling Results

## Slide 12: Uncertainties in PM2.5 Simulations
PM2.5 Concentrations (μg m-3)
Uncertainty (%)
Simulated Concentrations (μg m-3)
Concentration Percentiles (μg m-3)
2.5th
97.5th
50th
95% CI of 24-hr average PM2.5
July 23, 2006
Uncertainty of 24-hr average PM2.5
July 23, 2006
[Tian et al., 2010]

## Slide 13: Uncertainties in PM2.5 Response to Emission Controls
Emission reduction in point source
Concentration Reduction (μg m-3)
Emission reduction in mobile source
Larger uncertainty with larger emission reduction
Larger uncertainty for more uncertain sources
δεi - Emission uncertainties ΔEi - Emission reduction

## Slide 14: Uncertainties in First-Order Sensitivity of PM2.5
95% CI of 24-hr average PM2.5
sensitivity to point source emissions
July 23, 2006
Sensitivity Percentiles (μg m-3)
Simulated Sensitivity (μg m-3)
97.5th
50th
2.5th
95% CI of 24-hr average PM2.5
sensitivity to mobile source emissions
July 23, 2006
97.5th
50th
2.5th
Sensitivity Percentiles (μg m-3)
Simulated Sensitivity (μg m-3)
Uncertainty ≤ 36%
Uncertainty ≤ 18%

## Slide 15: Summary
Reduced-form model has been constructed using first- and second-order sensitivities obtained from CMAQ-HDDM-3D
Quantified emission-associated uncertainties of simulated 24-hr average PM2.5
- Lower than 45% in the presence of assumed emission inventory uncertainties
- Does not capture upset emission biases
- Can be easily applied to different combinations of emission uncertainties
Quantified uncertainties of emission control response
- Higher uncertainties with larger emission reductions
- Higher uncertainties for more uncertain emissions
Quantified uncertainties of first-order PM2.5 sensitivities
- Dependent on the uncertainty of the sensitivity parameter
Future studies
- Bias analysis using observations
- Control strategy optimization

## Slide 16: Questions?