## Slide 1: Ammonia Measurements by the NASA Tropospheric Emission Spectrometer (TES)
Karen Cady-Pereira1, Mark Shephard2, Daven Henze3, Juliet Zhu3, Jonathan Wrotny1, Robert Pinder4, John Walker4, John Nowak5, Armin Wisthaler6, Kang Sun7
1. Atmospheric and Environmental Research (AER)
2. Environment Canada
3. University of Colorado
4. Environment Protection Agency (EPA)
5. NOAA/CIRES
6. University of Innsbruck
7. Princeton University

## Slide 2: NH3 Sources
Bi-directional
Flux
AGRICULTURE
Animal waste (temperature dependent)
Fertilizer application
Industry
Fertilizer
Coal Mining
Power generation
Biomass burning
Automobiles (catalytic converters)
Large urban centers
  50% of NH3 in LA area

## Slide 3: NH3 in the atmosphere
Long-range import
Long-range export
PM2.5 Particles
NH3 + HNO3NH4NO3
2 NH3 + H2SO4(NH4)2SO4
Health impacts
Increase number of CCN
Affect cloud radiative properties
Climate change
NH3 forecast to increase

## Slide 4: NH3 from aircraft
NH3 is highly reactive highly variable in space and time
DISCOVER-AQ campaign in January 2013 in the San Joaquin Valley
Aircraft campaigns provide high quality data, but are not feasible for long term monitoring over large areas
~ 2 hours

## Slide 5: TES instrument
flies on NASA Aura (part of the polar orbiting “A-Train”)
launched in July 2004
well calibrated
FTS with a spectral resolution of 0.06 cm-1
5 x 8 km footprint
TES Global Survey Track
Two observation modes:
Global Surveys: 26 hours long, return to starting point every 16 days
Special Observations: higher sampling density over shorter tracks

## Slide 6: NH3 from TES
Simulated TES spectra and NH3 signal
18 ppbv at surface
Detectability is ~ 1 ppbv under ideal conditions
But thermal contrast also plays a role
TES is most sensitive to NH3 between 900 and 700 mbar
1 piece of information or less: DOFS<1.0
Collapse all information to a single point: RVMR
  Easier to compare with in situ measurements

## Slide 7: Surface and TES NH3 in DISCOVER-AQ 2013
TES and QCL NH3 measured in Tipton area in January 2013 are spatially well correlated
Open path Quantum Cascade Laser (QCL) on a moving platform collected data almost directly under TES transect (red symbols) in the San Joaquin Valley on January 28, 2013
Hotspot measured near Tipton

## Slide 8: TES and aircraft NH3 from DAQ
January 21
January 30
P3B aircraft @ 500 m
TES maximum sensitivity between 1 and 2 km

## Slide 9: CalNex 2010: California spring
CalNex: Campaign focused on air quality and climate change
  Aircraft and surface measurements and TES transects
    Central Valley, southern California basin, Pacific Ocean

## Slide 10: TES NH3 Validation
North Carolina
Intense livestock farming (hogs, chickens, turkeys)
EPA CAMNet NH3 monitoring network
TES high spatial density observations (transects)
Feb – Dec 2009
Allows detection of spatial variability and seasonal trends
CHALLENGE
  TES: instantaneous profile over 5x8 km
  CAMNet: two week average at a surface point
  Cloudy summers!

## Slide 11: Seasonal and spatial variability
NH3 vs time
NH3 vs source concentration
TES and surface measurements are qualitatively well correlated
Pinder et al., GRL, 2011

## Slide 12: Eastern China: 2007-2009
Surface NH3
Seasonal means from TES
TES NH3
TES transect path
Beijing
Beijing
Beijing
Shangdianzi
Meng et al., ACP, 2011
Shangdianzi

## Slide 13: South Asia: July-August 2007
Indus River Valley
High NH3 north of New Delhi and in the northern Indus valley

## Slide 14: Global NH3 results
TES NH3 RVMR from GS: 2006-2009
Shephard et al., ACP, 2011
Large increase between NH winter and summer
Hotspot over India
Biomass burning signal over South America and Africa

## Slide 15: Better emissions with TES NH3
Largest changes western US and Mexico
Used GEOS-Chem adjoint with TES NH3 profiles, averaging kernels and error covariances to optimize model
Optimized GC shows better agreement with AMoN network measurements
Zhu et al., 2013, JGR

## Slide 16: Final comments
Limitations
  TES is sensitive to only higher amounts (> 1.0 ppbv) of NH3
  Requires some thermal contrast to detect NH3
  Clouds reduce amount of useful data
TES data
  Show seasonal and spatial variability consistent with in situ measurements
  Have greater temporal and spatial coverage than aircraft campaigns or surface networks
  Used in an inverse modeling framework improved agreement between GEOS-Chem output and AMoN measurements
TES NH3 data available at:
  http://avdc.gsfc.nasa.gov/index.php?site=635564035&id=10&go=list&path=/NH3
  netcdf files with all NH3 retrievals for each month since September 2004

## Slide 17: Acknowledgements
  Markus Mueller and Tomas Mikoviny from the PTR instrument team
  PICARRO instrument team
  TES team at JPL
  Research was supported by
    the Jet Propulsion Laboratory, California Institute of Technology under contract to the National Aeronautics and Space Administration (NASA).
    CU support from NASA grant NNX10AG63G and EPA-STAR RD83455901

## Slide 18: TES NH3 and CO
Monthly NH3 RVMR
July 2010
Aug 2010
Sept 2010
Monthly CO at 681 hPa
NH3 from TES V005 operational product
Biomass burning in South America is evident in both CO and NH3 maps
High NH3 values over northern India

## Slide 19: CALNEX: TES vs Aircraft
TES May 14 transect @13:15 local
Partial P3 May 12 track
(flying at ~ 300 AGL @ 17:30 local)
NH3 measurements from TES and aircraft are well correlated

## Slide 20: Day vs Night: TES
DAY
Lower NH3 values
Sensitivity peaks between 900 and 750 mbar
NIGHT
Greater range of NH3 values
  More high values
Sensitivity peaks between surface and 900 mbar
Collapse of boundary layer
Pooling of NH3
CMAQ simulated
NH3 profile

## Slide 21: And now …
NH3
Shephard et al.[2011]