## Slide 1: Development of an Ozone Screening Tool for the Midwest
Alexander Cohan1, Scott Leopold2, Greg Yarwood3, Kirk Baker4
1LADCO
2Illinois EPA
3ENVIRON
4U.S. EPA
10/30/13

## Slide 2: Motivation
July 2010 - Sierra Club petitions EPA to designate air quality models for PSD permitting
January 2012 – EPA grants Sierra Club’s petition and commits to updating the Guideline on Air Quality Models (Appendix W)
Regional photochemical modeling is best science for addressing ozone impacts, but computational intensive and impractical for routine permitting
Regulators would like an easy to use screening tool to assess the ozone impact of stationary sources for PSD permitting applications

## Slide 3: Reduced Form Models
Use regional photochemical model results to develop a simplified localized framework
  Equivalency Ratio (Margaret McCourtney, MPCA)
  Interpollutant Trading Ratios (James Boylan, Georgia EPD)
  Response Surface Model (Carey Jang, EPA)
  Parametric Model (Greg Yarwood, ENVIRON)

## Slide 4: Background
Parametric Model (Yarwood, 2011)
  Screening tool developed for Sydney
    3 Km CAMx higher-order direct decoupled method (HDDM) simulations of the summer
    Assumptions:
      Ground source
      Located at center of
      emissions by mass
Yarwood, G., Scorgie, Y., Agapides, N., Tai, E., Karamchandani, P., Bawden, K., Spencer, J., Trieu, T, 2011. A screening method for ozone impacts of new sources based on high-order sensitivity analysis of CAMx simulations for Sydney. Proceedings, 10th Annual CMAS Conference, Chapel Hill, NC.

## Slide 5: Background
Base Emission Inventory
Single Point Emissions
CAMx
CAMx
Base Met
Base Ozone
Ozone W/ Point Source
HDDM Ozone Sensitivities
–
BF Ozone Impact
HDDM Ozone Impact
+
2nd order Taylor series
2nd Order Taylor Series

## Slide 6: Problem Statement
Question: How do ozone sensitivities to emission rates vary with emission rate and stack characteristics?
Approach: Use multiple CAMx HDDM simulations of individual point sources to train a statistical model to empirically relate

## Slide 7: Statistical Models
Potential statistical models
  CART
  Neural network
  Kriging
  Fixed-Effects
  Response Surface Model
Fixed-Effects (FE)
  Represents observed quantities in terms of explanatory variables that are treated as if the quantities were non-random
  Transparent and easy to implement

## Slide 8: Methodology
A linear parametric fit will not work!
Sensitivities behave like Gaussian plume
Seinfield & Pandis (1998)

## Slide 9: Methodology
  Sources to the left or right might behave differently…
  Use binomial expansion for α
  Fit parametric equation at each grid cell
  Solve for P1…P11 using R to minimize mean square error

## Slide 10: Methodology
Proof of concept conducted for test case in Illinois
Based on LADCO 2007 Modeling platform
4 km CAMx HDDM modeling of summer 2007

## Slide 11: Methodology
20 hypothetical point sources modeled with HDDM
  Stack diameter is linearly related to stack height (SH)
  Exit velocity of 44 ft/s
  Exit temperature 70 °f

## Slide 12: Methodology
FE Model
R
Model Fit
P1 … P11
HDDM Ozone Sensitivities PT01
ENOx , EVOC , x , y, SH
HDDM Ozone Sensitivities PT20
HDDM Ozone Sensitivities PTXX
ENOx , EVOC
FE Ozone Impact
2nd Order Taylor Series
2nd Order Taylor Series
HDDM Ozone Impact
FE Approach
HDDM Approach
FE Ozone Sensitivities

## Slide 13: Methodology
FE Model
R
Model Fit
P1 … P11
HDDM Ozone Sensitivities PT01
ENOx , EVOC , x , y, SH
HDDM Ozone Sensitivities PT20
HDDM Ozone Sensitivities PTXX
ENOx , EVOC
FE Ozone Impact
2nd Order Taylor Series
2nd Order Taylor Series
HDDM Ozone Impact
FE Approach
HDDM Approach
FE Ozone Sensitivities
Screening Tool

## Slide 14: Sensitivities from CAMx HDDM vs. FE
CAMx HDDM
FE Model

## Slide 15: Training Data Point 2
ENOx = 718 tpy, EVOC = 61 tpy, SH = 120 ft

## Slide 16: Training Data Point 5
ENOx = 80 tpy, EVOC = 197 tpy, SH = 48 ft

## Slide 17: Training Data Point 6
ENOx = 943 tpy, EVOC = 70 tpy, SH = 454 ft

## Slide 18: Training Data Point 9
ENOx = 610 tpy, EVOC = 25 tpy, SH = 194 ft

## Slide 19: Training Data Point 18
ENOx = 380 tpy, EVOC = 51 tpy, SH = 268 ft

## Slide 20: Testing Point 1
ENOx = 143 tpy, EVOC = 143 tpy, SH = 71 ft
Notes: 24

## Slide 21: Testing Point 2
ENOx = 6 tpy, EVOC = 292 tpy, SH = 177 ft
Notes: 21

## Slide 22: Testing Point 3
ENOx = 165 tpy, EVOC = 192 tpy, SH = 83 ft
Notes: 23

## Slide 23: Summary
FE matches HDDM training data well
FE/HDDM matches BF in magnitude and extent of impact, however BF produces a higher peak impact
FE Model would benefit from additional training data

## Slide 24: Future Work
Investigate differences in peak impact predicted from BF and HDDM
Examine different VOC profiles
Explore other statistical models
Apply methodology to develop PM screening tool

## Slide 25: Acknowledgments
Scott Leopold – IL EPA
Greg Yarwood – ENVIRON
Kirk Baker – OAQPS
Margaret McCourtney – MN PCA
Randall Robinson – EPA Region 5
Mark Derf – IN DEM

## Slide 26: 20 HDDM Modeled Point Sources

## Slide 27: LADCO 2007 Modeling Platform
Ozone Performance