## Slide 1
HCHO and NO2 column comparisons between OMI, GOME-2 and CMAQ
during 2013 SENEX campaign
Hyun Cheol Kim 1,2, Li Pan 1,2, Pius Lee 1, Rick Saylor 3, and Daniel Tong 1,2
1 NOAA/Air Resources Laboratory, College Park, MD
2 UMD/Cooperative Institute for Climate and Satellites, College Park, MD
3 NOAA/ARL/Atmospheric Turbulence and Diffusion Division, Oak Ridge, TN

## Slide 2: Background
Monitoring NO2 is important to investigate locations of natural and anthropogenic NOx emission sources, and chemical regimes according to Ozone-NOx-VOC chemistry.
HCHO is a common intermediate product from the degradation of volatile organic compounds (VOCs), it can be used as a proxy to monitor emissions of VOCs from biogenic, biomass burning, and anthropogenic sources.
Monitoring the spatial and temporal variability of VOC emissions in the southeast US region is crucial to understanding control processes in this region’s air quality, especially for ozone and secondary organic aerosols productions.

## Slide 3: The Goal of this presentation
How to compare space-born satellite measurements to fine scale regional chemistry model simulations
  How to resolve variable resolution issues
  Characteristics of different species
  Retrieval uncertainties
To discuss the Impact by different footprint pixel sizes for different satellite instruments and even within the same instrument.
NO2 and HCHO column comparisons during SENEX compaign (preliminary)

## Slide 4: NO2 & HCHO observations from space
Instrument | Satellite | Local pass | Resolution | Data
GOME | ERS | 10:30 LT | 320x40 km | 1996-2003
SCIAMACHY | ENVISAT | 10:00 LT | 30x60 km | 2002-2012
OMI | Aura | 13:30 LT | 13x24 km | 2004-
GOME-2 | MetOp-A MetOp-B | 09:30 LT | 40x80 km | 2007- 2013-

## Slide 5: NO2 and HCHO columns (CMAQ & Satellite)
CMAQ NO2
GOME-2 NO2
CMAQ HCHO
GOME-2 HCHO
Problems: Cannot capture fine-scale details (NO2), Retrieval is very noisy (HCHO)

## Slide 6: Method 1: Conservative remapping
f2
P1
P2
P3
P4
f1
f4
f3
Cj
Cj = (P1·f1+P2·f2+P3·3+P4·f4)/(f1+f2+f3+f4)
Overlapping fractions (fi,j) are calculated using IDL-based Geospatial Data Processor (IGDP)

## Slide 7: Method 2: Downscaling (DS)
where ki,j is the spatial weighting kernel of Pi in the position of Cj
GOME-2 NO2 raw pixels
CMAQ NO2 column
Spatial weighting kernel
Downscaled GOME-2 NO2 column
Each spatial weighting kernel is satellite pixel-specific, so the quantity in the original pixel never propagates out of original data pixel’s coverage

## Slide 8: Powered by IDL-based Geospatial Data Processor (IGDP)
Developed by NOAA/ARL funded by TCEQ/AQRP.
Fast and accurate polygon, polyline, and pixel data processing capability
Conservative conversion (e.g. regridding) between different map projections and domain settings.
GIS, model comparison
Emission processing (e.g. surrogate files)
Polygon, polyline, and pixels (GIS, Satellites, Emission)
Gridded world (Model)
IGDP

## Slide 9: Monthly averaged NO2 column S. California Aug. 2008
GOME-2
GOME-2/ds
CMAQ (09:30LT)
OMI
OMI/ds
CMAQ (13:30LT)

## Slide 10: How downscaling method works
Satellite measurement is strictly preserved within each footprint. Strength of model does not affect satellite measurement’s strength at all.
The only information that passed from model to satellite is relative spatial information within each satellite footprint.
Eventually, this method converts systematic negative bias due to coarse resolution to random errors, which can be cancelled out by temporal averaging.

## Slide 11
CMAQ
GOME-2
GOME-2/ds
Small-scale features are well reconstructed by downscaling method
Monthly mean NO2 columns (Jul 2011)
CMAQ, GOME-2, Adjusted GOME-2

## Slide 12
Monthly mean NO2 columns (Jul 2011)
CMAQ, OMI, Adjusted OMI
CMAQ
OMI/ds
OMI
Since OMI has better resolution than GOME-2, the adjustment effect in small that GOME-2 case, but it still shows clear improvement in urban cities.

## Slide 13: Difference (CMAQ-Sat)/Sat [%]
(CMAQ-GOME2)/GOME2
Resolution Adjusted
(CMAQ-OMI)/OMI
Resolution Adjusted

## Slide 14: HCHO column CMAQ & GOME-2 (Jul 2011)

## Slide 15: HCHO column comparison (CMAQ & GOME-2)
Difference (CMAS-GOME2)
% Difference (12km)
% Difference (108km)
% Difference (36km)

## Slide 16: Preliminary comparison with SENEX
Poster by Pan et al.
The SENEX campaign targets the investigation of the interactions between natural and anthropogenic emissions and their impact on air quality and climate change.
To support this field campaign, NOAA/Air Resources Laboratory provides high horizontal grid resolution (4km) CMAQ model simulations covering the Southeast U.S. to conduct a post-campaign analysis.

## Slide 17: NO2 column comparison (06/10~07/18 average)
CMAQ
GOME-2
GOME-2/ds
CMAQ (09:30LT)
OMI
OMI/ds
CMAQ (13:30LT)

## Slide 18: Time series comparison (domain average)
CMAQ NO2 column is mostly underestimated

## Slide 19: HCHO column comparison (06/10~07/18 average)
CMAQ 12km
CMAQ 108km (upscaled)
GOME-2 (12km)
GOME-2 (108km)

## Slide 20
Time series comparison (domain average)
CMAQ HCHO column is mostly overestimated

## Slide 21: Summary
We introduce conservative reconstruction method to compare coarse resolution satellite observation to fine-scale regional chemistry model simulations
For NO2 column and surface concentration, the downscaling method provides better agreement with fine scale regional simulation
Upscaling works better for HCHO due to its smoother spatial distribution and noises in satellite retrieval
SENEX aircraft comparison will be followed

## Slide 22: End

## Slide 23: Diurnal variation
Figure 7. Surface NO2 concentration diurnal variation over 70 AQS sites, (a) for Jan. 2008, and (b) for Aug. 2008. Blue line indicate CMAQ NO2 concentration in the 1st layer, gray dots represent AQS surface NO2 observations. GOME-2-inferred surface NO2 concentrations are shown in red rectangles (closed: DS+CR method, open: CR method), and OMI-inferred surface NO2 concentrations are shown in blue triangles (closed: DS+CR method, open: CR method).
(a)
(b)

## Slide 24: Surface NO2 comparison
GOME-2 inferred surface NO2 = (GOME-2 column / CMAQ column ) * CMAQ surface NO2