## Slide 1: Summary of the Emission Inventories compiled for the AQMEII Phase 2 Simulations
George Pouliot, Christian Hogrefe, Ryan Cleary,
Junhua Zhang, Mike Moran,Paul Makar, Shawn Roselle, Rohit Mathur
Office of Research and Development
National Exposure Research Laboratory Atmospheric Modeling and Analysis Division
October 29 2013
12th Annual CMAS Conference, Chapel Hill NC
October 29, 2013

## Slide 2: What is AQMEII?
AQMEII – Air Quality Modeling Evaluation International Initiative
Promote research on regional air quality model evaluation across the European and North American atmospheric modeling communities
Exchange of information on practices
Realization of inter-community activities
Identification of research priorities
First Workshop was held in April 2009; most recent was the 5th workshop in August 2013

## Slide 3: What is AQMEII Phase 2?
Build credibility for coupled models and provide a better representation of feedback processes,
aerosol, radiation, and cloud interactions and changes in air quality-climate interactions
Large reduction in the emissions of SO2 and NOx from both electric power and motor vehicle sectors in the United States and Europe during the past 20 years.
Examine coupled regional-scale models’ ability to properly simulate the changes observed in surface radiation, temperature, and concentrations from emission reductions from regulatory programs implemented in North America and Europe over the past few decades

## Slide 4: Purpose of this presentation
Analysis of emissions used in modeling exercise to help the understanding of the model results (dynamic evaluation)
Provide an idea of what types of analysis we are doing in conjunction with the rest of the AQMEII phase 2 project
Focus on US (and NA) in the presentation, but hope to do joint analysis with EU
Extend what was done in phase 1 emissions paper:
“Comparing emission inventories and model-ready emission datasets between Europe and North America for the AQMEII project” (Pouliot et al, 2012)

## Slide 5: Emission Inventories
Emission Inventories prepared for 2006 and 2010 for the modeling simulations will be compared
Some of the Comparisons:
  Changes in Criteria pollutants between 2006 and 2010
  Compare with EPA Trends data (Caution!)
  Compare 2006 AQMEII phase 2 with AQMEII phase 1
Focus on NOx and SO2 emissions for this presentation but will include some of the other criteria pollutants.

## Slide 6: US Sectors Used for NA Emissions in Phase 2
Emissions supplied for 12 US sectors typically used by U.S. EPA for regulatory modeling
Source Type | Description
afdust | Area source fugitive dust from anthropogenic sources, PM10 & PM2.5 only
ag | Area source emissions from agricultural operations, NH3 only
agfire | Area source emissions from crop residue burning
c1c2rail | Area source emissions from aircraft, locomotive, and marine (except class 3 vessels) (Aircraft includes only takeoff, landing, and ground operations.)
c3marine | Commercial marine port and inter-port Class 3 (C3) vessels defined as having displacement greater than 30 liters per cylinder.
nonpt | Area source emissions not included in other sectors (e.g., residential wood combustion)
nonroad | Off-road mobile source emissions from EPA’s National Mobile Inventory Model (NMIM)
onroad | On-road mobile source emissions using SMOKE/MOVES system
ptipm | Electric generating unit (EGU) point source emissions, includes Continuous Emission Monitoring (CEM) hourly data
ptnonipm | Non-EGU point source emissions (industrial source and no power generation)
ptfire | Wildland fires and prescribed burning fire emissions modeled as point sources
rwc | Residential Wood Combustion

## Slide 7: Canada/Mexico Sectors Used for NA Emissions in Phase 2
Emissions supplied for 8 sectors typically used by U.S. EPA for regulatory modeling
Source Type | Description
canafdust | 2006 Canada Area source fugitive dust from anthropogenic sources, PM10 & PM2.5 only
canag | 2006 Canada Area source emissions from agricultural operations, NH3 only
canar | 2006 Area source emissions not included in other sectors including nonroad from Canada excluding c3marine emissions (included in US inventory); also included are c1c2 marine emissions, rail emissions, and aircraft emissions
canon | 2006 Canada On-road mobile source emissions
canpt | 2006 Canada point source emissions
Mexar | 1999 Mexico area sources
mexon | 1999 Mexico onroad sources
mexpt | 1999 Mexico point sources

## Slide 8: 2006 North American Emissions
Comprised of data from the United States, Canada, and Mexico
Primary basis: U.S. EPA’s 2008 National Emission Inventory, version 2 (NEIv3), translated onto the 2007/2008 modeling platform described in EPA’s Technology Transfer Network Clearinghouse for Inventories and Emissions Factors (TTN/CHIEF)
2006-Specific Updates for AQMEII:
  2006 Continuous Emission Monitoring (CEM) data of SO2 and NOx from major point sources
  2006 wildfires (US only), daily with hourly plume rise
  2006 Canadian emissions and spatial surrogates
  2005 MOVES emission factors with 2006 VMT (US only)
Pollutants: NOx, VOC, CO, SO2, NH3, PM2.5, and PM10

## Slide 9: 2010 North American Emissions
Comprised of data from the United States, Canada, and Mexico
Primary basis: U.S. EPA’s 2008 National Emission Inventory, version 2 (NEIv3), translated onto the 2007/2008 modeling platform described in EPA’s Technology Transfer Network Clearinghouse for Inventories and Emissions Factors (TTN/CHIEF)
2010-Specific Updates for AQMEII:
  2010 Continuous Emission Monitoring (CEM) data of SO2 and NOx from major point sources
  2010 wildfires (US only), daily with hourly plume rise
  2009 MOVES emission factors with 2010 VMT (US only)
Pollutants: NOx, VOC, CO, SO2, NH3, PM2.5, and PM10

## Slide 10: Processing of NA Emissions for Phase 2 (EPA)
Emission Processing
  Performed using SMOKE system version 3.0
  Temporal allocation:
    Hour-specific for major point sources equipped with Continuous Emission Monitors (CEM), wildfire emissions, and biogenic emissions
    Annual emissions allocated to individual hours based on source-specific monthly, weekly, and diurnal factors
  Speciation:
    VOC speciated both for the CB-05 and SAPRC07 mechanism based on source-specific profiles
    Primary PM2.5 emissions split into sulfate, nitrate, EC, OC, and other primary PM2.5
  Spatial allocation:
    12km by 12km modeling grid using a Lambert Conformal projection
    Used 60+ spatial surrogates (population, roadways, railroads, ports, etc.) to perform source-specific spatial allocation of county-based emissions to the modeling grid
    No spatial allocation was performed for point sources because the exact latitude and longitude are known

## Slide 11
Chart: US NOx Emission Trends 2000-2012
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Fuel Combustion | 8818.9369 | 8453.6129 | 7488.1094 | 7038.9144 | 6589.7193 | 6329.5056 | 5898.7035 | 5467.9014 | 5037.0994 | 4004.5747 | 4081.6104 | 3955.8334 | 3695.3624
Industrial Processes | 942.9878 | 980.6818 | 1059.1603 | 1080.7634 | 1102.3665 | 1120.7555 | 1109.9937 | 1099.2319 | 1088.4701 | 1088.4701 | 1088.4701 | 1088.4701 | 1088.4701
Transportation | 12560.4881 | 11930.2152 | 12377.0158 | 12044.3739 | 11711.732 | 11325.2009 | 11009.8656 | 10694.5303 | 10379.1951 | 9875.535 | 8878.693 | 7560.6331 | 6114.4145
Miscellaneous
Total | 22598.4336 | 21548.5107 | 21134.8074 | 20394.704 | 19654.6005 | 19046.3751 | 18286.3432 | 17526.3113 | 16766.2794 | 15230.0947 | 14310.2884 | 12866.4516 | 11159.7619
Source: Derived from US EPA Trends Data: http://www.epa.gov/ttn/chief/trends/
(1970 - 2012 Average annual emissions, all criteria pollutants in MS Excel - June 2013

## Slide 12
Source: Derived from US EPA Trends Data: http://www.epa.gov/ttn/chief/trends/
(1970 - 2012 Average annual emissions, all criteria pollutants in MS Excel - June 2013
Chart: US SO2 Emission Trends 2000-2012
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Fuel Combustion | 14162.9248 | 13735.1471 | 12800.9825 | 12691.5352 | 12582.0878 | 12708.2757 | 11517.624 | 10326.9724 | 9136.3207 | 7109.5503 | 6505.7416 | 5887.8271 | 4667.4166
Industrial Processes | 1417.9798 | 1464.4244 | 1084.8664 | 1061.9449 | 1039.0233 | 1015.6921 | 941.2061 | 866.7202 | 792.2343 | 792.2343 | 792.2343 | 792.2343 | 792.2343
Transportation | 696.5544 | 687.8312 | 753.1235 | 828.6639 | 904.2044 | 976.616 | 730.8978 | 485.1796 | 239.4614 | 201.495 | 120.5044 | 52.6404 | 20.893
Miscellaneous
Total | 16346.9982 | 15931.6556 | 14773.9201 | 14714.0359 | 14654.1517 | 14826.3643 | 13319.9077 | 11813.4511 | 10306.9945 | 8242.2576 | 7557.4583 | 6871.6798 | 5619.522

## Slide 13
Pollutant | AQMEII Phase 1 (Full Domain) | AQMEII Phase 2 (Full Domain) | EPA Trends estimate (US only*)
SO2 | 16,839 | 15,477 | 13,320
NOx | 20,863 | 23,165 | 18,286
PM2.5 | 4,047 | 5,316 | 5,636
NH3 | 4,698 | 5,087 | 4,714
CO | 90,064 | 98,339 | 88,077
2006 Emission Estimates across all sectors in thousands of short tons
*includes wildfires from 2005NEI

## Slide 14
Pollutant | AQMEII Phase 2 (Full Domain) | EPA Trends estimate (US only)
SO2 | 11,032 | 7,557
NOx | 19,060 | 14,310
PM2.5 | 4,663 | 5,636
NH3 | 4,963 | 4,714
CO | 75,797 | 88,077
2010 Emission Estimates across all sectors in thousands of short tons

## Slide 15
Pollutant | 2010-2006 AQMEII Phase 2 (Full Domain) | 2010-2006 EPA Trends estimate (US only*)
SO2 | -4,445 (-29%) | -5,762 (-43%)
NOx | -4,105 (-18%) | -3,976 (-22%)
PM2.5 | -653 (-12%) | -309 (-5%)
NH3 | -124 (-2%) | +162 (+4%)
CO | -22,542 (-23%) | +14,403 (+20%)
2010 - 2006 Changes in emission Estimates across all sectors in thousands of short tons
Delta Emissions with % change in ()
*includes wildfires from 2005NEI and 2008 NEI

## Slide 16
Year | Area(mi2) | Pop (millions) | Number of Vehicles (millions) | Electric Generating Capacity Millions GWHr
2006 | 2.95 | 296 | 243 | 4.06
2010 | 2.95 | 307 | 240 | 4.13
Sources:
http://quickfacts.census.gov/qfd/states/00000.html
http://www.fhwa.dot.gov/policy/ohim/hs06/htm/mv1.htm
http://www.fhwa.dot.gov/policyinformation/statistics/2010/mv1.cfm
http://www.eia.gov/electricity
Basic Demographics and Related Statistics for US 2006 & 2010 (excluding AK,HI)

## Slide 17
NOX Emissions Difference

## Slide 18
SO2 Emissions Difference

## Slide 19: Further Steps
Do analysis for all Pollutants
Temporal Analysis
Biogenic/Natural Emissions Comparisons especially iosprene and monoterpenes
Include EU data and analysis?
Other?

## Slide 20: For an overview and evaluation of the WRF/CMAQ model results, Christian Hogrefe’s Presentation
Overview and Evaluation of AQMEII Phase 2 Coupled Simulations over North America
Model Evaluation Session, Dogwood Room
Wednesday October 30, 2013 3:30 PM