## Slide 1: Assessment of long-term simulations with various observations for better understanding of aerosol effects on radiation “brightening” in the US.
Chuen-Meei Gan, Jonathan Pleim, Rohit Mathur, Christian Hogrefe, Charles N. Long, Jia Xing, David Wong, Robert Gilliam, Shawn Roselle and Chao Wei

## Slide 2: Objective
The main goal of this project is to investigate the changes in anthropogenic emissions of SO2 and NOx over the past 21 years (1990-2010) across the United States (US), their impacts on anthropogenic aerosol loading over North America, and subsequent impacts on regional radiation budgets.

## Slide 3: Overview of coupled WRF-CMAQ model with feedback (fb) and without feedback (nfb)
WRFv3.4 & CMAQv5.02
Simulation period: 1990 - 2010
Resolution: 36 km, 1-hour
Nudging coefficients (lower than typical nudging coefficients of standard run):
  guv: 0.00005
  gt: 0.00005
  gq: 0.00001
PBL | ACM2 (Pleim 2007)
Microphysics | Morrison 2-moment
Chemistry | Carbon Bond 05
Surface layer | Pleim-Xiu
Cumulus | Kain-Fritsch (new Eta)
Radiation | RRTMG
Land Use | NLCD 50
Emissions:
Jia Xing, Jonathan Pleim, Rohit Mathur, George Pouliot, Christian Hogrefe, Chuen-Meei Gan, and Chao We., “Historical gaseous and primary aerosol emissions in the United States from 1990–2010”, Atmos. Chem. Phys., 13, 7531-7549, doi:10.5194/acp-13-7531-2013, 2013.
Poster Session 2
Emissions Inventories, Models, and Processes
26. Jia Xing - Development and validation of long-term emission inventories in the United States from 1990 to 2010

## Slide 4: Observations Overview
Surface networks used in this study:
SURFRAD, ARM, CASTNET & IMPROVE.
Variables of interest: SO4, NOx, PM2.5, AOD and SW radiation.
Analysis region is seperated by 100o into East (i.e. bon, psu, gwn & sgp) and West (i.e. fpk, tbl & dra) of USA.
Reference: Chuen-Meei Gan, Jonathan Pleim, Rohit Mathur, Christian Hogrefe, Charles Long, Jia Xing, Shawn Roselle and Chao Wei: “Assessment of the effect of air pollution controls on trends in shortwave radiation over the United States from 1995 through 2010 from multiple observation networks”, Atmos. Chem. Phys., 14, 1701-1715, doi:10.5194/acp-14-1701-2014, 2014.
A complete analysis of observed trends was presented in Gan et al. 2014.
Notes: Mainly focus on 6 sites from SURFRAD & 1 site from ARM.
Locate sites from CASTNET & IMPROVE which is the closest with each SURFRAD sites & consist the longest available measurements.
Annual mean for each sites, then average them for network mean.
They are shown as anomalies except AOD.

## Slide 5: CASTNET Comparison (time series)
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
CASTNET | 1.0718 | 1.3703 | 0.29489 | 0.64972 | 0.16519 | 0.28829 | 0.18979 | 0.23521 | 0.067307 | -0.080018 | 0.66173 | -0.37592 | -0.36459 | -0.67692 | -1.2185 | -1.2707
MODEL 16 YRS | 0.43763 | 0.39496 | 0.65359 | 0.91557 | 0.62513 | 0.37284 | 0.37474 | 0.05319 | -0.0051215 | -0.13158 | 0.12654 | -0.4569 | -0.45098 | -0.66783 | -1.0492 | -1.1926
MODEL 21 YRS | 0.575 | 0.685 | 0.355 | 0.1 | 0.402 | 0.305 | 0.263 | 0.521 | 0.783 | 0.493 | 0.24 | 0.242 | -0.079 | -0.138 | -0.264 | -0.006 | -0.589 | -0.583 | -0.8 | -1.182 | -1.325
EMIS SO2 21 YRS | 0.3236 | 0.5249 | 0.4713 | 0.6463 | 0.4638 | 0.5349 | 0.2996 | 0.356 | 0.304 | 0.1132 | -0.0077 | -0.0513 | -0.2842 | -0.2888 | -0.3143 | -0.3176 | -0.3998 | -0.4571 | -0.542 | -0.6588 | -0.716
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
CASTNET | 1.1371 | 0.7323 | 1.7386 | 1.3145 | 0.76313 | 1.0543 | 0.33637 | -0.12028 | 0.18149 | 0.26534 | 0.45022 | -0.41933 | -0.68623 | -0.82286 | -2.133 | -2.0226
MODEL 16 YRS | 1.758 | 1.035 | 1.486 | 1.342 | 1.561 | 0.727 | 0.334 | -0.194 | -0.361 | 0.117 | -0.254 | -0.44 | -0.986 | -1.436 | -2.305 | -2.385
MODEL 21 YRS | 3.424 | 2.94 | 1.523 | 1.237 | 2.215 | 1.049 | 0.327 | 0.777 | 0.633 | 0.852 | 0.018 | -0.375 | -0.903 | -1.069 | -0.591 | -0.962 | -1.149 | -1.695 | -2.145 | -3.013 | -3.093
EMIS SO2 21 YRS | 0.3236 | 0.5249 | 0.4713 | 0.6463 | 0.4638 | 0.5349 | 0.2996 | 0.356 | 0.304 | 0.1132 | -0.0077 | -0.0513 | -0.2842 | -0.2888 | -0.3143 | -0.3176 | -0.3998 | -0.4571 | -0.542 | -0.6588 | -0.716
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
CASTNET | -7.7404e-05 | -0.025077 | 0.035523 | 0.15893 | 0.0046279 | 0.095495 | 0.086328 | -0.014505 | 0.028928 | -0.0045054 | -0.013739 | -0.028839 | -0.054372 | -0.13041 | -0.12161 | -0.14586
MODEL 16 YRS | 0.045 | 0.051 | 0.059 | 0.062 | 0.081 | 0.028 | 0.03 | 0.005 | 0.005 | -0.01 | -0.033 | -0.039 | -0.048 | -0.065 | -0.073 | -0.099
MODEL 21 YRS | 0.148 | 0.097 | 0.098 | 0.027 | 0.055 | 0.018 | 0.024 | 0.033 | 0.036 | 0.055 | 0.002 | 0.004 | -0.022 | -0.022 | -0.036 | -0.06 | -0.066 | -0.074 | -0.091 | -0.1 | -0.126
EMIS SO2 21 YRS | 0.0567 | 0.0602 | 0.0575 | 0.0618 | 0.0671 | 0.0457 | 0.0089 | 0.0547 | 0.0232 | 0.029 | 0.0221 | 0.0301 | 0.0019 | -0.0256 | -0.0368 | -0.0548 | -0.067 | -0.0838 | -0.0689 | -0.0953 | -0.0869
WEST
EAST
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
CASTNET | -0.02291 | -0.0076601 | -0.0031101 | -0.045917 | 0.001283 | 0.009883 | 0.12235 | 0.04085 | -0.006717 | 0.011183 | 0.0030497 | 0.0050497 | -0.012484 | -0.026172 | -0.045922 | -0.087022
MODEL 16 YRS | -0.03135 | -0.063646 | 0.043547 | 0.031908 | 0.0058157 | 0.013651 | -0.0027372 | -0.027795 | -0.026962 | -0.0085588 | -0.02631 | 0.027282 | 0.025305 | 0.018306 | -0.0060222 | 0.027569
MODEL 21 YRS | 0.013 | 0.022 | 0.028 | 0.007 | 0.011 | -0.036 | -0.069 | 0.038 | 0.027 | 0.001 | 0.009 | -0.008 | -0.033 | -0.032 | -0.014 | -0.031 | 0.022 | 0.02 | 0.013 | -0.011 | 0.023
EMIS SO2 21 YRS | 0.0567 | 0.0602 | 0.0575 | 0.0618 | 0.0671 | 0.0457 | 0.0089 | 0.0547 | 0.0232 | 0.029 | 0.0221 | 0.0301 | 0.0019 | -0.0256 | -0.0368 | -0.0548 | -0.067 | -0.0838 | -0.0689 | -0.0953 | -0.0869
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
CASTNET | 0.86383 | 0.50446 | 0.44346 | 0.40846 | 0.43383 | 0.47766 | 0.32956 | 0.15479 | 0.26599 | -0.057534 | 0.087716 | -0.39593 | -0.45318 | -0.58148 | -0.92703 | -0.68928
MODEL 16 YRS | -0.0034614 | 0.084854 | 0.18254 | 0.028137 | 0.065528 | 0.28255 | 0.25431 | 0.14211 | 0.14349 | -0.096955 | -0.068703 | -0.26201 | -0.2359 | -0.094802 | -0.30954 | -0.11215
MODEL 21 YRS | -0.286 | -0.261 | -0.032 | 0.238 | 0.012 | 0.017 | 0.105 | 0.203 | 0.049 | 0.086 | 0.303 | 0.275 | 0.163 | 0.164 | -0.076 | -0.048 | -0.241 | -0.215 | -0.074 | -0.289 | -0.092
EMIS NO 21 YRS | 0.2153 | 0.3533 | 0.2998 | 0.3522 | 0.2985 | 0.3895 | 0.2802 | 0.2573 | 0.2493 | 0.1088 | 0.1008 | 0.005 | -0.0724 | -0.17 | -0.2475 | -0.23 | -0.3102 | -0.3726 | -0.3955 | -0.5559 | -0.5559
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
CASTNET | -0.044906 | 0.12889 | -0.0055565 | 0.047352 | 0.044519 | 0.065885 | 0.14175 | 0.049685 | 0.029319 | -0.034215 | -0.090581 | -0.074248 | -0.045781 | -0.076937 | -0.15574 | -0.046287
MODEL 16 YRS | -0.030342 | 0.064185 | -0.014321 | 0.058543 | 0.030598 | 0.0056867 | 0.0037016 | 0.01676 | 0.0013901 | -0.00039478 | -0.0095654 | -0.016975 | -0.045146 | -0.057705 | -0.023485 | 0.017068
MODEL 21 YRS | -0.093 | -0.062 | 0.003 | 0 | -0.027 | -0.019 | 0.075 | -0.003 | 0.07 | 0.042 | 0.017 | 0.015 | 0.028 | 0.013 | 0.011 | 0.002 | -0.006 | -0.034 | -0.047 | -0.012 | 0.028
EMIS NO 21 YRS | 0.381 | 0.3839 | 0.2854 | 0.2796 | 0.1852 | 0.1436 | 0.1584 | 0.192 | 0.1269 | 0.1633 | 0.1181 | 0.2845 | -0.0377 | -0.1414 | -0.1921 | -0.2636 | -0.3207 | -0.3828 | -0.4097 | -0.5261 | -0.4276
Notes: *Similar averaging technique is used for model and emission. Data is subset from each grid cell.
*no much change in the western but significant decreasing trends in the eastern US especially sulfate.
*also, emission trends do agree well with the obs.
*One of the possible reasons for better agreement for the last 10 years may be the improvement of instrumentation / technology and sufficient information to construct better emission datasets.

## Slide 6: CASTNET Comparison
CASTNET SO4 16 years
CASTNET SO2 16 years
CASTNET NO3 16 years
Model agreed well with observations especially the last 10 years comparisons.
Model is able to characterize the observed SO2 and SO4 trends.
Similar trends are shown in the emission trends (i.e. decreasing).

## Slide 7: IMPROVE Comparison (time series)
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
IMPROVE | 0.36512 | 0.71145 | 0.68326 | 0.65892 | 0.31401 | 0.41671 | 0.079963 | 0.12559 | 0.026705 | -0.20325 | 1.1252 | -0.042531 | -0.092728 | -0.53244 | -0.98173 | -1.0595
MODEL 16 YRS | 0.48341 | 0.66411 | 0.76762 | 1.2691 | 0.74916 | 0.42248 | 0.44796 | -0.09173 | 0.099747 | -0.24636 | 0.08773 | -0.57245 | -0.60166 | -0.86635 | -1.2607 | -1.3521
MODEL 21 YRS | 0.746 | 0.801 | 0.427 | 0.311 | 0.381 | 0.317 | 0.498 | 0.601 | 1.102 | 0.583 | 0.256 | 0.281 | -0.258 | -0.067 | -0.413 | -0.079 | -0.739 | -0.768 | -1.033 | -1.427 | -1.519
EMIS SO2 21 YRS | 0.6158 | 0.6327 | 0.4136 | 0.5715 | 0.5581 | 0.22 | 0.1593 | 0.1697 | 0.3261 | 0.3202 | 0.1139 | 0.0926 | -0.0116 | 0.0058 | -0.0615 | -0.0238 | -0.3332 | -0.519 | -0.782 | -1.1049 | -1.3633
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
IMPROVE | -0.023751 | -0.015648 | -0.0034895 | 0.042586 | -0.18138 | -0.0048989 | 0.02607 | -0.011675 | -0.030104 | 0.023423 | 0.13417 | 0.041351 | -0.0072836 | 0.0033865 | -0.0051837 | 0.015894
MODEL 16 YRS | 0.0076175 | -0.053007 | 0.04759 | 0.039792 | 0.0014138 | 0.011741 | -0.014794 | -0.032835 | -0.028388 | -0.0011936 | -0.033743 | 0.022086 | 0.019862 | 0.011946 | -0.022484 | 0.024396
MODEL 21 YRS | 0.012 | 0.022 | 0.033 | -0.003 | 0.011 | 0.003 | -0.058 | 0.043 | 0.035 | -0.003 | 0.007 | -0.02 | -0.038 | -0.033 | -0.006 | -0.038 | 0.017 | 0.015 | 0.007 | -0.027 | 0.02
EMIS SO2 21 YRS | 0.0567 | 0.0596 | 0.0568 | 0.061 | 0.0663 | 0.0452 | 0.0085 | 0.0549 | 0.0233 | 0.029 | 0.0221 | 0.0299 | 0.0022 | -0.0251 | -0.0365 | -0.0543 | -0.0663 | -0.0832 | -0.0685 | -0.0947 | -0.0869
WEST
EAST
Chart: 
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
IMPROVE | 0.046797 | -0.063673 | -0.25372 | -0.36652 | -0.33746 | 0.15376 | 0.16424 | 0.28643 | 0.23973 | 0.10696 | 0.24081 | -0.098932 | 0.039124 | -0.15759 | -0.27035 | -0.09896
MODEL 16 YRS | 0.1078 | 0.16519 | 0.35994 | 0.14126 | 0.20927 | 0.3468 | 0.31474 | 0.070224 | 0.16525 | -0.1148 | -0.075725 | -0.40855 | -0.36808 | -0.22096 | -0.48976 | -0.2026
MODEL 21 YRS | -0.302 | -0.295 | 0.106 | 0.3 | 0.134 | 0.111 | 0.169 | 0.364 | 0.145 | 0.213 | 0.35 | 0.318 | 0.074 | 0.169 | -0.111 | -0.072 | -0.405 | -0.364 | -0.217 | -0.486 | -0.199
EMIS NO 21 YRS | 0.8567 | 0.9744 | 0.8232 | 0.8386 | 0.7992 | 0.7021 | 0.6066 | 0.5626 | 0.6056 | 0.6005 | 0.2723 | -0.0014 | -0.0504 | -0.3495 | -0.5924 | -0.5952 | -0.8783 | -1.0364 | -1.1446 | -1.4822 | -1.5114
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
IMPROVE | -0.050567 | -0.027832 | -0.11478 | -0.076815 | -0.19485 | 0.0019724 | 0.079034 | 0.075082 | 0.0043235 | 0.045633 | -0.00089399 | -0.021508 | 0.020406 | -0.0057899 | -0.0014204 | 0.03388
MODEL 16 YRS | -0.0056267 | 0.073756 | -0.0013901 | 0.055042 | 0.025696 | 0.010368 | 0.014176 | 0.019613 | 0.027928 | 0.032108 | -0.018965 | -0.038038 | -0.063084 | -0.074585 | -0.031219 | -0.025778
MODEL 21 YRS | -0.114 | -0.082 | 0 | -0.022 | -0.058 | 0.012 | 0.091 | 0.016 | 0.072 | 0.043 | 0.028 | 0.031 | 0.037 | 0.045 | 0.049 | -0.002 | -0.021 | -0.046 | -0.057 | -0.014 | -0.009
EMIS NO 21 YRS | 0.3837 | 0.3852 | 0.2866 | 0.2801 | 0.1834 | 0.1409 | 0.1566 | 0.1896 | 0.1252 | 0.1607 | 0.1166 | 0.2841 | -0.0382 | -0.1401 | -0.191 | -0.2602 | -0.3181 | -0.381 | -0.4092 | -0.5256 | -0.4291

## Slide 8: IMPROVE Comparison
IMPROVE SO4 16 years
IMPROVE NO3 16 years
In general, the surface measured concentrations agreed well with the model predictions (16-10 years comparison) for both networks especially SO4.
This finding shows that model is able to replicate the long-term trends which give confident in examining the aerosol direct effect.

## Slide 9: SURFRAD Aerosol Optical Depth (AOD)
Chart: East
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | 0.14876 | 0.16314 | 0.14349 | 0.14457 | 0.17178 | 0.17409 | 0.15729 | 0.15605 | 0.14577 | 0.15301 | 0.15894 | 0.1544 | 0.12616 | 0.13547
MODEL 16 YRS | 0.089634 | 0.095535 | 0.094963 | 0.09588 | 0.10128 | 0.091539 | 0.09706 | 0.087816 | 0.096749 | 0.08666 | 0.086966 | 0.083899 | 0.080437 | 0.079607 | 0.076152 | 0.067909
MODEL 21 YRS | 0.087948 | 0.095467 | 0.092123 | 0.089382 | 0.090111 | 0.089634 | 0.095535 | 0.094963 | 0.09588 | 0.10128 | 0.091539 | 0.09706 | 0.087816 | 0.096749 | 0.08666 | 0.086966 | 0.083899 | 0.080437 | 0.079607 | 0.076152 | 0.067909
Chart: West
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | 0.07611 | 0.07548 | 0.070758 | 0.086341 | 0.080234 | 0.085461 | 0.084935 | 0.072625 | 0.072337 | 0.081922 | 0.091927 | 0.088552 | 0.089596 | 0.083203
MODEL 16 YRS | 0.028144 | 0.032779 | 0.028794 | 0.029095 | 0.043225 | 0.031235 | 0.036444 | 0.030064 | 0.038546 | 0.034356 | 0.031931 | 0.040999 | 0.03335 | 0.034972 | 0.033104 | 0.032321
MODEL 21 YRS | 0.027336 | 0.032332 | 0.033301 | 0.027983 | 0.031763 | 0.028144 | 0.032779 | 0.028794 | 0.029095 | 0.043225 | 0.031235 | 0.036444 | 0.030064 | 0.038546 | 0.034356 | 0.031931 | 0.040999 | 0.03335 | 0.034972 | 0.033104 | 0.032321
SURFRAD AOD 16 years
Both simulations and observations show a decreasing trend in eastern US and an slightly increasing trend in western US.
This is because many control programs under the CAA were aimed at reducing the pollution concentrations mainly in the developed area but the pollution concentrations were low at the rural western monitors from the beginning.
This finding shows that the implementation of CAA does affect the US in particular eastern US.
As a result of the reduction of particulate matter, the AOD is reduced over the past 16 years.
WEST |  |  |  | EAST |  |  | 
14 yrs obs | 16 yrs sim | 10 yrs obs | 10 yrs sim | 14 yrs obs | 16 yrs sim | 10 yrs obs | 10 yrs sim
0.0009 | 0.0002 | 0.0005 | 0.00003 | -0.001 | -0.002 | -0.003 | -0.002
Notes: *even thought the AOD from model is underestimate but it still capable to capture the trend from observed.

## Slide 10: SURFRAD Shortwave (SW) Radiation (Rad) with Feedback (FB)
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -0.76872 | -2.4347 | 0.057633 | -6.3595 | -4.1119 | -1.1672 | -1.0687 | 0.86854 | 1.0733 | 1.9415 | 0.1097 | 1.5111 | 1.9502 | 1.0095 | 2.3601 | 2.4606
MODEL 16 YRS | 0.4203 | -0.2524 | 0.25246 | -1.0871 | -1.3633 | -0.63613 | -0.78211 | 0.23134 | -0.32288 | -0.33633 | -0.20212 | -0.080971 | 0.0012115 | 0.49194 | 1.5447 | 2.1214
MODEL 21 YRS | 0.54371 | -0.57221 | 0.26121 | 0.68405 | 0.61533 | 0.32454 | -0.34815 | 0.15671 | -1.1829 | -1.459 | -0.73189 | -0.87786 | 0.13558 | -0.41864 | -0.43208 | -0.29787 | -0.17673 | -0.094544 | 0.39619 | 1.4489 | 2.0257
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -1.489 | -2.4858 | -4.0759 | -3.3127 | -5.9446 | -0.45355 | 3.2175 | 0.6841 | 2.2185 | -0.15905 | -1.1563 | 1.3563 | 1.9487 | 2.4887 | 4.4795
MODEL 16 YRS | 0.65566 | 0.0048532 | 0.87178 | 0.30811 | -1.3986 | -0.50334 | -0.59502 | 1.4657 | -0.41803 | -0.12071 | -0.21383 | -1.524 | -0.72883 | 0.29373 | 1.0055 | 0.89708
MODEL 21 YRS | 0.69332 | -0.091729 | -1.0246 | 1.2301 | -0.065546 | 0.60931 | -0.041492 | 0.82544 | 0.26176 | -1.445 | -0.54969 | -0.64136 | 1.4193 | -0.46438 | -0.16706 | -0.26017 | -1.5703 | -0.77517 | 0.24738 | 0.95912 | 0.85074
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -1.6181 | -5.8612 | -7.9158 | -8.5385 | 3.8713 | -1.894 | 1.827 | -0.93204 | -2.6612 | -3.7146 | 5.177 | 4.6422 | 4.8687 | 1.7347 | -4.5202 | 9.1468
MODEL 16 YRS | -0.73283 | -4.0446 | -4.1685 | -5.0071 | 4.0589 | 1.4752 | -1.1741 | -2.2549 | -3.6695 | -1.6232 | 3.1405 | 3.9363 | 4.713 | 0.33711 | -3.299 | 8.3126
MODEL 21 YRS | -1.7235 | 0.94683 | -4.386 | -8.6605 | -1.0266 | 0.19528 | -3.1165 | -3.2404 | -4.079 | 4.987 | 2.4033 | -0.24594 | -1.3268 | -2.7414 | -0.69507 | 4.0686 | 4.8644 | 5.6411 | 1.2652 | -2.3708 | 9.2407
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -3.3091 | -0.65128 | -4.6921 | -2.9209 | -5.4364 | -0.74296 | 3.7339 | -1.1642 | -0.033819 | -0.89082 | 0.060525 | 4.0906 | 4.6325 | 1.5843 | 2.8557
MODEL 16 YRS | -4.2889 | -0.35399 | 2.412 | -1.0932 | -3.3835 | -1.189 | -0.51009 | 1.2869 | 1.0527 | -1.3727 | -0.9135 | -0.6668 | 2.535 | 4.7272 | 2.0689 | -0.31092
MODEL 21 YRS | 3.2629 | 0.033947 | -5.978 | -2.1759 | -1.4979 | -3.8918 | 0.043189 | 2.8092 | -0.69603 | -2.9863 | -0.79181 | -0.11291 | 1.6841 | 1.4498 | -0.97556 | -0.51632 | -0.26962 | 2.9322 | 5.1244 | 2.466 | 0.086262
WEST
EAST
SURFRAD all-sky SW rad 16 years
SURFRAD clear-sky SW rad 16 years
Brightening effect
Notes: *both of them (all sky and clear-sky) illustrate increasing trend in the rad.
*Larger trend in the all-sky simulation, but it can due to cloud effect and aerosol indirect effect.
*in order to exam only aerosol direct effect, we need to focus on clear-sky scenario.
*even thought the model clear-sky SW rad show smaller trend but it still able to represent the observed trend.

## Slide 11: SURFRAD Clear-sky Direct & Diffuse SW Rad (FB)
WEST
EAST
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | 1.9638 | 1.0838 | 3.5649 | -6.3876 | -1.8934 | 0.18996 | -0.67648 | 0.4877 | 0.19863 | 2.5052 | -0.95139 | 1.0829 | 0.73761 | -2.1241 | -0.1769 | 0.94253
MODEL 16 YRS | -0.39609 | -2.6394 | -1.4674 | -2.7724 | -4.3792 | -1.1483 | -3.3627 | 0.22839 | -2.5437 | -0.10121 | 0.31368 | 1.0888 | 2.3858 | 2.6807 | 4.3095 | 7.8035
MODEL 21 YRS | 0.6717 | -3.379 | -1.7844 | -0.44297 | -0.78948 | -0.038324 | -2.2816 | -1.1096 | -2.4146 | -4.0215 | -0.79053 | -3.0049 | 0.58615 | -2.1859 | 0.25656 | 0.67144 | 1.4466 | 2.7436 | 3.0384 | 4.6672 | 8.1613
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -0.21308 | 1.4381 | -1.846 | 0.36941 | -1.9603 | 0.60051 | 2.9832 | 0.39526 | 1.5294 | -0.40175 | -2.4948 | -1.4872 | -1.5296 | -1.3111 | 3.7209
MODEL 16 YRS | 2.6823 | 0.49145 | 2.3721 | 2.1039 | -3.4468 | 0.35625 | -1.3947 | 2.6295 | -2.1164 | -0.96975 | 0.41224 | -3.6055 | -0.56358 | -0.48531 | 0.46405 | 1.0703
MODEL 21 YRS | 3.3652 | 0.025289 | -1.2914 | 2.934 | 0.33224 | 2.347 | 0.15612 | 2.0368 | 1.7686 | -3.7821 | 0.020916 | -1.7301 | 2.2942 | -2.4518 | -1.3051 | 0.076909 | -3.9409 | -0.89891 | -0.82064 | 0.12872 | 0.73499
SURFRAD clear-sky direct SW rad 16 years
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -2.7197 | -3.5178 | -3.5035 | 0.028281 | -2.1861 | -1.3482 | -0.39406 | 0.37577 | 0.87068 | -0.57009 | 1.0552 | 0.42329 | 1.2038 | 3.1279 | 2.5327 | 1.5138
MODEL 16 YRS | 0.81639 | 2.387 | 1.7199 | 1.6853 | 3.0159 | 0.51216 | 2.5806 | 0.0029513 | 2.2208 | -0.23512 | -0.51579 | -1.1698 | -2.3846 | -2.1887 | -2.7648 | -5.6821
MODEL 21 YRS | -0.13987 | 2.8074 | 2.0462 | 1.1276 | 1.4054 | 0.36346 | 1.9341 | 1.2669 | 1.2324 | 2.563 | 0.059236 | 2.1277 | -0.44997 | 1.7678 | -0.68805 | -0.96872 | -1.6227 | -2.8375 | -2.6416 | -3.2178 | -6.135
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -1.2649 | -3.9133 | -2.2217 | -3.6736 | -3.9746 | -1.0492 | 0.23327 | 0.28044 | 0.68241 | 0.236 | 1.3345 | 2.8392 | 3.474 | 3.7963 | 0.75452
MODEL 16 YRS | -2.0266 | -0.4866 | -1.5003 | -1.7958 | 2.0482 | -0.85959 | 0.79973 | -1.1638 | 1.6984 | 0.84904 | -0.62607 | 2.0815 | -0.16525 | 0.77904 | 0.54142 | -0.17323
MODEL 21 YRS | -2.6886 | -0.11618 | 0.26762 | -1.7031 | -0.39695 | -1.7368 | -0.19677 | -1.2105 | -1.506 | 2.338 | -0.56976 | 1.0895 | -0.87401 | 1.9882 | 1.1389 | -0.33624 | 2.3714 | 0.12458 | 1.0689 | 0.83124 | 0.11659
SURFRAD clear-sky diffuse SW rad 16 years
The observed clear-sky diffuse SW rad is increasing which is opposite of what would be expected if changes in clear-sky rad were just attributable to changes in the aerosol direct effect.
Notes: If it is due to the aerosol direct effect, SWC direct should increase while SWC diffuse decrease. However, in the obs, the SWC direct shown no much trend (slightly increase) while the SWC diffuse increase significantly.

## Slide 12: SURFRAD Comparison
Annual mean of AOD versus clear-sky SW radiation between 1995 - 2010
For all-sky SW radiation, the "brightening" occurs at the same time that cloudiness exhibits a decreasing trend suggesting the possibility that indirect effects of decreasing aerosols may be a contributing factor. However, trends in cloud cover can have many other reasons.
The clear-sky SW radiation may be associated at least in part with a decrease in aerosols, particularly in the eastern US where substantial reductions in anthropogenic emissions of SO2 and NOx, resulted from the implementation of CAA.
However, analysis of the clear-sky diffuse SW radiation shows that the radiative impacts of decreasing aerosol concentrations are confounded by other factors.
 | WEST |  |  |  | EAST |  |  | 
 | 16 yrs obs | 16 yrs sim | 10 yrs obs | 10 yrs sim | 16 yrs obs | 16 yrs sim | 10 yrs obs | 10 yrs sim
SW | 0.5131 | 0.2454 | 0.5824 | 0.2609 | 0.6296 | 0.4222 | 0.5567 | 0.5072
SWC | 0.4799 | 0.0015 | 0.5278 | 0.0715 | 0.3691 | 0.1077 | 0.3055 | 0.2253
SW DIR | 0.1739 | 0.4575 | -0.0723 | 0.4385 | 0.4149 | 0.7614 | 0.4213 | 1.0551
SW DIF | 0.4009 | -0.2072 | 0.6481 | -0.1742 | 0.2555 | -0.3318 | 0.2104 | -0.5313
SWC DIR | 0.0005 | -0.1239 | -0.0052 | 0.0194 | -0.0085 | 0.5264 | -0.022 | 0.8532
SWC DIF | 0.4781 | 0.1255 | 0.532 | 0.0521 | 0.3764 | -0.4187 | 0.3267 | -0.628
AOD | 0.0009 | 0.0002 | 0.0005 | 0.00003 | -0.0012 | -0.0015 | -0.0026 | -0.0024

## Slide 13: Contrail effect on SW radiation
Monthly US system (international and domestic) aircraft airborne flight hours for the period January 1996 through December 2010 for the sum of passenger and cargo flights. (source: US Bureau of transportation Statistics)
Figure 12: US Airways and Delta combined domestic routes.
(source: http://www.proaerobusiness.com/route_maps.htm)
As a result of the increasing air traffic, the contrails persistence can potentially increase the diffuse radiation.
Characterization of contrails or ice cloud properties (crystal shapes, contrail altitude and etc.) are important.
Other factors: “clear-sky” definition, aerosol semi-direct and indirect effect and other cloud effects.
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -1.2649 | -3.9133 | -2.2217 | -3.6736 | -3.9746 | -1.0492 | 0.23327 | 0.28044 | 0.68241 | 0.236 | 1.3345 | 2.8392 | 3.474 | 3.7963 | 0.75452
MODEL 16 YRS | -2.0266 | -0.4866 | -1.5003 | -1.7958 | 2.0482 | -0.85959 | 0.79973 | -1.1638 | 1.6984 | 0.84904 | -0.62607 | 2.0815 | -0.16525 | 0.77904 | 0.54142 | -0.17323
MODEL 21 YRS | -2.6886 | -0.11618 | 0.26762 | -1.7031 | -0.39695 | -1.7368 | -0.19677 | -1.2105 | -1.506 | 2.338 | -0.56976 | 1.0895 | -0.87401 | 1.9882 | 1.1389 | -0.33624 | 2.3714 | 0.12458 | 1.0689 | 0.83124 | 0.11659
WEST
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -2.7197 | -3.5178 | -3.5035 | 0.028281 | -2.1861 | -1.3482 | -0.39406 | 0.37577 | 0.87068 | -0.57009 | 1.0552 | 0.42329 | 1.2038 | 3.1279 | 2.5327 | 1.5138
MODEL 16 YRS | 0.81639 | 2.387 | 1.7199 | 1.6853 | 3.0159 | 0.51216 | 2.5806 | 0.0029513 | 2.2208 | -0.23512 | -0.51579 | -1.1698 | -2.3846 | -2.1887 | -2.7648 | -5.6821
MODEL 21 YRS | -0.13987 | 2.8074 | 2.0462 | 1.1276 | 1.4054 | 0.36346 | 1.9341 | 1.2669 | 1.2324 | 2.563 | 0.059236 | 2.1277 | -0.44997 | 1.7678 | -0.68805 | -0.96872 | -1.6227 | -2.8375 | -2.6416 | -3.2178 | -6.135
EAST

## Slide 14
SURFRAD clear-sky SW Rad (FB vs. NFB)
WEST
EAST
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -0.76872 | -2.4347 | 0.057633 | -6.3595 | -4.1119 | -1.1672 | -1.0687 | 0.86854 | 1.0733 | 1.9415 | 0.1097 | 1.5111 | 1.9502 | 1.0095 | 2.3601 | 2.4606
SF sim 16 YRS | 0.4203 | -0.2524 | 0.25246 | -1.0871 | -1.3633 | -0.63613 | -0.78211 | 0.23134 | -0.32288 | -0.33633 | -0.20212 | -0.080971 | 0.0012115 | 0.49194 | 1.5447 | 2.1214
NF sim 16 YRS | -0.036 | -0.217 | 0.696 | -0.726 | 0.266 | -0.107 | 0.048 | -0.167 | 0.313 | -0.68 | -0.3 | -0.024 | -0.083 | 0.284 | 0.422 | 0.313
SF sim 21 YRS | 0.54371 | -0.57221 | 0.26121 | 0.68405 | 0.61533 | 0.32454 | -0.34815 | 0.15671 | -1.1829 | -1.459 | -0.73189 | -0.87786 | 0.13558 | -0.41864 | -0.43208 | -0.29787 | -0.17673 | -0.094544 | 0.39619 | 1.4489 | 2.0257
NF sim 21 YRS | -0.323 | -0.762 | -0.153 | -0.281 | 0.091 | 0.053 | -0.128 | 0.785 | -0.637 | 0.356 | -0.018 | 0.137 | -0.078 | 0.402 | -0.591 | -0.211 | 0.065 | 0.006 | 0.373 | 0.511 | 0.402
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -1.489 | -2.4858 | -4.0759 | -3.3127 | -5.9446 | -0.45355 | 3.2175 | 0.6841 | 2.2185 | -0.15905 | -1.1563 | 1.3563 | 1.9487 | 2.4887 | 4.4795
SF sim 16 YRS | 0.65566 | 0.0048532 | 0.87178 | 0.30811 | -1.3986 | -0.50334 | -0.59502 | 1.4657 | -0.41803 | -0.12071 | -0.21383 | -1.524 | -0.72883 | 0.29373 | 1.0055 | 0.89708
NF sim 16 YRS | -0.396 | -0.32 | 0.056 | -0.572 | -0.349 | -0.7 | -0.298 | 0.974 | 0.122 | -0.17 | -0.394 | -0.337 | 0 | 0.924 | 0.871 | 0.589
SF sim 21 YRS | 0.69332 | -0.091729 | -1.0246 | 1.2301 | -0.065546 | 0.60931 | -0.041492 | 0.82544 | 0.26176 | -1.445 | -0.54969 | -0.64136 | 1.4193 | -0.46438 | -0.16706 | -0.26017 | -1.5703 | -0.77517 | 0.24738 | 0.95912 | 0.85074
NF sim 21 YRS | -0.074 | -0.244 | -1.163 | 0.372 | -0.311 | -0.308 | -0.231 | 0.145 | -0.483 | -0.26 | -0.611 | -0.209 | 1.063 | 0.211 | -0.081 | -0.305 | -0.248 | 0.089 | 1.013 | 0.96 | 0.678
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | 1.9638 | 1.0838 | 3.5649 | -6.3876 | -1.8934 | 0.18996 | -0.67648 | 0.4877 | 0.19863 | 2.5052 | -0.95139 | 1.0829 | 0.73761 | -2.1241 | -0.1769 | 0.94253
SF sim 16 YRS | -0.39609 | -2.6394 | -1.4674 | -2.7724 | -4.3792 | -1.1483 | -3.3627 | 0.22839 | -2.5437 | -0.10121 | 0.31368 | 1.0888 | 2.3858 | 2.6807 | 4.3095 | 7.8035
NF sim 16 YRS | -0.009 | -0.25 | 0.684 | -0.728 | 0.26 | -0.087 | 0.017 | -0.191 | 0.253 | -0.719 | -0.278 | 0.043 | -0.164 | 0.36 | 0.456 | 0.353
SF sim 21 YRS | 0.6717 | -3.379 | -1.7844 | -0.44297 | -0.78948 | -0.038324 | -2.2816 | -1.1096 | -2.4146 | -4.0215 | -0.79053 | -3.0049 | 0.58615 | -2.1859 | 0.25656 | 0.67144 | 1.4466 | 2.7436 | 3.0384 | 4.6672 | 8.1613
NF sim 21 YRS | -0.298 | -0.766 | -0.085 | -0.315 | 0.046 | 0.08 | -0.161 | 0.773 | -0.64 | 0.349 | 0.001 | 0.105 | -0.103 | 0.341 | -0.63 | -0.19 | 0.131 | -0.075 | 0.449 | 0.545 | 0.441
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -0.21308 | 1.4381 | -1.846 | 0.36941 | -1.9603 | 0.60051 | 2.9832 | 0.39526 | 1.5294 | -0.40175 | -2.4948 | -1.4872 | -1.5296 | -1.3111 | 3.7209
SF sim 16 YRS | 2.6823 | 0.49145 | 2.3721 | 2.1039 | -3.4468 | 0.35625 | -1.3947 | 2.6295 | -2.1164 | -0.96975 | 0.41224 | -3.6055 | -0.56358 | -0.48531 | 0.46405 | 1.0703
NF sim 16 YRS | -0.293 | -0.392 | -0.1 | -0.529 | -0.22 | -0.534 | -0.275 | 1.027 | 0.005 | -0.424 | -0.383 | -0.3 | -0.057 | 0.999 | 0.869 | 0.606
SF sim 21 YRS | 3.3652 | 0.025289 | -1.2914 | 2.934 | 0.33224 | 2.347 | 0.15612 | 2.0368 | 1.7686 | -3.7821 | 0.020916 | -1.7301 | 2.2942 | -2.4518 | -1.3051 | 0.076909 | -3.9409 | -0.89891 | -0.82064 | 0.12872 | 0.73499
NF sim 21 YRS | 0.07 | -0.1 | -0.965 | 0.4 | -0.228 | -0.242 | -0.341 | -0.048 | -0.478 | -0.168 | -0.483 | -0.224 | 1.078 | 0.056 | -0.372 | -0.331 | -0.249 | -0.005 | 1.051 | 0.92 | 0.658
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -2.7197 | -3.5178 | -3.5035 | 0.028281 | -2.1861 | -1.3482 | -0.39406 | 0.37577 | 0.87068 | -0.57009 | 1.0552 | 0.42329 | 1.2038 | 3.1279 | 2.5327 | 1.5138
SF sim 16 YRS | 0.81639 | 2.387 | 1.7199 | 1.6853 | 3.0159 | 0.51216 | 2.5806 | 0.0029513 | 2.2208 | -0.23512 | -0.51579 | -1.1698 | -2.3846 | -2.1887 | -2.7648 | -5.6821
NF sim 16 YRS | -0.027 | 0.033 | 0.011 | 0.002 | 0.006 | -0.02 | 0.032 | 0.024 | 0.06 | 0.039 | -0.022 | -0.067 | 0.08 | -0.076 | -0.035 | -0.04
SF sim 21 YRS | -0.13987 | 2.8074 | 2.0462 | 1.1276 | 1.4054 | 0.36346 | 1.9341 | 1.2669 | 1.2324 | 2.563 | 0.059236 | 2.1277 | -0.44997 | 1.7678 | -0.68805 | -0.96872 | -1.6227 | -2.8375 | -2.6416 | -3.2178 | -6.135
NF sim 21 YRS | -0.025 | 0.004 | -0.068 | 0.034 | 0.046 | -0.027 | 0.033 | 0.012 | 0.002 | 0.007 | -0.019 | 0.032 | 0.025 | 0.061 | 0.039 | -0.021 | -0.066 | 0.081 | -0.076 | -0.034 | -0.04
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SURFRAD | -1.2649 | -3.9133 | -2.2217 | -3.6736 | -3.9746 | -1.0492 | 0.23327 | 0.28044 | 0.68241 | 0.236 | 1.3345 | 2.8392 | 3.474 | 3.7963 | 0.75452
SF sim 16 YRS | -2.0266 | -0.4866 | -1.5003 | -1.7958 | 2.0482 | -0.85959 | 0.79973 | -1.1638 | 1.6984 | 0.84904 | -0.62607 | 2.0815 | -0.16525 | 0.77904 | 0.54142 | -0.17323
NF sim 16 YRS | -0.103 | 0.072 | 0.156 | -0.043 | -0.13 | -0.166 | -0.023 | -0.053 | 0.117 | 0.253 | -0.011 | -0.037 | 0.057 | -0.076 | 0.002 | -0.017
SF sim 21 YRS | -2.6886 | -0.11618 | 0.26762 | -1.7031 | -0.39695 | -1.7368 | -0.19677 | -1.2105 | -1.506 | 2.338 | -0.56976 | 1.0895 | -0.87401 | 1.9882 | 1.1389 | -0.33624 | 2.3714 | 0.12458 | 1.0689 | 0.83124 | 0.11659
NF sim 21 YRS | -0.144 | -0.145 | -0.199 | -0.028 | -0.083 | -0.066 | 0.11 | 0.194 | -0.005 | -0.092 | -0.128 | 0.014 | -0.015 | 0.154 | 0.291 | 0.026 | 0 | 0.094 | -0.038 | 0.039 | 0.02
Notes: *For the clear-sky SW radiation, the NF case shows a very flat trend (SWC, direct and diffuse).
*This finding proves that the aerosol direct effect does play a role in the “brightening” phenomena.
*More works need to be done to address the causes of the increase of measured clear-sky SW diffuse radiation.

## Slide 15: Conclusion
In general, the coupled WRF-CMAQ model is capable to replicate the observed trends in surface concentration and AOD especially the last 10 years. This finding illustrates the importance of the accuracy of the emission.
In conclusion, this analysis suggest that there was a SW radiation “brightening” over the past 16 years in the US especially in the east but less apparent in the west.
The western US could be influenced by local terrain influences as well as episodic long-range pollution transport which may contribute to the lack of a clear association between trends in aerosol burden and surface radiation at these locations.
However, analysis of the clear-sky diffuse SW radiation shows that the radiative impacts of decreasing aerosol concentrations are confounded by other factors.
There are several possible interpretations to resolve this seeming contradiction such as increasing contrails from air traffic, classification of “clear-sky” conditions in the radiation retrieval methodology and indirect aerosol and other cloud effects.
On going tests: Ice clouds simulation tests to identify inconsistencies in observed diffuse radiation.

## Slide 16: Thank you! Questions?
  Acknowledgment:
  This research was performed while Chuen-Meei Gan held a National Research Council Research Associateship Award at US EPA.
  The research presented in this study was supported through an interagency agreement between the US Department of Energy (funding IA DE-SC0003782) and the US Environmental Protection Agency (funding IA RW-89-9233260).
  The author also would like thank John Augustine from NOAA-SURFRAD for his support and assistance in obtaining the SURFRAD data.
  Dr. Long acknowledges the support of the Climate Change Research Division of the US Department of Energy as part of the Atmospheric System Research (ASR) Program.
*Special thanks to all the co-authors for their contributions and support.

## Slide 17: Extra Slides

## Slide 18: Case study: SW Rad Aerosol Forcing
Mean aerosol SW Radiative Forcing |  |  | W/m2/year | 
 | dT | RFaer (Eqt1) | Obs SW trend | Obs SWC trend
Aug et al. | -0.0016 | 0.0518 | 0.6875 | 
obs_east | -0.0012 | 0.0388 | 0.6866 | 0.4732
obs_west | 0.0009 | -0.0291 | 0.5024 | 0.4697
model_east_16yrs | -0.0015 | 0.0486 | 0.4222 | 0.1027
model_west_16yrs | 0.0002 | -0.0065 | 0.2454 | 0.0015
BON_aeronet | -0.003 | 0.0972 | 1.0328 | 0.7598
bon_surfrad | -0.0008 | 0.0253 | 1.0328 | 0.7598
=
So (extraterrestrial downward SW flux at the TOA at 40oN) = 343 W/m2
α is computed SURFRAD network mean surface albedo of continental aerosols = 0.2522
Δτ is the measured change in 500-nm AOD
g is the typical asymmetry parameter for continental aerosols = 0.87
ωo is a representative single scattering albedo of continental aerosol = 0.97