## Slide 1
Donna B. Schwede1, Deborah Luecken1, John Walker2,
George Pouliot1, Wyat Appel1, James Kelly3, Kirk Baker3
1National Exposure Research Lab, US EPA, RTP, NC
2National Risk Management Laboratory, US EPA, RTP, NC
3Office of Air Quality Planning and Standards, US EPA, RTP, NC
Improvements to the characterization of organic nitrogen chemistry and deposition in CMAQ

## Slide 2
Acknowledgements
Chris Lehman (National Atmospheric Deposition Program
DISCOVER AQ Team
CALNEX Team
Ron Cohen (Lawrence Berkeley National Laboratory)
Melinda Beaver (EPA)
Daiwen Kang (Computer Sciences Corporation)

## Slide 3
Background & Motivation
Characterizing nitrogen deposition is important
  Excess nitrogen deposition can lead to acidification and eutrophication
    Decreases in forest growth
    Loss of species diversity and shifts in species distributions
    Harmful algal blooms
  Needed as input for critical loads assessments
    Critical load – threshold above which harmful effects occur
Studies estimate that organic N contributes 10-30% of total N budget
Current version of CMAQ provides only a basic treatment and greatly underestimates organic N deposition
Nitrogen species (except for NH3, NOx) are NOT included in the National Emission Inventory; emissions inventories are focused on ozone and PM which limits what we can model

## Slide 4
Sources of Organic Nitrogen
(from Cape et al, 2011)
Focus is here for now

## Slide 5
Organic N Speciation
Measurement techniques are improving and more speciated data are becoming available, but we still don’t know the complete picture
Many more organic N compounds are being measured than we have chemistry and emissions for
  Rocky Mountains study (Benedict et al, 2012) – 404 different nitrogen-containing organic compounds identified in air samples
  NJ study (Altieri et al, 2009) – 402 N-containing organic compounds determined in rainwater
Modeling 400+ species is not practical for air quality modeling

## Slide 6
Current Treatment in CMAQ
Some organic N species such as PAN, PPN, and MPAN are explicitly modeled
Many N species are not explicitly tracked … the chem mechanism is targeted for ozone and lumps species by # of carbons
  Organic nitrates are lumped into NTR (CB05), RNO3 (SAPRC)
  e.g. dimethyl amine – ALK5 in SAPRC07 and ALD2 in CB05
Species are lumped for wet deposition and deposition velocity calculations

## Slide 7
Differences Between Species
Henry’s Law (affects dry and wet deposition)
Reactivity (affects chemical lifetime)

## Slide 8
Species | Functional groups | Reaction rate with OH | Photolysis rate | Solubility | Represents
NTRALK | -ONO2 | low | low | low | First generation nitrates from alkanes
NTROH | -ONO2, -OH | low | low | high | First generation nitrates from alkene
NTRCN | -ONO2, =O | Med-high | high | Low-med | Second+ generation carbonyl and aldehyde nitrates
NTRCNOH | -ONO2, =O, -OH | Med-high | high | high | Second+ generation hydroxycarbonyl nitrates
NTRPX | -ONO2, -OOH, | med | high | high | Anthropogenic nitrates formed from reaction with HO2
NTRM | C=C, -OH, -ONO2 | high | low | high | First generation nitrates from biogenics
NTRI | -ONO2, -OH, =O | high | high | high | Second+ generation nitrates from biogenics
New Approach in CMAQ
*** See Deborah Luecken’s poster for details

## Slide 9
CMAQ Run summary
CMAQ model Configuration
  CMAQ v5.0.2
    New BEIS algorithm
    Bidirectional NH3
    CB05 (base and new (E7))
    Enhanced O3 dep due to ocean iodide
    GEOS-Chem boundary conditions
  Met
    WRF v3.4
    KF Trigger
    PX LSM
    ACM2

## Slide 10
Difference in Concentration
Difference (new - base) in monthly average concentration of total organic alkyl nitrates in the atmosphere between new scheme and base scheme.

## Slide 11
Difference in Wet Deposition
New - Base

## Slide 12
Difference in Dry Deposition
New - Base

## Slide 13
Comparisons w/ Measurements
Field studies
  Bondville, IL wet deposition study
    2010 study designed to explore feasibility of measuring wet deposition of bulk Organic N concentrations at NTN and AIRMoN sites
    Wet only collector (no dry dep interference); not filtered (filter can introduce organics); refrigerated samples
    Organic N by difference

## Slide 14
Bondville – Precipitation Chemistry

## Slide 15
Comparisons w/ Measurements
Air Quality System (AQS) Sites
  Ambient air quality monitoring information from EPA, state, local, and tribal agencies
  5000 current monitors

## Slide 16
AQS Concentrations - 2011
O3
Total Nitrate

## Slide 17
Comparisons w/ Measurements
Field studies
  Deriving Information on Surface Conditions from Column and Vertically Resolved Observations Relevant to Air Quality. (DISCOVER-AQ) Baltimore, MD
    2011 study combining satellite, airborne, and ground-based observations to study urban air pollution

## Slide 18
DISCOVER - AQ
ANs – Alkyl Nitrates
(NTRx)
Essex Site
PNs – Peroxyacyl Nitrates
(PAN, PANx,OPAN, MPAN)
Padonia Site

## Slide 19
DISCOVER-AQ
Base
New (E7)
ANs
PNs
NOy
HNO3

## Slide 20
Comparisons w/ Measurements
Field studies
  California Research at the Nexus of Air Quality and Climate Change (CALNEX) – Bakersfield, CA
    2010 study combining satellite, aircraft, and ground-based observations to study atmospheric transport and chemistry and emissions inventories

## Slide 21
CALNEX
ANs
PNs

## Slide 22
CALNEX
ANs

## Slide 23
Summary
Understanding of chemistry and emissions of organic N is a rapidly growing field, but there is still much to learn and improve in the modeling
Organic N is an important component of the nitrogen budget, but has been historically underpredicted
Recent changes to the organic N treatment in CMAQ have resulted in improved model performance
Additional comparisons with measurements are needed

## Slide 24
Future Work
Expand evaluation using other data sets
Begin working on model improvements for other organic N species
  Amines – importance in OH reactivity
Chemical mechanism work
  Expand the focus of chemical mechanisms beyond ozone/PM
  Track more of the nitrogen species explicitly
Improve emissions characterizations to include nitrogen species other than HNO3 and NOx