## Slide 1
Synoptic perspectives of pollutant transport patterns observed from satellites over East Asia
Hyun Cheol Kim 1,2, Pius Lee1, Soontae Kim3, Changhan Bae3, Byeong-Uk Kim4, and Eunhye Kim3
1 NOAA/Air Resources Laboratory, College Park, MD
2 UMD/Cooperative Institute for Climate and Satellites, College Park, MD
3 Ajou University, Dept. of Environmental Engineering, Suwon, Korea
4 Georgia Environmental Protection Division, Atlanta, GA

## Slide 2: Motivation
In recent years, wintertime high pollutant episodes are serious concerns in East Asia
Reasons for recent increase is not clear: increase of anthropogenic? Meteorological impact?
What is the role of regional-scale or long-range transport in air pollution in East Asia?
What is the best way to monitor near real-time transport of pollutants? Can satellite monitor them?
(Beijing, Jan. 29,2013, Reuters/China Daily)
(Jan. 17, 2014, Seoul, Korea)

## Slide 3: Wintertime AOD time series
Inter-annual variations of wintertime AOD over China and Korea are well correlated

## Slide 4: Seasonal transport patterns in East Asia (from literatures)
(Kim et al., 2014)
Type 3-5: Dominant northerly wind (>70%)
Type 2: Usual pathway for springtime Yellow Sand transport
March – May, 2001
ACE-Asia campaign
(Kim et al., 2005)
During cool season (Fall-Spring) Northwesterly wind is dominant.

## Slide 5: Data & method
MODIS AOD (NASA)
  Composite image from regular MODIS AOD and Deep Blue algorithm
  Indicator for aerosol
OMI/GOME-2 NO2 column (NASA & ESA)
  Indicator for (fresh) anthropogenic emission
  KNMI retrievals. GOME-2 uses both satellite products (MetOp-A & MetOp-B)
WRF/CMAQ AQF system (Ajou Uiversity)
Weather map (KMA)
  Overlaid to NO2 VCD using IGDP tool (GIS georeferencing technique)

## Slide 6: Wintertime East Asia synoptic flow patterns
H
L
Midlatitude
Cyclogenesis
Extension of
Siberian High
“Cold surges”
Siberian
High
China
Korea
Japan

## Slide 7: 3 important flow patterns
High pressure system (initiated from Siberian High) is a crucial common component in high pollutant events in East Asia
Type 1: Dominant high pressure system over China
Type 2: High pressure system first, then pushed by low pressure system (& cold front)
Type 3: Stationary high pressure system over China or Yellow Sea

## Slide 8: Type 1 : Dominant high pressure system
High pressure extends from Siberian High, and reaches to Chinese east coast.
(Northern) weak low pressure system often exists, and just balances westerly flow.

## Slide 9
MODIS AOD
GOME-2 NO2
Surface PM2.5
(Ajou U. AQF)
OMI NO2
Simulated PM distributions are well detectable from MODIS AOD, GOME-2 NO2 VCD, and OMI NO2 VCD
Apr. 6
Apr. 6
Apr. 6
Apr. 6
Apr. 7
Apr. 7
Apr. 7
Apr. 7

## Slide 10: Type 2: Pollutants pushed by cold front
STEP 1: High pressure system builds up pollutants and moves them to Manchurian region
STEP 2: Cold frontal activity associated with low pressure system pushes down pollutants

## Slide 11: Type 2: Day by day development
Nov. 4, 2013
Nov. 5, 2013
Nov. 6, 2013
Nov. 7, 2013
AOD
NO2
PM2.5

## Slide 12
GOME-2 NO2
CMAQ PM2.5 (Snapshot)
MODIS AOD
CMAQ PM2.5 (Animation)

## Slide 13: Type 3: Stationary high pressure system
Time series at Seoul Metropolitan Area (SMA)
Stationary high pressure over East China or Yellow Sea caused a very strong pollutant event (Feb. 26)

## Slide 14
Several days of significant stagnant High pressure system caused a serious high PM event in China and Korea
Feb. 19
Feb. 20
Feb. 21
Feb. 22
Feb. 23
Feb. 24
Feb. 25
Feb. 26
Feb. 27

## Slide 15: Conclusion
Synoptic patterns in East Asia are important in producing and transporting this region’s pollutants. We used satellite observations, combined with synoptic weather maps, to demonstrate their impacts.
High pressure systems provide favorable conditions for pollution development, with cloudless and subsiding atmosphere. It also provide eastward transport in the north side (e.g. Manchuria).
Low pressure system forces pollutants eastward. When balanced with high pressure system, it keeps pumping Chinese pollutants to Korea and Japan. When the low pressure system is strong, it pushes out pollutants, developed under high pressures, to Pacific Ocean. Unique shallow band-shaped plumes were identifiable form multiple satellite observations. Cold frontal activity is also important in lifting of pollutants.
Stagnant high pressure system at the Yellow Sea caused a significant high PM episodes in China and Korea (Feb. 25, 2014).
Accurate predicting of synoptic systems are crucial in forecasting and understanding pollutant transports in East Asia.