## Slide 1: Organic nitrates and ozone over eastern US
Jingqiu Mao (Princeton/NOAA GFDL), Larry Horowitz, Peter M. Edwards, Kyung-Eun Min, Steve Brown, Ilana B. Pollack, Thomas B. Ryerson, Martin Graus, Carsten Warneke, Jessica B. Gilman, Brian M. Lerner, Andy Neuman, John B. Nowak, Patrick R. Veres, James M. Roberts, Felipe Lope-Hilker, Ben H. Lee, Joel A. Thornton, Jennifer B. Kaiser, Frank N. Keutsch, Glenn M. Wolfe, Thomas F. Hanisco, Joost A. De Gouw, Kenneth C. Aikin, Kelley C. Wells, Dylan B. Millet, Vaishali Naik, Fabien Paulot, Meiyun Lin, Daniel J. Jacob
Funding from NOAA CPO

## Slide 2: Summertime ozone over eastern US is a long-standing problem for most global models
(Fiore et al., 2009, JGR)
Multimodel mean
Obs from CASTNET surface sites
Northeast US
Southeast US
Multimodel mean
Obs from CASTNET surface sites
This bias is attributed to the treatment of isoprene chemistry in the model.
Notes: Fiore: Model and obs are for 2001
Naik: AM3 is 1980-2000, CASTNET is 1988-2009

## Slide 3
A new isoprene chemistry for global models
(Mao et al., JGR, 2013)
ISOPO2 + NO is based on Paulot et al. (2009, ACP).
ISOPO2 + HO2 is based on Paulot et al. (2009, Science).
Isomerization of ISOPO2 is based on
Peeters et al. (2009, PCCP) and Crounse et al. (2011, PCCP) .

## Slide 4
First generation of isoprene nitrates degraded to second generation nitrates!
Second generation isoprene nitrates (C3-C4)
First generation isoprene nitrates (C5)
Overall NOx recycling efficiency is around 55%!
(Paulot et al., 2009, ACP)

## Slide 5
The International Consortium on Atmospheric Transport and Transformation (ICARTT) aircraft study: July-August 2004
Extensive measurements on isoprene oxidation products, including total alkyl nitrates (∑ANs)
Chemical transport model (GEOS-Chem) at 2x2.5 degree

## Slide 6
Mean vertical profiles during ICARTT
O3 has no bias in boundary layer and free troposphere.
HCHO provides good constraint on isoprene emissions.
Observations
GEOS-Chem
(Mao et al., JGR, 2013)

## Slide 7
Total organic nitrates excluding peroxyacylnitrates (∑ANs)
Model well reproduced ∑ANs.
∑ ANs is dominated by secondary organic nitrates.
∑ANs vs. HCHO
∑ANs vs. O3
Model well reproduced ∑ANs vs. HCHO and ∑ANs vs. O3 correlations.
These correlations cannot be reproduced by a fast isomerization channel of ISOPO2.
Vertical profiles
Speciation of ∑ANs
(Mao et al., JGR, 2013)

## Slide 8
NOy budget in eastern U.S. boundary layer for July 2004
Species | Emission | Chemical (P-L) | Dry Deposition | Wet Deposition | Net Export
NOx | 386 | -337 | 44 | ------ | 5
PANs |  | 24 | 13 | ------ | 11
∑ANs |  |  |  |  | 
ANs |  | 18 | 7.4 | 3.6 | 7
R4N2 |  | 10 | 0.5 | ------- | 10
HNO3 |  | 277 | 180 | 110 | -3
Export of ∑ANs > Export of PANs
(Mao et al., JGR, 2013)
(Unit Gg N)

## Slide 9
New chemistry
Previous studies without NOx recycling
Current anthro NOx emissions (2004)
Reduce current anthro NOx emissions by 50%
Isoprene↑
NOx ↓
OH ↓
O3 ↓
Surface ozone response to isoprene emissions
NOx emissions↓
Sensitivity of ozone to isoprene emissions ↓
(Mao et al., 2013, JGR)

## Slide 10
Field studies over Southeast US in the summer of 2013
SENEX (NOAA)
SOAS (NSF & EPA)
NOMADSS (NCAR)
Two aircrafts based at Smyrna, TN and a tower located at Centerville, Alabama.
Measurements include VOC, NOx, ozone, aerosols, CCN etc.
GFDL provided C180 nudge simulations to SENEX data archive.
A modeling workshop to be held in GFDL this summer.

## Slide 11
SENEX 2013 (NOAA)
SENEX (Southeast) flight track
Colored by ozone
June 3rd to July 10th
GFDL AM3 model
Fully coupled chemistry-climate model
Nudging wind with GFS meteorological field
Global high resolution (50 x 50 km)
MEGAN biogenic emissions (process-based emission)
New isoprene chemistry (Mao et al., 2013 JGR)

## Slide 12
Mean vertical profiles during SENEX
Plumes have been filtered by NOx/NOy<0.4, NOx<4 ppbv, CH3CN<225 pptv.
Model tends to overestimate ozone by 5-10 ppb.
By including a high yield of daytime terpene nitrates (27%), ozone can be reduced by <1 ppb in boundary layer.
By including a high yield of nitrate from terpene + NO3, ozone can be reduced by < 1ppb in boundary layer.

## Slide 13
Influence of nighttime NOx chemistry on daytime ozone
The limiting step is NO2 + O3 reaction.
With 40 ppb of O3, nighttime NOx lifetime is about 8 hours.
The production of NO3 can be mainly considered as a sink for NOx.
Organic nitrate yield of isoprene + NO3 is ~70%>> daytime yield (11.7%)
Organic nitrate yield of terpenes + NO3 is 40-50% (Fry et al., 2009,2011, ACP)

## Slide 14
(Stull, 1988)
Sunrise
After sunset, many VOCs and OVOCs are frozen in the residual layer.
10am
Sunset

## Slide 15
Three night flights during SENEX
Altitude (m)/100
Measured NO2 (ppb)
Modeled NO2 (ppb)
Most plumes are emitted at 500 – 1000 m ( in residual layer).
NO2 in plume is 10-30 ppbv, not high enough to titrate ozone.
Power plants
Atlanta
Power plants

## Slide 16
Remarkable feature : Large amount of VOCs remain in residual layer!
Altitude (m)/100
Measured HCHO (ppb)
Modeled HCHO (ppb)
HCHO is around 4 ppb at different heights, indicating a well mixed residual layer from the last day.
Acetaldehyde is around 1 ppb throughout the night (PAN precursor)
Isoprene (not shown) is about 1-2 ppb in residual layer.
Well mixed HCHO in residual layer.

## Slide 17
Model world
Real world
Model assumed well-mixed lowest layer.
A potential problem in global models for nighttime chemistry
60 m
70 m
130 m

## Slide 18
NOx emitted into the residual layer will:
be oxidized faster through NO2 + O3 (more ozone),
A lot more isoprene in residual layer to react than surface layer (bigger volume),
(3) contribute less to surface ozone.
NOx
NO3
PAN
OVOCs
Organic nitrates
Residual layer
Advection and mixing in free trop
NOx
Residual layer
NO3
Organic nitrates
NOx
Surface ozone
Stable boundary layer
Emitted in residual layer
Emitted in surface layer
Consistent with Paul Shepson’s measurements during SOAS.
Maybe some PAN is being formed at night?

## Slide 19
We now calculate the upper limit of the effect of vertically resolved nighttime NOx emissions (assuming all emissions into the residual layer are removed instantly).
Not much difference on afternoon NOx, where we do most aircraft sampling.
But you can see difference on ozone, 5-10 ppb.

## Slide 20
Zeroing out nighttime NOx emission in the model (30% of total anthropogenic NOx emissions)
This improves afternoon ozone by 5 ppb in the model.
If we assume those nighttime NOx can be converted to PAN, this may also improve PAN simulation.

## Slide 21
Current best estimate of daytime isoprene nitrate yield is ~12%, with ~50% recycling efficiency of NOx.
-- This results in a positive dependence of surface ozone on isoprene emissions throughout the U.S.
-- Good agreement between observed and modeled total alkyl nitrates provides additional constraints on isoprene chemistry.
Nighttime BVOCs oxidation is a sink for NOx
-- Sink can be more efficient for NOx emitted in residual layer (high O3, VOCs).
-- This may help to reduce surface ozone bias in global models.
-- Important for nitrogen export, as more PANs and alkyl nitrates may be produced in residual layer
Summary