## Slide 1: Cost estimate and control effective of multi-pollutant abatement from the power sector in the Yangtze River Delta region, China
Jian Sun and Joshua S. Fu*
Civil and Environmental Engineering
Energy Science and Engineering
University of Tennessee, Knoxville, TN
and
Computer Science and Mathematics Division
Oak Ridge National Laboratory
Thanks to Prof Shuxiao Wang, Tsinghua University, China to provide Chinese cost information and emission data
and
Dr. Carey Jang to use the CoST – CE in the ABaCAS framework
13th CMAS Conference, October 28, 2014

## Slide 2: Main
Introduction
Methodology
Results & Discussion
Conclusion

## Slide 3: 1. Introduction
Why do we consider “cost”?
Large amount of pollutants is emitted from different sources and will cause environment pollution and health issues. To avoid it, we need to install new control technology or retrofit the old devices to reduce the emission of pollutants. So associated investment for installation or retrofit is required, which refers to the “cost” here.

## Slide 4: 1. Introduction (con’t)
Air Pollution
Control Technology
Cost

## Slide 5: 1. Introduction (con’t)
History:
US EPA has developed different tools to calculate the cost:
(1) Air Compliance Advisor7.5 (ACA7.5, 2003);
(2) AirControlNET4.1 (ACN4.1, 2006);
(3) Control Strategy Tool (CoST, replacement for ACN, 2008)
Taiwan EPA:
TECAS (Taiwan Emission & Cost Analysis System)

## Slide 6: 1. Introduction (con’t)
Basic concepts:
Pollutant type (NOx, SO2, PM2.5, etc)
Pollutant emission sources (power plant, industry, domestic (area), mobile, etc)
Pollu. reduction tech.
Cost for installation & retrofit
NOx: SNCR, SCR, LNB, etc.
SO2: FGD
PM2.5: CYC, WET, ESP, FF, ESPFF

## Slide 7: 1. Introduction (con’t)
Goals:
  Model the pollutant reduction amount and total retrofit cost associated with the control strategy;
  Apply to various types of emission sources;
  Example: provide reference for making YRD air pollution control regulations;

## Slide 8: 1. Introduction (con’t)
CoST-Community Edition model:
Control cost analysis component of ABaCAS (Air Benefit and Cost and Attainment Assessment System);
ABaCAS: An integrated tool to provide assessment of emissions control cost, and their associated air quality attainment and health benefits;

## Slide 9: 1. Introduction (con’t)
ABaCAS website: http://www.abacas-dss.com
Home page
Detailed introduction
Download packages

## Slide 10: 1. Introduction (con’t)
Four key components
CoST: The first input

## Slide 11: 1. Introduction (con’t)
Main interface of ABaCAS
Main interface of CoST-CE

## Slide 12: Main
Introduction
Methodology
Results & Discussion
Conclusion

## Slide 13: 2. Methodology
Below is the equations that will be used in the cost calculation:
R: The remaining amount of pollutant after applying the control technology, ton;
E: The original emission of pollutant, ton;
EFF: The reduction efficiency of control efficiency, %;
A: The reduction amount of pollutant, ton;
E’: The current emission of pollutant, ton;
rp: The target percentage of reduction, %;
M: The additional removed amount of pollutant after retrofitting the
control technology, ton;

## Slide 14: 2. Methodology (con’t)
TC: The total cost of retrofitting control technology, Million RMB;
CC: The capital cost of control technology, RMB/MW;
FOM: The fix operation & maintenance cost over the life time of device (thirty years here), RMB/MW;
FUEL: The fuel cost over the life time of device (thirty years here), RMB/MW;
P: The unit capacity, MW;
The cost to retrofit control technology at one power plant:

## Slide 15: 2. Methodology (con’t)
The objective of cost model:

## Slide 16: Main
Introduction
Methodology
Results & Discussion
Conclusion

## Slide 17: 3. Results & Discussion
Calculate the control cost in CoST-CE model
RSM-VAT result using the input factor from CoST-CE model (offline-linkage)

## Slide 18: 3. Results & Discussion (con’t)
1. Set control percent
2. Choose province
3. Run & Output

## Slide 19: 3. Results & Discussion (con’t)
SO2 emission reductions (%) relative to current emissions vs. total abatement cost (million 2010 US Dollars) for the YRD region
With the CoST-CE output, the control cost curves can be calculated:
a). SO2
SO2 emission reductions (%) relative to current emissions vs. total abatement cost (million 2010 US Dollars) for provinces in the YRD region

## Slide 20: 3. Results & Discussion (con’t)
b). NOX
NOX emission reductions (%) relative to current emissions vs. total abatement cost (million 2010 US Dollars) for the YRD region
NOX emission reductions (%) relative to current emissions vs. total abatement cost (million 2010 US Dollars) for provinces in the YRD region

## Slide 21: 3. Results & Discussion (con’t)
c). PM2.5
PM2.5 emission reductions (%) relative to current emissions vs. total abatement cost (million 2010 US Dollars) for the YRD region
PM2.5 emission reductions (%) relative to current emissions vs. total abatement cost (million 2010 US Dollars) for provinces in the YRD region

## Slide 22: 3. Results & Discussion (con’t)
Region | SO2 | NOX | PM2.5
 | % | % | %
Shanghai | 54.24 | 63.15 | 93.41
Jiangsu | 49.82 | 76.36 | 96.74
Zhejiang | 43.09 | 49.61 | 96.60
YRD | 47.77 | 66.88 | 96.21
Maximum additional sector-wide emission reduction percentages for each pollutant in each province in the YRD region

## Slide 23: 3. Results & Discussion (con’t)
Region | SO2 | NOX | PM2.5
 | Million 2010 USD | Million 2010 USD | Million 2010 USD
Shanghai | 208 | 920 | 596
Jiangsu | 613 | 4174 | 2077
Zhejiang | 351 | 1428 | 1278
YRD | 1172 | 6522 | 3950
Total control cost for maximum additional sector-wide emission reduction percentages for each pollutant in each province in the YRD region

## Slide 24: 3. Results & Discussion (con’t)
Calculate the control cost in CoST-CE model
RSM-VAT (Response Surface Modeling-Visualization and Analysis Tool) results using the input factor from CoST-CE model (interactive linkage)

## Slide 25: 3. Results & Discussion (con’t)
RSM-VAT: Tool to build up a “real-time” response between pollution concentration and emission reduction control using CMAQ modeling data.
Functional design
Main interface

## Slide 26: 3. Results & Discussion (con’t)
1. Create input factor file
How to link CoST-CE and RSM-VAT?
2. Save as CSV file

## Slide 27: 3. Results & Discussion (con’t)
3. Input factor file in RSM
4. Visualize the effect

## Slide 28: 3. Results & Discussion (con’t)
a) Emission inventory for YRD in 2010
Region | Power Plant |  | Industry & Domestic |  | Mobile | 
 | NOX | PM2.5 | NOX | PM2.5 | NOX | PM2.5
 | 1000 tons/year | 1000 tons/year | 1000 tons/year | 1000 tons/year | 1000 tons/year | 1000 tons/year
Shanghai | 178.48 | 12.59 | 179.99 | 95.41 | 109.54 | 3.97
Jiangsu | 707.69 | 62.49 | 612.39 | 610.77 | 427.5 | 29.44
Zhejiang | 531.74 | 53.73 | 372.3 | 255.47 | 362.7 | 17.91
YRD | 1417.91 | 128.81 | 1164.68 | 961.65 | 899.74 | 51.32
Sector-wide emission inventory of NOx and PM2.5 for each province at YRD region

## Slide 29: 3. Results & Discussion (con’t)
b) PM2.5 control effect on PM2.5 at Jan, 2010
Max. PP control at Zhejiang
Max. PP control at Shanghai
Max. PP control at Jiangsu
Original
Max. PP Control at YRD
Max: 205 µg/m3

## Slide 30: 3. Results & Discussion (con’t)
b) PM2.5 control effect on PM2.5 at Jan, 2010
Original
Max. PP Control at YRD
Same Max. Control Percent for YRD Industry/Domestic Emission
Same Max. Control Percent for YRD Mobile Emission
Max: 205 µg/m3

## Slide 31: 3. Results & Discussion (con’t)
c) PM2.5 control effect on PM2.5 at Aug, 2010
Original
Max. PP Control at YRD
Same Max. Control Percent for YRD Industry/Domestic Emission
Same Max. Control Percent for YRD Mobile Emission
Max: 276 µg/m3

## Slide 32: 3. Results & Discussion (con’t)
d) Total PM2.5 control cost vs. PM2.5 conc. change for power plant in Jan, 2010 (+: increase; -: decrease)
Region | PM2.5 Control Percent | Total Control Cost | PM2.5 conc. Change
 | % | Million 2010 US Dollars | µg/m3
Shanghai | 25.13 | 24 | -0.066
 | 52.05 | 187 | -0.132
 | 72.57 | 372 | -0.184
 | 93.41 | 596 | -0.241
Jiangsu | 23.87 | 176 | -0.122
 | 56.85 | 880 | -0.292
 | 76.38 | 1353 | -0.392
 | 96.74 | 2077 | -0.49
Zhejiang | 26.21 | 140 | -0.06
 | 39.93 | 308 | -0.09
 | 64.84 | 710 | -0.144
 | 96.6 | 1278 | -0.216
Control Cost
Control Effect

## Slide 33: 3. Results & Discussion (con’t)
Region | PM2.5 Control Percent | Total Control Cost | PM2.5 conc. Change
 | % | Million 2010 US Dollars | µg/m3
Shanghai | 25.13 | 24 | -0.064
 | 52.05 | 187 | -0.133
 | 72.57 | 372 | -0.185
 | 93.41 | 596 | -0.238
Jiangsu | 23.87 | 176 | -0.117
 | 56.85 | 880 | -0.278
 | 76.38 | 1353 | -0.373
 | 96.74 | 2077 | -0.473
Zhejiang | 26.21 | 140 | -0.052
 | 39.93 | 308 | -0.079
 | 64.84 | 710 | -0.128
 | 96.6 | 1278 | -0.191
e) Total PM2.5 control cost vs. PM2.5 conc. change for power plant in Aug, 2010 (+: increase; -: decrease)
Control Cost
Control Effect

## Slide 34: 3. Results & Discussion
Region | PM2.5 Control Percent | Total Control Cost | PM2.5 conc. Change
 | % | Million 2010 US Dollars | µg/m3
Shanghai | 25.13 | 24 | -0.064
 | 52.05 | 187 | -0.133
 | 72.57 | 372 | -0.185
 | 93.41 | 596 | -0.238
Jiangsu | 23.87 | 176 | -0.117
 | 56.85 | 880 | -0.278
 | 76.38 | 1353 | -0.373
 | 96.74 | 2077 | -0.473
Zhejiang | 26.21 | 140 | -0.052
 | 39.93 | 308 | -0.079
 | 64.84 | 710 | -0.128
 | 96.6 | 1278 | -0.191
e) Total PM2.5 control cost vs. PM2.5 conc. change for power plant in Aug, 2010 (+: increase; -: decrease)
Control Cost
Control Effect

## Slide 35: 4. Conclusion
Shanghai has the largest maximum additional emission reduction percent for SO2 in the YRD region;
Jiangsu Province has the largest maximum additional emission reduction percent for NOx and PM2.5 in the YRD region
The maximum total control cost for Jiangsu Province is higher than that for Zhejiang Province and Shanghai, considering the total capacity of power plants and current installation status of control technology;
Reducing PM2.5 emission at power plant requires high total control cost, but has little effect on the ambient PM2.5 concentration.
Industry/Domestic PM2.5 emission dominates the PM2.5 concentration at YRD region based on the emission inventory;
Policy decision should be made by balancing the total control cost and its actual air quality benefit.

## Slide 36: 2013 ABaCAS Conference/Training Workshop (Hangzhou, 6/05-07)
2014 ABaCAS Conference/Training Workshop (Beijing, 5/28-30)

## Slide 37
Guangzhou (China) –
Summer (Mid of June) 2015
Joshua S. Fu
University of Tennessee, Knoxville, TN, USA
Shuxiao Wang
Tsinghua University, Beijing, China
Yun Zhu
South China University of Technology, Guangzhou, China
The 3rd ABaCAS Training Workshop/Conference

## Slide 38
Acknowledgement
Thanks for the funding support
USEPA
Energy Foundation
Institute for Security and Sustainable Environment, University of Tennessee

## Slide 39
Thank you for you Attention
QUESTION?