## Slide 1: Remote Sensing of Atmospheric Ammonia from the Cross-track Infrared Sounder (CrIS): Application to Air Quality Studies in California and the Southeast US
M. J. Alvarado1, K. E. Cady-Pereira1, M. W. Shephard2,
J. D. Hegarty1, C. R. Lonsdale1, D. K. Henze3,
M. Turner3
1Atmospheric and Environmental Research
2Environment Canada
3Univerisity of Colorado - Boulder
Copyright 2014, Government sponsorship acknowledged.

## Slide 2: NH3 is an important PM2.5 precursor
Long-range import
Long-range export
PM2.5
NH3 + HNO3NH4NO3
2 NH3 + H2SO4(NH4)2SO4
Increase incidence of cardiovascular and respiratory diseases
Increase number of CCN
Harmful algal blooms
Loss of species diversity
SO2, NOX decreasing
but NH3 forecast to increase
Nitrogen Deposition

## Slide 3: NH3 sources are not well known
Bi-directional
Flux
AGRICULTURE
Animal waste (temperature dependent)
Fertilizer application
Industry
Fertilizer
Coal Mining
Power generation
Biomass burning
Automobiles (catalytic converters)
Large urban centers
  50% of NH3 in LA area (Nowak et al., GRL, 2012)

## Slide 4: Monitoring NH3 is difficult
NH3 is highly reactive
 highly variable in space and time
NH3 from an Open path Quantum Cascade Laser (QCL) on a moving platform in the San Joaquin Valley during DISCOVER-AQ 2013.
Miller et al., AMT 2013

## Slide 5: Better emissions with TES NH3
Largest changes western US and Mexico
Used GEOS-Chem adjoint with TES NH3 profiles, averaging kernels and error covariances to optimize model
Optimized GC shows better agreement with AMoN network measurements
Zhu et al., 2013, JGR

## Slide 6: Using TES to constrain NH3 near Bakersfield during CalNEX
TES shows that CARB emissions underestimate NH3 during TES overpass (~1:30 PM LT).
Appears to be caused by incorrect diurnal distribution of NH3 emissions.
See Hegarty et al. CMAS 2014 presentation, “Evaluation of CMAQ Simulations of NH3 in California using Satellite Observations from TES” from yesterday for details
TES NH3 (ppb)
CMAQ NH3 (ppb)
Notes: Discuss some of the differences in TES versus CMAQ.

## Slide 7: Why switch to CrIS?
 | TES | CrIS
Satellite | AURA | NPP
Available Data | July 2004-present | October 2011-present
Resolution | 0.06 cm-1 | 0.625 cm-1
Footprint | 5x8 km rectangle | 14 km diameter circle
Repeat cycle | Once every 16 days | Daily
Equatorial crossing | 1:30 am and 1:30 pm | 1:30 am and 1:30 pm
Noise in NH3 window | 0.09 – 0.12 K | 0.03 – 0.06 K
TES is past its design lifetime, taking little new data, and has low spatial coverage
CrIS could monitor global NH3 with high spatial coverage for many more years (>2022)

## Slide 8: NH3 signal from TES and CrIS
Simulated spectra and NH3 signal
18 ppbv at surface
Detectability is ~1 ppbv under ideal conditions
But thermal contrast also plays a role
TES
CrIS

## Slide 9: TES and CrIS Sensitivity to NH3
Both instruments most sensitive to NH3 between 950 and 600 mbar
TES is more sensitive to amounts lower in the atmosphere
1 piece of information or less: DOFS<1.0
Collapse all information to a single point: RVMR
  Easier to compare with in situ measurements, models and other instruments
TES
CrIS

## Slide 10: CrIS NH3 Retrieval: Simulated Spectra
Notes: Doubled NH3 emissions in GEOS-Chem to generate “true” profiles
Profiles fed into RT model and CrIS noise added to get simulated spectrum.
Test ability of retrieval to reproduce the “true” profiles

## Slide 11: TES and CrIS versus surface NH3
QCL directly under TES transect in the San Joaquin Valley on January 28, 2013
QCL Surface Data
TES Transect Data
CrIS Swath Data

## Slide 12: Application of CrIS NH3 to California

## Slide 13: Application of CrIS NH3 to SENEX

## Slide 14: Future Work on CrIS NH3 Retrieval
  Validate against SENEX, FRAPPE, and other field NH3 measurements.
  Use CMAQ adjoint to test ability of CrIS to optimize NH3 emissions.
  Deliver CrIS NH3 retrieval algorithm to NASA
NH3 mixing ratios (ppbv) measured by the NOAA WP-3 aircraft during SENEX 2013. (Figure courtesy of Jesse Bash, US EPA NERL.)
SENEX Flights with NH3 Measurements

## Slide 15: Summary
A prototype NH3 retrieval for CrIS, based on the TES algorithm, has been built and tested
  LOD ~ 1 ppb, DOFS < 1.0, sensitive slightly higher in atmosphere than TES
  Algorithm performs well for simulated spectra
  Qualitatively similar to surface data from DISCOVER-AQ
  Further validation needed (e.g., SENEX and FRAPPE)
CrIS NH3 retrievals will be used to study NH3 emissions in California and Southeast US (e.g., SENEX)
Algorithm will be delivered to NASA SIPS for processing

## Slide 16: Acknowledgements
Juliet Zhu, Colorado State University
John Walker and Robert Pinder, EPA
Armin Wisthaler, University of Innsbruck
Kang Sun and Mark Zondlo, Princeton
Amy Jo Scarino, NASA Langley
Ming Luo, Jet Propulsion Laboratory, California Institute of Technology
    NOAA CPO AC4 Program Grant Numbers NA13OAR4310060 and NA14OAR4310129
TES Science Team
NASA Suomi-NPP Science Team

## Slide 17: CrIS microwindows and constraints
Lower spectral resolution of CrIS required different microwindows.
A priori and constraints from TES (Shephard et al., 2011)
  Polluted, Moderately polluted, and Unpolluted profiles
A priori selected based on signal to noise ratio (SNR) and thermal contrast