## Slide 1: Modeling the Co-Benefits of Carbon Standards for Existing Power Plants
STI-6102
Stephen Reid, Ken Craig,
Garnet Erdakos
Sonoma Technology, Inc.
Jonathan Levy
Boston University
Presented at the
13th Annual CMAS Conference
Chapel Hill, NC
October 29, 2014
Charles Driscoll,
Habibollah Fakhraei
Syracuse University
Kathy Fallon Lambert
Harvard Forest, Harvard University
Joel Schwartz,
Jonathan Buonocore
Harvard School of Public Health

## Slide 2: Outline
Background
  EPA Clean Power Plan
  Study objectives
Methods
  Overview
  Emissions scenarios
  CMAQ modeling
  BenMAP modeling
Results
Conclusions

## Slide 3: EPA Clean Power Plan
Carbon pollution standards for existing power plants released June 2, 2014.
Background
Projected to reduce carbon emissions from U.S. power plants by 30% from 2005 levels.
In 2012, the electric power sector accounted for 38% of CO2 emissions and 31% of GHG emissions in the U.S.
From EPA’s Overview of Greenhouse Gases (http://www.epa.gov/climatechange/ghgemissions/gases/co2.html)

## Slide 4: Potential Co-Benefits
Power plants are also a significant source of SO2, NOx, and mercury (Hg).
These pollutants are precursors for PM2.5 (SO2 and NOx) and ozone (NOx), which contribute to human health effects.
Background
For ecosystems, these pollutants contribute to acid rain, vegetation damage, and Hg bio- accumulation in fish.
Emissions contributions from EPA’s 2011 NEI

## Slide 5: Study Objectives
Inform the federal rulemaking process by
Modeling the potential co-benefits of various carbon standard scenarios.
Integrating human health and ecosystem health impacts to capture the geographic range of benefits.
Background
Estimating the economic value of benefits.
Communicating results to policy makers, with a focus on state agencies.
PM2.5
Ozone (O3)

## Slide 6: Overview of Approach
Methods
Policy scenarios developed by the Bipartisan Policy Center (BPC) and the Natural Resources Defense Council (NRDC), modeled by ICF International.
Notes:   2020 Reference Case and three 2020 policy cases with various levels of stringency and flexibility

## Slide 7: Emissions Scenarios (1)
2020 Reference Case
  Business-as-usual scenario
  Benchmarked to EIA’s Annual Energy Outlook of 2013
  Assumes full implementation of current clean air policies (e.g., EPA’s Mercury and Air Toxics Standard)
Scenario 1
  Low-stringency alternative
  Compliance options limited to “inside the fenceline” changes
  Results in national average emission rates of 907 kg/MWh for coal plants and 454 kg/MWh for gas plants
Methods

## Slide 8: Emissions Scenarios (2)
Scenario 2
  Moderate stringency with wide range of compliance options
  Most similar to standards proposed by EPA
  Results in national average emission rates of 680 kg/MWh for coal plants and 454 kg/MWh for gas plants
Scenario 3
  High-stringency alternative
  Mimics the impacts of a national tax on CO2 emissions
  Results in national average emission rates of 544 kg/MWh for coal plants and 385 kg/MWh for gas plants
Methods

## Slide 9: Emissions Scenarios (3)
Methods
Changes in CO2 emissions by scenario

## Slide 10: CMAQ Modeling (1)
CMAQ v4.7.1
Based on EPA’s 2007/2020 Modeling Platform
Year 2007 meteorology from WRF v3.1
CB05 gas chemistry AE5 aerosol chemistry
Multi-pollutant options engaged for mercury chemistry
Methods

## Slide 11: CMAQ Modeling (2)
4 CMAQ Simulations
  2020 reference case
  3 future-year (2020) emissions policy scenarios
Gridded air quality concentrations and deposition rates on a 12-km CONUS domain
CMAQ outputs post-processed for subsequent health, ecosystem analyses
Methods
CMAQ Modeling Grid
12-km grid cell resolution
396 x 246 grid cells

## Slide 12: BenMAP Modeling
EPA’s Benefits Mapping and Analysis Program (BenMAP) CE version 1.0.8
Calculates the health benefits of air quality management scenarios
BenMAP run with
  2020 population forecasts
  Incidence and prevalence rates of health outcomes
  Concentration-response functions developed by the project team
Health impacts calculated as additional benefits of carbon standards
Methods

## Slide 13: PM2.5 Co-Benefits (1)
Results

## Slide 14: PM2.5 Co-Benefits (2)
Results
Generally modest changes for Scenario 1, with PM2.5 disbenefits of up to 0.4 µg/m3
For Scenario 2, PM2.5 decreases of 0.15 to 1.35 µg/m3 occur across much of the eastern U.S.
Scenario 3 results similar to Scenario 2, but at a much higher cost

## Slide 15: Ozone Co-Benefits
Results
Insignificant ozone co-benefits for Scenario 1
For Scenario 2, peak 8-hr ozone concentration decreases of 0.7 to 3.6 ppb across the Ohio River Valley and Central U.S.

## Slide 16: Health Co-Benefits (1)
Results
National-scale health benefits by scenario

## Slide 17: Health Co-Benefits (2)
Results

## Slide 18: Summary
Stringency level and compliance options for carbon standards impact pollutant co-benefits.
Scenario 1, which focuses on plant retrofits, could increase co-pollutant emissions.
Scenario 2, which is most similar to EPA’s proposal, provides the greatest air quality and human health benefits (3,500 premature deaths avoided in 2020).
Scenario 3 benefits are similar to Scenario 2 but at a higher cost.
Conclusions

## Slide 19: Ongoing Work
Part 3 of the project is underway and focuses on ecosystem analyses
W126 analysis of benefits to forests and crops from ozone concentration reductions
Visibility analysis for Class I areas
Evaluation of changes in critical N loadings
Acidification recovery of soils and surface waters
Conclusions

## Slide 20: Project Website
For additional information, visit:
http://eng-cs.syr.edu/carboncobenefits
Conclusions

## Slide 21: Contacts
Stephen Reid, STI
sreid@sonomatech.com
Kathy Fallon Lambert, Harvard Forest
klambert01@fas.harvard.edu
Dr. Charles Driscoll, Syracuse University
ctdrisco@syr.edu
sonomatech.com @sonoma_tech