## Slide 1: EPA's 2011v6.2 Platform Future Year Emissions Inventory Projections
October 6, 2015
Alison Eyth, Rich Mason (EPA OAQPS EIAG*) Alexis Zubrow (Volpe, DOT)
* Emission Inventory and Analysis Group

## Slide 2: Base Year NEI is the Basis for Projections
NEI data submitted by states, locals, tribes (S/L/T) and EPA into the Emissions Inventory System (EIS)
Five categories
  Point/Facility Inventory (point locations)
  Nonpoint (county-based) – includes biogenics
  Onroad mobile sources from MOVES model (except CA)
  Nonroad mobile sources from NONROAD / NMIM
  Events (day-specific fires from SMARTFIRE)
EPA and S/L/T data are blended to create the NEI
  http://www.epa.gov/ttn/chief/net/2011inventory.html
EIS outputs a “flat file” in a format input to SMOKE
2011 NEI Version 2 was released in March, 2015
  Included many improvements over 2011 NEI Version 1
Notes: Give a quick introduction to emissions modeling
Specifics about 2011v6.2 platform

## Slide 3: Emissions Modeling Process
Inventories (annual, monthly, daily, hourly)
Met. Data
Chart: PM2.5 (tons)
Gridded, hourly, speciated emissions in a format for an air quality model
Temporal Profiles
Speciation Profiles
Spatial Surrogates
SMOKE
SMOKE software performs temporal allocation, spatial allocation, and speciation to create…
Ancillary Data: profiles and cross references
Notes: Go quickly: Ancillary data = temporal profiles, speciation profiles, spatial surrogates

## Slide 4: Emissions Models Used for 2011v6.2 Base Year and Projections
Biogenic Emission Inventory System (BEIS): creates air quality model-ready biogenic emissions (new: v3.61 is embedded in SMOKE)
Motor Vehicle Emission Simulator (MOVES): generates emission factors for onroad mobile sources that can be combined with activity data within SMOKE (new: MOVES2014)
National Mobile Inventory Model (NMIM): generates inventories for nonroad mobile sources (being replaced by MOVES)
Integrated Planning Model (IPM) new v5.14: generates EGU emissions for future years

## Slide 5: Future Year Projections
Estimate changes between base and future years
  Changes in activity levels (e.g., VMT, # wood stoves)
  Rules / technology changes in intervening years
  New units, closures, consent decrees
  Interpolation / extrapolation often difficult or technically not defensible
Projection techniques vary by sector
  Use models for future emissions (EGUs-IPM, onroad-MOVES)
  Apply factors - both for activity changes and controls
  Stand-alone inventories: new kilns, ethanol, biodiesel plants
  Hold constant: biogenics, fires (only anthro. change)
Each platform uses consistent methods for a set of future years (2017 and 2025 for 2011v6.2)

## Slide 6: Future Year Ancillary Data
Most ancillary data is the same in base and future year modeling
Meteorology is held constant
Spatial surrogates are constant
Temporal profiles are constant for most sectors (except for EGUs)
Speciation profiles are constant for many sources
  Updated for mobile sources to account for changes in fuels in future years
Notes: Go quickly

## Slide 7: EGU Projections based on IPM
IPM is a multi-regional, dynamic, deterministic linear programming model of the U.S. electric power sector
  Provides forecasts of least-cost capacity expansion, electricity dispatch, and emission control strategies that meet constraints
IPM 5.14 reflects impacts of federal and state laws and regulations through 12/2014 in the intervening years
Produces winter, summer, and annual emissions
  Pollutants: CAPs, Hg, HCl, CO2
  Output years: 2016, 2018, 2020, 2025, 2030, 2040, 2050
  Years not directly produced by IPM mapped to others
EGUs for which emissions are predicted by IPM are identified in the NEI point inventory and substituted with IPM output data in future years
  IPM postprocessor creates a flat file that can be read by SMOKE

## Slide 8: Map of IPM regions
Notes: Detail in northeast, Mississippi valley, CA

## Slide 9: EGU Temporal Allocation for Future Years
Allocate IPM winter and summer emissions to unit-specific 2011 hourly temporal pattern of the CEMS data for that season, when possible
Otherwise, sources are temporalized using regional average profiles to allocate emissions to month, then day, then hour
  Used for units that are new, have no 2011 emissions, change fuels from base to future, or have large predicted emission increases
  Profiles are region-, fuel-, and pollutant-specific

## Slide 10: Example of Unit-specific EGU Temporal Profiles
Summer emissions at this unit going down in future
Note: Average profiles do not include gaps in service

## Slide 11: Emissions Capped at Historic Annual Max Levels

## Slide 12: Regional Average Profiles
Use for unmatched units, new units, fuel switches, 0 base year
Profiles now vary by fuel (coal, gas, composite) and region
Diurnal profiles now vary by winter, summer, and composite
  Previous platforms only used composite

## Slide 13: Onroad Projections Overview
Reflect some changes in MOVES input databases:
  Regulatory impacts (also incorporated into MOVES code)
  Inspection and Maintenance programs
  Vehicle age distributions
  Fuel changes
  Speciation changes due to fuel changes
SMOKE: Future year VMT and other activity data
Constant between base year and future year:
  Counties for which emission factors are computed (i.e., “representative counties”)
  Meteorology
  Temporal profiles and spatial surrogates
    Updated for 2011v6.2 (see Technical Support Document)
Notes: CDB is where you update age distribution/fleet mix, I/M program. MOVES databases for LEV standards and regional fuel changes by year. Regulations are controlled by MOVES

## Slide 14: Vehicle Miles Traveled Projections
Use Annual Energy Outlook (AEO) 2014 to get overall magnitude (varies slightly due to vehicle / fuel mix)
2011v6.2 adjusts light duty (LD) VMT projections geographically based on human population projections
AEO projection
County adjustments
Notes: Point out that there is variation even in the national projection b/c of difference mix of vehicle/fuels by state/county

## Slide 15: Projecting Vehicle Age Distribution
Recession
Recession
Each plot shows fraction of vehicles
Shift in recession to older section of age distribution to maintain model year impacts
Dampening of spikes/troughs occurs over time due to scrappage
2018
2025
Years before modeled year
Years before modeled year

## Slide 16: Non-EGU Point and Nonpoint
Control Strategy Tool within Emissions Modeling Framework is used to project most NEI non-EGU point and nonpoint inventories
  Exceptions include stand-alone future year inventories (e.g., biodiesel and cellulosic plants, new cement kilns)
Input data “packets” created from many data sources
  Packet Types: Closures, projections, control percentage
  Data from: AEO, EPA offices (e.g., rules), state / local / regional organizations, consent decrees, NEI submissions
  Very complex to integrate data from all sources together
2011v6.2 updates
  Growth for non-EGU industrial sources
  Updates to oil and gas, residential wood combustion, commercial marine vessels, boilers, fugitive dust

## Slide 17: Impact of Projections
Chart: 2011 and 2025 Projected Emissions
| 2011 NH3 | 2025 NH3 | 2011 NOX | 2025 NOX | 2011 PM10 | 2025 PM10 | 2011 PM2.5 | 2025 PM2.5 | 2011 SO2 | 2025 SO2 | 2011 VOC | 2025 VOC
Point | 96757.4829 | 118626.6788 | 3746251.192 | 3129112.3073 | 764606.0774 | 778775.7539 | 537054.9981 | 558105.689 | 5768773.055 | 2342171.1399 | 1000695.2549 | 1059266.8694
Nonpoint | 3633033.3713 | 3727293.9629 | 2651424.9907 | 2326097.5636 | 7811470.1625 | 8674839.9998 | 1860803.4524 | 1944786.208 | 418119.9427 | 164098.3941 | 6799650.678 | 7421184.7166
Onroad | 120804.7297 | 85520.6244 | 5719979.4735 | 1707692.0598 | 367667.3423 | 280816.3528 | 194689.9116 | 83019.151 | 29664.7476 | 13759.0384 | 2709470.0842 | 904712.6397
Nonroad | 2627.0831 | 3542.6129 | 1630300.8494 | 794769.9419 | 162416.9117 | 77614.5353 | 154656.656 | 72788.4811 | 4031.02 | 2087.607 | 2024419.0286 | 1179394.8868
Fires | 329329.6399 | 329329.6399 | 333398.2052 | 333398.2052 | 2171987.4337 | 2171987.4337 | 1844262.9097 | 1844262.9097 | 165773.1045 | 165773.1045 | 4688094.4516 | 4688094.4516
NH3
NOx
PM10
PM2.5
SO2
VOC
Annual tons
Notes: NH3 slight increase; Onroad NOx going down a lot and point some, nonpoint PM10 going up, Point SO2 going down, Nonpoint VOC going up, but Nonroad going down

## Slide 18: Challenges for projections
Placement of new sources
Quantifying impacts of rules
  Incorporating state rules
Meteorological changes
Keeping up with data changes (e.g., AEO 2015)
International emissions and projections
  Only have 2010 for Canada
  EPA developed 2008-based projections for Mexico
Projecting fires and their impact on biogenics
Projections of changes in land use/population
  Spatial surrogates could be updated for future years

## Slide 19: 2011v6.2 Emissions Modeling Platform Data Availability
Data and documentation is available from http://www.epa.gov/ttn/chief/emch/index.html#2011
  TSD (Final Ozone NAAQS, Proposed ozone transport)
  2011NEIv2-based inventories, scripts, ancillary data
  Speciation profiles for CB05, CB6, SAPRC07
  Spatial surrogates for 4km, 12km, 36km
  Temporal profiles
  2015 EIC training class on modeling / projections
  IPM 5.14 base case data available at new URL:
    http://www.epa.gov/airmarkets/powersectormodeling.html
    Other EPA web page locations will be changing 10/1
  Ongoing NODA for 2011/2017: comments due 10/23
    EPA-HQ-OAR-2015-0500 - Contact eyth.alison@epa.gov