## Slide 1: Improving NOAA NAQFC PM2.5 predictions with bias correction approach
Jianping Huang1,2, Jeff McQueen2, Perry Shafran1,2,
Irina Djalalova3,4, James Wilczak4, Ho-Chun Huang1,2, Pius Lee5,
Li Pan5,6, Daniel Tong5,6, Youhua Tang5,6 , Geoff DiMego2,
Sikchya Upadhayay7,8, Ivanka Stajner8
1: IMSG; 2: NOAA/NCEP; 3: CIRES/UCB; 4: NOAA/ESRL; 5: NOAA/ARL; 6: UMD;
7: Syn Tech; 8: NOAA/OSTI
Presented to the 14th Annual CMAS Conference
October 7, 2015, UNC-Chapel Hill, NC

## Slide 2: Motivation and Objectives
NAQFC has been providing O3 operational forecast for the US since 2004. However, PM2.5 forecast is still on experimental status
To incorporate a bias correction approach into the NAQFC for improving PM2.5 predictions
To determine an optimal configuration for real-time forecast application

## Slide 3: Outline
Update of NAQFC
Current issue of NAQFC PM2.5 predictions
Bias correction method: Analog Ensemble
Evaluation of PM2.5 bias correction
Summary

## Slide 4
PRDGEN
(met interpolator)
PREMAQ
NMM-B
CMAQ
(v4.6)
NGAC(dust)
+ GEOS/Chem
BlueSky
(smoke)
Bias Correction
Post
AirNow Obs
G2O FVS
verification
A flow-chart of the NAQFC
(new changes as indicated by the red dashed boxes)
2005 NEI
+ 2011 NEI

## Slide 5: Current issues of PM2.5 predictions
Significant seasonal biases
over-prediction in winter
under-prediction in summer
Sources of biases
emissions ?
Met inputs like PBLH ?
CMAQ itself?
LBCs?
Over-prediction in winter is getting improvement and Under-prediction in summer is unchanged

## Slide 6
Current issue of PM2.5 predictions
Jan/2015
Jul/2015
Jan/2015
Jul/2015

## Slide 7: Analog Ensemble for PM2.5 Bias Correction
Analog metric is determined by (Monache et al. 2011)
where Ft is current NWP forecast valid at future time t, At’ is analog at past time t’, Nv is the number of variables , is half the number of additional computation time, wi weight, standard deviation
(Source: Djalalova et al., 2015)

## Slide 8: Configurations of NAQFC runs
Met inputs: NMMB 12-km (bgrd3d files)
Emissions: 2005 NEI + part of 2011 NEI (without mobile sources) + Blue Sky fire/smoke emissions (no gas)
CMAQ: CB05 gas-phase mechanism + Aero 4 module + 35 vertical levels
Lateral Boundary Conditions: NGAC dust + 2006 GEOS/Chem simulations (for gas + others of PM2.5)
Bias Correction for PM2.5:
- Analog Ensemble
- Analog search variables: PM2.5 + T+WS/WD

## Slide 9: Configurations of NAQFC runs (cont.)
Testing periods:
- January 2015 (winter)
- July 2015 (summer)
Runs | Raw PM2.5 | Bias corrected PM2.5
Operational |  | 
Parallel |  | 
CMAQBIACOR1 |  | 3 members + 8 weeks
CMAQBIACOR2 |  | 10 members+ 8 weeks
CMAQBIACOR3 |  | 3 members + 5 months

## Slide 10: Comparison of five runs for July 2015
at 16th fcst hour
RMSE
Crit_Suc_Indx
For the 2-months training period, the 10-member scenario does not help
For the 3-members scenario, 2 months and 5 months training period have similar performance

## Slide 11: Testing for winter month (Jan/2015)
Diurnal pattern was improved;
Day to day variability was lost on some days
WUS
EUS
WUS
EUS

## Slide 12
Testing for winter month (cont.)
WUS
EUS
Over-prediction reduced over EUS
RMSE was still high during night time
RSME
Before Bias Correction
After Bias Correction

## Slide 13: Testing for summer month(July 2015)
EUS
WUS
EUS
WUS
EUS
Diurnal variation was captured very well but the July 4th case was not captured.

## Slide 14: Testing for summer month(cont.)
WUS
EUS
RSME
Under-prediction was improved in summer and
RSME was not changed during nighttime.
Before Bias Correction
After Bias Correction

## Slide 15: A case study on July 4th
EUS
WUS
Before Bias Correction
After Bias Correction

## Slide 16: Summary and conclusions
Analog Ensemble bias corrections has been tested by NOAA/NAQFC for improving PM2.5 predictions.
Training period and number of ensemble members are the key for the bias correction. With configuration of 8-week training period and 3 ensemble members, the Analog bias correction may capture the diurnal pattern quite well. But daily variability needs further improvement.
RMSE was reduced significantly during daytime but little improvement during nighttime.
High PM2.5 cases like July 4th, dust, and smoke episodes are still a challenge.
Notes: Smoke and dust, ozone, anthropogenic PM now in one unified system with CMAQ Unified
Now using a version of CMAQ supported by EPA CMAS community Supported
First time in 7 years we’ve seen consistent improvement in ozone predictions Updated
Inclusion of PM in operational model provides refliable PM product for all of U.S. Reliable