## Slide 1: Evidence for an increasing geographic region of influence on ozone air pollution in the eastern United States
Evidence for an increase in the photochemical lifetime of ozone in the eastern United States
Presented at the 14th CMAS Meeting
Wednesday October 7th, 2015
Presentation by:
Dan Goldberg, Ph.D. Candidate
Co-authors: Tim Vinciguerra, Tim Canty, Chris Loughner, Ross Salawitch & Russ Dickerson

## Slide 2: Motivation for this study…
The state of Maryland is very interested in the role of the interstate transport of ozone.
Science objectives:
How much ozone is generated locally vs. transported from upwind regions?
What are the future trends in surface ozone?
Is ozone being simulated for the right reasons?

## Slide 3: Motivation for this study…
Surface data taken from AQS sites in the Baltimore-Washington area
Why is the bottom-third rising?
Red – Top third of the O3 distribution
Blue – Bottom third of the O3 distribution
Is it due to:
An increase in the global ozone background?
A decrease in chemical processes that remove ozone?
Perhaps a combination of both, but for this presentation I will focus on the second option.

## Slide 4: CAMx v6.10 with Ozone Source Apportionment

## Slide 5: Ozone Source Apportionment Examples
The CAMx software can attribute ozone to different source regions.
Surface ozone, once formed, can be transported 100’s km downwind from the original source.
MD
OH
PA

## Slide 6: Ozone from the model boundary
Ozone from the boundary is uniformly greater than 15 ppbv.
Some locations, especially close to the boundaries, are higher.
Ozone attributed to areas beyond the model domain, i.e., Texas, Cal, Asia

## Slide 7
Summer 2011: Ozone Source Attribution
Baltimore, MD
BC=boundary conditions

## Slide 8
Summer 2018: Ozone Source Attribution
The attribution of ozone in all states decreases 10 – 25 % over 7 years.
The only portion to increase is the ozone attributed to the model boundary.
Baltimore, MD
BC=boundary conditions

## Slide 9
Trends in the Apportionment of Surface Ozone
Boundary and meteorology are initialized identically in each simulation.
Total surface ozone has decreased and is projected to further decrease.
  Sources inside the model domain will decrease.
  If the sources outside the model domain remain the same, ozone attributed to these sources will increase.
Mean 8-hr max in Baltimore, MD

## Slide 10
Trends in the Apportionment of Surface Ozone
An increasing role of the boundary is seen in all metropolitan areas in the eastern United States.
Mean July concentration of ozone (ppbv) attributed to the boundary
What is causing this increase???
Ironically, we think it’s related to reductions in NOx and VOCs

## Slide 11: How is O3 chemically produced?
NO + HO2  NO2 + OH
NO2 + hν  NO + O
O2 + O  O3
As NOx and VOC emissions decrease, ozone production rates will also decrease.

## Slide 12: How is O3 chemically destroyed?
O3 + HO2  2 O2 + OH
O3 + OH  O2 + HO2 (minor)
How is NO2 chemically destroyed?
NO2 + OH  HNO3
NO2 + NO3  N2O5 + H2O  2 HNO3 (minor)
As NOx and VOC emissions decrease, ozone loss rates will also decrease.

## Slide 13: Change in Ox (O3+NOy–NO) Loss Rates
2002
2018
MD Avg: 1.5 ppb/hr
MD Avg: −0.3 ppb/hr
MD Avg: 1.2 ppb/hr
Ox is lasting longer in the troposphere
2018 – 2002

## Slide 14: Change in the NO2+OH reaction rates
NO2 is lasting longer especially in urban areas
MD Avg: 0.4 ppb/hr
MD Avg: −0.2 ppb/hr
MD Avg: 0.2 ppb/hr
2002
2018
2018 – 2002

## Slide 15
HO2 Chemistry in the eastern United States
Mean July 2011 daytime (7 AM – 7 PM EDT) HO2 concentrations
The HO2 + O3 reaction can be an important sink of Ox (O3+NO2+…) when HO2 >15 pptv.

## Slide 16
Change in daytime HO2 concentrations between July 2002 and 2018
Surface
2 km
5 km
1 km
Daytime HO2 concentrations are decreasing in most areas.
This is increasing the lifetime of ozone when reaction with HO2 is important.
Ozone lifetime with respect to reaction with HO2 increases from 9.0 to 9.5 days.
15

## Slide 17
Change in daytime HO2 concentrations between July 2002 and
July 2018 (with VOC reductions ONLY)
Surface
2 km
5 km
1 km
Anthropogenic VOC reductions are partially (but not fully) responsible for the decrease in HO2 concentrations.

## Slide 18: Curtain plots of Ozone at the Boundary during July 2011
Modeling domain
MOZART is marginally higher in the lower layers at all boundaries, except the Southeast.
GEOS–Chem has higher ozone in the mid–troposphere, especially at the western boundary (which is the boundary that most often influences ozone in the eastern United States).

## Slide 19: Conclusions
  We use boundary condition ozone as a reactive tracer to discover that:
  Nonlinearities associated with NOx and VOC emission reductions are responsible for an increase in the photochemical lifetime of ozone.
  Ozone produced from distant sources will remain in the atmosphere for a longer time.
  This is an unintended consequence of the policies to reduce these emissions.

## Slide 20: Future Work
Implement a better representation of current year boundary conditions using satellites and ozonesondes.
  Henderson et al., 2014; Fiore et al., 2014
Use future year boundary conditions for future year regional model scenarios.

## Slide 21: Model Verification: Surface O3 at Maryland sites

## Slide 22: Model Verification: Surface O3 at CASTNET sites