## Slide 1
Air Quality Reanalysis
(Configuration for 2010 HTAP production)
14th CMAS, Chapel Hill, NC October 5-7, 2015
Greg Carmichael1, Pius Lee2 , Youhua Tang2 , Li Pan2 , Hyuncheol Kim2, Daniel Tong2 , Brad Pierce3, Ted Russell4, Yongtao Hu4, Talat Odman4, Dick McNider5,
Arastoo Pour Biazar5, Yang Liu6, Ed Hyer7, Ken Pickering8
1 College of Engineering, University of Iowa, Iowa City, IA
2Air Resources Lab., NOAA Center for Weather and Climate Prediction, College Park, MD
3National Environmental Satellite and Information Service (NESDIS), Madison, WI
4School of Civil and Environmental Engr., Georgia Institute of Technology, Atlanta, GA
5Department of Atmospheric Science, University Alabama, Huntsville AL
6Department of Environmental Health, Emory University, Atlanta, GA
7Naval Research Laboratory, Monterey, CA
8Atmospheric Chemistry and Dynamics Lab., NASA, Greenbelt MD

## Slide 2
Constrained
Satellite
Products
Global
Assimilation
+ AQ Assessments
+ State Implementation Plan Modeling
+ Rapid deployment of on-demand rapid-response forecasting; e.g., new fuel type,…, etc.
+ Health Impacts assessments
+ Demonstration of the impact of observations on AQ distributions
+ Ingestion of new AQAST products into operations
http://acmg.seas.harvard.edu/aqast/projects.html
AQAST Project: Air Quality Reanalysis
(Translating Research to Services)
Posters D1_03: Ho-Chun Huang
D2_10: Min Huang
D2_34: Li Pan
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: Objective: Best estimated state of the chemical composition of the atmosphere (lower troposphere)
A sizeable user group: AQ application as well as health epidemiology scenarios
A ‘reanalysis’ is a climate or weather model simulation of the past that includes data assimilation of historical observations. The observations can be very comprehensive (satellite, in situ, multiple variables) or relatively sparse (say, sea level pressure only), and the models themselves are quite varied. Generally these models are drawn from the weather forecasting community (at least for the atmospheric components) which explains the odd terminology. An ‘analysis’ from a weather forecasting model is the 6 hour (say) forecast from the time of observations. Weather forecasting groups realized a decade or so ago that the time series of their weather forecasts (the analyses) could not be used to track long term changes because their models had been updated many times over the decades. Thus the idea arose to ‘re-analyze’ the historical observations with a single consistent model. These sets of 6 hour forecasts using the data available at each point are then more consistent in time (and presumably more accurate) that the original analyses were.

## Slide 3
Applications of Reanalysis
Ozone – modeled (~ 3 yr data lag) & monitor (~ 1 yr data lag), both from EPA
PM2.5 mass - modeled (~ 3 yr data lag) & monitor (~ 1 yr data lag), both from EPA
Air Toxics - benzene, formaldehyde, modeled from EPA, 2005 only (NATA)
Reanalysis would be able to provide PM2.5 speciation data with national coverage at county level, which are highly valuable for health effects studies
AQAST-8 Dec 2-4, 2014, Atlanta, GA
Notes: Tracking currently group their data into 4 categories. The first order application of our reanalysis data would be in the subcategory “Outdoor Air” under “Environments”.
The call out box shows what Tracking currently has and the data limitations
Second order application would be to provide more up to date air toxics data – needs further discussion to make it useful to Tracking.

## Slide 4
NOMADS
RSIG .
Goal: A user friendly downloadable archive
analysis
New
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: Long term – user, and on-demand subseting and downloading gui e.g.
NOAA Operational Model Archive and Distribution System
Remote Sensing Information Gateway

## Slide 5
Lightning NOx
AIRNow
Cloud-obs Photolysis rates
Isoprene
& PAR
done
done
done
Yet to do
testing
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: Raqms
The RAQMS analyses include assimilation of real-time Aura MLS stratospheric ozone profiles (above 50mb) and cloud cleared OMI total column ozone as well as Terra and Aqua MODIS aerosol optical depth that uses modeled upper tropospheric RH to filter potential cirrus cloud contamination. Wild fire emissions are based on Terra and Aqua MODIS fire detections.
HMS

## Slide 6: Optimal Interpolation (OI)
OI simplifies the cost function minimization (Dee et al. Q. J. R. Meteor. Soc. 1998) by limiting the analysis problem to a subset of obs.
Obs far away (beyond background error correlation length scale) have no effect in the analysis.
Injection of obs through OI takes place at 1800 UTC for AOD obs and 6 unevenly spaced intervals for AIRNow obs.
AQAST-8 Dec 2-4, 2014, Atlanta, GA

## Slide 7
MODIS AOD & AIRNow PM2.5 assimilated
For initial condition adjustment
00Z
06Z
12Z
19Z
AIRNOW PM2.5, PM10, Ozone
MODIS AOD (Terra and Aqua)
14Z
17Z
18Z
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: 6 hour forecasts and retain the optimal analysis states

## Slide 8: Analysis field Verification: AIRNOW O3 & PM 2.5 over CONUS
Fire-work
PM2.5 low biases: esp. daytime
SO42-, Criegee
SOA
Small fires
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: ,Raqms
The RAQMS analyses include assimilation of real-time Aura MLS stratospheric ozone profiles (above 50mb) and cloud cleared OMI total column ozone as well as Terra and Aqua MODIS aerosol optical depth that uses modeled upper tropospheric RH to filter potential cirrus cloud contamination. Wild fire emissions are based on Terra and Aqua MODIS fire detections.

## Slide 9
WRF 3.2.1 for meteorological fields
  NCEP North American Regional Reanalysis (NARR) 32-km resolution inputs
  NCEP ADP surface and soundings observational data
  MODIS landuse data for most recent land cover status
  3-D and surface nudging, Noah land-surface model
SMOKE 2.6 for CMAQ ready gridded emissions
  NEI inventory projected to 2011 using EGAS growth and existing control strategies
  BEIS3 biogenic emissions based on BELD3 database
  GOES biomass burning emissions: ftp://satepsanone.nesdis.noaa.gov/EPA/GBBEP/
CMAQ 4.6 revised to simulate gaseous & PM species
  SAPRC99 mechanism, AERO4, ISORROPIA thermodynamic, Mass conservation,
  Updated SOA module (Baek et. al. JGR 2011) for multi-generational oxidation of semi-volatile organic carbons
Analysis fields as IC and forecast with Total AOD Assimilation basis for LBCs
12 km
36 km
4 km
IC/BC of Base and AOD_DA cases
DISCOVER-AQ
GA_Tech
4 km
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: Calculate differences between forecasts (B) and observations (O) at each AIRNOW station as a time series
Pair up AIRNOW stations, and calculate the correlation coefficients between the two time series at the paired stations
Plot the correlation as a function of the distance between the two stations,
Intercept Rz can be used to calculate the ratio between model error (EB) and and observational error (including representative error)
Horizontal length scale can be inferred as well

## Slide 10: Analysis field Verification: AIRNOW O3 & PM 2.5 over BW SIP
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: Raqms
The RAQMS analyses include assimilation of real-time Aura MLS stratospheric ozone profiles (above 50mb) and cloud cleared OMI total column ozone as well as Terra and Aqua MODIS aerosol optical depth that uses modeled upper tropospheric RH to filter potential cirrus cloud contamination. Wild fire emissions are based on Terra and Aqua MODIS fire detections.

## Slide 11
PM2.5 24h avg | Obs mean | Mean bias | RMSE | Corr. Coef.
L42 | 12.3 | -7.7 | 10.4 | 0.4
L42RAQMS | 12.3 | -5.4 | 8.5 | 0.5
L42-Fire1 | 12.3 | -7.6 | 10.6 | 0.3
L42-Fire1-OI4 | 12.3 | -1.11 | 6.65 | 0.61
CONUS
PM2.5 24h avg | Obs mean | Mean bias | RMSE | Corr. Coef.
Base | 19.8 | -0.67 | 24.18 | 0.49
With L42-Fire1-OI4 field to derive LBC | 19.8 | 1.15 | 5.79 | 0.53
DISCOVER-AQ
GA_Tech
4 km
Application of analysis field for State Implementation Planning
14th CMAS, Chapel Hill, NC October 5-7, 2015

## Slide 12: Lightning Process currently used in CMAQ 5.0*
*CMAQ Version 5.0 and higher contains a scheme based on Allen et al. (2012, ACP) that was funded under NASA Applied Sciences Air Quality Program project (Ken Pickering, PI):
    Method for estimating lightning flash rates
    LNOx production per flash
    Method of allocating LNOx production in the vertical
NLDN (National Lightning Detection Network) data
Map to CMAQ grid
Calculate Total monthly Lightning flash Count over each grid
Model’s convective Precipitation rate
Model’s strike count (monthly total)
Mean LTratio used in
CMAQ NLDN/Model
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: Options in CMAQ:
On-line: Use convective precipitation rate from WRF to
parameterize flash rate
On-line: Use convective precipitation rate from WRF to
parameterize flash rate, but scale model predicted rate
such that monthly total flashes in each grid cell match
the numbers observed by the National Lightning Detection
Network (adjusted for detection efficiency and IC/CG ratio)
Off-line: Use observed hourly, gridded flash rates from NLDN
in calculation of 4-D LNOx production rates

## Slide 13
13
Preparation for operational compliance: Change OI to
Grid-point Statistical Interpolation (GSI):
Minimize this cost function successively in time (1,…., -1, )

## Slide 14: Share GSI-CMAQ configuration, meteorological and emission files with GaTech for perturbation study:
Solve for Rj that minimizes 2
Georgia Institute of Technology
uncertainties
number of obs
number of sources
DDM-3D calculated sensitivity of concentration i to source j emissions
emission adjustment ratio
weigh for the amount of change in source strengths
Courtesy: Yongtao Hu et al., “Source impacts
can be used for dynamic air quality
management” CMAS 2014
Notes: 14

## Slide 15
Construction & applications of a Regional Chemical Reanalysis service:
The analysis forward model is tested and used to generate July 2011
analysis fields.
Data Set assimilated: RAQMS (MLS, OMI O3, MODIS AOD); HMS Fire; GOES cloud fraction for photolytic rate correction; MODIS AOD; AIRNow PM2.5
July 2011 analysis fields was used by Georgia Tech for a 14-day SIP simulation and showed significant improvement in RMSE
DISCOVER-AQ related lessons-learned that can help this project:
  Flight transects to help fine tune vertical structure
Next sets: VIIRS AOD, Fire-work emissions, lightning NOx; OMI SO2;
PAR adjustment by retrievals
Verification to include data from O3 lidar network & AERONET
Transition assimilation codes to GSI-based NCEP ops compliance
Production mode generation of analysis field for 2010
Application and development of end-users:
  Health impact studies (Lee and Liu 2014, IJER & Public Health)
  HTAP tasks
  Outreach: Hosted in RSIG and NOAA forecasting sites
Summary
14th CMAS, Chapel Hill, NC October 5-7, 2015
Notes: An important source of pm -- strong sensitivity to seasonality and geographical characteristics

## Slide 16
16
EXTRA SLIDES
Contact: Pius.Lee@noaa.gov
http://www.arl.noaa.gov/

## Slide 17
LNOx Production Per Flash:
500 moles NOx per flash assumed for continental US based on
INTEX-A GEOS-Chem results (e.g., Hudman et al., 2007, JGR)
and cloud-resolved model simulations for individual storms
constrained by anvil aircraft observations from several
field programs (Ott et al., 2010, JGR)
However, estimates of LNOx production from OMI observations
over the Gulf of Mexico and surrounding coastal regions
are ~190 to 250 moles per flash (Pickering et al., 2015, JGR,
to be submitted)
User can modify moles per flash for IC and CG flashes
Vertical Distribution of LNOx Production:
Based on Koshak et al. (2014, Atmos. Res.) vertical distributions
of lightning channel lengths from Northern Alabama Lightning
Mapping Array -- work sponsored by NASA Applied Science
Air Quality Program

## Slide 18
Deep Convective Clouds and Chemistry (DC3) Case Study – May 29-30, 2012
Multicell storm in
NW Oklahoma in
early evening of
May 29 sampled by
NASA DC-8 and
NCAR G-V; storm
simulated using
WRF-Chem at 1-km
resolution
Model-calculated reflectivity and aircraft tracks
Trajectories show transport of storm outflow to Southern Appalachians by early afternoon May 30, where NO2 peak was detected by OMI and DC3 research aircraft
Pickering, Cummings, Allen
WRF-Chem -- Vertical Cross Section for NOx
WRF-Chem (cloud-resolved) 0100 UT
14th CMAS, Chapel Hill, NC October 5-7, 2015

## Slide 19: MODIS (Moderate Resolution Imaging Spectroradiometer) AOD
http://terra.nasa.gov/About/
Orbit: | 705 km, 10:30 a.m. descending node (Terra) or 1:30 p.m. ascending node (Aqua)
Swath Dimensions: | 2330 km (cross track) by 10 km (along track at nadir)
Spatial Resolution: | 250 m (bands 1-2) 500 m (bands 3-7) 1000 m (bands 8-36)
Courtesy :NESDIS
National correlation map between AIRNow measurement and MODIS AOD
Typically good correlation between
surface PM2.5 and AOD retrieved
by MODIS